## Slide 1
Flood Frequency
First Street Foundation (FSF) |  |  | 
Flood Recurrence Interval and Flood Size (2022, 2037, 2052)* | Annual Probability (flooding at least 1 cm) | Cumulative Probability - Flooding at least once over 30 years | First Street Risk Description
500 yr (1 in 500) | 0.2% | >0% | Any Risk
100 yr (1 in 100) | 1% | >26% | Substantial Risk
20 yr (1 in 20) | 5% | > 85% | 
5 yr (1 in 5) | 20% | >99% | Almost Certain Risk
Climate scenarios available for 3 flood depth years (2022-today, 2037-15 years, 2052-30 years) |  |  | 
2022 Flood Study Sources: FEMA and First Street Foundation (FSF)
FEMA |  |  | 
Flood Recurrence Interval and Flood Size | Annual Probability | Cumulative Probability - Flooding at least once over 30 years | FEMA Risk Description
 | 0.2% + 1 ft. |  | Risk
500 yr (1 in 500) | 0.2% | 6% | Moderate Risk
100 yr (1 in 100) Plus confidence error | 1%+ |  | 
100 yr (1 in 100) | 1% | 26% | High Risk
50 yr (1 in 50) | 2% | 45% | High Risk
25 yr (1 in 25) | 4% | 71% | High Risk
10 yr (1 in 10) | 10% | 96% | High Risk
Climate scenarios generated from BFE + 1 ft. or 1%+ Recurrence interval |  |  | 
Frequency: Probability that a flood of a specific size will be equaled or exceeded in any given year.
5-, 10-, 20-, 25-, 50-, 100-, and 500-year flood elevations (above sea level) refer to expected water levels of the 20%, 10%, 5%, 4%, 2%, 1%, and 0.2% annual chance flood events.

## Slide 2
FEMA Flood Frequency Levels

## Slide 3
FSF Flood Frequency Levels

## Slide 4
FEMA 500-YR (0.2%)

## Slide 5
FSF 500-YR (0.2%)

## Slide 6
Flood Models and Studies
Source: FEMA
Relationship between flood recurrence intervals and the probability of an event occurring within a given period

## Slide 7
Flood Characteristics
Flood Characteristics Impacting Community
Frequency: Probability that a flood of a specific size will be equaled or exceeded in any given year
  5-, 10-, 20-, 25-, 50-, 100-, and 500-year flood elevations (above sea level) refer to expected water levels of the 20%, 10%, 5%, 4%, 2%, 1%, and 0.2% annual chance flood events. A 1000-yr flood has a 0.1% chance of happening in any given year.
  FEMA’s 1%+ flood elevations measures how high the 100-year flood could be given the statistical uncertainties in flood modeling. It represents the upper 84-percent confidence limit of the statistical error for calculating the 1-percent annual chance event.
  The relative frequency of any given flood (e.g., 5-year or 10-year) serves as a useful reference point when selecting a mitigation options and evaluating cost effectiveness.
Depth: Flood depth or water surface elevation above the ground surface
  Critical during design considerations, as it is often the primary factor in evaluating the potential for flood damage
  Flood depth sources include flood models and high water marks which measure the degree of flooding
Velocity: Speed at which the floodwaters are flowing
  Flowing water often causes erosion and scour, as well as debris impacts and hydrodynamic forces.
  FEMA’s detailed engineering studies provide river/stream flows
Duration: Measure of how long water remains above normal levels.
  Prolonged contact with floodwaters may make some mitigation measures, including dry flood-proofing, inappropriate because of the increased chance of seepage and potential structural failure.
  Long periods of inundation are more likely to cause greater damage to structural members and finishes than short periods of flooding.
Rate of Floodwater Rise and Fall: Floodwater that rises very quickly with little or now warning
  Steep topography and locations with small drainage areas may experience flash flooding in which floodwater can rise very quickly with little or no warning.
  High-velocity water flows usually accompany flash floods and preclude certain types of flood mitigation measures, especially those requiring human intervention
  Rapid rates of the rise and fall of floodwater can also lead to unequal hydrostatic pressures on a building. The probability of unequal hydrostatic pressures increases when building exteriors are designed to be watertight
Historical Information: Use past information like the high-water marks of the 2016 Flood as an indication of the nature and severity of effects likely to occur during future events.
Source: FEMA 2013

## Slide 8
Rainelle New Reconstruction
First Floor Height ABOVE 2016 Flood HWM; 1-percent chance (100-yr) flood
5.9’ (FEMA 1% + 2’ FBD)
9.9’ (FEMA 1%+ / 100-Yr; 0.2%)
6.5’ (2016 High Water)
8.2’ (FSF 1% / 100-Yr)
12.2’ (FSF 0.2% / 500-Yr )
 | HEIGHT (ft.)
BUILDING | 
First Flood Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FSF 20% (5-Yr) | 2.3
FEMA 1% (100-Yr) | 3.9
FEMA 100-Yr + 2.0 Ft. Freeboard | 5.9
2016 Flood HWM | 6.5
FSF 1% (100-Yr) | 8.2
FEMA 1%+, 0.2% | 9.9
FSF 0.2% (500-Yr) | 12.2
182 Seventh Street, Rainelle, WV, 25962
Building 13-13-0001-0054-0000_182
3.9’ (FEMA 1% / 100-Yr)
2.3’ (FSF 20% / 5-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
First Floor Height BELOW 1%+, 0.2-percent chance (500-yr) floods
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.

## Slide 9
Flood Visualization 4 feet

## Slide 10
Flood Visualization 8 feet

## Slide 11
Building 13-13-0001-0054-0000_182
Chart: Building Value ($) Between years 2015-2022
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
 | 26040 | 26340 | 2880 | 0 | 21060 | 21060 | 20820 | 20880

## Slide 12
Sewell Creek Flood Study Profile
2022 Preliminary 1% Base Flood (100-Yr) Elevation 1850.7 ft for Building 13-17-0009-0026-0000_138
New 2022 FEMA Maps
Only the floodway or main channel of the 2012 FEMA flood maps was mapped and not the floodway fringe of the 1% chance (100-yr) floodplain.
The 2022 base flood elevation (100-yr) for a majority of Rainelle between 1st and 14th Streets is 2,393 feet. A similar base flood elevation was mapped for the 1987 flood maps for structures northwest of Main Street (U.S. 60).
The “1-percent plus” is a measure of how high the 1% flood even could be given the statistical uncertainties in flood modeling. The backwater flooding from Meadow River results in more uncertainty of the flood model and thus a wider confidence level. The 1%+ flood elevation is six feet higher than 1% elevation and same as the 02%.
182 7th Street (Bldg.13-13-0001-0054-0000_182
Confluence of Little Sewell Creek
Confluence of Wolfren Creek
Sewell Creek 2022 Flood Study Profile
The "Regulatory Floodway" is the channel of a river or other watercourse and the adjacent land areas that must be reserved in order to discharge the base flood without cumulatively increasing the water surface elevation more than a designated height. Source: FEMA

## Slide 13
WSS New Reconstruction
First Floor Height (FFH) ABOVE 1-percent chance (100-yr) flood
7.4’ (FEMA 1% / 100-Yr + 2’ FBD)
6.4’ (FEMA 1%+; Climate BFE+1)
6.5’ (2016 High Water)
7.4’ (FSF 0.2% / 500-Yr)
7.2’ (FEMA 0.2% / 500-Yr )
 | HEIGHT (ft.)
BUILDING | 
First Flood Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FSF 20% (5-Yr) | 3.4
FEMA 1% (100-Yr) | 5.4
FSF 1% (100-Yr) | 5.7
FEMA 1%+; Climate (BFE + 1ft) | 6.4
2016 Flood HWM | 6.5
FEMA 0.2% (500-Yr) | 7.2
FEMA 100-Yr + FBD | 7.4
FSF 0.2% (500-Yr) | 7.4
138 Mill Street, White Sulphur Springs, WV, 24986
Building 13-17-0009-0026-0000_138
5.4’ (FEMA 1% / 100-Yr)
3.4’ (FSF 20% / 5-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
First Floor BELOW 2016 HWM; 1%+,0.2-percent chance (500-yr) floods

## Slide 14
Building 13-17-0009-0026-0000_138
Chart: Building Value($) Between 2015-2022
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
 | 14520 | 14580 | 1440 | 0 | 39360 | 40140 | 40500 | 41400

## Slide 15
Howard Creek Flood Study Profile
https://data.wvgis.wvu.edu/pub/NSF/FloodProfiles/54025CV002B.pdf#page=43
2022 Preliminary 1% Base Flood (100-Yr) Elevation 1850.7 ft for Building 13-17-0009-0026-0000_138
Preliminary 2022 FEMA Maps
2022 Base Flood Elevation increased 1 to 1.5 feet from the 2012 FEMA Map between Dry Creek Bridge (Big Draft Rd) and Wades Creek Bridge (Garden St)
Bldg. 13-17-0009-0026-0000_138 1% WSEL 1850.7 ft.
Confluence of Dry Creek
Confluence of Wades Creek
For bridges shown on the flood profile, the structure is represented by an “I” symbol. The top of the bridge symbol represents the top of road and the bottom of the symbol represents the low chord (or low steel) of the bridge.
1.5’ ponding upslope
of Garden Street Bridge
FEMA FIS Technical Reference 2019
3.5’ ponding upslope
of Big Draft Bridge

## Slide 16
Thousand Year Flood?
WVNSTV 2021
WV Public Broadcasting 2016
WVNSTV 2022
Some websites like MH3WV clarify it as a 1,000-year rainfall event according to the NWS

## Slide 17
Thousand Year Flood?

## Slide 18
1,000-Year Flood?
What is a 1,000-year flood?
The term “1,000-year flood” means that, statistically speaking, a flood of that magnitude (or greater) has a 1 in 1,000 chance of occurring in any given year. In terms of probability, the 1,000-year flood has a 0.1% chance of happening in any given year. These statistical values are based on observed data.
How can a 1,000-year rainfall not result in a 1,000-year flood?
It comes down to a number of factors, including the pattern of movement of the rainstorm in each particular watershed, the conditions of the soil and plant matter in the watershed, and the timing of the rainstorm in one watershed versus other watersheds. For example, if the ground is already saturated before a rainstorm, much of the rain will run off into streams, but if the ground is dry, it will soak up more of the rain and the runoff will be less significant.
Source: USGS | NOAA Climate.gov | NWS Blacksburg
In the immediate aftermath of the June 2016 flood, USGS and the Federal Emergency Management Agency (FEMA) initiated a cooperative study to evaluate the flood’s magnitude, extent, and probability of occurrence.
A Thousand-year Downpour or Rainfall is different than a Thousand-year Flood

## Slide 19
1,000-Year Flood?
Source: FEMA
THE FLOOD IN JUNE 2016 WAS NOT A RARE, “1 IN 1,000 YEAR EVENT.” ALTHOUGH THE AMOUNT OF RAIN THAT FELL WAS UNUSUAL, RAINFALL AND FLOODING ARE DIFFERENT.
Most of the June 2016 peak flows examined by USGS were found to be much more likely than a “1,000 year event.” In fact, the most extreme flooding was found to have 0.2% chance of happening in any given year (1 in 500) to a 5% chance (1 in 20).

## Slide 20
1,000-Year Flood?
THE LATEST DATA SHOW THAT THE LEVEL OF FLOODING THAT OCCURRED IN 2016 COULD HAPPEN MORE FREQUENTLY THAN PREVIOUSLY THOUGHT. IN MANY AREAS, THAT EVENT HAS AT LEAST A 1% CHANCE OF HAPPENING EACH YEAR IN THE FUTURE.
For all but one of the gages analyzed, what used to have a 1% chance of happening each year, now has a greater chance of happening each year. In other words, what was considered the “100 year flow (1%)” could now be called the “21 year flow (4.8%)” for the gage at the Meadow River (watershed for Rainelle) at Nallen or the “77 year flow (1.3%)” for the Greenbrier River at Alderson (watershed for White Sulphur Springs).
Greenbrier River at Alderson
Source: FEMA
Source: USGS Report |AEP Meadow River | Pubs Site
USGS Study: Three annual exceedance probability (AEP) curves calculated using the Expected Moments Algorithm (EMA) method were used to compare 100-year (AEP 0.0100) annual peak stream flows at 12 streamflow-gaging stations, measured from initiation of the period of record (POR) at each streamflow-gaging station through 1990, 2015, and 2016.