## Slide 1
Mitigation Measures
Category | Mitigation Indicator | White Sulphur Springs | Rainelle
Mitigated Structures | Mitigation Reconstruction or Elevated Structures to Design Flood Elevation (DFE) | 15 | 45
 | Rehabilitated/Repaired Structures | 394 | 278
 | Unmitigated Low Value Structures | 14 | 49
 | Structures Removed (vacant parcel) | 394 | 278
Open Space Preservation | Buyout Parcels (Deed Restricted) | 16 | 18
 | Community-Owned Vacant Parcels | 66 | 88
 | Area of Open Space Preservation (OSP) | 5 Acres | 3 Acres
 | Ratio of Open Space Preservation (OSP to SFHA) | 2.6% | 4.5%
Building Value Recovery | Net Value 2016-2022 Tax Assessment Value | + $6.1 Million | - $1.0 Million
Loss Avoidance 100-year Flood | Loss Avoidance by Elevating or Removing Structures (preliminary results) | $2.6 million | $2.3 million

## Slide 2
Mitigation Measures (continued)
Category | Mitigation Indicator | White Sulphur Springs | Rainelle
Resiliency to Future Floods | Percent Residential Structures in 100-year floodplain elevated to Design Flood Elevation (DFE) | 58% | 30%
Higher Standards | Freeboard (safety elevation factor above BFE) | 2 ft. | 2 ft.
 | Community Rating System (above min. requirements) | No | No
Floodplain Management | Incorporated Place a compacted floodplain management area to enforce floodplain ordinance | Yes | Yes
 | Continuity of operations and immediate response to disasters | ? | ?
 | Record keeping (permits, EC’s, substantial damage) | ? | ?
Flood Insurance | Number of Policies 2019 | 133 | 44
Risk Communications | Flood Risk Disclosure Laws in West Virginia | F grade | F grade
 | Outreach to property owners about changes to flood maps (mapped in/mapped out of SFHA) | ? | ?

## Slide 3
Floodplain Building Value Recovery
Chart: Cumulative Building Values in Floodplain (2015-2022)
| 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
White Sulphur Springs | 22597283.3333 | 23033150 | 13433616.6667 | 21459933.3333 | 22383366.6667 | 22912900 | 26221233.3333 | 29151350
Rainelle | 13098033.3333 | 13256766.6667 | 5003433.3333 | 9445883.3333 | 11004566.6667 | 11092116.6667 | 11349883.3333 | 12304966.6667
COMMUNITY | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Rainelle (n=326) | 13.1 Million | 13.3 Million | 5.0 Million | 9.4 Million | 11.0 Million | 11.1 Million | 11.3 Million | 12.3 Million
White Sulphur Springs (n=409) | 22.6 Million | 23.0 Million | 13.4 Million | 21.5 Million | 22.4 Million | 22.9 Million | 26.2 Million | 29.2 Million
Source: Tax assessment database. May not include values for tax exempt properties.

## Slide 4
Rainelle Relocation Community

## Slide 5
WSS Relocation Community

## Slide 6
Rainelle Mitigated Properties

## Slide 7
WSS Mitigated Properties

## Slide 8
Building Design Flood Elevation

## Slide 9
Building Design Flood Elevation

## Slide 10
Rainelle Mitigation Reconstruction
First Floor Height ABOVE 2016 Flood HWM; 1-percent chance (100-yr) flood
5.9’ (FEMA 1% + 2’ FBD)
9.9’ (FEMA 1%+ / 100-Yr; 0.2%)
6.5’ (2016 High Water)
8.2’ (FSF 1% / 100-Yr)
12.2’ (FSF 0.2% / 500-Yr )
 | HEIGHT (ft.)
BUILDING | 
First Flood Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FSF 20% (5-Yr) | 2.3
FEMA 1% (100-Yr) | 3.9
FEMA 100-Yr + 2.0 Ft. Freeboard | 5.9
2016 Flood HWM | 6.5
FSF 1% (100-Yr) | 8.2
FEMA 1%+, 0.2% | 9.9
FSF 0.2% (500-Yr) | 12.2
182 Seventh Street, Rainelle, WV, 25962
Building 13-13-0001-0054-0000_182
3.9’ (FEMA 1% / 100-Yr)
2.3’ (FSF 20% / 5-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
First Floor Height BELOW 1%+, 0.2-percent chance (500-yr) floods
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.

## Slide 11
WSS Mitigation Reconstruction
First Floor Height (FFH) ABOVE 1-percent chance (100-yr) flood
7.4’ (FEMA 1% / 100-Yr + 2’ FBD)
6.4’ (FEMA 1%+; Climate BFE+1)
6.5’ (2016 High Water)
7.4’ (FSF 0.2% / 500-Yr)
7.2’ (FEMA 0.2% / 500-Yr )
 | HEIGHT (ft.)
BUILDING | 
First Flood Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FSF 20% (5-Yr) | 3.4
FEMA 1% (100-Yr) | 5.4
FSF 1% (100-Yr) | 5.7
FEMA 1%+; Climate (BFE + 1ft) | 6.4
2016 Flood HWM | 6.5
FEMA 0.2% (500-Yr) | 7.2
FEMA 100-Yr + FBD | 7.4
FSF 0.2% (500-Yr) | 7.4
138 Mill Street, White Sulphur Springs, WV, 24986
Building 13-17-0009-0026-0000_138
5.4’ (FEMA 1% / 100-Yr)
3.4’ (FSF 20% / 5-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
First Floor BELOW 2016 HWM; 1%+,0.2-percent chance (500-yr) floods

## Slide 12
Thousand Year Flood?
WVNSTV 2021
WV Public Broadcasting 2016
WVNSTV 2022
Some websites like MH3WV clarify it as a 1,000-year rainfall event according to the NWS

## Slide 13
Example Areas of Focus
in White Sulphur Springs

## Slide 14
Example Areas of Focus
in White Sulphur Springs…

## Slide 15
Example Areas of Focus
in Rainelle

## Slide 16
Example Areas of Focus
in Rainelle…

## Slide 17
Examples of Mitigation Reconstruction
in White Sulphur Springs
Building ID: 13-17-0008-0152-0000_195
Flood Tool Link
Building ID: 13-17-0009-0009-0000_148
Flood Tool Link
Building ID: 13-17-0009-0009-0000_148
Flood Tool Link

## Slide 18
Example of Mitigation Reconstruction
in Rainelle
Building ID: 13-13-0001-0069-0000_108
Flood Tool Link
Building ID: 13-13-0005-0165-0000_256
Flood Tool Link
Building ID: 13-13-0001-0054-0000_182
Flood Tool Link

## Slide 19
Criteria, Rationale, and Data Sources
Mitigation Indicator | Criteria | Rationale | Data Source
Total Elevated Structures, Reconstruction to Design Flood Elevation (DFE) | Number of newly Constructed or remodeled structures elevated to Design Flood Elevation (DFE) (2 ft above the BFE) on open or closed foundations | A comprehensive inventory of mitigated structures results in more accurate building level risk assessments and shows how communities have applied flood adaptive measures in response to major flood events. | Elevation certificates, building pictures (step 7” rise, cinder block 8”), and major post-disaster mitigation reconstruction projects (1977 and 2016 floods)
Percent Structures Elevated to DFE in Total Residential Buildings | Percentage of the elevated structures in the total residential buildings in SFHA |  | 
Loss Avoidance by Elevating Structures | Difference between loss estimates in communities using the Hazus model with the first floor height of 1 ft (not elevated) and elevated to DFE (2 ft above BFE) | With significant investment being made in mitigation by elevating, demonstrating cost-effectiveness is crucial for continued support. Loss Avoidance Studies (LAS) quantify the losses avoided (also known as damage prevented or benefits) due to the implementation of the projects. | BLRA of 10/19/2022 (based on 2022 tax assessment), Total Exposure in Floodplain (TEIF), Building percent damage estimate values, Depth grids
Buyout Parcels | Number of verified buyout land parcels located within floodplains that experience frequent flooding and damage due to flood events altered, purchased, or have deed restrictions placed upon them by FEMA or other agencies | Buyout properties can prevent loss of life and property damage. Property owners/communities with public lands in floodplains are compensated for their land, and the land usually becomes public green space or restored to its natural floodplain function. | Data of Natural Resources Conservation Service (NRCS) to identify the verified buyout parcels with floodplain easements

## Slide 20
Criteria, Rationale, and Data Sources
Mitigation Indicator | Criteria | Rationale | Data Source
Area of Open Space Preservation (OSP) | Area of preserved open spaces with no existing buildings or structures, filling, large pavement, or other encroachment to flood flows located in the community’s regulatory floodplains including the SFHA as shown on the community’s Flood Insurance Rate Map (FIRM) attached with a signed statement by a public or creditable private owner or some regulations on the parcel preventing from construction, fillings, or other encroachments on flood flows in the future. | Open Space Preservation restores the floodplain to its natural function and provides opportunities for credits from FEMA’s Community Rating System (CRS). | Data of Natural Resources Conservation Service (NRCS) for buyout properties & FEMA FIRM (2012 & 2022)
Ratio of Open Space Preservation (OSP to SFHA) | Ratio of the preserved open spaces in the impact adjusted Special Flood Hazard Area (SFHA) (after removing waterbodies larger than 10 acres in addition to the federally owned lands). |  | 
Number of Policies | Number of flood insurance policies in force in the community | Although higher number of policies in force can equate to a riskier area, it can show more mitigation policies in force. | Community Information System (CIS) 2019