## Slide 1
WSS Unmitigated
First Floor Height (FFH) BELOW FEMA 1-percent chance (100-yr) flood
6.0’ (FEMA 1% / 100-Yr + 2’ FBD)
4.5’ (FEMA 1%+; Climate)
4.0’ (2016 High Water)
3.4’ (FSF 0.2% / 500-Yr)
5.3’ (FEMA 0.2% / 500-Yr )
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 2.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FSF 20% (5-Yr) | 0.0
FSF 1% (100-Yr) | 1.5
FSF 0.2% (500-Yr) | 3.4
FEMA 1% (100-Yr) | 4.0
2016 Flood HWM | 4.0
FEMA 1%+ (Climate) | 4.5
FEMA 0.2% (500-Yr) | 5.3
FEMA 100-Yr + FBD | 6.0
220 Central Avenue, White Sulphur Springs, WV, 24986
Building 13-17-0008-0139-0000_220
4.0’ (FEMA 1% / 100-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
First Floor BELOW 2016 HWM; 1%+,0.2-percent chance (500-yr) floods
1.5’ (FSF 1% / 100-Yr)

## Slide 2
Rainelle Unmitigated
First Floor Height (FFH) BELOW FEMA 1-percent chance (100-yr) flood
6.0’ (FEMA 1% / 100-Yr + 2’ FBD)
10.1’ (FEMA 1%+; Climate)
8.3’ (2016 High Water)
12.1’ (FSF 0.2% / 500-Yr)
9.9’ (FEMA 0.2% / 500-Yr )
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 0.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FSF 20% (5-Yr) | 2.1
FEMA 1% (100-Yr) | 4.0
FEMA 100-Yr + FBD | 6.0
FSF 1% (100-Yr) | 8.1
2016 Flood HWM | 8.3
FEMA 0.2% (500-Yr) | 9.9
FEMA 1%+ (Climate) | 10.1
FSF 0.2% (500-Yr) | 12.1
166 7th Street, Rainelle, WV, 25962
Building 13-13-0001-0047-0000_166
4.0’ (FEMA 1% / 100-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
First Floor BELOW 2016 HWM; 1%+,0.2-percent chance (500-yr) floods
8.1’ (FSF 1% / 100-Yr)
2.1’ (FSF 1% / 100-Yr)

## Slide 3
190 Crescent Avenue, White Sulphur Springs, WV, 24986
Flood vents < 1ft from ground
Elevated (potentially to BFE), but not to DFE (highest depth for structure = 2.5 ft)
Mechanicals at ground level
354 Horton Ave. E, Rainelle, WV, 25962
Some flood vents < 1 ft from ground
Some vents > 1ft from ground; Elevated but not to BFE (3.4 ft)
Mechanicals at ground level
184 Central Venue, White Sulphur Springs, WV, 24986
Partial Mitigation
Elevated
No flood vents
Mechanicals at ground level
Flood vents < 1 ft from ground
Mechanicals elevated
Elevated, but not to BFE (3.9 ft)