## Slide 1
Building Exposure
White Sulphur Springs and Rainelle
Category | Exposure Indicator | White Sulphur Springs | Rainelle | Ratio* in WV Incorporated Areas (2021)
Buildings by Flood Zone (Count & Value) | Total Primary Building Count in Floodplain | 425 (Rank***: 12th) | 338 (Rank: 18th) | 59 (Median)
 | Building Ratio b/w Floodplain & Community Total | 26% | 34% | 9%
 | Total Primary Building Value in Floodplain of Community | $41.02M (Rank: 16th) | $16.89M | $6.42M (Median)
 | Median Building Value in Floodplain | $49K | $38K | $42K
 | Building Count in Floodway** (High Velocity) | 105 (Rank: 6th) | 47 (Rank: 18th) | 12 (Avg.)
 | Percent Building Count in Floodway** (High Velocity & Depth) | 25% | 14% | 8%
 | New Maps: Bldgs. “Mapped In” SFHA | 75 (Rank: 11th) | 325 (Rank: 3rd) | 19 (Avg.)
 | New Maps: Bldgs. % Count “Mapped In” SFHA | 18% | 96% | 14%
 | New Maps: Bldgs. “Mapped In” Floodway | 14 | 38 | 97
 | New Maps: Bldgs. “Mapped Out” SFHA | 117 (Rank: 8th) | 1 | 19 (Avg.)
 | New Maps: Bldgs. % Count “Mapped Out” SFHA | 28% | 0% | 14%
Category | Exposure Indicator | White Sulphur Springs | Rainelle | Ratio* in WV Incorporated Areas (2021)
Building Ownership | Owner Occupied Residential Buildings in Floodplain | 208 | 153 | 65%
 | Percent Owner Occupied Residential Buildings in Floodplain | 49% | 45% | 
Building Occupancy and Value | Residential Building Count in Floodplain | 372 (Rank: 12th) | 250 | 44
 | Percent Count Residential Building in Floodplain | 88% | 74% | 81%
 | Non-Residential Building Count in Floodplain | 53 | 88 (Rank: 11th) | 12
 | Percent Count Non-Residential Bldgs. in Floodplain | 12% | 26% | 19%
 | Residential Building Value in Floodplain | $20.45M (Rank: 16th) | $9.29M | $2.11M
 | Percent Residential Value in Floodplain | 50% | 55% | 31%
 | Non-Residential Building Value in Floodplain | $20.56M | $7.60M | $2.99M
 | Percent Non-Residential Value in Floodplain | 50% | 45% | 69%
 | Mobile Homes in Floodplain | 4 | 14 | 5
 | Percent Mobile Homes in Residential Buildings in Floodplain | 1% | 4% | 11%
Category | Exposure Indicator | White Sulphur Springs | Rainelle | Median & Ratio in WV Incorporated Areas (2021)
Building Year Construction/ FIRM Status | Median Construction Year in Floodplain | 1940 | 1950 | 1947
 | % Pre-FIRM Structures (includes “unknown”) | 88% | 77% | 77%
 | % Post-FIRM Structures (also “mapped-in SFHA” Post-FIRM structures regulated to Pre-FIRM) | 12% | 23% | 13%
Physical Structural Vulnerability (Basements, Stories, & Value) | Primary Buildings with Basements in Floodplain | 93 | 27 | 37%
 | Percent Count Buildings with Basements in Floodplain | 22% | 8% | 
 | One-Story Residential Buildings in Floodplain | 336 | 292 | 69%
 | Percent Count One-Story Residential Buildings in Floodplain | 79% | 86% | 
 | Red Tag: Dilapidated/Vacant Residential & Commercial Buildings | 20 | 56 | 6
 | Percent Low Valued (Red Tag) Structures | 5% | 17% | 4%
* For numbers and dollar values, used median, or average where the median was zero or too low, in the state’s 213 incorporated areas
** Floodway includes both the effective and advisory floodways (2012 & 2022 checked manually)
*** Ranks mentioned based on the BLRA data of April 2022 where the community is among the top 20 incorporated areas in WV
The red texts show large difference, to the risk side, from the state ratios.
The green texts show large difference, to the resilience side, from the state ratios.
Flood Risk Assessment in Rainelle:
Exposure,
Vulnerability, and
Loss Indicators
Building Exposure…
White Sulphur Springs and Rainelle
Building Exposure/Physical Vulnerability
White Sulphur Springs and Rainelle
Significant Structures Exposure
White Sulphur Springs and Rainelle
The red texts show large difference, to the risk side, from the state ratios.
Category | Exposure Indicator | White Sulphur Springs | Rainelle | Average in WV Incorporated Areas (2021)
Significant Structures Count | Number of Essential Facilities in the Moderate Risk 0.2%-Annual-Chance Floodplain | 2 | 2 | 2
 | Number of Community Assets (Non-Historical) in the High-Risk 1%-Annual-Chance Floodplain | 8 | 7 | 3
Exposure, Examples of Low Valued Structures in Floodplain
Rainelle
Human Exposure/Loss
White Sulphur Springs and Rainelle
WV GIS Technical Center
May 2023
Physical Flood Loss
White Sulphur Springs and Rainelle
Category | Loss Indicator | White Sulphur Springs | Rainelle | Rate* in WV Incorporated Areas (2021)
Physical (Building) Loss By 1%-Annual-Chance Flood Event | TEIF Building Dollar Loss Estimates | $1,225K | $994K | $1,246K (Avg.)
 | TEIF Building Loss Ratio | 3% | 6% | 10%
 | Median Individual Building Damage | $3K | $2K | $7K (Mdn.)
 | Substantial Damage (>50%) Estimates | 0 89 in 2016 Flood | 1 | 7 (Avg.)
 | Percent Substantial Damage Estimates | 0% | 0% | 6% (Avg.)
 | Moderate Damage (10-50%) Estimates | 78 98 in 2016 Flood | 106 | 47 (Avg.)
 | Percent Moderate Damage Estimates | 18% | 31% | 34% (Avg.)
 | Building Debris Removal Estimates | 450 ton | 809 ton | 165 ton (Mdn.)
 | Number of Previous Paid Losses | 89 | 152 (Rank**: 20th) | 63 (Avg.)
 | Dollar Amount of Previous Insurance Claims | $2,975K (Rank: 15th) | $3,720K (Rank: 10th) | $845K (Avg.)
 | Number of Repetitive Loss Structures | 2 | 23 | 3 (Mdn.)
Structures with High Building Loss (Estimated)
Rainelle
Social Vulnerability Indicators
White Sulphur Springs and Rainelle
Vulnerability Indicators |  | White Sulphur Springs | Rainelle | State Ratio | National Ratio
 | Poverty Rate | 14.4% | 37.0% | 17.3% | 12.9%
 | Unemployment Rate | 21.4% | 33.6% | 23.8% | 14.7%
 | Vulnerable Ages Ratio | 41.7% | 39.8% | 30.8% | 28.3%
 | Disability Ratio | 17.8% | 26.9% | 18.7% | 13.0%
 | Population Growth Ratio | -9.1% | -20.9% | -3.2% | 7.4%
 | Renter-Occupied Ratio | 42.8% | 43.0% | 26.8% | 36.0%
 | Housing Values Less than $50K Housing Median Value | 3.9% $125,700 | 37.5% $59,400 | 16.9% $119,600 | 6.6% $229,800
The red texts show more than 5% of difference, to the vulnerability side, from the state ratios.
Building Exposure, High-Value Structures
Rainelle
Residential vs. Non-Residential Parcels
Rainelle
Tax Class, Owner- vs. Renter-Occupied Parcels
Rainelle
Building Exposure, Future Map Conditions
Rainelle
Building Damage Loss Estimates
Rainelle
Infrastructure Exposure, Inundated Transportation
Rainelle
Renters clearing away their belongings after the 2016 flood
An inundated basement in the 2016 flood
Building ID: 13-13-0001-0176-0000_214
Building ID: 13-13-0001-0127-0000_178
Church of God in Rainelle:
Building ID: 13-13-0005-0366-0000_373
Hazard occupancy Class: REL1 (Religious)
FIRM Status: Post-FIRM regulated to Pre-FIRM
Appraised Value: $435,000 (Highest in significant structures)
Highest Value:
Building ID: 13-13-0004-0194-0000_506
Hazard Occupancy Class:
FIRM Status: Post-FIRM (1994)
regulated to Pre-FIRM
Appraised Value: $1,443,900
(New flood study mapped-in SFHA)
Highest Residential (RESx) Value:
Building ID: 13-13-0009-0011-0000_242
Hazard Occupancy Class: RES1 (Residential 1 Family)
FIRM Status: Pre-FIRM (1967)
Appraised Value: $107,400
(New flood study mapped-in SFHA)
Highest Apartment Building Value:
Building ID: 13-13-0005-0341-0000_249
Hazard Occupancy Class: RES3B (Multi-Family 3-4 Units)
FIRM Status: Pre-FIRM (1960)
Appraised Value: $63,900
(New flood study mapped-in SFHA)
Highest Building Loss (USD)
in Rainelle:
Building ID: 13-13-0001-0077-0000_144
Hazard Occupancy Class: RES1 (Residential 1 Family)
FIRM Status: Post-FIRM regulated to Pre-FIRM (2005)
Water Depth in Structure: 3.7 ft (minus rated -4 ft)
Appraised Value: $92,800
Estimated Building Loss: $41,667
Building Damage Percentage: 45%
Highest Building Damage Percentage
in Rainelle:
Building ID: 13-13-0001-0091-0000_435
Hazard Occupancy Class: RES2 (Mobile Home)
FIRM Status: Pre-FIRM (1973)
Water Depth in Structure: 2.7 ft (minus rated -3 ft)
Appraised Value: $11,600
Estimated Building Loss: $8,120
Building Damage Percentage: 70%
Category | Exposure Indicator | White Sulphur Springs | Rainelle | Median & Ratio in WV Incorporated Areas (2021)
Human Exposure | Estimated Population Residing in High-Risk Flood Zones | 1026 | 582 | 114
 | Percentage of Population Residing in High-Risk Flood Zones | 39% | 43% | 10%
Human Loss By 1%-Annual-Chance Flood Event | Displaced Population Estimates | 462 (Rank: 17th) | 487 (Rank: 16th) | 173 (Avg.)
 | Percent of Community Population Displaced | 17% | 36% | 13%
 | Estimated Population in Need of Short-Term Shelter | 104 (Rank: 18th) | 123 (Rank: 14th) | 37 (Avg.)
* For numbers and dollar values, used median, or average where the median was zero or too low, in the state’s 213 incorporated areas
** Ranks mentioned based on the BLRA data of April 2022 where the community is among the top 20 incorporated areas in WV
The red texts show large difference, to the risk side, from the state ratios.
For Greenbrier County, Red Cross sheltering data from the 2016 flood was compared to the shelter model estimates. According to the Red Cross shelter data, a total of 114 people stayed at six designated Red Cross shelters during the flood event. However, many displaced residents also stayed at unregistered shelters, including the 300 people at the Greenbrier Resort and 129 people at the Baptist Church gymnasium in Rainelle. If the registered persons of the Red Cross Shelters requiring shelter are summed together at 543 people, then this estimate is close to the shelter need model estimate of 603 people for Greenbrier County.