## Slide 1
Risk MAP (Jefferson Co. Preliminary Flood Maps)
Risk Planning (Build Flood Resiliency)
Pre-Disaster Planning Preload WV Flood Tool Structures into FEMA’s SDE Software Update Emergency Response & Hazard Mitigation Plans using risk assessments for major storm event
Higher Standards - Municipalities Apply for CRS status Adopt higher Freeboard value of 3 ft. in floodplain mgmt. ordinance
Verify Risk Layers on WV Flood Tool Building-level assessments Open space properties Repetitive Loss Areas
Risk Mapping (Review New Flood Risk Maps)
Map Changes BFE’s (e.g., 24’ BFE change at Harpers Ferry) Floodplain Width (e.g., Shepherdstown)
SFHA Building Changes Mapped-in/Mapped Out Bldgs. LOMAs (SFHA bldgs. mapped out)
Risk Communications Outreach Letters for building changes in SFHA/Floodway
Future Map Discovery Map Zone AE Upgrades for Potomac / Shenandoah Rivers?
Risk MAP: Reduce Loss of Life and Property
Risk Assessment (Quantify Flood Risk)
Statewide Risk Assessment (aggregate level or summary reports) River/Stream Scale County Scale Unincorporated Area Scale Incorporated Area Scale Shepherdstown Harpers Ferry
Building Level Risk Assessments Unmitigated Structures Mitigated Structure
WV Flood Resiliency Framework
Web link to Slide Deck

## Slide 2
Map Changes – Harpers Ferry
Harpers Ferry: BFE change minus 24 ft.

## Slide 3
Map Changes - Shepherdstown
Harpers Ferry: BFE change minus 24 ft.
Shepherdstown: FEMA Change Viewer
Shepherdstown: WV Flood Tool

## Slide 4
Map Changes – Jefferson County
WV Flood Tool (Risk MAP View)
WV Flood Tool Public View
Floodway

## Slide 5
Buildings Mapped-In / Out of Preliminary SFHA
Floodway
Difference between FEMA’s 2009 and 2024 flood studies

## Slide 6
SFHA Building Changes: Mapped-In/Out
COMMUNITY IDENTIFICATION |  | Estimated structures in the Community | Estimated structures in the preliminary flood high hazard area | Estimated structures newly mapped in | Estimated structures newly mapped out
Community Name | Community Type |  |  |  | 
Jefferson County* | Unincorporated | 20,397 | 317 | 55 | 220
Bolivar | Incorporated | 616 | 4 | 4 | 0
Charles Town | Incorporated | 3,670 | 21 | 4 | 8
Harpers Ferry | Incorporated | 276 | 31 | 30 | 0
Ranson | Incorporated | 2,918 | 50 | 1 | 28
Shepherdstown | Incorporated | 735 | 76 | 29 | 20
JEFFERSON | County | 28,612 | 499 | 123 | 276
County Net Change in structures: - 153
County Net Change in floodway structures: - 14
* Unincorporated Area

## Slide 7
Buildings Mapped into Floodway
Double-wide Mobile Home in Ranson (FD: 2.2 ft)
$33K; Year Built: 1993 (Post-FIRM)
(Building ID: 19-08-0006-0019-0001_407)
Single-wide Mobile Home in Jefferson County* (FD: 7.0 ft)
$25K; Minus Rated: 3.5 ft; Year Built: Unknown
(Building ID: 19-02-0020-0031-0000_30)
Single Family Dwelling in Jefferson County* (FD: 14.0 ft)
$8K; Minus Rated: 10.3 ft; Year Built: 1979 (Pre-FIRM)
(Building ID: 19-06-008F-0007-0000_457)
Structures mapped from Floodplain Fringe into Floodway

## Slide 8
FEMA Region 3 Toolkit for New Flood Studies
Mail Merge Template for SFHA Mapped-in Structures
Jefferson County and Shepherdstown have 55 and 29 buildings, respectfully, mapped into the SFHA
Incorporate 1% Floodplain Building Risk Assessment Inventory into Mitigation and NFIP/CRS Management Activities
Hardy County Risk MAP
Kanawha County - Elk River PMR
Greenbrier County Risk MAP
Counties which recently sent outreach letters to homeowners:
Risk Communications: SFHA Map Change Letters

## Slide 9
276
Mapped Out SFHA
SFHA Buildings Changes: LOMAs for Mapped Out
Jefferson County
All building symbols in the floodplain fringe will become “red color” once flood maps are effective
Floodway
Mapped-out structures of the SFHA may qualify for LOMAs
WV Flood Tool LiDAR LOMA: Instructions | Guide

## Slide 10
FLOOD DEPTH MEDIAN: Floodplain structures along the Shenandoah River have high flood depths compared to 156 other major rivers/streams in the state.
MEDIAN BUILDING VALUE: Town Run and Shenandoah River rank first and fourth, respectively, of 156 major rivers/streams in the state with the highest median value of structures in high-risk flood areas.
River/Stream Building Risk Assessment
# | STATE CATEGORY RANK | River/Stream Floodplain | Building Characteristics | CATEGORY SCORE
 |  |  | Building Median Value | 
1 | 1 | Town Run | $247,700 | 100.0%
2 | 4 | Shenandoah River | $95,100 | 98.0%
3 | 24 | Potomac River | $57,300 | 85.1%
WV Risk Explorer: Stream Risk Comparison Report
# | STATE CATEGORY RANK | River/Stream Floodplain | Floodplain Characteristics |  | CATEGORY SCORE
 |  |  | Floodplain Length | Flood Depth Median | 
1 | 12 | Shenandoah River | 30.2 Miles | 7.4 Ft | 92.9%
2 | 2 | Potomac River | 143.8 Miles | 4.5 Ft | 99.3%
3 | 147 | Town Run | 2.1 Miles | 0.2 Ft | 5.8%

## Slide 11
River/Stream Building Risk Assessment
Top rivers with high building counts in SFHA are Potomac River (166), Shenandoah River (81) and Town Run (73). Town Run has highest building dollar exposure.
Region 9 Rivers/Streams
Shepherdstown

## Slide 12
Category | Flood Risk Indicator | Value for Jefferson | Indicator Score (0 - 100%) | Indicator Rating
Building Characteristics | Building Median Value | $97,450 (Median $42,200) | 100.0% | VERY HIGH
 | Bldg. Subgrade Basements Ratio | 49.5% | 94.4% | VERY HIGH
 | Bldg. Year Minus Rated Post-FIRM Ratio | 9.4% | 81.4% | Very High
Community Assets | Community Assets Historical | 120 | 94.4% | VERY HIGH
Building Damage Loss | Bldg. Substantial Damage Ratio | 24.0% | 90.7% | VERY HIGH
JEFFERSON COUNTY ranks “very high” or in the top 20% of all 55 counties in the state for the five risk indicators below. View Top 20% Risk Indicators Report for county. Click on Risk Factor links for rationales/recommendations.
JEFFERSON COUNTY UNINCORPORATED* ranks “very high” or in the top 20% of all 55 unincorporated areas in the state for the six risk indicators below. View Top 20% Risk Indicators Report for incorporated area.
Jefferson County Risk Assessment
Category | Flood Risk Indicator | Value for Jefferson County* - Unincorporated | Indicator Score (0 - 100%) | Indicator Rating
Floodplain Characteristics | Flood Depth Median | 4.7 Ft | 94.4% | VERY HIGH
Building Characteristics | Building Median Value | $93,150 (Median $37,350) | 100.0% | VERY HIGH
 | Bldg. Subgrade Basements Ratio | 48.9% | 98.1% | VERY HIGH
 | Bldg. Year Minus Rated Post-FIRM Ratio | 14.5% | 90.7% | VERY HIGH
Community Assets | Community Assets Historical | 26 | 100.0% | VERY HIGH
Building Damage Loss | Bldg. Substantial Damage Ratio | 29.7% | 90.7% | VERY HIGH
1
4
1
2
4
1
4
Statewide Rank
among the Top 5
#

## Slide 13
Jefferson County Building Risk Assessment
Jefferson County has a high number of Historical Community Assets on the National Register.
Jefferson County has very high Building Values, or more than double the statewide median value.
Source: Statewide Building-Level Risk Assessment
High Building Values
High Historical Buildings

## Slide 14
Jefferson County Resiliency
(3) Jefferson County has higher NFIP Insurance Penetration Rate than other counties
(2) Jefferson County has the lowest Social Vulnerability Index in the State
(1) Jefferson County has no Essential Facilities in the high or moderate risk floodplains

## Slide 15
Jefferson County Unincorporated* Resiliency
Jefferson County Unincorporated has a high Freeboard safety factor of 3 feet
Jefferson County Unincorporated has a high CRS Rating of Class 7

## Slide 16
Shepherdstown Risk Assessment
Building Value and Density.
Median Building Value ranks first of 229 incorporated places in the state. High density of buildings in small area.
Pre-FIRM and Basements.
Nearly 90% of structures are Pre-FIRM and nearly half have basements.
Historical Buildings.
Most building are in the National Historic District.
Sources: WV Flood Tool’s Risk Map View & Statewide Building-Level Risk Assessment
Refer to online All Risk Indicators Report

## Slide 17
Shepherdstown 3D Flood Movie
Click here to view 3D Flood Movie of Shepherdstown

## Slide 18
Example Urban Flooding
View Videos of 2021 Morgantown Flooding along Popenoe Run on Patteson Drive near WVU stadium that may occur similarly on Town Run in Shepherdstown
Courtesy of WV Hazard Library

## Slide 19
Harpers Ferry Risk Assessment
Sources: WV Flood Tool’s Risk Map View & Statewide Building-Level Risk Assessment
Building Substantial Damage Ratio highest of all 229 incorporated places in the state
Pre-FIRM Building Ratio highest of all 229 incorporated places in the state
Refer to online All Risk Indicators Report

## Slide 20
High Water Mark
Greenbrier River
Knapp Creek
744 Shenandoah St, Harpers Ferry, WV, 25425
Building ID: 19-05-0004-0025-0000_801A
Historical structure built in 1845
14’ (1936 High Water Mark)
8’ (1996 High Water Mark)
Harpers Ferry Risk Assessment
1936 Flood of Record

## Slide 21
Historical Flood Research (Harpers Ferry, WV)
Engraving of the flood in Harpers Ferry, from Harper’s Weekly, October 20, 1870
(Image courtesy of Yesterday’s America)
October 1870 Flood
(42 fatalities)
Link to WV Flood Fatality Dashboard

## Slide 22
Harpers Ferry 3D Flood Movie
Click here to view 3D Flood Movie of Harpers Ferry

## Slide 23
Utilities in Floodplain (High $ Exposure)
City of Charles Town Wastewater Treatment Plant (FD: 1 ft)
Highest CA Value ($6.8M) in Jefferson County
(Building ID: 19-03-0008-0001-0000_842)
Value source inflation adjusted to 2021
Shepherdstown Water Works Water Treatment Plant (FD: ? ft)
(Building ID: 19-10-0001-0052-0000_309) ($3.1M)
Value source inflation adjusted to 2021
Harpers Ferry Bolivar PSD Wastewater
Treatment Plant (FD: 1 ft)
(Building ID: 19-05-0004-0025-0000_192) ($462K)
Value source inflation adjusted to 2021
Backwater

## Slide 24
Building Flood Profile - Unmitigated
 | HEIGHT (ft.)
BUILDING | 
Freeboard (FBD) | 3
FLOOD DEPTH | 
FEMA 1% (100-Yr) | 13.6
FEMA 100-Yr + FBD | 16.6
FEMA 0.2% (500-Yr) | 19.6
Post-FIRM
Single Family Dwelling in Jefferson County*
Appraised Value: $217K
(Building ID: 19-04-0013-0059-0000_89)
Flood Source: Shenandoah River
13.6’ (FEMA 1% / 100-Yr)
16.6’ (FEMA 1% + / 100-Yr +)
19.6’ (FEMA 0.2% / 500-Yr)
Ground Level
Rivermist Lane, Harpers Ferry
Repetitive Loss Area / Area of Mitigation Interest

## Slide 25
Single Family Dwelling in Jefferson County*
in Floodway
Appraised Value: $95K
(Building ID: 19-04-0013-0058-0000_97)
Flood Source: Shenandoah River
13.7’ (FEMA 1% / 100-Yr)
16.7’ (FEMA 1% + / 100-Yr +)
19.7’ (FEMA 0.2% / 500-Yr)
Ground Level
Pre-FIRM
 | HEIGHT (ft.)
BUILDING | 
Freeboard (FBD) | 3
FLOOD DEPTH | 
FEMA 1% (100-Yr) | 13.7
FEMA 100-Yr + FBD | 16.7
FEMA 0.2% (500-Yr) | 19.7
Building Flood Profile - Unmitigated
Rivermist Lane, Harpers Ferry
Repetitive Loss Area / Area of Mitigation Interest

## Slide 26
Flood Profile
 | HEIGHT (ft.)
BUILDING | 
Freeboard (FBD) | 3
FLOOD DEPTH | 
FEMA 1% (100-Yr) | 9.9
FEMA 100-Yr + FBD | 12.9
FEMA 0.2% (500-Yr) | 18.9
Single Family Dwelling in Jefferson County*
Elevated in Floodway
Appraised Value: $265K
(Building ID: 19-06-009H-0019-0000_781)
Flood Source: Shenandoah River
Post-FIRM
Ground Level
9.9’ (FEMA 1% / 100-Yr)
14.9’ (FEMA 1% + / 100-Yr +)
18.9’ (FEMA 0.2% / 500-Yr)
Building Flood Profile – Mitigated to DFE