## Slide 1
Flood Frequency
First Street Foundation (FSF) |  |  | 
Flood Recurrence Interval and Flood Size (2022, 2037, 2052)* | Annual Probability (flooding at least 1 cm) | Cumulative Probability - Flooding at least once over 30 years | First Street Risk Description
500 yr (1 in 500) | 0.2% | >0% | Any Risk
100 yr (1 in 100) | 1% | >26% | Substantial Risk
20 yr (1 in 20) | 5% | > 85% | 
5 yr (1 in 5) | 20% | >99% | Almost Certain Risk
Climate scenarios available for 3 flood depth years (2022-today, 2037-15 years, 2052-30 years) |  |  | 
2022 Flood Study Sources: FEMA and First Street Foundation (FSF)
FEMA |  |  | 
Flood Recurrence Interval and Flood Size | Annual Probability | Cumulative Probability - Flooding at least once over 30 years | FEMA Risk Description
500 yr (1 in 500) | 0.2% | 6% | Moderate Risk
100 yr (1 in 100) Plus confidence error | 1%+ |  | 
100 yr (1 in 100) | 1% | 26% | High Risk
50 yr (1 in 50) | 2% | 45% | High Risk
25 yr (1 in 25) | 4% | 71% | High Risk
10 yr (1 in 10) | 10% | 96% | High Risk
Climate scenarios generated from BFE + 1 ft. or 1%+ Recurrence interval |  |  | 
5-, 10-, 20-, 25-, 50-, 100-, and 500-year flood elevations (above sea level) refer to expected water levels of the 20%, 10%, 5%, 4%, 2%, 1%, and 0.2% annual chance flood events.
The Differences between FEMA Flood Maps and Flood Risk Factors by FSF |  | 
Differences | FEMA | (FSF)
Scale of Flood Risk | Mapping Risk by Zones | Identifying the Risk on Property Level
Future Risk | Maps are not Adjusting based on Climate Change & and its impact on Future Floods | Considering the effect of Sea level Rise & Atmospheric Change in the next 30 years on Flood Risk
Insurance Rates | Maps are Intended to Inform Flood Insurance Rates | Does not Determine Whether the Property Needs Flood Insurance
Development Requirement | Determining Development for the Areas at Risk | Assessing Risk for an Individual Property
Frequency: Probability that a flood of a specific size will be equaled or exceeded in any given year.

## Slide 2
Frequency: Probability that a flood of a specific size will be equaled or exceeded in any given year
  5-, 10-, 20-, 25-, 50-, 100-, and 500-year flood elevations (above sea level) refer to expected water levels of the 20%, 10%, 5%, 4%, 2%, 1%, and 0.2% annual chance flood events. A 1000-yr flood has a 0.1% chance of happening in any given year.
  FEMA’s 1%+ flood elevations measures how high the 100-year flood could be given the statistical uncertainties in flood modeling. It represents the upper 84-percent confidence limit of the statistical error for calculating the 1-percent annual chance event.
  The relative frequency of any given flood (e.g., 5-year or 10-year) serves as a useful reference point when selecting a mitigation options and evaluating cost effectiveness.
Depth: Flood depth or water surface elevation above the ground surface
  Critical during design considerations, as it is often the primary factor in evaluating the potential for flood damage
  Flood depth sources include flood models and high water marks which measure the degree of flooding
Velocity: Speed at which the floodwaters are flowing
  Flowing water often causes erosion and scour, as well as debris impacts and hydrodynamic forces.
  FEMA’s detailed engineering studies provide river/stream flows
Duration: Measure of how long water remains above normal levels.
  Prolonged contact with floodwaters may make some mitigation measures, including dry flood-proofing, inappropriate because of the increased chance of seepage and potential structural failure.
  Long periods of inundation are more likely to cause greater damage to structural members and finishes than short periods of flooding.
Rate of Floodwater Rise and Fall: Floodwater that rises very quickly with little or now warning
  Steep topography and locations with small drainage areas may experience flash flooding in which floodwater can rise very quickly with little or no warning.
  High-velocity water flows usually accompany flash floods and preclude certain types of flood mitigation measures, especially those requiring human intervention
  Rapid rates of the rise and fall of floodwater can also lead to unequal hydrostatic pressures on a building. The probability of unequal hydrostatic pressures increases when building exteriors are designed to be watertight
Historical Information: Use past information like the high-water marks of the 2016 Flood as an indication of the nature and severity of effects likely to occur during future events.
Flood Characteristics
Flood Characteristics Impacting Community
Relationship between flood recurrence intervals and the probability of an event occurring within a given period
Flood Models and Studies

## Slide 3
182 SEVENTH ST, Rainelle, WV, 25962
Building Flood Profile
13-13-0001-0054-0000_182
Rainelle

## Slide 4
No Inundation
Building’s Ground Elevation
10% Probability of Flood in a year (10-year flood)

## Slide 5
0’ (FEMA 4% / 25-Yr)
4% Probability of Flood in a year (25-year flood)

## Slide 6
1.9’ (FEMA 2% / 50-Yr)
2% Probability of Flood in a year (50-year flood)

## Slide 7
3.1’ (FEMA 1% /100-Yr)
1% Probability of Flood in a year (100-year flood)

## Slide 8
9.9’ (FEMA 0.2% /500-Yr)
9.9’ (FEMA 1% +/ 84% CL)
0.2% Probability of Flood in a year (500-year flood)

## Slide 9
7.5’ (2016 High Water)
2016 High Watermark
High Watermark

## Slide 10
182 Seventh Street, Rainelle, WV, 25962
1.9’ (FEMA 10% / 10-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
Building: 13-13-0001-0054-0000_182
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 1.9
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) Climate | 

## Slide 11
182 Seventh Street, Rainelle, WV, 25962
3.1’ (FEMA 1% / 100-Yr)
1.9’ (FEMA 10% / 10-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
Building: 13-13-0001-0054-0000_182
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 1.9
2016 Flood HWM | 
FEMA 1% (100-Yr) | 3.1
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) Climate | 

## Slide 12
182 Seventh Street, Rainelle, WV, 25962
9.9’ FEMA 1%+ (84% CL)
3.1’ (FEMA 1% / 100-Yr)
1.9’ (FEMA 10% / 10-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
Building: 13-13-0001-0054-0000_182
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 1.9
2016 Flood HWM | 
FEMA 1% (100-Yr) | 3.1
FEMA 100-Yr + FBD | 5.1
FEMA 1%+ (84% CL) | 9.9
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) Climate | 

## Slide 13
182 Seventh Street, Rainelle, WV, 25962
9.9’ FEMA 1%+ (84% CL)
7.5’ (2016 High Water)
3.1’ (FEMA 1% / 100-Yr)
1.9’ (FEMA 10% / 10-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
Building: 13-13-0001-0054-0000_182
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 1.9
2016 Flood HWM | 7.5
FEMA 1% (100-Yr) | 3.1
FEMA 100-Yr + FBD | 5.1
FEMA 1%+ (84% CL) | 9.9
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) Climate | 

## Slide 14
182 Seventh Street, Rainelle, WV, 25962
9.9’ FEMA 1%+ (84% CL)
7.5’ (2016 High Water)
9.9’ (FEMA 0.2% / 500-Yr )
3.1’ (FEMA 1% / 100-Yr)
1.9’ (FEMA 10% / 10-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
Building: 13-13-0001-0054-0000_182
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 1.9
2016 Flood HWM | 7.5
FEMA 1% (100-Yr) | 3.1
FEMA 100-Yr + FBD | 5.1
FEMA 1%+ (84% CL) | 9.9
FEMA 0.2% (500-Yr) | 9.9
FSF 0.2% (500-Yr) Climate | 

## Slide 15
182 Seventh Street, Rainelle, WV, 25962
9.9’ FEMA 1%+ (84% CL)
7.5’ (2016 High Water)
9.9’ (FEMA 0.2% / 500-Yr )
3.1’ (FEMA 1% / 100-Yr)
12.2’ (FSF 0.2% / 500-Yr)
1.9’ (FEMA 10% / 10-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
Building: 13-13-0001-0054-0000_182
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 9
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 1.9
2016 Flood HWM | 7.5
FEMA 1% (100-Yr) | 3.1
FEMA 100-Yr + FBD | 5.1
FEMA 1%+ (84% CL) | 9.9
FEMA 0.2% (500-Yr) | 9.9
FSF 0.2% (500-Yr) Climate | 12.2

## Slide 16
Building Flood Profile
White Sulphur Springs

## Slide 17
Building Flood Profile

## Slide 18
Building Flood Profile
13-17-0009-0026-0000_138
138 Mill Street, White Sulphur Springs, WV, 24986

## Slide 19
10% Probability of Flood in a year (10-year flood)
Building’s Ground Elevation
1.7’ (FEMA 10% / 10-Yr)

## Slide 20
4% Probability of Flood in a year (25-year flood)
2.0’ (FEMA 4% / 25-Yr)

## Slide 21
2% Probability of Flood in a year (50-year flood)
3.4’ (FEMA 2% / 50-Yr)

## Slide 22
1% Probability of Flood in a year (100-year flood)
5.4’ (FEMA 1% / 100-Yr)

## Slide 23
0.2% Probability of Flood in a year (500-year flood)
7.2’ (FEMA 0.2% / 500-Yr)

## Slide 24
2016 High Watermark
6.5’ (2016 High Water)
High Watermark

## Slide 25
182 Seventh Street, Rainelle, WV, 25962
Building: 13-13-0001-0054-0000_182
Building 13-17-0009-0026-0000_138
0.7’ (FEMA 10% / 10-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 0.7
FEMA 4% (25-Yr) | 
FEMA 2% (50-Yr) | 
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 26
182 Seventh Street, Rainelle, WV, 25962
Building: 13-13-0001-0054-0000_182
Building 13-17-0009-0026-0000_138
2.0’ (FEMA 4% / 25-Yr)
0.7’ (FEMA 10% / 10-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 0.7
FEMA 4% (25-Yr) | 2.0
FEMA 2% (50-Yr) | 
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 27
182 Seventh Street, Rainelle, WV, 25962
Building: 13-13-0001-0054-0000_182
Building 13-17-0009-0026-0000_138
2.0’ (FEMA 4% / 25-Yr)
0.7’ (FEMA 10% / 10-Yr)
3.4’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 0.7
FEMA 4% (25-Yr) | 2.0
FEMA 2% (50-Yr) | 3.4
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 28
182 Seventh Street, Rainelle, WV, 25962
Building: 13-13-0001-0054-0000_182
6.4’ FEMA 1%+ (84% CL)
Building 13-17-0009-0026-0000_138
5.4’ (FEMA 1% / 100-Yr)
2.0’ (FEMA 4% / 25-Yr)
0.7’ (FEMA 10% / 10-Yr)
3.4’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 0.7
FEMA 4% (25-Yr) | 2.0
FEMA 2% (50-Yr) | 3.4
2016 Flood HWM | 
FEMA 1% (100-Yr) | 5.4
FEMA 100-Yr + FBD | 7.4
FEMA 1%+ (84% CL) | 6.4
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 29
182 Seventh Street, Rainelle, WV, 25962
Building: 13-13-0001-0054-0000_182
6.4’ FEMA 1%+ (84% CL)
6.5’ (2016 High Water)
Building 13-17-0009-0026-0000_138
5.4’ (FEMA 1% / 100-Yr)
2.0’ (FEMA 4% / 25-Yr)
0.7’ (FEMA 10% / 10-Yr)
3.4’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 0.7
FEMA 4% (25-Yr) | 2.0
FEMA 2% (50-Yr) | 3.4
2016 Flood HWM | 6.5
FEMA 1% (100-Yr) | 5.4
FEMA 100-Yr + FBD | 7.4
FEMA 1%+ (84% CL) | 6.4
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 30
182 Seventh Street, Rainelle, WV, 25962
Building: 13-13-0001-0054-0000_182
6.4’ FEMA 1%+ (84% CL)
6.5’ (2016 High Water)
7.2’ (FEMA 0.2% / 500-Yr )
Building 13-17-0009-0026-0000_138
5.4’ (FEMA 1% / 100-Yr)
2.0’ (FEMA 4% / 25-Yr)
0.7’ (FEMA 10% / 10-Yr)
3.4’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 0.7
FEMA 4% (25-Yr) | 2.0
FEMA 2% (50-Yr) | 3.4
2016 Flood HWM | 6.5
FEMA 1% (100-Yr) | 5.4
FEMA 100-Yr + FBD | 7.4
FEMA 1%+ (84% CL) | 6.4
FEMA 0.2% (500-Yr) | 7.2
FSF 0.2% (500-Yr) | 

## Slide 31
182 Seventh Street, Rainelle, WV, 25962
Building: 13-13-0001-0054-0000_182
6.4’ FEMA 1%+ (84% CL)
6.5’ (2016 High Water)
7.2’ (FEMA 0.2% / 500-Yr )
Building 13-17-0009-0026-0000_138
5.4’ (FEMA 1% / 100-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 6.4
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 0.7
FEMA 4% (25-Yr) | 2.0
FEMA 2% (50-Yr) | 3.4
2016 Flood HWM | 6.5
FEMA 1% (100-Yr) | 5.4
FEMA 100-Yr + FBD | 7.4
FEMA 1%+ (84% CL) | 6.4
FEMA 0.2% (500-Yr) | 7.2
FSF 0.2% (500-Yr) | 7.4
7.4’ (FSF 0.2% / 500-Yr)
2.0’ (FEMA 4% / 25-Yr)
0.7’ (FEMA 10% / 10-Yr)
3.4’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark

## Slide 32
Building Flood Profile
20-02-0006-0044-0000_306
306 Maywood Ave., Clendenin, WV, 25045
Clendenin

## Slide 33
10% Probability of Flood in a year (10-year flood)
Building’s Ground Elevation
2.0’ (FEMA 10% / 10-Yr)

## Slide 34
4% Probability of Flood in a year (25-year flood)
6.0’ (FEMA 4% / 25-Yr)

## Slide 35
2% Probability of Flood in a year (50-year flood)
9.5’ (FEMA 2% / 50-Yr)

## Slide 36
1% Probability of Flood in a year (100-year flood)
12.3’ (FEMA 2% / 50-Yr)

## Slide 37
0.2% Probability of Flood in a year (500-year flood)
20.5’ (FEMA 0.2% / 500-Yr)

## Slide 38
9.5’ (FEMA 2% / 50-Yr)
2016 High Watermark
High Watermark
10.5’ (2016 High Water)

## Slide 39
306 Maywood Ave., Clendenin, WV, 25045
Building 20-02-0006-0044-0000_306
2.0’ (FEMA 10% / 10-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 12.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 2.0
FEMA 4% (25-Yr) | 
FEMA 2% (50-Yr) | 
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 40
306 Maywood Ave., Clendenin, WV, 25045
Building 20-02-0006-0044-0000_306
2.0’ (FEMA 10% / 10-Yr)
6.0’ (FEMA 4% / 25-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 12.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 2.0
FEMA 4% (25-Yr) | 6.0
FEMA 2% (50-Yr) | 
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 41
306 Maywood Ave., Clendenin, WV, 25045
Building 20-02-0006-0044-0000_306
2.0’ (FEMA 10% / 10-Yr)
6.0’ (FEMA 4% / 25-Yr)
9.5’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 12.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 2.0
FEMA 4% (25-Yr) | 6.0
FEMA 2% (50-Yr) | 9.5
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 42
10.5’ (2016 High Water)
306 Maywood Ave., Clendenin, WV, 25045
Building 20-02-0006-0044-0000_306
2.0’ (FEMA 10% / 10-Yr)
6.0’ (FEMA 4% / 25-Yr)
9.5’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 12.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 2.0
FEMA 4% (25-Yr) | 6.0
FEMA 2% (50-Yr) | 9.5
2016 Flood HWM | 10.5
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark

## Slide 43
16.5’ FEMA1%+ (84% CL)
10.5’ (2016 High Water)
306 Maywood Ave., Clendenin, WV, 25045
Building 20-02-0006-0044-0000_306
12.3’ (FEMA 1% / 100-Yr)
2.0’ (FEMA 10% / 10-Yr)
6.0’ (FEMA 4% / 25-Yr)
9.5’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 12.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 2.0
FEMA 4% (25-Yr) | 6.0
FEMA 2% (50-Yr) | 9.5
2016 Flood HWM | 10.5
FEMA 1% (100-Yr) | 12.3
FEMA 100-Yr + FBD | 14.3
FEMA 1%+ (84% CL) | 16.5
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 44
16.5’ FEMA1%+ (84% CL)
10.5’ (2016 High Water)
306 Maywood Ave., Clendenin, WV, 25045
Building 20-02-0006-0044-0000_306
12.3’ (FEMA 1% / 100-Yr)
20.5’ (FEMA 0.2% / 500-Yr)
2.0’ (FEMA 10% / 10-Yr)
6.0’ (FEMA 4% / 25-Yr)
9.5’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 12.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 2.0
FEMA 4% (25-Yr) | 6.0
FEMA 2% (50-Yr) | 9.5
2016 Flood HWM | 10.5
FEMA 1% (100-Yr) | 12.3
FEMA 100-Yr + FBD | 14.3
FEMA 1%+ (84% CL) | 16.5
FEMA 0.2% (500-Yr) | 20.5
FSF 0.2% (500-Yr) | 

## Slide 45
16.5’ FEMA1%+ (84% CL)
10.5’ (2016 High Water)
24.6’ (FSF 0.2% / 500-Yr)
306 Maywood Ave., Clendenin, WV, 25045
Building 20-02-0006-0044-0000_306
12.3’ (FEMA 1% / 100-Yr)
20.5’ (FEMA 0.2% / 500-Yr)
2.0’ (FEMA 10% / 10-Yr)
6.0’ (FEMA 4% / 25-Yr)
9.5’ (FEMA 2% / 50-Yr)
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 12.0
Freeboard (FBD) | 2.0
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 2.0
FEMA 4% (25-Yr) | 6.0
FEMA 2% (50-Yr) | 9.5
2016 Flood HWM | 10.5
FEMA 1% (100-Yr) | 12.3
FEMA 100-Yr + FBD | 14.3
FEMA 1%+ (84% CL) | 16.5
FEMA 0.2% (500-Yr) | 20.5
FSF 0.2% (500-Yr) | 24.6

## Slide 46
34-06-0011-0090-0000_113
113 Valley Ave, Richwood, WV
Building Flood Profile
Richwood

## Slide 47
2% Probability of Flood in a year (50-year flood)
2.8’ (FEMA 2% / 50-Yr)
Building’s Ground Elevation

## Slide 48
1% Probability of Flood in a year (100-year flood)
3.5’ (FEMA 1% / 100-Yr)

## Slide 49
0.2% Probability of Flood in a year (500-year flood)
8.3’ (FEMA 0.2% / 500-Yr)

## Slide 50
Building’s Ground Elevation
2016 High Watermark
High Watermark
1.0’ (2016 High Water)

## Slide 51
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
1.0’ (2016 High Water)
Building 34-06-0011-0090-0000_113
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
Building 34-06-0011-0090-0000_113
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 8
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 
2016 Flood HWM | 1.0
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 
113 Valley Ave, Richwood, WV

## Slide 52
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
2.8’ (FEMA 2% / 50-Yr)
1.0’ (2016 High Water)
Building 34-06-0011-0090-0000_113
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 8
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 2.8
2016 Flood HWM | 1.0
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 
113 Valley Ave, Richwood, WV

## Slide 53
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
3.5’ (FEMA 1% / 100-Yr)
2.8’ (FEMA 2% / 50-Yr)
1.0’ (2016 High Water)
9.0’ FEMA1%+ (84% CL)
Building 34-06-0011-0090-0000_113
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 8
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 2.8
2016 Flood HWM | 1.0
FEMA 1% (100-Yr) | 3.5
FEMA 100-Yr + FBD | 5.5
FEMA 1%+ (84% CL) | 9.0
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 
113 Valley Ave, Richwood, WV

## Slide 54
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
3.5’ (FEMA 1% / 100-Yr)
2.8’ (FEMA 2% / 50-Yr)
1.0’ (2016 High Water)
Building 34-06-0011-0090-0000_113
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
8.3’ (FEMA 0.2% / 500-Yr)
9.0’ FEMA1%+ (84% CL)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 8
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 2.8
2016 Flood HWM | 1.0
FEMA 1% (100-Yr) | 3.5
FEMA 100-Yr + FBD | 5.5
FEMA 1%+ (84% CL) | 9.0
FEMA 0.2% (500-Yr) | 8.3
FSF 0.2% (500-Yr) | 
113 Valley Ave, Richwood, WV

## Slide 55
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
USGS 2016 Flood High Water Mark
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 8
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | NA
FEMA 4% (25-Yr) | NA
FEMA 2% (50-Yr) | 2.8
2016 Flood HWM | 1.0
FEMA 1% (100-Yr) | 3.5
FEMA 100-Yr + FBD | 5.5
FEMA 1%+ (84% CL) | 9.0
FEMA 0.2% (500-Yr) | 8.3
FSF 0.2% (500-Yr) | 6.7
8.3’ (FEMA 0.2% / 500-Yr)
113 Valley Ave, Richwood, WV
The Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 2016 flood plus freeboard.
3.5’ (FEMA 1% / 100-Yr)
2.8’ (FEMA 2% / 50-Yr)
1.0’ (2016 High Water)
9.0’ FEMA1%+ (84% CL)
6.7’ (FSG 0.2% / 500-Yr)
Building 34-06-0011-0090-0000_113

## Slide 56
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
Camden on Gauley
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
91 RIVERSIDE DR, Camden On Gauley, WV, 26208
Building Flood Profile

## Slide 57
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 
FEMA 2% (50-Yr) | 
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 58
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
4.4’ (FEMA 4% / 25-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 4.4
FEMA 2% (50-Yr) | 
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 59
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
6.7’ (FEMA 2% / 50-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
4.4’ (FEMA 4% / 25-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 4.4
FEMA 2% (50-Yr) | 6.7
2016 Flood HWM | 
FEMA 1% (100-Yr) | 
FEMA 100-Yr + FBD | 
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 60
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
8.3’ (FEMA 1% / 100-Yr)
6.7’ (FEMA 2% / 50-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
4.4’ (FEMA 4% / 25-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 4.4
FEMA 2% (50-Yr) | 6.7
2016 Flood HWM | 
FEMA 1% (100-Yr) | 8.3
FEMA 100-Yr + FBD | 10.3
FEMA 1%+ (84% CL) | 
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 61
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
10.7’ FEMA 1%+ (84% CL)
8.3’ (FEMA 1% / 100-Yr)
6.7’ (FEMA 2% / 50-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
4.4’ (FEMA 4% / 25-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 4.4
FEMA 2% (50-Yr) | 6.7
2016 Flood HWM | 
FEMA 1% (100-Yr) | 8.3
FEMA 100-Yr + FBD | 10.3
FEMA 1%+ (84% CL) | 10.7
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 62
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
10.7’ FEMA 1%+ (84% CL)
9.1’ (2016 High Water)
8.3’ (FEMA 1% / 100-Yr)
6.7’ (FEMA 2% / 50-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
4.4’ (FEMA 4% / 25-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 4.4
FEMA 2% (50-Yr) | 6.7
2016 Flood HWM | 9.1
FEMA 1% (100-Yr) | 8.3
FEMA 100-Yr + FBD | 10.3
FEMA 1%+ (84% CL) | 10.7
FEMA 0.2% (500-Yr) | 
FSF 0.2% (500-Yr) | 

## Slide 63
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
10.7’ FEMA 1%+ (84% CL)
9.1’ (2016 High Water)
12.7’ (FEMA 0.2% / 500-Yr )
8.3’ (FEMA 1% / 100-Yr)
6.7’ (FEMA 2% / 50-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
4.4’ (FEMA 4% / 25-Yr)
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 4.4
FEMA 2% (50-Yr) | 6.7
2016 Flood HWM | 9.1
FEMA 1% (100-Yr) | 8.3
FEMA 100-Yr + FBD | 10.3
FEMA 1%+ (84% CL) | 10.7
FEMA 0.2% (500-Yr) | 12.7
FSF 0.2% (500-Yr) | 

## Slide 64
81 RIVERSIDE DR, Camden On Gauley, WV, 26208
51-04-0003-0006-0000_81
 | HEIGHT (ft.)
BUILDING | 
First Floor Height | 4
Freeboard (FBD) | 2
FLOOD DEPTH | 
FEMA 10% (10-Yr) | 1.9
FEMA 4% (25-Yr) | 4.4
FEMA 2% (50-Yr) | 6.7
2016 Flood HWM | 9.1
FEMA 1% (100-Yr) | 8.3
FEMA 100-Yr + FBD | 10.3
FEMA 1%+ (84% CL) | 10.7
FEMA 0.2% (500-Yr) | 12.7
FSF 0.2% (500-Yr) | 14.8
10.7’ FEMA 1%+ (84% CL)
9.1’ (2016 High Water)
12.7’ (FEMA 0.2% / 500-Yr )
8.3’ (FEMA 1% / 100-Yr)
14.8’ (FSF 0.2% / 500-Yr)
6.7’ (FEMA 2% / 50-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA
Building: 51-04-0003-0006-0000_81
USGS 2016 Flood High Water Mark
1.9’ (FEMA 10% / 10-Yr)
4.4’ (FEMA 4% / 25-Yr)

## Slide 65
309 8th St, Marlinton, WV, 24954
7’ (1985 High Water Mark)
8.8’ (FEMA DRAFT NFHL 0.2% / 500-Yr )
3.6’ (FEMA 1% / 100-Yr)
9.4’ (FSF 0.2% / 500-Yr)
0.4’ (FEMA 10% / 10-Yr)
2.7’ (FEMA 2% / 50-Yr)
First Street Foundation (FSF)
FLOOD DEPTHS:
FEMA Draft NFHL (2023)
1985 Flood High Water Mark
Ideally, the Design Flood Elevation (DFE) should be the BFE plus 2 feet of freeboard. The DFE should also be above the high-water marks of the 1985 flood plus freeboard.
Building: 38-08-0003-0023-0000
FEMA Effective (2010)
4.8’ (FEMA DRAFT NFHL 1% / 100-Yr)
Flood Intervals | Height (ft.) | Source
FEMA 10% / 10-Yr | 0.4 | Flood Profile (Effective 2010)
FEMA 2% / 50-yr | 2.7 | Flood Profile (Effective 2010)
FEMA 1% / 100-yr | 3.6 | Flood Profile (Effective 2010)
FEMA 100-yr + 2.0 Ft. Freeboard (DFE) | 5.6 | Design flood elevation (DFE)
High Water Mark (1985 Flood) | 7.0 | Picture
FEMA Draft NFHL 100-yr | 4.8 | WV Flood Tool (Draft 2023)
FEMA 500-yr | 8.8 | WV Flood Tool (Draft 2023)
FSF 500-yr | 9.4 | FSF Flood Depth (2022)
1985 Flood High Water Mark
1900 Commercial Structure
Marlinton

## Slide 66
FEMA 10% Annual Chance (10-year)
Community Flood Profile
Assessing the Percentage of Inundated Area in Different Flood Intervals
White Sulphur Springs
Notes: White Sulfur Springs FEMA 10yr Aerial

## Slide 67
FEMA 10% Annual Chance (10-year)
White Sulphur Springs, WV
96% probability of flooding at least once over 30 years
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
26 ft.
13% of White Sulphur Springs is in the 10% Annual Flood Chance
Notes: White Sulfur Springs FEMA 10yr Aerial

## Slide 68
FEMA 4% Annual Chance (25-year)
White Sulphur Springs, WV
17% of White Sulphur Springs is in the 4% Annual Flood Chance
71% probability of flooding at least once over 30 years
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
29 ft.
Notes: White Sulfur Springs FEMA 25yr Aerial

## Slide 69
FEMA 2% Annual Chance (50-year)
White Sulphur Springs, WV
20% of White Sulphur Springs is in the 2% Annual Flood Chance
45% probability of flooding at least once over 30 years
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
30 ft.
Notes: White Sulfur Springs FEMA 50yr Aerial

## Slide 70
FEMA 1% Annual Chance (100-year)
White Sulphur Springs, WV
22% of White Sulphur Springs is in the 1% Annual Flood Chance
26% probability of flooding at least once over 30 years
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
35 ft.
Notes: White Sulfur Springs FEMA 100yr Aerial

## Slide 71
Climate
Change
FEMA 1% +Annual Chance (100-year)
White Sulphur Springs, WV
26% probability of flooding at least once over 30 years
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
35 ft.
25% of White Sulphur Springs is in the 1% +Annual Flood Chance
Notes: White Sulfur Springs FEMA 100yr PLUS Aerial

## Slide 72
FEMA 0.2% Annual Chance (500-year)
White Sulphur Springs, WV
18% of White Sulphur Springs is in the 0.2% Annual Flood Chance
6% probability of flooding at least once over 30 years
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
18 ft.
Notes: White Sulfur Springs FEMA 500yr Aerial

## Slide 73
Rainelle

## Slide 74
96% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
30 ft.
Residential
Non-Residential
FEMA 10% Annual Chance (10-year)
Rainelle, WV
13% Rainelle is in the 10% Annual Flood Chance
Notes: FEMA 10year Aerial

## Slide 75
FEMA 4% Annual Chance (25-year)
71% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
30 ft.
Residential
Non-Residential
Rainelle, WV
20% Rainelle is in the 4% Annual Flood Chance
Notes: FEMA 25year Aerial

## Slide 76
FEMA 2% Annual Chance (50-year)
Rainelle, WV
45% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
30 ft.
Residential
Non-Residential
26% Rainelle is in the 2% Annual Flood Chance
FEMA 2% Annual Chance (50-year)
Rainelle, WV
Notes: FEMA 50year Aerial

## Slide 77
FEMA 2% Annual Chance (50-year)
Rainelle, WV
26% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
30 ft.
Residential
Non-Residential
FEMA 1% Annual Chance (100-year)
Rainelle, WV
31% Rainelle is in the 1% Annual Flood Chance
Notes: FEMA 100year Aerial

## Slide 78
FEMA 2% Annual Chance (50-year)
Rainelle, WV
26% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
30 ft.
Residential
Non-Residential
FEMA 1%+ Annual Chance (100-year)
Rainelle, WV
Climate
Change
31% Rainelle is in the 1% + Annual Flood Chance
Notes: FEMA 100year PLUS Aerial

## Slide 79
FEMA 2% Annual Chance (50-year)
Rainelle, WV
6% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
30 ft.
Residential
Non-Residential
FEMA 0.2% Annual Chance (100-year)
Rainelle, WV
37% Rainelle is in the 0.2% Annual Flood Chance
Notes: FEMA 500year Aerial

## Slide 80
Clendenin

## Slide 81
96% probability of flooding at least once over 30 years
Clendenin, WV
FEMA 10% Annual Chance (10-year)
Residential
Non-Residential
13.4% of Clendenin is in the 10% Annual Flood Chance
0.1 ft.
FLOOD DEPTH
27.8 ft.

## Slide 82
71% probability of flooding at least once over 30 years
Clendenin, WV
FEMA 4% Annual Chance (25-year)
Residential
Non-Residential
19% of Clendenin is in the 4% Annual Flood Chance
0.1 ft.
FLOOD DEPTH
27.8 ft.

## Slide 83
45% probability of flooding at least once over 30 years
Clendenin, WV
FEMA 2% Annual Chance (50-year)
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
35.2 ft.
22.5% of Clendenin is in the 2% Annual Flood Chance

## Slide 84
26% probability of flooding at least once over 30 years
Clendenin, WV
FEMA 1% Annual Chance (100-year)
Residential
Non-Residential
23.5% of Clendenin is in the 1% Annual Flood Chance
0.1 ft.
FLOOD DEPTH
38.1 ft.

## Slide 85
26% probability of flooding at least once over 30 years
Clendenin, WV
FEMA 1%+ Annual Chance (100-year)
Residential
Non-Residential
23.5% of Clendenin is in the 1%+ Annual Flood Chance
0.1 ft.
FLOOD DEPTH
42.4 ft.
Climate
Change

## Slide 86
6% probability of flooding at least once over 30 years
Clendenin, WV
FEMA 0.2% Annual Chance (500-year)
Residential
Non-Residential
25% of Clendenin is in the 0.2% Annual Flood Chance
0.1 ft.
FLOOD DEPTH
43.6 ft.

## Slide 87
Richwood

## Slide 88
Richwood, WV
FEMA 10% Annual Chance (10-year)
96% probability of flooding at least once over 30 years
Residential
Non-Residential
Cherry River
0.1 ft.
FLOOD DEPTH
11.8 ft.
7% of Richwood is in the 10% Annual Flood Chance

## Slide 89
Richwood, WV
FEMA 4% Annual Chance (25-year)
71% probability of flooding at least once over 30 years
Residential
Non-Residential
Cherry River
0.1 ft.
FLOOD DEPTH
14.7 ft.
11% of Richwood is in the 4% Annual Flood Chance

## Slide 90
Richwood, WV
FEMA 2% Annual Chance (50-year)
45% probability of flooding at least once over 30 years
Residential
Non-Residential
Cherry River
0.1 ft.
FLOOD DEPTH
17.3 ft.
16% of Richwood is in the 2% Annual Flood Chance

## Slide 91
Richwood, WV
FEMA 1% Annual Chance (100-year)
26% probability of flooding at least once over 30 years
Residential
Non-Residential
Cherry River
0.1 ft.
FLOOD DEPTH
17.9 ft.
18% of Richwood is in the 1% Annual Flood Chance

## Slide 92
Richwood, WV
FEMA 1%+ Annual Chance (100-year)
26% probability of flooding at least once over 30 years
Residential
Non-Residential
Cherry River
0.1 ft.
FLOOD DEPTH
26.7 ft.
22% of Richwood is in the 1%+ Annual Flood Chance
Climate
Change

## Slide 93
Richwood, WV
FEMA 0.2% Annual Chance (500-year)
6% probability of flooding at least once over 30 years
Residential
Non-Residential
Cherry River
0.1 ft.
FLOOD DEPTH
28.6 ft.
22% of Richwood is in the 0.2% Annual Flood Chance

## Slide 94
Camden-on-Gauley

## Slide 95
Camden-on-Gauley, WV
FEMA 10% Annual Chance (10-year)
96% probability of flooding at least once over 30 years
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
22.1 ft.
10% of Camden is in the 10% Annual Flood Chance

## Slide 96
Camden-on-Gauley, WV
FEMA 4% Annual Chance (25-year)
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
25.3 ft.
71% probability of flooding at least once over 30 years
12% of Camden is in the 4% Annual Flood Chance

## Slide 97
Camden-on-Gauley, WV
FEMA 2% Annual Chance (50-year)
Residential
Non-Residential
0.1 ft.
FLOOD DEPTH
27.3 ft.
45% probability of flooding at least once over 30 years
12% of Camden is in the 2% Annual Flood Chance

## Slide 98
Camden-on-Gauley, WV
FEMA 1% Annual Chance (100-year)
Residential
Non-Residential
26% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
29.3 ft.
14% of Camden is in the 1% Annual Flood Chance

## Slide 99
Camden-on-Gauley, WV
FEMA 1+% Annual Chance (100-year)
Residential
Non-Residential
26% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
31.5 ft.
Climate
Change
13% of Camden is in the 1%+ Annual Flood Chance

## Slide 100
Camden-on-Gauley, WV
FEMA 0.2% Annual Chance (500-year)
Residential
Non-Residential
6% probability of flooding at least once over 30 years
0.1 ft.
FLOOD DEPTH
32.5 ft.
15% of Camden is in the 0.2% Annual Flood Chance

## Slide 101
Percentage of Area
Chart: Percentage of Inundated Area in each Community
| Camden | Clendenin | Rainelle | Richwood | White Sulphur Springs
10% Probability of Flood in a year (10-year flood) | 0.1 | 0.134 | 0.13 | 0.07 | 0.13
4% Probability of Flood in a year (25-year flood) | 0.12 | 0.19 | 0.2 | 0.11 | 0.17
2% Probability of Flood in a year (50-year flood) | 0.12 | 0.225 | 0.26 | 0.16 | 0.2
1% Probability of Flood in a year (100-year flood) | 0.13 | 0.235 | 0.31 | 0.22 | 0.25
1+% Probability of Flood in a year (84% Cimate Change) | 0.13 | 0.235 | 0.31 | 0.22 | 0.25
0.2% Probability of Flood in a year (500-year flood) | 0.15 | 0.25 | 0.37 | 0.22 | 0.27

## Slide 102
Flood Intervals | Percentage of Inundated Area in each Community |  |  |  | 
 | Camden | Clendenin | Rainelle | Richwood | White Sulphur Springs
10% Probability of Flood in a year (10-year flood) | 10% | 13.4% | 13% | 7% | 13%
4% Probability of Flood in a year (25-year flood) | 12% | 19% | 20% | 11% | 17%
2% Probability of Flood in a year (50-year flood) | 12% | 22.5% | 26% | 16% | 20%
1% Probability of Flood in a year (100-year flood) | 14% | 23.5% | 31% | 18% | 22%
*1+% Probability of Flood in a year (84% Climate Change) | 13% | 23.5% | 31% | 22% | 25%
0.2% Probability of Flood in a year (500-year flood) | 15% | 25% | 37% | 22% | 27%
* The 1-percent-plus flood elevation is defined as a flood elevation derived by using discharges that are at the upper 84-percent confidence limit as calculated in the gage analysis for the 1- percent-annual-chance event for the Flood Risk Project (FEMA, 2019)