## Slide 1
Statewide Flood Risk Assessment, WVFRF, Feb. 2024
July 1961 (22 + 2 landslide fatalities), Kanawha County
June 2016 (23 fatalities), Rainelle
November 1985 (47 fatalities in WV), Moorefield
February 1972 (125 fatalities including 4 missing), Huntington
Flood Hazard Risk
Top 5 Counties | Modified Total SFHA Area (acres)
Hampshire | 26,607
Kanawha | 23,929
Mason | 23,117
Greenbrier | 21,615
Randolph | 20,523
Structure Risk
Building Counts / Ratios
Structures in Regulatory Floodplain (SFHA): 83,556 (8.2% Bldgs. in WV)
Structures in High-Risk Advisory Zones: 13,503
Structures in All High-Risk Floodplains: 97,059 (9.6% of Bldgs. in WV)
Buildings in High-Risk Floodway: 8,239 (9.9% of SFHA Bldgs.)
Structures in Estimated Depths of Greater than 10 ft: 2,015
Building Types / Value
Total Building Value in Floodplain: $10,473M
Exposed Residential Count Ratio: 88.6%
Residential Value in Floodplain: $4,324M (41.3%)
High-Value (> 1M) Residential Count: 36
Non-Residential Value in Floodplain: $6,149M
Building Year / New Construction
Pre-FIRM in Floodplain Ratio: 73.7%
Post-FIRM in Floodplain Ratio: 26.3%
Significant Structures
Floodplain Essential Facilities: 491 (25.6% in WV)
(K 12 Schools, 911 Centers, Police/Fire Depts., Hospitals, Nursing Homes)
Floodplain Non-Hist. Community Assets: 2,116
(Religious, government, utility, EMS, postsecondary educational)
Floodplain Historical Community Assets: 3,159
(National Register, in historic districts before 1930)
Physical Damage Estimates
Total Estimated Building Loss: $854.6M
(8.2% of Exposure Value)
Substantial Damage Buildings: 6,587 (6.8% of Floodplain Bldgs.)
Transportation Infrastructure
Inundated Roads: 2,550 miles (6.4%)
Flood Depth > 3 ft: 1,267 miles
Top 5 Counties | BLDG. in SFHA
Kanawha | 12,259
Logan | 4,605
Ohio | 3,260
Boone | 3,201
Mingo | 3,032
Majority of Building Stock is RESIDENTIAL. Unincorporated Areas typically have higher residential building counts than Incorporated Places.
Vulnerable Structures
Manufactured Homes in Floodplain: 23,329 (24%)
Floodplain Buildings with Basements Ratio: 27.9%
One-Story Floodplain Residential Buildings Ratio: 75.4%
Renter-Occupied Housing in Floodplain Ratio: 26.6%
Low-Value (< $10K) Floodplain Buildings Ratio: 7.4%
People / Social Risk
31% of the state has mapped Detailed Flood Zones containing 65% of the buildings in Regulatory Floodplains
Total Modified Area of Regulatory Floodplains (aSFHA) in West Virginia, excluding large open water lakes (> 10 acres), large rivers (bank-to-bank > 500 ft.), and federal lands (> 10 acres): 528,635 acres (3.4% of the State’s Area)
32 Federally-Declared Flood Disasters in West Virginia since 1953
Human Exposure
Population Residing in High-Risk Floodplains:
200,255 (11.1% of WV population)
Top 5 Counties | WV SVI
McDowell | 100.0%
Wyoming | 98.1%
Mingo | 96.3%
Clay | 94.4%
Webster | 92.6%
Social Vulnerability Index (WV SVI)
(0% to 100%)
Combines indicators of:
Poverty Rate
Unemployment Rate
Vulnerable Ages Rate
Disability Rate
Population without a High School Diploma
Population Change
Median Housing Unit Value
Percentage of Mobile Homes in Housing Units
Human Impacts
Population Displaced: 118,856 (6.6% of WV population)
Short-Term Shelter Population: 22,930 (5,697 Companion Pets)
2016 Flood Fatalities
23 Victims
Three younger than 15 yrs.
Eleven 15 to 64 yrs.
Nine over 65 yrs.
Five with Health Conditions or Disabilities
Nine Risky Behavior
Chesapeake, Kanawha County, August 2023
Near Kimball, McDowell County, July 2001