## Slide 1
Statewide Flood Risk Assessment & WV Flood Tool
(TEIF – Total Exposure in Floodplain)
Kurt Donaldson and Maneesh Sharma WV GIS Technical Center West Virginia University kdonalds@wvu.edu
April 19, 2022 WV State Mitigation Planning Workshop
 Devastating June 2016 Flood

## Slide 2
Risk Assessment Layers on Flood Tool
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8771562&y=4715438&l=7&v=2
Potential Flood, Dam Failure and Landslide Vulnerabilities on WV Flood Tool’s RiskMAP View Hardy County, West Virginia
Landslide
Dam
Flood Zone
https://www.google.com/maps/@38.9409315,-78.805837,1690a,35y,44.59t/data=!3m1!1e3

## Slide 3
WV Statewide Risk Assessment
Building Level Risk Assessment

## Slide 4
WV Building-Level Flood Risk Assessment
BUILDING INVENTORY
Primary Building Identification & Hazus Attributes Essential Facilities & Community Assets
FLOOD LOSS MODELS Open Hazus FAST
Flood Depths Building Damage Estimates
COMMUNITY ENGAGEMENT
Risk Assessment Data Verification
Mitigation Actions Identified
BLDG. LEVEL RISK ASSESSMENT (BLRA) DATABASE
Building Level & Community Level Outputs
Methodology
Consistent methodology statewide
Semi-automated workflows
Continuous cycle to improve and update assessments
Building-Level Flood Risk Assessments support:
Hazard Mitigation Plans
Floodplain Management
Community Assisted Visits
Community Rating System
Benefits
More detailed and accurate assessments
Automated scripts generate outputs quickly
Cost savings through efficiencies
Helps multiple stakeholders
Comprehensive Building Risk Spatial Database
Building-Level Risk Assessment (BLRA) Cycle
1
2
3
4
Tabular Output
Map Output
Published to WV Flood Tool
BLRA Cycle and Methodology

## Slide 5
Access Risk Assessment Info
Building Level Risk Assessment (BLRA) Products
GIS Files
Tables (Excel)
  Community Level (CL)
  Building (or Feature) Level (BL) with links to online maps
    Table Extracts
    Top Lists
Maps
  Interactive Web Maps
  Graphics and Maps
Reports (Word Docs)
3D Flood Visualizations
Use the Risk Information Index to access Data and Products
Most of the risk assessment data can be viewed on the RiskMAP View of the WV Flood Tool

## Slide 6
Risk Assessment Data Verification
Use Building-Level (BL) Tables to identify Most Vulnerable Structures
Statewide BLRA (GIS)
BLRA County Tables organized by region
BLRA Data Extract Tables: High Building Value, High Damage Loss, High Minus Ratings
BLRA Statewide Top Lists: Building Value, Flood Depth, Damage Loss $, Damage Loss %, Minus Rated, Mitigated Structures
Risk Indicator Matrices: Exposure and Damage Loss Matrices of Risk Indicators

## Slide 7
Statewide Hazard Assessment
294 Statistical Geographies form 286 Communities which form
55 Counties which form
11 PDC Regions which form
1 Statewide Flood Risk Assessment
SPLIT COMMUNITY | COUNTY 1 | COUNTY 2
Alderson | Greenbrier | Monroe
Huntington | Cabell | Wayne
Montgomery | Fayette | Kanawha
Nitro | Kanawha | Putnam
Paden City | Tyler | Wetzel
Smithers | Fayette | Kanawha
Wheeling | Marshall | Ohio
Weirton | Brooke | Hancock
94% of WV Communities have Special Flood Hazard Areas (SFHA)
PDF Map
213 incorporated areas
+55 unincorporated areas 268 NFIP Communities +18 no SFHA communities
286 WV Communities
+ 8 split communities
294 Statistical Geographies
268 Flood-Prone Communities

## Slide 8
Statewide Flood Risk Assessment
Detailed Floodplain Building Inventory
Building Inventory Objectives
  Identify Primary Structures points
  Verify Building Identification
    E-911 Address
    Parcel geometry and assessment record
    Aerial and StreetView Images
    Building Sketches (parcel assessment record)
  Determine Building Characteristics (Occupancy Class, Cost, Basement, Foundation Type, Stories, Area, etc.)
    Default Characteristics derived from Assessment Records
    Overriding Modified Building Characteristics from user-defined values
  Ensure Building Point in most Restrictive Flood Zone
  Iterative Process and QC Checks to make more accurate
Record Data Issues and Data Gaps
BUILDING INVENTORY
Primary Building Identification & Hazus Attributes Essential Facilities & Community Assets
1

## Slide 9
Building Inventory
GIS Specialist conducting Building Inventory

## Slide 10
2021 R4 Floodplain Building Inventory
Vulnerability Risk Assessment
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8985707&y=4589317&l=3&v=2
Enhanced inventory of more than 98,000 building in high-risk floodplains completed by WVU in 2021 and published to WV Flood Tool
Refer to Overview and Other Resources about WV Flood Tool

## Slide 11
301.a Definition of “Building”
2 or more exterior walls and a roof affixed to a site
Manufactured (mobile) home
Travel trailer without wheels
CRS Manual Page 300-4
Building Definition

## Slide 12
“Not a Building”
Open pavilions, carports, underground pump stations, trailers, etc. are not buildings
Accessory structures are not counted
CRS Manual Page 300-5
Primary Structure: Not a Building
All primary structures in high-risk flood zones are inventoried.
Essential Facilities in moderate-risk flood zones also inventoried.

## Slide 13
Multiple Structures in a Single Parcel
Single Building Point for Multiple Buildings on a Single Parcel/Assessment
  Outbuildings and detached structures associated with a Primary Structure as a single point that correlates with Building Appraisal Value.
  Multiple buildings associated with commercial, industrial, or agricultural sites are identified as a single Primary Structure point if all structures are in the flood zone and can be correlated with Total Building Appraisal Value in Assessment Report.
Multiple Building Points in Single Parcel/Assessment (see example below – 4 Apt. Bldgs.)
  Points are associated with each Primary Structure in Flood Zone. Associated Model Input Parameters (Cost, Area, Occupancy Class, etc.) are recorded as separate building records. 3 apartments below are primary.
682
680B
680A
Flood Tool Assessment Report
Flood Tool Map View
The Web Parcel Assessment Reports provide a breakdown of individual building values and characteristics in single parcel
PID: 31-15-0054-0215-0000
682
680A
680B

## Slide 14
2021 R9 Floodplain Building Inventory
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8680577&y=4786710&l=3&v=2

## Slide 15
Floodplain Building-Level Risk
High-Risk Effective & Advisory
1%-Annual-Chance (100-Yr) Floodplains
All Risk Assessment and Mitigation Layers are displayed on the RiskMAP View of the WV Flood Tool
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8938946&y=4550516&l=9&v=2
White Sulphur Springs

## Slide 16
Primary Structures (Martinsburg)
Martinsburg’s primary structures viewable on the Risk MAP View of the WV Flood Tool. Symbol letters indicate general occupancy (Residential, Commercial, Other Non-Residential).

## Slide 17
2002 Building Inventory
Building Inventories
<< USACE Inventoried Floodplain Structures >>
http://wvgis.wvu.edu/data/dataset.php?ID=230
Nearly 20 years ago more than 80,000 structures in the floodplain were inventoried by the Pittsburgh District Army Corps of Engineers using statewide 1996-99 1-meter resolution Digital Orthophoto Quarter Quads. A combination of FEMA's Q3 and DFIRM floodplain data (available for 37 of the 55 counties) was overlaid onto DOQQ's.

## Slide 18
Statewide Building Inventories
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9070843&y=4497058&l=11&v=2
1998 Aerial Imagery
2018 Aerial Imagery
2002 USACE Inventory
Elkhorn Creek, McDowell County
2021 WVU Inventory

## Slide 19
USACE 2002 Building Inventory
2002 USACE Inventory
Buyout Properties since 2002 USACE Inventory
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9069713&y=4496689&l=10&v=2
Elkhorn Creek, McDowell County

## Slide 20
WV Statewide Risk Assessment
GIS Data for Enhanced Building Inventory

## Slide 21
GIS Data Development
Parcels Site Addresses Aerial Imagery Elevation
Parcels, Assessment Records, Aerial Imagery important for pinpointing flood-risk structures
Migrate six counties from paper to digital parcels
Flood-risk communities with missing or incorrect E-911 addresses
County Leaf-off imagery no older than 5 years
Statewide 1-meter DEM and 1-ft. contours. Flood Studies, Depth & WSEL Grids
BUILDING INVENTORY
GIS Reference & Elevation Data Flood Studies Depth & WSEL Grids Building Stock
1
More info about WV Flood Tool’s Reference Layers

## Slide 22
Ground Elevation: 1-ft. Contours
1-FOOT CONTOUR ELEVATION VALUE OF 600 FEET MATCHES 1-METER GRID SURFACE ELEVATION OF 600 FEET DISPLAYED IN QUERY RESULTS PANEL
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9177701&y=4611497&l=13&v=1
FEMA LiDAR-Derived Products: 1-Meter DEM and 1-Foot Contours
Elevation: 600 ft.
Source: FEMA 2018
1-ft Contours Display at two Highest Zoom Levels (1:564 and 1:282 Map Scales)
600 ft.
Make Contour Lines visible under REFERENCE LAYERS
1-foot contours published for 10 counties

## Slide 23
Mount Hope – 2010 Imagery
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9034811&y=4564776&l=11&v=1

## Slide 24
Mount Hope – 2015 Imagery
The 2015 aerial imagery shows structures have been removed but E-911 addresses are still indicated
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9034811&y=4564776&l=11&v=1

## Slide 25
Mount Hope – 2020 Imagery
The 2020 aerial imagery showing buyout properties (green polygons) and updated E-911 addresses
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9034818&y=4564756&l=12&v=1

## Slide 26
Leaf-Off Aerial Imagery Web Service
2021 Harrison County Aerial Imagery
https://services.wvgis.wvu.edu/arcgis/rest/services/Imagery_BaseMaps_EarthCover/wv_imagery_WVGISTC_leaf_off_mosaic/MapServer?f=jsapi
Counties provide leaf-off imagery
for State Imagery Web Service
Cached to 1:282 Zoom Level or Map Scale

## Slide 27
New 2019 Leaf-Off Aerial Imagery
http://www.mapwv.gov/floodtest/?wkid=102100&x=-9176629&y=4583554&l=13&v=1
New 2019 Imagery
on Flood Tool
Braxton
Cabell
Calhoun
Clay
Doddridge
Gilmer
Harrison
Jackson
Marshall
Monongalia
Ohio
Pocahontas
Putnam
Roane
Taylor
Tucker
Tyler
Wayne
Wetzel
Wirt
Cows in the Floodway
West Fork Twelvepole Creek, Wayne County
Choose WV Best Leaves Off Base Map
4-Inch Pixel Resolution

## Slide 28
Statewide E-911 Addresses
Missing Address Site Numbers
Berkeley Springs, WV

## Slide 29
Improved Property Parcel Mapping
Logan County
1322 WEST FORK RD TRLR, WEST FORK, WV, 25508
https://mapwv.gov/parcel/?pid=23-02-0109-0019-0004
Parcel 23-02-0109-0019-0004
Parcel Geometry Map Accuracy Improved
High Risk Advisory Zone

## Slide 30
State GIS Data Contracts
2 State Contracts for Aerial Imagery, Parcels, and Addresses
Map PDF

## Slide 31
Building Footprints
2018 Microsoft Building Footprints (for WV): 1,020,048 structure footprints
2021 FEMA's USA Structures (for WV): 1,085,876 structure footprints
2022 WVU Building Footprints (in progress)
Verification Layer: WV Building-Level Risk Assessment (BLRA): 98,467 points of primary structures located in the 1%-annual-chance floodplain

## Slide 32
Building Unique Identifier
Parcel ID | 01-08-0011-0069-0000
Address | 604 S Main St, Philippi, West Virginia, 26416
01 | - | 08 | - | 0011 | - | 0069 | - | 0000
County |  | District |  | Map |  | Parcel |  | Suffix
Building Identifier (Parcel ID + Address No.) | 01-08-0011-0069-0000_604
Link to Property Record
Link to Structure Record
Click here for more info on Building Identification

## Slide 33
Property Identification – Bldg. ID
Share Link: https://www.mapwv.gov/flood/map/?wkid=102100&x=-8909292&y=4742427&l=12&v=1
X,Y COORD.
ADDRESS
SHARE LINK
PARCEL
Address: 604 Main St, Philippi, WV 26416
Building ID:
(Parcel ID + Address No.)
01-08-0011-0069-0000_604
604 S. Main St., Philippi, WV 26416
Parcel ID: 01-08-0011-0069-0000

## Slide 34
Building 19-07-022B-0021-0000_7170
<< 781 Avon Bend Road, Charles Town, WV 25414 >>
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8664166&y=4753097&l=13&v=0
Built 2011
Crawl Basement
10 ft. Water Depth
Building ID: 19-07-022B-0021-0000_7170

## Slide 35
Risk Assessment
FLOOD ZONE MAP INFORMATION
What flood zone map information is available now or in the future?

## Slide 36
Historical Flood Information
High-Water Marks Graphic
Historical flood information including high water marks of past flooding events should be reviewed.
STORY MAPS:
Flood Risk in West Virginia: What We Learned from the June 2016 Flood
WV Flooded Towns, June 2016. The Historic Flooding of Southern West Virginia on June 23, 2016
FEMA Region 3 Report Understanding Flood Dangers in Central West Virginia: LESSONS LEARNED FROM THE JUNE 2016 FLOOD

## Slide 37
High Risk Advisory Zones
Preliminary NFHL
Advisory A
Updated AE
Preliminary NFHL
Advisory A
Updated AE
More info on High-Risk Advisory Zones

## Slide 38
Advisory: Building Future Map Conditions
High-Risk Effective & Advisory
1%-Annual-Chance (100-Yr) Floodplains
Residential Structure “mapped out” of SFHA
Future Map Conditions for structures are inventoried for counties with mapped High-Risk Advisory Floodplains
Commercial Structure “mapped in” of SFHA
Residential Structure “remains same” in SFHA
WV Flood Tool Map Link

## Slide 39
Map RevisionsHigh Risk Advisory Zones
Advisory Flood Zone* | Map Revision Type | Initiated | Applicable Zones
Preliminary NFHL or DFIRM | Risk MAP Restudy or Study | FEMA | A and AE Zones
Draft NFHL or DFIRM | Risk MAP Restudy or Study | FEMA | A and AE Zones
Advisory A | AFH Model-Backed Studies | State CTP | Approximate A Zone
Updated AE | Non-Restudy Redelineation | State CTP | AE Zone
* Note: Advisory Floodplains may be mapped outside of the official FIRM
High-Risk Advisory Zone Flood Products: (1) Advisory Floodplain Boundary, (2) Flood Height Grid, (3) Flood Depth Grid
Refer to WV Flood Tool Glossary for more information

## Slide 40
Active FEMA Flood Studies
Flood Study Project Status Map PDF
FEMA is creating new flood maps for communities in eastern and southern West Virginia. All flood maps will be updated with the new LiDAR.

## Slide 41
Draft NFHL
Draft NFHL
Draft NFHL Flood Zone: Pre-Preliminary FEMA National Flood Hazard Layers (NFHL) pending to become effective on updated Flood Insurance Rate Maps (FIRMs)

## Slide 42
Preliminary NFHL (Rainelle, WV)
Example of mapped in structures to new SFHA from Preliminary Flood Study of Rainelle, WV. Mapped in structures (orange circles) and flood loss estimates are updated in the statewide Building Level Risk Assessment (BLRA).
Rainelle, Greenbrier County

## Slide 43
Draft NFHL (Summers County)
Example of mapped in structures to new SFHA from Preliminary Flood Study along Summer-Greenbrier county border near Glenray. Mapped in structures (orange circles) and flood loss estimates are updated in the statewide Building Level Risk Assessment (BLRA).
Draft NFHL

## Slide 44
New Flood Maps
The June 2016 Flood High-Water Mark was 9.1 feet for Building 51-04-0003-0007-0000_91 located near the town Camden-On-Gauley (Webster County) on the Gauley River. The Base Flood Elevation is increasing by 6 feet on the new FEMA flood maps for this location.
FEMA is creating new flood maps for select communities in Region 4 which will alter the floodplain boundaries and base flood elevations. The new flood maps will affect the at-risk building inventories as well. The BFE is increasing 6 feet at this location.
Gauley River

## Slide 45
Zone A Mapping (Advisory)
15 Counties have no Advisory Base Flood Heights for A Zones
PDF Map
Advisory Flood Height Handout

## Slide 46
AE Redelineation (Advisory)
All Non-Restudy Areas: Redelineated AE Floodplains with Depth/WSEL grids mapped using LiDAR-derived 1-meter elevation data resolution
PDF Map
Redelineation Methodology

## Slide 47
Updated AE: BFE Non-Restudy
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8916222&y=4610916&l=12&v=1
FLOOD HEIGHTS (Example for Pocahontas County)
Non-Restudy Base Flood Elevation Heights displayed in Flood Query Results Panel
Data Products: Redelineated Floodplains, Water Surface Elevation Grid, Depth Grid
Flood Query Panel
NFHL X-Section Popup Window

## Slide 48
Updated AE (Camp Dawson)

## Slide 49
Updated AE (Camp Dawson)
Major Riverine Flooding Forecasted for Camp Dawson on 1 March 2021.
USGS Cheat River Stream Gage at Rowlesburg, WV

## Slide 50
Updated AE (Camp Dawson)
Camp Dawson, Preston County, a military complex on the Cheat River, has one of the highest cumulative building dollar exposures ($276M) and building damage loss estimates ($20M) in the State. A hydrograph on March 1, 2021, predicted major riverine flooding at 22.2 ft. (8 feet above flood stage of 16 feet); however, fortunately the flooding forecast for major flooding did not occur.
High value building exposure of Camp Dawson structures in AE Zone (WV Flood Tool Risk Map View)

## Slide 51
Updated AE Depth (Camp Dawson)
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8868186&y=4786467&l=9&v=2

## Slide 52
Flood Risk Assessment
FLOODPLAIN BUIDLING INVENTORY & FUTURE MAP CONDITIONS
What buildings are at risk?
Other Flood Risk Indicators
FEMA Risk Indicators: Community Engagement Prioritization (CEP) 2019
Disadvantaged Community Graphics

## Slide 53
Building Estimates
84,351 structures in SFHA
13,996 structures in “High-Risk” Advisory (Orange Zones)
354 Essential Facilities in High-Risk Flood Zones (K-12 Schools, 911 Centers, Police/Fire Stations Depts., Hospitals, Nursing Homes)
38 Essential Facilities in Regulatory Floodway
503 Essential Facilities total in both high and moderate risk floodplains
Buildings Pre-FIRM/Post-FIRM
67% are Pre-FIRM (majority)
26% are Post-FIRM
7% are unknown
Based on Building Year of assessment data
Statewide Building Inventory
Community | Buildings in SFHA
Kanawha County* | 8,890
Logan County* | 5,247
Mingo County* | 3,393
Boone County* | 3,313
Wheeling** | 2,836
Lincoln County* | 2,563
McDowell County* | 2,408
Raleigh County* | 2,252
Mercer County* | 2,233
Wyoming County* | 2,226
Wayne County* | 2,221
Putnam County* | 1,902
Cabell County* | 1,887
Charleston | 1,872
Wood County* | 1,562
Fayette County* | 1,528
Randolph County* | 1,268
Greenbrier County* | 1,182
Marion County* | 1,162
Huntington** | 1,148
Top 20 Communities
All ESSENTIAL FACILITIES SHOULD BE FIELD VERIFIED
Building Counts by Flood Zone

## Slide 54
Building Stock in Flood Zones
Although only 31% of the State has mapped Detailed Flood Zones (AE / AO / AH), the Detailed Flood Zones contain 65% of the Building Stock Located in SFHA. Most of the buildings are in mapped Detailed Flood Zones.
FLOOD HAZARD ZONES
Stream Miles Length
69% Approximate A
31% Detailed Zones
Special Flood Hazard Area
84,351 buildings
35% in Approximate Zone A
65% in Detailed Zone AE (9% in Regulatory Floodway)
BUILDINGS IN SHADED X
Moderate Risk
44,415 structures in 500-YR floodplains
9,718 structures in Levee Protected Zones
BUILDINGS IN NON-REGULATORY ZONES
13,966 Structures (14%) mapped in High-Risk Zone Advisory A / AE
98,317 Total High-Risk
PDF Map

## Slide 55
Potential Detailed Flood Studies
Objective: Evaluate potential Approximate A Zone rivers/streams for more comprehensive Detailed Flood Studies where clusters of buildings with high damage potential exist. The cluster analysis identifies a higher density (or higher development) of structures located in the Approximate A Zone. Refer to Zone A Cluster Analysis for more information.
Zone A Cluster PDF Tax Maps

## Slide 56
Potential Detailed Flood Studies
Rank | 1 | 2 | 3 | 4 | 5
BUILDING COUNT | Buckhannon | East Fork Twelvepole | Potomac | Shenandoah | Cacapon
 | 47 | 42 | 38 | 31 | 28
BUILDING DOLLAR EXPOSURE | Shenandoah | Cheat | Buckhannon | Tygart Valley | Potomac
 | $10.7M | $3.1M | $2.0M | $2.0M | $1.9M
BUILDING DAMAGE LOSS | Shenandoah | Cheat | Potomac | Buckhannon | Tygart Valley
 | $5.5M | $1.7M | $1.3M | $1.3M | $1.3M
DAMAGE ≥ 50% | Buckhannon | East Fork Twelvepole | Potomac | Shenandoah | Cacapon
 | 44 | 38 | 35 | 25 | 25
Water Depth in Structure ≥ 10 feet: Flooding exceeds entire first floor of non-elevated structures
Highest Building Flood Depth for Approximate A Zone Rivers/Streams (table extract). Sorted on building flood depth. Click on Flood Tool map link to view location.
River/Stream Name | Flood Depth Value (ft.) | Web Link | County | Flood Depth Source | Hazard Occupancy Code | Building Exposure ($)
Shenandoah River | 33.0 | FT | JEFFERSON COUNTY | HEC-RAS | COM8 | 532,300
South Branch Potomac | 28.5 | FT | HARDY COUNTY | HEC-RAS | RES2 | 1,710
Gauley River | 24.3 | FT | FAYETTE COUNTY | HEC-RAS | RES1 | 9,000
Beech Fork | 24.2 | FT | WAYNE COUNTY | HEC-RAS | GOV1 | 496,266
New River | 20.6 | FT | FAYETTE COUNTY | HEC-RAS | RES1 | 18,100
Zone A Cluster Analysis

## Slide 57
Potential Detailed Flood Studies
WV Flood Tool’s Risk MAP View – Building Damage Loss Estimate Percent Layer: In the Risk MAP View of the WV Flood Tool, the risk assessment layer, Building Damage Loss Estimate (%), provides a relationship between high flood depths and flood loss estimates of substantially damaged structures (> 50% damage). High building-level damage percentages typically correlate to structures in Approximate A Zones with high base flood depths for a 1% annual chance flood.
Zone A Cluster Analysis

## Slide 58
Potential Detailed Flood Studies
Building Damage Loss Estimate: Purple triangle symbol indicates Substantial Damage of Structure > 50%
High Water Marks
Shenandoah River (Harpers Ferry) Zone A Cluster A high-value wastewater treatment plant is associated with the high building exposure values of this Zone A cluster. Building 19-05-0004-0025-0000_744 has high-water marks on building side.
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8652936&y=4767965&l=11&v=2
Harpers Ferry, WV
Zone A Cluster Analysis

## Slide 59
Acreage of the SFHA (Top 20)
Modified aSFHA = Total aSFHA minus (1) large water bodies and (2) federal lands > 10 acres
County Unincorporated | Modified aSFHA
HAMPSHIRE COUNTY | 26,388
MASON COUNTY | 21,771
KANAWHA COUNTY | 21,196
GREENBRIER COUNTY | 20,060
RANDOLPH COUNTY | 19,842
WOOD COUNTY | 17,523
HARDY COUNTY | 16,850
JACKSON COUNTY | 15,300
WAYNE COUNTY | 13,521
PENDLETON COUNTY | 13,218
LINCOLN COUNTY | 11,137
BERKELEY COUNTY | 10,300
CABELL COUNTY | 10,278
POCAHONTAS COUNTY | 10,092
PRESTON COUNTY | 9,965
PUTNAM COUNTY | 9,934
NICHOLAS COUNTY | 8,999
WEBSTER COUNTY | 8,907
MINERAL COUNTY | 8,885
RALEIGH COUNTY | 8,719
Incorporated Place | County | Modified aSFHA
CHARLESTON, CITY OF (SPLIT) | KANAWHA COUNTY | 1,486
WHEELING, CITY OF (SPLIT) | OHIO COUNTY | 1,318
PARKERSBURG, CITY OF | WOOD COUNTY | 1,217
HUNTINGTON, CITY OF (SPLIT) | CABELL COUNTY | 823
NEW MARTINSVILLE, CITY OF | WETZEL COUNTY | 652
BUCKHANNON, CITY OF | UPSHUR COUNTY | 616
POINT PLEASANT, CITY OF | MASON COUNTY | 614
MOUNDSVILLE, CITY OF | MARSHALL COUNTY | 563
MARLINTON, TOWN OF | POCAHONTAS COUNTY | 494
MOOREFIELD, TOWN OF | HARDY COUNTY | 475
WEIRTON, CITY OF (SPLIT) | HANCOCK COUNTY | 456
CLARKSBURG, CITY OF | HARRISON COUNTY | 453
FAIRMONT,CITY OF | MARION COUNTY | 408
MORGANTOWN, CITY OF | MONONGALIA COUNTY | 387
MILTON, CITY OF | CABELL COUNTY | 377
BUFFALO, TOWN OF | PUTNAM COUNTY | 342
ELEANOR, TOWN OF | PUTNAM COUNTY | 340
PRINCETON, CITY OF | MERCER COUNTY | 332
BARBOURSVILLE, VILLAGE OF | CABELL COUNTY | 314
DUNBAR, CITY OF | KANAWHA COUNTY | 313
Top 20 Unincorporated / Incorporated Areas with Highest Acreage of SFHA (aSFHA)
Sample Community-Level Tabular Report

## Slide 60
Ratio of aSFHA to Community Area
Ratio = Acreage of SFHA (aSFHA) divided by Community Area
County Unincorporated | aSFHA
MASON COUNTY | 7.8%
WOOD COUNTY | 7.6%
JEFFERSON COUNTY | 6.8%
HAMPSHIRE COUNTY | 6.4%
CABELL COUNTY | 6.1%
MORGAN COUNTY | 5.7%
WIRT COUNTY | 5.4%
JACKSON COUNTY | 5.1%
BERKELEY COUNTY | 5.1%
TYLER COUNTY | 4.9%
PUTNAM COUNTY | 4.6%
HARDY COUNTY | 4.5%
PLEASANTS COUNTY | 4.5%
MINERAL COUNTY | 4.3%
WAYNE COUNTY | 4.2%
LINCOLN COUNTY | 4.0%
KANAWHA COUNTY | 3.9%
CALHOUN COUNTY | 3.6%
HARRISON COUNTY | 3.3%
BROOKE COUNTY | 3.3%
7.8%
5.1%
4.6%
6.1%
3.9%
7.6%
2.2%
5.4%
Unincorporated Areas
Data Table Source: Ratio of aSFHA to Community Area

## Slide 61
Ratio of aSFHA to Community Area
Ratio = Acreage of SFHA (aSFHA) divided by Community Area
47%
Top 20 Incorporated Areas with Highest Ratio of SFHA Acreage to Community Area
Incorporated Places | County | aSFHA
FRIENDLY, TOWN OF | TYLER COUNTY | 58.5%
HAMBLETON, TOWN OF | TUCKER COUNTY | 50.0%
REEDY, TOWN OF | ROANE COUNTY | 48.0%
BRUCETON MILLS | PRESTON COUNTY | 47.2%
PARSONS, CITY OF | TUCKER COUNTY | 43.5%
ELIZABETH, TOWN OF | WIRT COUNTY | 42.9%
HENDERSON, TOWN OF | MASON COUNTY | 42.6%
PINE GROVE, TOWN OF | WETZEL COUNTY | 42.4%
MATEWAN, TOWN OF | MINGO COUNTY | 41.7%
CAPON BRIDGE TOWN | HAMPSHIRE COUNTY | 40.0%
SMITHERS, TOWN OF | KANAWHA COUNTY | 40.0%
CHESAPEAKE, TOWN OF | KANAWHA COUNTY | 39.4%
ALBRIGHT,TOWN OF | PRESTON COUNTY | 38.9%
ROWLESBURG, TOWN OF | PRESTON COUNTY | 38.5%
GARY, CITY OF | MCDOWELL COUNTY | 37.9%
NEW MARTINSVILLE | WETZEL COUNTY | 37.6%
MILTON, CITY OF | CABELL COUNTY | 37.5%
ALDERSON, TOWN OF | MONROE COUNTY | 37.3%
HARTFORD, TOWN OF | MASON COUNTY | 36.4%
BANCROFT, TOWN OF | PUTNAM COUNTY | 35.5%
Bruceton Mills, WV

## Slide 62
Building Risk by River/Stream
Ohio River has highest building count and damages estimate
Stream | Bldg. Count | Bldg. Exposure ($) | Building Damage ($) | SDE ≥ 50%
Ohio River | 7,230 | $886M | $114M | 907
Kanawha River | 6,939 | $1,467M | $52M | 254
Elk River | 2,442 | $234M | $17M | 179
Guyandotte River | 1,404 | $184M | $5M | 45
Greenbrier River | 1,396 | $102M | $22M | 290
Little Kanawha River | 1,136 | $148M | $10M | 113
Mud River | 1,132 | $105M | $9M | 63
Island Creek (Logan Co) | 1,110 | $54M | $9M | 168
Clear Fork | 1,078 | $50M | $6M | 95
Pond Fork | 952 | $63M | $4M | 128
Buffalo Creek (Logan Co) | 930 | $41M | $4M | 57
PDF Map

## Slide 63
Building Risk by Region
Region 3 Highest % and Density
Regions 1, 2, and 3 comprise 56% of flood-risk buildings
Regions 10 and 11 high density
PDF Map

## Slide 64
R4 Building Risk by Flood Source
Computed for 1% (100-yr) floodplain
Region 4 PDF Map Primary Flood Sources
Flood Sources | Building Count | Dollar Exposure ($)
FAYETTE COUNTY |  | 
Armstrong Creek | 275 | $13,334K
Kanawha River | 242 | $46,459K
GREENBRIER COUNTY |  | 
Greenbrier River* | 528 | $60,728K
Howard Creek* | 364 | $94,870K
Sewell Creek* | 333 | $14,716K
Dry Creek | 197 | $19,183K
NICHOLAS COUNTY |  | 
Cherry River* | 374 | $15,719K
POCAHONTAS COUNTY |  | 
Greenbrier River** | 418 | $29,097K
Knapp Creek | 110 | $13,882K
WEBSTER COUNTY |  | 
Elk River | 312 | $16,938K
Gauley River** | 106 | $8,420K
* 2016 Disaster Restudy |  | 
Greenbrier River totals for Greenbrier and Pocahontas counties: 946 buildings in 1% floodplain, $90M dollar exposure
RA Tables: Buildings by River/Stream Name
Building Counts and Building Exposure $ Values by Stream Name
Greenbrier River in Region 4 has the most structures in the 1%-annual-chance floodplain
Howard Creek in Greenbrier County has the highest building dollar exposure of all communities in Region 4

## Slide 65
Building Risk by Watershed
Lower Kanawha Watershed has highest building count, building exposure, and damage loss estimate
PDF Map

## Slide 66
Countywide Building Counts (Top 20)
Primary buildings in the High-Risk effective and advisory 1%-annual chance (100-yr) floodplains
Rank | County | Region # | BUILDING TYPE |  |  |  | HIGH-RISK FLOOD ZONES |  |  | Floodplain Building Ratio
 |  |  | % Resi-dential | % Com-mercial | % Other | % Unknown | Effective | Advisory | Total Bldg. Count | 
1 | KANAWHA | 3 | 89% | 7% | 3% | 1% | 12,847 | 2,071 | 14,918 | 15%
2 | LOGAN | 2 | 87% | 9% | 3% | 2% | 4,539 | 939 | 5,478 | 30%
3 | MCDOWELL | 1 | 87% | 5% | 3% | 5% | 3,678 | 1,395 | 5,073 | 26%
4 | BOONE | 3 | 78% | 6% | 3% | 13% | 3,727 | 1,068 | 4,795 | 39%
5 | MINGO | 2 | 86% | 5% | 5% | 4% | 3,114 | 749 | 3,863 | 24%
6 | OHIO | 10 | 85% | 9% | 5% | 0% | 3,142 | 175 | 3,317 | 17%
7 | WYOMING | 1 | 90% | 5% | 4% | 1% | 2,019 | 1,145 | 3,164 | 24%
8 | CABELL | 2 | 86% | 7% | 5% | 2% | 2,368 | 518 | 2,886 | 7%
9 | GREENBRIER | 4 | 78% | 8% | 12% | 2% | 1,714 | 1,004 | 2,718 | 12%
10 | RALEIGH | 1 | 84% | 8% | 8% | 1% | 2,350 | 363 | 2,713 | 6%
11 | LINCOLN | 2 | 83% | 3% | 14% | 1% | 2,555 | 91 | 2,646 | 22%
12 | WAYNE | 2 | 89% | 4% | 5% | 2% | 2,421 | 219 | 2,640 | 12%
13 | WOOD | 5 | 87% | 7% | 6% | 0% | 2,463 | 103 | 2,566 | 6%
14 | MERCER | 1 | 89% | 6% | 4% | 1% | 2,295 | 206 | 2,501 | 7%
15 | PUTNAM | 3 | 85% | 5% | 10% | 0% | 2,066 | 384 | 2,450 | 9%
16 | WETZEL | 10 | 71% | 7% | 21% | 1% | 2,006 | 91 | 2,097 | 21%
17 | MASON | 2 | 67% | 4% | 27% | 3% | 1,859 | 95 | 1,954 | 13%
18 | RANDOLPH | 7 | 78% | 7% | 11% | 4% | 1,697 | 225 | 1,922 | 11%
19 | HARRISON | 6 | 80% | 6% | 13% | 1% | 1,475 | 409 | 1,884 | 5%
20 | FAYETTE | 4 | 85% | 7% | 7% | 1% | 1,254 | 551 | 1,805 | 7%
Top 5 Counties with highest building counts: Kanawha (14,918), Logan (5,478), and McDowell (5,073), Boone (4,795), and Mingo (3,683)
Top 5 counties with highest percentage of countywide buildings in the high-risk floodplains: Boone (39%), Logan (30%), McDowell (26%), Wyoming (24%), Mingo (24%), and Lincoln (22%)

## Slide 67
Countywide: # Buildings in 1% Floodplain
County-Wide
2,718
1,161
895
1,805
883
In Region 4, Greenbrier County has the most buildings in the 1% Annual Chance Floodplain
Primary structures located in high-risk effective and advisory 1%-annual-chance (100 year) floodplains
PDF Map

## Slide 68
% of Buildings in High-Risk Floodplain
High Percentage of Marlinton’s Buildings in Floodplain
Community Map
Countywide Map

## Slide 69
Community Building Counts (Top 20)
Primary buildings inventoried in 2022 the High-Risk 1%-annual chance (100-yr) floodplains. The building inventory includes both regulatory effective Special Flood Hazard Areas (SFHA) and non-regulatory advisory flood zones.
Unincorporated Areas
Incorporated Places
County Unincorporated | Total Buildings
Kanawha County* | 8,890
Logan County* | 5,247
Mingo County* | 3,393
Boone County* | 3,313
Lincoln County* | 2,563
McDowell County* | 2,408
Raleigh County* | 2,252
Mercer County* | 2,233
Wyoming County* | 2,226
Wayne County* | 2,221
Putnam County* | 1,902
Cabell County* | 1,887
Wood County* | 1,562
Fayette County* | 1,528
Randolph County* | 1,268
Greenbrier County* | 1,182
Marion County* | 1,162
Hampshire County* | 1,094
Harrison County* | 1,019
Monongalia County* | 1,004
Community Name | Total Buildings
Wheeling** | 2,836
Charleston | 1,872
Huntington** | 1,148
Dunbar | 1,068
New Martinsville | 817
Wellsburg | 791
Nitro** | 732
St. Albans | 683
Buckhannon | 606
Keyser | 511
Clarksburg | 455
White Sulphur Springs | 428
Milton | 419
South Charleston | 389
Marlinton | 381
Welch | 366
Oceana | 358
Rainelle | 340
Weston | 339
Moundsville | 335
Communities
Rank | Community Name | Region | Total Buildings
1 | Kanawha County* | 3 | 8,890
2 | Logan County* | 2 | 5,247
3 | Mingo County* | 2 | 3,393
4 | Boone County* | 3 | 3,313
5 | Wheeling** | 10 | 2,836
6 | Lincoln County* | 2 | 2,563
7 | McDowell County* | 1 | 2,408
8 | Raleigh County* | 1 | 2,252
9 | Mercer County* | 1 | 2,233
10 | Wyoming County* | 1 | 2,226
11 | Wayne County* | 2 | 2,221
12 | Putnam County* | 3 | 1,902
13 | Cabell County* | 2 | 1,887
14 | Charleston | 3 | 1,872
15 | Wood County* | 5 | 1,562
16 | Fayette County* | 4 | 1,528
17 | Randolph County* | 7 | 1,268
18 | Greenbrier County* | 4 | 1,182
19 | Marion County* | 6 | 1,162
20 | Huntington** | 2 | 1,148
** Split Community
* Unincorporated Area

## Slide 70
Community Level: # Bldgs. in 1% Floodplain
Community-Wide
Region 4 has a total of 7,123 structures in the high-risk effective and advisory 1%-annual-chance (100 yr.) floodplains valued at $525,285 million. Greenbrier County (ranked 15th in the State) has the highest countywide building count in the region.
White Sulphur Springs has the most buildings in the 1% Annual Chance Floodplain for Region 4
White Sulphur Springs
Primary structures located in high-risk effective and advisory 1%-annual-chance (100 year) floodplains
PDF Map

## Slide 71
R4 County and Community Rankings
** Split Community Source: Region 4 Community-Level Building Exposure Table
Highest building dollar exposure in the 1% floodplain:
White Sulphur Springs (incorporated)
Greenbrier County Unincorporated (unincorporated)
Greenbrier County (countywide)
Highest number of primary structures in the 1% floodplain:
White Sulphur Springs (incorporated)
Fayette County Unincorporated (unincorporated area)
Greenbrier County (countywide)
Greenbrier COUNTY has the highest building counts and dollar exposure
Fayette and Greenbrier UNINCORPORATED AREAS have the highest building counts and dollar exposure, respectively.
White Sulphur Springs INCORPORATED AREA has the highest 1% flood zone building counts and dollar exposure
Risk Assessment:

## Slide 72
R4 Community Bldgs Risk by Flood Zone
Region 4 Table
Community-Level Flood Zone Breakdown
Risk Assessment:
According to future flood maps, Fayette, Greenbrier, and Pocahontas counties have many structures being mapped into the higher risk 1%-annual-chance floodplain.
Webster Unincorporated and Richwood Incorporated have the most structures in the floodway. Buildings in the main channel of the river or stream, or close to the flood source, will be subject to the greatest flood depths, highest velocities, and greatest debris potential.

## Slide 73
Building Value ($) Floodplain Exposure
High Building Values of military complexes in Preston and Mineral counties result in increased Unincorporated ranking
Community Map
County Map

## Slide 74
Median Building Value
PDF Map

## Slide 75
Building Risk Reports
All Regions: Community Assets Report
All Regions: Essential Facilities Report
All Regions: Building Types & Exposure
Incorporate information from Risk Assessment Reports into local hazard mitigation planning

## Slide 76
Residential versus Non-Residential
Community | RESIDENTIAL |  |  |  |  | COMMERCIAL NON-RESIDENTIAL |  | OTHER NON-RESIDENTIAL |  | TOTAL BUILDING VALUE |  | 
Community Name | # | % Count |  | Value ($) | % Value | # | Value ($) | # | Value ($) | # | Value ($) | Rank1
Ansted | 1 | 100.0% |  | $66K | 100.0% | 0 | $0K | 0 | $0K | 1 | $66K | 19
Fayette County* | 1425 | 93.2% |  | $50,385K | 66.9% | 57 | $6,523K | 47 | $18,398K | 1529 | $75,307K | 2
Gauley Bridge | 21 | 46.7% |  | $869K | 27.4% | 24 | $2,302K | 0 | $0K | 45 | $3,171K | 11
Meadow Bridge | 21 | 91.3% |  | $695K | 96.8% | 2 | $23K | 0 | $0K | 23 | $718K | 16
Montgomery** | 13 | 86.7% |  | $1,083K | 25.2% | 1 | $1,000K | 1 | $2,215K | 15 | $4,298K | 
Mount Hope | 32 | 84.2% |  | $787K | 65.1% | 4 | $101K | 2 | $322K | 38 | $1,210K | 14
Oak Hill | 50 | 90.9% |  | $2,262K | 95.3% | 5 | $111K | 0 | $0K | 55 | $2,373K | 12
Pax | 32 | 82.1% |  | $925K | 67.9% | 3 | $98K | 4 | $340K | 39 | $1,362K | 13
Smithers** | 63 | 85.1% |  | $2,064K | 55.8% | 8 | $837K | 3 | $796K | 74 | $3,698K | 
FAYETTE | 1658 | 91.1% |  | $59,136K | 64.1% | 104 | $10,994K | 57 | $22,071K | 1819 | $92,201K | 2
Alderson** | 121 | 84.6% |  | $6,485K | 56.7% | 17 | $1,028K | 5 | $3,931K | 143 | $11,443K | 5**
Falling Springs | 3 | 100.0% |  | $157K | 100.0% | 0 | $0K | 0 | $0K | 3 | $157K | 18
Greenbrier County* | 1101 | 93.1% |  | $103,297K | 77.7% | 68 | $6,511K | 13 | $23,065K | 1182 | $132,873K | 1
Rainelle | 253 | 74.4% |  | $8,392K | 55.4% | 78 | $5,751K | 9 | $1,006K | 340 | $15,149K | 4
Ronceverte | 34 | 50.7% |  | $1,354K | 4.5% | 32 | $4,436K | 1 | $24,000K | 67 | $29,790K | 3
Rupert | 58 | 93.5% |  | $2,321K | 73.2% | 2 | $291K | 2 | $561K | 62 | $3,173K | 10
White Sulphur Springs | 375 | 87.6% |  | $18,910K | 36.4% | 42 | $5,144K | 11 | $27,940K | 428 | $51,994K | 1
GREENBRIER | 1945 | 87.4% |  | $140,916K | 57.6% | 239 | $23,161K | 41 | $80,503K | 2225 | $244,580K | 1
Nicholas County* | 624 | 90.2% |  | $21,060K | 68.1% | 42 | $6,646K | 26 | $3,230K | 692 | $30,936K | 4
Richwood | 265 | 80.5% |  | $7,518K | 55.8% | 47 | $1,399K | 17 | $4,556K | 329 | $13,473K | 6
Summersville | 23 | 63.9% |  | $1,497K | 11.3% | 11 | $1,657K | 2 | $10,109K | 36 | $13,263K | 7
NICHOLAS | 912 | 86.3% |  | $30,075K | 52.1% | 100 | $9,703K | 45 | $17,895K | 1057 | $57,672K | 5
Durbin | 23 | 85.2% |  | $645K | 72.4% | 2 | $157K | 2 | $89K | 27 | $891K | 15
Marlinton | 286 | 75.1% |  | $15,309K | 44.3% | 82 | $9,635K | 13 | $9,586K | 381 | $34,529K | 2
Pocahontas County* | 502 | 93.0% |  | $23,166K | 84.7% | 23 | $2,460K | 15 | $1,731K | 540 | $27,358K | 5
POCAHONTAS | 811 | 85.5% |  | $39,120K | 62.3% | 107 | $12,252K | 30 | $11,406K | 948 | $62,779K | 4
Addison | 107 | 84.9% |  | $3,855K | 32.7% | 15 | $3,053K | 4 | $4,892K | 126 | $11,799K | 8
Camden-On-Gauley | 13 | 61.9% |  | $263K | 45.9% | 4 | $32K | 4 | $279K | 21 | $573K | 17
Cowen | 28 | 80.0% |  | $814K | 15.4% | 4 | $92K | 3 | $4,375K | 35 | $5,281K | 9
Webster County* | 839 | 94.1% |  | $25,759K | 51.1% | 27 | $2,685K | 26 | $21,957K | 892 | $50,400K | 3
WEBSTER | 987 | 91.9% |  | $30,690K | 45.1% | 50 | $5,861K | 37 | $31,502K | 1074 | $68,053K | 3
SUMMARY | 6,313 | 88.5% |  | $299,937K | 56.3% | 600 | $61,971K | 210 | $163,376K | 7,123 | $525,285K | 
Alderson (Greenbrier/Monroe) Split Community Total: |  |  |  |  |  |  |  |  |  |  |  | 
Alderson** | 175 | 0.0% | $8,869K |  | 60.4% | 24 | $1,482K | 10 | $4,332K | 209 | $14,683K | 5
1 Group Rank on Community Type: County, Unincorporated, Incorporated. Table ranking by Region and not Statewide.
Building Dollar Exposure Report: Residential versus Non-Residential

## Slide 77
Non-Residential % of Building Stock
Majority of Building Stock is RESIDENTIAL. Incorporated Places typically have high non-residential building counts than Unincorporated Areas.
PDF Map

## Slide 78
Non-Residential Value ($) of Building Stock
Monongalia, Preston, and Mineral Unincorporated Areas have utilities and military complexes of high value that significantly increases total non-residential values
PDF Map

## Slide 79
Non-Residential Building Exposure
PDF Map
Top non-residential structure in the 1%-annual-chance floodplain with the highest building value for REGION 4 is the Ronceverte Wastewater Treatment Plant ($24M)

## Slide 80
Non-Residential Utilities
Utility structures have some of the highest building values in the State
PDF Map

## Slide 81
R4 Non-Residential: High Bldg. Values
Unincorporated ** Split Community Region 4: Tabular Building-Level Report Link: https://data.wvgis.wvu.edu/pub/RA/State/BL/BLRA/R4_BLRA_Full_List/ Region 4: Top 10% Data Extract of High Building Dollar Exposure: https://data.wvgis.wvu.edu/pub/RA/State/BL/Extract/HighBldgValue/ State Top 100: Building Exposure: https://data.wvgis.wvu.edu/pub/RA/State/BL/Top-List/Top100/
FAYETTE COUNTY Community Name | WV Flood Tool Link | FAYETTE COUNTY Owner Name or Building ID | Hazard Occupancy Code | General Occupancy | Building Appraisal
Smithers** | FT | BOARD OF EDUCATION FAY CO | EDU1 | Other | $ 17,343,724
Montgomery** | FT | LAIRD FOUNDATION INC | COM6 | Commercial | $ 5,254,600
Smithers** | FT | BOARD OF EDUCATION FAY CO | EDU1 | Other | $ 4,213,763
Fayette County* | FT | WHITE OAK PUBLIC SERVICE DIST | COM4 | Commercial | $ 4,000,000
Fayette County* | FT | CITY OF MT HOPE | COM4 | Commercial | $ 3,000,000
Montgomery** | FT | LIVING WATERS CHRISTIAN FELLOWSHIP (TRUSTEES) | REL1 | Other | $ 2,214,940
Fayette County* | FT | ARMSTRONG PUB SERV DIST | COM4 | Commercial | $ 2,000,000
Fayette County* | FT | CLONCH INDUSTRIES INC | IND1 | Commercial | $ 1,285,200
Highly valued buildings in 1% Floodplain for Fayette County. Which high-valued-structures are vulnerable to riverine flooding?
Community Engagement and Verification: Region 4 has a total of 7,123 structures in the 1%-annual-chance floodplain valued at $525,285 million
Building-Level Verification: Verify the highly valued buildings using the building-level risk assessment (BLRA) table, Top 10% data extract high-building dollar exposure, statewide top building exposure listing, and Risk MAP View of the WV Flood Tool. For buildings inventoried in the 1% floodplains, review the most expensive residential and non-residential buildings located in the high-risk flood zones sorted on building appraisal value from largest to smallest value. Identify building-level mitigation and outreach strategies.

## Slide 82
R4 Non-Residential: High Bldg. Values
GREENBRIER COUNTY Community Name | WV Flood Tool Link | GREENBRIER COUNTY Owner Name or Building ID | Hazard Occupancy Code | General Occupancy | Building Appraisal
Ronceverte | FT | THE CITY OF RONCEVERTE WWP | GOV1 | Other | $24,000,000
White Sulphur Springs | FT | GREENBRIER CO BD OF ED | EDU1 | Other | $ 8,542,982
Greenbrier County* | FT | W V DEPARTMENT OF CORRECTION | GOV1 | Other | $ 4,067,092
Alderson** | FT | BOARD OF EDUCATION | EDU1 | Other | $ 3,508,927
Ronceverte | FT | B A MULLICAN LUMBER & MANUFACT URING CO L P | IND1 | Commercial | $ 2,043,400
Rainelle | FT | PARK CENTER INC | COM1 | Commercial | $ 1,443,900
White Sulphur Springs | FT | BANK OF WHITE SULPHUR SPRINGS | COM5 | Commercial | $ 1,186,700
Greenbrier County* | FT | WHATCOAT UNITED METHODIST CHURCH | REL1 | Other | $ 768,240
Highly valued buildings in 1% Floodplain for Greenbrier County. Which high-valued-structures are vulnerable to riverine flooding?
Unincorporated ** Split Community Region 4: Tabular Building-Level Report Link: https://data.wvgis.wvu.edu/pub/RA/State/BL/BLRA/R4_BLRA_Full_List/ Region 4: Top 10% Data Extract of High Building Dollar Exposure: https://data.wvgis.wvu.edu/pub/RA/State/BL/Extract/HighBldgValue/ State Top 100: Building Exposure: https://data.wvgis.wvu.edu/pub/RA/State/BL/Top-List/Top100/

## Slide 83
Residential % of Building Stock
Majority of Building Stock is RESIDENTIAL. Unincorporated Areas typically have higher residential building counts than Incorporated Places.
PDF Map

## Slide 84
Residential Value ($) of Building Stock
Monongalia, Preston, and Mineral Unincorporated Areas have utilities and military complexes of high value that significantly increases total non-residential values
PDF Map

## Slide 85
Residential: Top Single-Family $ Exposure
74% of million-dollar RESIDENTIAL structures in State are located along Howard Creek in Greenbrier County
Howard Creek
PDF Map

## Slide 86
Residential: High Building $ Exposure
White Sulphur Springs
Mapped-In Draft Floodplain (Future SFHA)
Four Homes along Howard Creek with Total Building Value of $8.2 million mapped into new Draft Floodplain. Building status changed when newer Preliminary Floodplain published in 2021.
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8942775&y=4547402&l=11&v=2

## Slide 87
Residential: Mobile Home %
Manufactured homes are of lightweight construction and more vulnerable to flood damage
23% of the mobile homes in West Virginia are in the High-Risk Flood Zones
27% of the total residential buildings located in the 1% floodplain are manufactured homes
13.8% of the total occupied residential units in West Virginia compared to a 5.5% U.S. average. (Source: Census)
PDF Map

## Slide 88
Permanent Structures?
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8663702&y=4797889&l=11&v=2
Building ID: 02-08-0001-0030-0000_3458

## Slide 89
Recreational Vehicles
<< WV Quick Guide resource >>
https://emd.wv.gov/MitigationRecovery/Documents/Floodplain%20Management%20in%20WV%20Quick%20Guide.pdf

## Slide 90
Residential: Single Family Dwellings
1 Group Rank on Community Type: County, Unincorporated, Incorporated. Table ranking by Region and not Statewide.
Building Dollar Exposure Report: Single Family Dwellings
Community |  | SINGLE FAMILY HOME |  | MANUFACTURED (MOBILE) HOME |  |  | SINGLE FAMILY TOTAL |  | 
Community Name | County | Count | Value ($) | Count | % Count | Value ($) | Count | Value ($) | Group Rank1
Ansted | FAYETTE | 1 | $66K | 0 | 0.0% | $0K | 1 | $66K | 18
Fayette County* | FAYETTE | 1165 | $44,640K | 239 | 17.0% | $4,131K | 1404 | $48,771K | 2
Gauley Bridge | FAYETTE | 17 | $619K | 1 | 5.6% | $10K | 18 | $629K | 15
Meadow Bridge | FAYETTE | 13 | $551K | 7 | 35.0% | $113K | 20 | $664K | 13
Montgomery** | FAYETTE | 11 | $931K | 1 | 8.3% | $15K | 12 | $945K | 3
Mount Hope | FAYETTE | 31 | $771K | 1 | 3.1% | $16K | 32 | $787K | 12
Oak Hill | FAYETTE | 47 | $2,173K | 2 | 4.1% | $39K | 49 | $2,212K | 7
Pax | FAYETTE | 28 | $827K | 4 | 12.5% | $97K | 32 | $925K | 10
Smithers** | FAYETTE | 54 | $1,802K | 6 | 10.0% | $77K | 60 | $1,879K | 2
 | FAYETTE | 1367 | $52,379K | 261 | 16.0% | $4,499K | 1628 | $56,877K | 2
Alderson** | GREENBRIER | 107 | $5,786K | 10 | 8.5% | $248K | 117 | $6,034K | 1
Falling Springs | GREENBRIER | 2 | $137K | 1 | 33.3% | $20K | 3 | $157K | 17
Greenbrier County* | GREENBRIER | 822 | $96,262K | 264 | 24.3% | $6,626K | 1086 | $102,888K | 1
Rainelle | GREENBRIER | 229 | $7,621K | 16 | 6.5% | $579K | 245 | $8,200K | 3
Ronceverte | GREENBRIER | 29 | $1,138K | 0 | 0.0% | $0K | 29 | $1,138K | 9
Rupert | GREENBRIER | 45 | $1,974K | 11 | 19.6% | $329K | 56 | $2,302K | 6
White Sulphur Springs | GREENBRIER | 338 | $15,856K | 4 | 1.2% | $125K | 342 | $15,981K | 1
 | GREENBRIER | 1572 | $128,774K | 306 | 16.3% | $7,926K | 1878 | $136,699K | 1
Nicholas County* | NICHOLAS | 455 | $17,833K | 165 | 26.6% | $2,939K | 620 | $20,772K | 5
Richwood | NICHOLAS | 217 | $6,725K | 42 | 16.2% | $630K | 259 | $7,356K | 4
Summersville | NICHOLAS | 19 | $1,423K | 3 | 13.6% | $55K | 22 | $1,478K | 8
 | NICHOLAS | 691 | $25,981K | 210 | 23.3% | $3,624K | 901 | $29,605K | 5
Durbin | POCAHONTAS | 15 | $499K | 7 | 31.8% | $130K | 22 | $629K | 14
Marlinton | POCAHONTAS | 244 | $8,263K | 22 | 8.3% | $354K | 266 | $8,617K | 2
Pocahontas County* | POCAHONTAS | 400 | $21,017K | 90 | 18.4% | $1,504K | 490 | $22,521K | 4
 | POCAHONTAS | 659 | $29,779K | 119 | 15.3% | $1,988K | 778 | $31,767K | 3
Addison | WEBSTER | 95 | $3,434K | 11 | 10.4% | $211K | 106 | $3,645K | 5
Camden-On-Gauley | WEBSTER | 9 | $171K | 4 | 30.8% | $92K | 13 | $263K | 16
Cowen | WEBSTER | 13 | $423K | 15 | 53.6% | $391K | 28 | $814K | 11
Webster County* | WEBSTER | 598 | $20,815K | 238 | 28.5% | $4,885K | 836 | $25,700K | 3
 | WEBSTER | 715 | $24,842K | 268 | 27.3% | $5,580K | 983 | $30,422K | 4
SUMMARY |  | 5,004 | $261,756K | 1,164 | 19.6% | $23,616K | 6,168 | $285,371K | 

## Slide 91
State Flood Risk Assessment
SIGNIFICANT STRUCTURES OF IMPORTANCE
What critical facilities are at risk?

## Slide 92
Essential Facilities 0.2% Floodplain
16
8
5
4
4
Fayette County is ranked 8th in the State for the most essential facilities. The town of Marlinton is ranked 7th of all incorporated places.
PDF Map

## Slide 93
Essential Facilities
Rank | Community Name | County | Community Type | WV RPDC Region | Essential Facilities in High & Moderate Risk Flood Zones
1 | Kanawha County* | KANAWHA | Unincorporated | 3 | 23
2 | Charleston | KANAWHA | Incorporated | 3 | 19
3 | Huntington** | CABELL & WAYNE | Incorporated | 2 | 16
4 | Wayne County* | WAYNE | Unincorporated | 2 | 12
5 | Boone County* | BOONE | Unincorporated | 3 | 12
6 | Logan County* | LOGAN | Unincorporated | 2 | 11
7 | Mingo County* | MINGO | Unincorporated | 2 | 10
8 | South Charleston | KANAWHA | Incorporated | 3 | 9
9 | Raleigh County* | RALEIGH | Unincorporated | 1 | 8
10 | Wheeling** | MARSHALL & OHIO | Incorporated | 10 | 8
11 | McDowell County* | MCDOWELL | Unincorporated | 1 | 7
12 | Lincoln County* | LINCOLN | Unincorporated | 2 | 6
13 | Weston | LEWIS | Incorporated | 7 | 6
14 | New Martinsville | WETZEL | Incorporated | 10 | 6
15 | Welch | MCDOWELL | Incorporated | 1 | 5
16 | Cabell County* | CABELL | Unincorporated | 2 | 5
17 | Madison | BOONE | Incorporated | 3 | 5
18 | Dunbar | KANAWHA | Incorporated | 3 | 5
19 | Buffalo | PUTNAM | Incorporated | 3 | 5
20 | Fayette County* | FAYETTE | Unincorporated | 4 | 5
Includes Schools, Hospitals, Nursing Homes, Police Stations, Fire Stations, and E-911 Dispatch Centers
Essential Facilities Table and Reports

## Slide 94
R4 Essential Facilities
Risk Assessment
58% or 15 of the 26 flood-prone communities in Region 4 have essential facilities vulnerable to flooding. The county with the most essential facilities is Fayette County (ranked 8th for all counties), while the incorporated town with the highest number of facilities is Marlinton (ranked 7th for all municipalities in State) in Pocahontas County. Hospitals and nursing homes with immobile patients or residents are particularly vulnerable to a flood disaster. Small towns situated mostly in the floodplain are more challenged than unincorporated areas or larger cities to identify suitable sites that provide a high level of protection from flooding.
WV Flood Tool Map Link: https://www.mapwv.gov/flood/map/?wkid=102100&x=-8915613&y=4610416&l=8&v=2
The town of Marlinton (Pocahontas County) and Fayette County have a large number of essential facilities
R4 Essential Facilities Report
Marlinton

## Slide 95
R4 Essential Facilities
Community Name | County | Facility Name | Facility Type | Flood Tool Link | Flood Depth | Building Damage Percent
Alderson** | GREENBRIER | Alderson Elementary School | School | FT | 3.5 | 8.0
Marlinton | POCAHONTAS | Marlinton Police Department | Police Station | FT | 2.2 | 7.6
Marlinton | POCAHONTAS | Marlinton Volunteer Fire Department | Fire Station | FT | 2.2 | 7.7
Fayette County* | FAYETTE | Loup Creek Volunteer Fire Department - Robson | Fire Station | FT | 1.1 | 0.9
Community Engagement and Verification: There are 25 facilities in the high risk effective and advisory 1%-annual-chance (100-yr) flood level and 12 facilities in the moderate risk 0.2%-annual-chance (500-yr) flood level. No essential facilities exist in the Regulatory Floodway.
Review the accuracy and completeness of all active essential facilities. Report any facilities that are missing. Verify the facilities and location using the CL Report / Tables, BL Tables, and RiskMAP View of the WV Flood Tool.
* Unincorporated Area
** Split Community

## Slide 96
Community Assets (Non-Historical)
The town of Marlinton has six government and two utility buildings
Marlinton
PDF Map

## Slide 97
Community Assets
Risk Assessment
Community Assets: A total of 170 community assets (non-historical) were inventoried in the 1%-annual-chance floodplain for the Region 4 Planning and Development Council. Fayette County has the largest number of inventoried community resources (n=53) of which the majority are religious buildings. The town of Marlinton (ranked 3rd of all incorporated areas) has six government and two utility buildings (ranked 5th) located in the floodplain.
R4 Community Assets Report
WV Flood Tool Map Link: https://www.mapwv.gov/flood/map/?wkid=102100&x=-8914626&y=4611336&l=8&v=2
Marlinton
The town of Marlinton (Pocahontas County) and Fayette County have many community assets

## Slide 98
Community Assets
Community Name | County | Historical Place | Facility Type | Flood Tool Link | Flood Depth | Building Damage Percent
Ronceverte | GREENBRIER | Ronceverte Water Treatment Plant | Utilities | FT | 9.6 | 21%
Fayette County* | FAYETTE | United States Postal Service Office | Government | FT | 7.0 | 15%
Webster County* | WEBSTER | United States Postal Service | Government | FT | 5.5 | 7%
Webster County* | WEBSTER | Craigsville Public Service District | Utilities | FT | 5.1 | 29%
Fayette County* | FAYETTE | New River Gorge Visitor Contact Center | Government | FT | 4.8 | 14%
Community Engagement and Verification: A total of 170 community assets (non-historical) and 102 historical buildings were inventoried in the 1%-annual-chance floodplain for the Region 4
Review the accuracy and completeness of all active community assets. Report any structures that are missing. Verify the buildings and location using the CL Report / Tables, BL Tables, and Risk MAP View of the WV Flood Tool. Review and identify mitigation strategies for the community assets vulnerable to flooding.
* Unincorporated Area
** Split Community

## Slide 99
Highly Valued ($) Utility
Mitigation: Examples of mitigation measures for utilities include:
Emergency response plan
Barriers around key assets
Elevated electrical equipment
Emergency generators
Bolted down chemical tanks
$24M Ronceverte Wastewater Treatment Plant (on the State’s Top 100 List)
Risk Assessment: In 2018, the new Ronceverte's wastewater treatment plant was constructed at a cost of $24 million. All structures of the wastewater treatment plant are in the effective high-risk floodplain at a 1% (100-year) estimated flood inundation depth of 9.5 feet. At the treatment plant location, the 0.2% (500-year) estimated flood inundation depth is about two feet higher than that of the 1% floodplain. The USGS high water marks show the maximum inundation of 3.24 feet above the ground at the facility site for the 2016 flood event. The structures are also located in a preliminary floodplain at a 1% (100-year) estimated inundation depth of 6.5 feet. The preliminary floodplain delineated based on the new flood study is under review to become effective.
Flood Tool Map Link
The Ronceverte Wastewater Treatment Plant is the highest valued, non-residential flood-prone structure inventoried for Region 4.

## Slide 100
Historical Structures (Building Year)
The towns of Mount Hope and Ronceverte are two of the oldest communities in the region with building year median values of 1920
Mount Hope
Ronceverte
PDF Map

## Slide 101
Historical Community Assets
Mitigation: A designated historic structure can obtain the benefit of subsidized flood insurance through the NFIP even if it has been substantially improved or substantially damaged so long as the building maintains its historic designation.
Community Name | County | Facility Name | Facility Type | Flood Tool Link | Flood Depth | Building Damage Percent
Mount Hope | FAYETTE | Mount Hope Historic District | National Register | FT | 6.8 | 46%
Fayette County* | FAYETTE | Bank of Glen Jean | National Register | FT | 4.8 | 14%
Alderson** | GREENBRIER | Alderson Historic District | National Register | FT | 4.8 | 14%
Ronceverte | GREENBRIER | Ronceverte Historic District | National Register | FT | 4.4 | 43%
Mount Hope | FAYETTE | Mount Hope Historic District | National Register | FT | 4.3 | 13%
Alderson** | GREENBRIER | Alderson Historic District | National Register | FT | 4.2 | 27%
Historical Buildings (Region 4)
Source Data: https://data.wvgis.wvu.edu/pub/RA/State/BL/CommunityAsset/
* Unincorporated Area
** Split Community
Risk Assessment: Buildings identified within National Register Areas or registered historic districts are older than 1930. Greenbrier County is ranked 7th in the State as having the most historical buildings (n=56) in the high-risk floodplain of which the majority are located in the city of Ronceverte (ranked 14th of all incorporated areas). The split community of Alderson and the city of Mount Hope also have significant numbers of historical buildings in the high-risk floodplain (18 and 16 rank respectively).

## Slide 102
National Register Areas
Community Name | County | Historic Name | # Bldg. Points in NR Area (estimate) | Flood Tool Link
Alderson** | GREENBRIER | Alderson Historic District | 45 | FT
Ronceverte | GREENBRIER | Ronceverte Historic District | 35 | FT
Mount Hope | FAYETTE | Mount Hope Historic District | 18 | FT
Richwood | NICHOLAS | Downtown Richwood Historic District | 10 | FT
Risk Assessment: For communities with the most National Register Areas in the State that intersect the 1% floodplain, Greenbrier County (12 NR Areas) is ranked 4th and Fayette County (7 NR Areas) ranked 7th
Ronceverte Historic District
Alderson Historic District
National Register Areas (Region 4)

## Slide 103
Board of Risk & Insurance Management (BRIM)
The WV Board of Risk and Insurance Management (BRIM) database according to the 2018 data extract stores facility and building value information for more than 150 West Virginia State agencies (e.g., State Capitol, DNR Park Buildings, DOH Facilities, DOE Schools, WVU Buildings) representing 15,111 records, The building values are important source for tax exempt buildings that have no or unreliable replacement values listed in the statewide tax assessment database. Only 48% (n=7,304) of the total records of the non-spatial BRIM database have city-style addresses, of which only 41% (n=6,273) of the records could be spatially geocoded to site or street address matches.
The BRIM database provides building values for schools and other tax-exempt state facilities
Upgrading and maintaining the Board of Risk and Insurance Management (BRIM) as a spatial database is a Mitigation Action Goal of the Statewide Hazard Mitigation Plan.
PDF Map

## Slide 104
Other Flood Risk Indicators
Flood Risk Assessment
Flood Damage Loss Models
What is the degree of damage or flood loss?
FEMA Risk Indicators: Community Engagement Prioritization (CEP) 2019
Disadvantaged Community Graphics
FLOOD LOSS MODELS Open Hazus FAST
Flood Depths Building Damage Estimates
2

## Slide 105
Hazus Flood Loss Estimation Program
Slide courtesy of FEMA
A GIS-based natural hazard analysis tool developed and freely distributed by FEMA
FEMA’s Hazus Flood Assessment Structure Tool (FAST)
Riverine Hazus Level-2 Analysis
1% Annual Flood Event
Python Programs

## Slide 106
Depth-Damage Function (DDF) Values

## Slide 107
Post-FIRM Structure in Floodway
Building ID | 19-06-009H-0019-0000_781
Full E-911 Address | 781 AVON BEND RD, CHARLES TOWN, WV, 25414
GIS Parcel ID | 19-06-009H-0019-0000
Plus Code | 87F46599+H9X
WV Flood Tool Link | https://mapwv.gov/flood/map/?wkid=102100&x=-8664164.49652&y=4753089.59353&l=13&v=0
WV Parcel Assessment Link | https://mapwv.gov/Assessment/Detail/?PID=1906009H001900000000
Full Owner Address | 9299 ALL SAINTS RD, LAUREL, MD 20723
Occ | RES1
Cost | 170200
NumStories | 2
FoundationType | 5
FirstFloorHt | 4
Area | 2496
UserDefinedFltyId | 453
Latitude | 39.218996
Longitude | -77.83151391
Depth_Grid | 9.825653
Depth_in_Struc | 5.825653076
flExp | 1
SOID | R12N
BDDF_ID | 107
BldgDmgPct | 23.7
BldgLossUSD | $40,254
ContentCostUSD | $85,100.00
CDDF_ID | 23.00
ContDmgPct | 37.95
ContentLossUSD | $32,299
DebrisID | RES1NBFT4
Debris_Tot | 
Restor_Days_Min | 270
Restor_Days_Max | 450
GridName | AFH_wm.tif
Building ID | 19-06-009H-0019-0000_781
Full E-911 Address | 781 AVON BEND RD, CHARLES TOWN, WV, 25414
Full Owner Address | 9299 ALL SAINTS RD, LAUREL, MD 20723
GIS Parcel ID | 19-06-009H-0019-0000
Lat | 39.218996
Long | -77.83151391
Plus Code | 87F46599+H9X
WV Flood Tool Link | https://mapwv.gov/flood/map/?wkid=102100&x=-8664164.49652&y=4753089.59353&l=13&v=0
WV Parcel Assessment Link | https://mapwv.gov/Assessment/Detail/?PID=1906009H001900000000
CID | 540065
Community Name | JEFFERSON COUNTY *
Stream Name | Shenandoah River
Watershed (HUC8) | Shenandoah (2070007)
Flood Zone Designation | Effective 100 yr Zone AE - Floodway
Floodway | Yes
Year Built | 2011
FIRM Status | Post-FIRM
Hazard Occupancy Code | RES1
Stories | 2
Basement Type | Crawl
First Floor Height | 4.0
Building Appraisal | $170,200
Structure Area | 2496
Flood Depth Value | 9.8
Flood Depth Source | HEC-RAS
WSEL Value | 376.0
WSEL Source | UAE
Ground Elevation | 366.2
Ground Elevation Source | 2012 FEMA Jefferson, Berkeley & Morgan Lidar
Grade | C+
Tax Class | 2
Land Use Description | Residential 1 Family
Exterial Wall Type | Aluminum
Building Inputs
Water Depth Input
OpenHazus FAST Utility Building Impact Output
BLDG. LEVEL RISK ASSESSMENT (BLRA) DATABASE
Building Level & Community Level Outputs
3

## Slide 108
Top Non-Residential Loss Estimates
PDF Map

## Slide 109
Top Residential Damage Loss ($)
PDF Map

## Slide 110
Median Damage Value
PDF Map

## Slide 111
Substantial Damage Estimates
PDF Map

## Slide 112
R9 Substantial Damage Estimates
Community Name | County | Count Total | Value Total | TEIF Loss Total | TEIF Loss Ratio Total | Median Percent Damage | Median Dollar Damage | Debris Damage Total | High Damage Count (BldgDmgPct >= 50% OR BldgLossUSD > $10k)
Berkeley County* | BERKELEY | 635 | $52,931K | $5,729K | 11% | 65% | $15K | 6,172 | 188
Martinsburg | BERKELEY | 75 | $62,324K | $14,105K | 23% | 9% | $4K | 136 | 8
 | BERKELEY | 710 | $115,255K | $19,834K | 17% | 54% | $13K | 6,308 | 196
Jefferson County* | JEFFERSON | 526 | $70,260K | $6,047K | 9% | 39% | $21K | 4,434 | 183
Bolivar | JEFFERSON | 3 | $251K | $118K | 47% | 48% | $37K | 135 | 3
Charles Town | JEFFERSON | 27 | $3,180K | $27K | 1% | 4% | $3K | 12 | 0
Harpers Ferry | JEFFERSON | 31 | $6,965K | $4,785K | 69% | 74% | $131K | 4,683 | 30
Ranson | JEFFERSON | 80 | $5,305K | $16K | 0.3% | 4% | $2K | 4 | 0
Shepherdstown | JEFFERSON | 66 | $18,724K | $1,058K | 6% | 8% | $14K | 427 | 38
 | JEFFERSON | 733 | $104,685K | $12,052K | 12% | 30% | $21K | 9,695 | 254
Morgan County* | MORGAN | 484 | $69,867K | $7,057K | 10% | 41% | $16K | 4,368 | 166
Bath | MORGAN | 129 | $35,224K | $2,621K | 7% | 10% | $11K | 698 | 44
Paw Paw | MORGAN | 30 | $2,770K | $16K | 1% | 6% | $3K | 19 | 0
 | MORGAN | 643 | $107,862K | $9,695K | 9% | 22% | $14K | 5,085 | 210
Generated using FEMA’s Hazus flood loss software program for a 1%-annual-chance (100-yr) flood event
Statewide 17% $6K
Damage Loss Tables

## Slide 113
Flood Damage Visualizations
<< Harpers Ferry Flood Risk 3D Visualization Movie >> https://data.wvgis.wvu.edu/pub/RA/_resources/3Dflood/HarpersFerry_Jefferson_3D_Flood_2020_mp4.mp4

## Slide 114
Debris Removal
PDF Map

## Slide 115
Post-FIRM Structures (New Development)
PDF Map

## Slide 116
Post-FIRM Minus-Rated Structures
PDF Map

## Slide 117
Road Inundation: 1% Flood
<< Highest Road Flooding Risk in the Nation >> According to the nonprofit First Street Foundation’s October 2021 report titled "The 3rd National Risk Assessment: Infrastructure on the Brink," 46 percent of the roads in the state and 51 percent of the state’s critical facilities — the highest state-level figures in the Nation — would be closed by flooding.
PDF Map

## Slide 118
Road Inundation: 1% Flood

## Slide 119
Road Inundation Models
Community Name | County | Roads in Flood Plain (miles) | Roads Flooded (miles) | Roads Below 1ft (Ratio) | Roads 1 to 3ft (Ratio) | Roads Above 3ft (Ratio)
Berkeley County* | BERKELEY | 25.7 | 17.0 | 21% | 22% | 57%
Martinsburg | BERKELEY | 0.8 | 0.5 | 60% | 20% | 20%
 | BERKELEY | 26.5 | 17.5 | 22% | 22% | 55%
Bath | MORGAN | 1.7 | 1.5 | 7% | 47% | 47%
Morgan County* | MORGAN | 35.7 | 22.0 | 13% | 17% | 70%
Paw Paw | MORGAN | 0.7 | 0.1 | 0% | 0% | 100%
 | MORGAN | 38.1 | 23.6 | 13% | 19% | 69%
1%-annual-chance (100-yr) flood event
I-81 Middle Creek
US 522 Warm Spring Run

## Slide 120
Population in Floodplains
County Unincorporated | WV RPDC Region | % of Population Residing in High- Risk Flood Zone
Boone County* | 3 | 42%
Logan County* | 2 | 37%
McDowell County* | 1 | 34%
Lincoln County* | 2 | 33%
Mingo County*` | 2 | 31%
Tyler County* | 5 | 29%
Wetzel County* | 10 | 29%
Doddridge County* | 6 | 28%
Webster County* | 4 | 28%
Clay County* | 3 | 28%
Wyoming County* | 1 | 25%
Pendleton County* | 8 | 23%
Kanawha County* | 3 | 23%
Wirt County* | 5 | 21%
Tucker County* | 7 | 20%
Summers County* | 1 | 18%
Wayne County* | 2 | 17%
Ritchie County* | 5 | 17%
Pocahontas County* | 4 | 16%
Calhoun County* | 5 | 16%
Community Name | County | % of Population Residing in High-Risk Flood Zone
Keystone | MCDOWELL | 100%
Northfork | MCDOWELL | 100%
Rhodell | RALEIGH | 100%
Henderson | MASON | 100%
Friendly | TYLER | 100%
Anawalt | MCDOWELL | 87%
Kimball | MCDOWELL | 86%
Sylvester | BOONE | 86%
Gary | MCDOWELL | 77%
Nitro** | KANAWHA & PUTNAM | 70%
Hartford | MASON | 66%
Marlinton | POCAHONTAS | 65%
Valley Grove | OHIO | 64%
Bruceton Mills | PRESTON | 60%
Smithfield | WETZEL | 60%
Harman | RANDOLPH | 58%
Wellsburg | BROOKE | 56%
Clendenin | KANAWHA | 56%
Buffalo | PUTNAM | 54%
Kermit | MINGO | 52%
** Split Community
12% of West Virginia’s total population live in the high-risk flood zones
Unincorporated Areas
Incorporated Places
Data Source

## Slide 121
Short-Term Shelter Needs
Incorporated Areas
Unincorporated Areas
Generated using FEMA’s Hazus flood loss guidelines for a 1%-annual-chance (100-yr) flood event
PDF Map
PDF Map

## Slide 122
Population Change
Municipality | Population Growth Rate
Rainelle | -20.9%
White Sulphur Springs | -9.1%
Clendenin | -30.4%
Richwood | -19.1%
Camden-on-Gauley | -25.4%
These disadvantaged communities had a negative population growth rate between the 2010 and 2020 censuses. FEMA's report Community Resilience Indicator Analysis: County-Level Analysis of Commonly Used Indicators from Peer-Reviewed Research uses population change as a risk factor. A reduction in population reduces local tax income and community resources to respond to a disaster.
Data Source
Community Map
County Map

## Slide 123
State Risk Assessment
DATA FIELD VERIFICATION of MITIGATED PROPERTIES
COMMUNITY ENGAGMENT
IDENTIFY MITIGATED ACTIONS FOR HAZARD MITIGATION PLANS
What mitigation actions can be identified

## Slide 124
Field Verification
781 Avon Bend Road, Charles Town, WV 25414 Parcel ID: 19-06-009H-0019-0000 Building ID: 19-06-009H-0019-0000_781 WV Flood Tool Link: https://mapwv.gov/flood/map/?wkid=102100&x=-8664165&y=4753090&l=13&v=1
Modified Foundation Type and First Floor Height – Rerun Hazus Flood Loos Model
COMMUNITY ENGAGEMENT
Risk Assessment Data Verification
Mitigation Actions Identified
4

## Slide 125
Field Verification
Field Verification of the structure located at 781 Avon Bend Road in Charles Town along the Shenandoah River in the Regulatory Floodway reveals that this Post-FIRM (2011) structure is built on a piles foundation. The Foundation Type/First Floor Height will be changed in the Building Inventory and the OpenHazus Flood Assessment Structure Tool (FAST) utility executed again for this structure.
The estimated Base Flood Water Depth for this structure is 10 feet.
781 Avon Bend Road, Charles Town, WV 25414 Building ID 19-06-009H-0019-0000_781
WV Flood Tool Link: https://mapwv.gov/flood/map/?wkid=102100&x=-8664165&y=4753090&l=13&v=1
Field Verified from Shenandoah River
Field Verification is important to improve the accuracy of certain properties!

## Slide 126
Buckhannon, WV
Mitigated Properties - Verification
https://mapwv.gov/flood/map/?wkid=102100&x=-8929946&y=4721378&l=10&v=2
Verify BUYOUT PROPERTY Parcel
Verify MITIGATED STRUCTURE
Elevation Certificate
of Elevated Structure (Bldg. Diagrams 5-8)

## Slide 127
Buyout Properties
PDF Map

## Slide 128
Mitigated Structure – EC Bldg. #6
Building Diagram 6: Elevated Building with Enclosure (using piers, piles, posts)
Partial Enclosure

## Slide 129
Mitigated Structure – First Floor Height
Use Elevation Certificates and Building Pictures to identify Residential Elevated Structures > 5 ft.
16 blocks x 8” = 11 ft.
Elevation Certificate (Diagram 7)
631.0 ft. (C2b) – 619.0 ft. (C2f) = 12 ft.
19 steps x 7” rise = 11 ft.
Newly built Elevated Structure not shown on aerial imagery
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9056061&y=4648497&l=12&v=1
Building Picture
Base Flood Depth
is 6.7 ft.

## Slide 130
Example Mitigated Structure
Elevated Building on Solid Foundation Walls (Full-Story)
Walkout Opening
Full-Story Enclosure
Building 08-06-0006-0058-0001 on the Elk River in Clay County

## Slide 131
Potential Structures for Mitigation
Source Graphic

## Slide 132
Potential Structures for Wet Floodproofing
Source Graphic

## Slide 133
Areas of Mitigation Interests / Repetitive Loss Areas
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8669471&y=4802931&l=9&v=2
Repetitive Loss Areas
Substantial Damage Estimates
High-Water Marks
Buyout Properties

## Slide 134
Areas of Mitigation (AoMI) Interest
PDF Map
In progress

## Slide 135
Areas of Mitigation (AoMI) Interest
PDF Map
PDF Map

## Slide 136
Repetitive Loss Structures
PDF Map
PDF Map

## Slide 137
Local Community Engagement
COMMUNITY ENGAGMENT & VERIFICATION
+
Floodplain Building Risk Inventory
Essential Facilities & Community Assets
Mitigated Structures
Buyout Properties
Areas of Mitigation Interest
Other Mitigation Activities
Local Hazard Mitigation Plan
Primary Objective: Incorporating Mitigation Actions in Local Hazard Mitigation Planning
Risk Assessment Data for Community Engagement, Verification, and Identifiable Mitigation Actions incorporated into Local Hazard Plans

## Slide 138
Community Engagement Focus 1-2
 |  |  | Tables |  | Map | Report | 
Primary Focus Areas of Statewide Risk Assessment | Community Engagement | Specific Activities for Mitigation Plan | Com- munity Level (CL) | Bldg. (BL) or Feature (FL) Level | Flood Tool Risk MAP | Report | Include Answers to Questions below in Hazard Mitigation Plan
Floodplain Building Risk Inventory | Incorporate 1% Annual Chance Floodplain Building Risk Assessment Inventory into Mitigation and NFIP/CRS Management Activities | For pre-disaster planning and emergency preparedness, preload floodplain structures into FEMA’s Substantial Damage Estimator Tool |  | Yes |  |  | For each community, quantify the number and type of buildings structures at risk for a 1%-annual-chance flood event to include the degree of flood risk?
 |  | Local outreach to property owners about SFHA changes from new flood studies |  | Yes |  |  | 
 |  | Include Community-Level Flood Risk Assessment Profile of Built Environment into Hazard Mitigation Plan | Yes | Yes | Yes | Yes | 
Essential Facilities & Community Assets | Identify Mitigation Actions for Essential Facilities and Community Assets | Confirm essential facilities inventoried in high and moderate risk floodplains | Yes | Yes | Yes |  | Which essential facilities and community assets are most vulnerable to flooding? Which facilities can be mitigated?
 |  | For mitigation plan, identify a minimum of two (2) mitigation actions for essential facilities and community assets for each county | Yes | Yes | Yes | Yes | 
 |  | Incorporate essential facility and community assessment risk assessment tables in hazard mitigation plan |  |  |  |  | 
Local Community Engagement
Hazard Mitigation Plan Engagement

## Slide 139
Floodplain Building Risk Assessment
Incorporate Riverine 1% Annual Chance Floodplain Building Inventory into Mitigation and NFIP/CRS Management Activities
Include Community-Level Flood Risk Assessment Profile of Built Environment into Hazard Mitigation Plan: Incorporate into hazard mitigation plan community-level floodplain building counts, SFHA future map building conditions, building dollar exposure, building type (Residential/Non-Residential Occupancy Type, Building Year Pre/Post-FIRM), and building damage estimates (Minus Rated Structures, 1% Damage Loss Flood Models)
Preload Flood Risk Structures into FEMA’s Substantial Damage Estimator Tool: Upload building inventory data into SDE. The entire statewide flood risk inventory of 98,000 1% floodplain structures can be preloaded into FEMA’s SDE Tool.
  SDE Assessments: Install FEMA’s Substantial Damage Estimator Tool version 3.0. Preload 1% floodplain countywide residential/non-residential structures into FEMA’s damage estimator software. Communities are eligible for CRS credit for preloaded structures in SDE. https://www.fema.gov/emergency-managers/risk-management/building-science/substantial-damage-estimator-tool
  As part of pre-disaster planning and emergency readiness, each county should perform a residential and non-residential substantial damage assessment for potential high damage loss structures. Submit damage estimates and feedback for mitigation plan and maintenance.
  Flood Map Restudy (if applicable). Prepare community outreach communications for flood restudies (mapped into SFHA, mapped out of SFHA). Restudied areas require updating floodplain management ordinance and an opportunity to review state model ordinance and incorporate higher standards.

## Slide 140
Preload Structures into SDE
STEP 2: Community performs practice Substantial Damage Assessments for Residential and Non-Residential Properties
STEP 1: Community preloads Floodplain Properties into FEMA’s Substantial Damage Estimator software
Greenbrier County has 2,225 Structures that can be uploaded
SDE Upload Files and Instructions
Incorporate 1% Floodplain Building Risk Assessment Inventory into Mitigation and NFIP/CRS Management Activities

## Slide 141
Flood Study Map Changes
FEMA Region 3 Toolkit for New Flood Studies
Mail Merge Template for SFHA Mapped-in Structures
White Sulphur Springs has 68 buildings being mapped into the SFHA
Incorporate 1% Floodplain Building Risk Assessment Inventory into Mitigation and NFIP/CRS Management Activities

## Slide 142
Essential Facilities & Community Assets
Identify Mitigation Actions for Essential Facilities and Community Assets
For mitigation plan, incorporate a minimum of two (2) identifiable mitigation actions for essential facilities and community assets for each county.
Compare existing essential facilities inventoried to previous plan update and denote any mitigation progress.
Review top statewide building listing of high-value dollar essential facilities/community assets exposure and substantial damage.
Identify socio-economic effects if key facilities are not restored to original function within days after flood event.
Review existing emergency action plans.
Incorporate into CRS Activity 510 Floodplain Management Planning (FMP)

## Slide 143
Community Engagement Focus 3-5
Local Community Engagement
Hazard Mitigation Plan Engagement
 |  |  | Tables |  | Map | 
Primary Focus Areas of Statewide Risk Assessment | Community Engagement | Specific Activities for Mitigation Plan | Com- munity Level (CL) | Bldg. (BL) or Feature (FL) Level | Flood Tool Risk MAP | Include Answers to Questions below in Hazard Mitigation Plan
Mitigated Structures | Validate Mitigated Structures and Post-FIRM Development | Determine if Post-FIRM minus-rated structures are mitigated | Yes | Yes | Yes | Which Post-FIRM structures in the 1% floodplain have been mitigated?
 |  | In the mitigation plan, include a table that describes the number and types of mitigated structures for each flood prone community | Ongoing | Yes | Yes | 
Buyout Properties | Confirm Mitigated Buyout Properties | Confirm buyout properties are allowable for open space purposes only | Yes | Yes | Yes | How many mitigated buyout properties in each community exist?
 |  | In the mitigation plan, include a table that lists the number of verified and unverified mitigated buyout properties | Yes | Yes | Yes | 
Areas of Mitigation Interest | Evaluate Areas of Mitigation Interest or Repetitive Loss Areas | Determine the mitigation status of Post-FIRM building construction, repetitive loss structures, substantial damage estimates, and buyout properties for designated Areas of Mitigation Interest. |  | Yes |  | What are the Areas of Mitigation Interest or Repetitive Loss Areas identified for mitigation?
 |  | In the mitigation plan, include a table that lists and describes the areas of mitigation interest for each community | Ongoing | Yes |  | 

## Slide 144
Mitigated Structures
Validate Mitigated Structures and Post-FIRM Development
Mitigation Plan Cross Walk Requirements: For mitigation plan, verify Post-FIRM mitigated structures provided in minus-rated property tables.
Determine if Post-FIRM minus-rated structures are mitigated. Focus initially on structures with the highest minus ratings (or highest water-in-depth values) and high dollar loss estimates. For each structure of interest identify if a permit and elevation certificate are on file. Annotate permit and elevation certificate information on minus-rated table. Submit building pictures if no elevation certificates exist.
In the mitigation plan, include a table that describes the number and types of mitigated structures for each flood prone community.
Identify mitigation actions for specific structures, to include outreach/education to community/ homeowners about mitigation best practices, mitigation funding opportunities, NFIP office involvement for non-compliant structures).

## Slide 145
Buyout Properties
Confirm Mitigated Buyout Properties
Mitigation Plan Cross Walk Requirements: For mitigation plan, validate verified and unverified properties.
Confirm buyout properties are allowable for open space purposes only. Every three years communities are required to inspect and certify that buyout properties are uses only for allowable open space purposes. Source: https://www.fema.gov/sites/default/files/2020-07/fy15_hma_addendum.pdf
  Verify all deed-restricted buyout properties are shown on the WV Flood Tool.
  Unverified properties (possible buyout properties) are compiled from the statewide property tax database where the parcel intersects the high-risk 1% floodplain, maximum building value is $1000, and part of the owner name contains “commission” or “council” or “city” or “town.”
In the mitigation plan, include a table that lists the number of verified and unverified mitigated buyout properties.
List a minimum of two properties for each county that should be considered for buyout mitigation. Discuss potential properties in mitigation plan.

## Slide 146
Areas of Mitigation (AoMI) Interest
Areas of Mitigation (AoMI) are identified by Repetitive Loss structures, Substantial Damage Model Estimates, Mitigated Properties, Flood Depths, High-Water Marks, and Similar Topography. Graphics of reference data for AoMI determinations:
Areas of Mitigation Interest (AoMI)
Repetitive Loss Structures
Buyout Properties
High Flood Depths or Water Depths-in-Structure
High-Water Marks
Building Damage $ Non-Residential |Building Damage $ Residential
Substantial Damage Estimates

## Slide 147
Community Rating System
8.5x11 PDF Graphic
11x17 PDF Graphic