## Slide 1
Region 9 Flood Risk Assessment
Morgan County Vulnerability Risk Assessment
Kurt Donaldson, WVU
8/24/2021

## Slide 2
Primary Flood Sources (Morgan)
Flood Source | Building Count | Dollar Exposure ($)
MORGAN COUNTY |  | 
Cacapon River | 199 | $15,546K
Warm Spring Run | 185 | $69,686K
Potomac River | 64 | $4,663K
Computed for 1% (100-yr) floodplain
Region 9 PDF Map Link

## Slide 3
Active Flood Studies
Flood Study Project Status Map PDF
Yellow Spring Run (Morgan)
Evans Run (Berkeley)

## Slide 4
Floodplain Measurements
Community Name | County | Stream Length(mi) -Zones: AE,AH,AO | Stream Length (mi) -Effective A | Stream Length (mi) – Advisory A | Total Length (mi) | Detailed Zone % | Approx. A Zone % | Advisory Zone %
BERKELEY COUNTY * | BERKELEY COUNTY | 67.9 | 90.2 | 55.6 | 213.7 | 32% | 42% | 26%
MARTINSBURG | BERKELEY COUNTY | 4.1 | 0.5 | 0.5 | 5.1 | 81% | 10% | 9%
 | BERKELEY COUNTY | 72.1 | 90.7 | 56.0 | 218.8 | 33% | 41% | 26%
BATH | MORGAN COUNTY | 1.4 | 0.0 | 0.0 | 1.4 | 97% | 1% | 1%
MORGAN COUNTY* | MORGAN COUNTY | 36.3 | 121.4 | 14.8 | 172.5 | 21% | 70% | 9%
PAW PAW, TOWN OF | MORGAN COUNTY | 0.2 | 0.7 | 0.0 | 0.9 | 23% | 77% | 0%
 | MORGAN COUNTY | 37.8 | 122.1 | 14.8 | 174.8 | 22% | 70% | 8%
Community Name | County | Total Community Area (acres) | Total SFHA Area (acres) | Modified Total SFHA Area (acres)1 | Ratio of aSFHA to Community Area
BERKELEY COUNTY * | BERKELEY COUNTY | 201,588 | 8,837 | 8,820 | 4.4%
MARTINSBURG | BERKELEY COUNTY | 4,259 | 139 | 128 | 3.0%
HEDGESVILLE, TOWN OF | BERKELEY COUNTY | 85 | 0 | 0 | 0.0%
MORGAN COUNTY* | MORGAN COUNTY | 146,585 | 7,231 | 7,210 | 4.9%
BATH | MORGAN COUNTY | 215 | 20 | 20 | 9.3%
PAW PAW | MORGAN COUNTY | 340 | 119 | 119 | 35.0%
1 Areas excluded from Total aSFHA: Open water lakes > 10 acres; Large river bank-to-bank > 500 ft.; Federal lands > 10 acres |  |  |  |  | 
Floodplain Area (acres)
Floodplain Length (miles)

## Slide 5
Building Counts by Flood Zone
Community Name | County |  | SFHA - FUTURE MAP CONDITIONS |  |  |  |  | HIGH-RISK FLOOD ZONES |  | 
 |  |  | Floodway | No Change SFHA | Mapped in SFHA | Mapped Out SFHA |  | Effective | Advisory | Total
Berkeley County* | BERKELEY |  | 6 | 325 | 88 | 216 |  | 547 | 88 | 635
Martinsburg | BERKELEY |  | 7 | 39 | 8 | 21 |  | 67 | 8 | 75
 | BERKELEY |  | 13 | 364 | 96 | 237 |  | 614 | 96 | 710
Bolivar | JEFFERSON |  | 0 | 0 | 3 | 0 |  | 0 | 3 | 3
Charles Town | JEFFERSON |  | 5 | 12 | 1 | 9 |  | 26 | 1 | 27
Harpers Ferry | JEFFERSON |  | 0 | 1 | 30 | 0 |  | 1 | 30 | 31
Jefferson County* | JEFFERSON |  | 37 | 233 | 39 | 217 |  | 487 | 39 | 526
Ranson | JEFFERSON |  | 3 | 49 | 0 | 28 |  | 80 | 0 | 80
Shepherdstown | JEFFERSON |  | 0 | 62 | 1 | 3 |  | 65 | 1 | 66
 | JEFFERSON |  | 45 | 357 | 74 | 257 |  | 659 | 74 | 733
Bath | MORGAN |  | 56 | 34 | 16 | 23 |  | 113 | 16 | 129
Morgan County* | MORGAN |  | 102 | 209 | 38 | 135 |  | 446 | 38 | 484
Paw Paw | MORGAN |  | 0 | 13 | 0 | 17 |  | 30 | 0 | 30
 | MORGAN |  | 158 | 256 | 54 | 175 |  | 589 | 54 | 643

## Slide 6
Buildings Inventories
High-Risk Effective & Advisory
1%-Annual-Chance (100-Yr) Floodplains

## Slide 7
Future Building Map Conditions
SFHA AND FUTURE MAP CONDITIONS | Select counties have non-regulatory, advisory flood zones (orange zones on WV Flood Tool) that indicate future map conditions of the Special Flood Hazard Area (SFHA).
Floodway | Floodways cans be dangerous because water may flow very fast. Development is not allowed unless there is "no rise" in flood elevations, floodway elevations, and floodway widths are certified. Structures in floodways may require special consideration for mitigation measures.
No Change SFHA | No Change in SFHA designation where High-Risk Effective and Advisory Floodplains overlap. When future map restudies are completed and new FIRMs become effective, it is predicted that structures with this designation are neither "mapped in" nor "mapped out" of the SFHA.
Mapped In SFHA | Structures potentially "mapped-in" the SFHA according to mapped High-Risk Advisory Floodplains based on more accurate topography and model-backed A Zones. The "mapped-in" structures most likely will be included in the SFHA when future FEMA Restudies are done and new FIRMS become effective. Communities should review all "mapped-in" structures. Homeowners are at higher risk to flooding and should be contacted about Flood Insurance Preferred Risk Policies and other potential mitigation measures.
Mapped Out SFHA | Structures potentially "mapped-out" the SFHA according to mapped Advisory Floodplains and most likely will NOT be included in the SFHA when the new FIRMs become effective from future Restudies. Communities should review all "mapped-out" structures for LiDAR LOMAs. Although these structures may be mapped to a lesser flood risk designation, property owners should be encouraged to purchase Flood Insurance Preferred Risk Policies at lower premiums. Morgan County example ¦ Berkeley County example

## Slide 8
Primary Structures (Bath)
Martinsburg’s primary structures viewable on the Risk MAP View of the WV Flood Tool. Symbol letters indicate general occupancy (Residential, Commercial, Other Non-Residential).

## Slide 9
Essential Facilities (Morgan County)
Community Name | County | Facility Name | Facility Type | Flood Tool Link | Flood Depth | Building Damage Percent
Morgan County* | MORGAN | Berkeley Springs High School | School | FT | 1.4 | 1.9
Morgan County* | MORGAN | WV State Police Troop 2 | Police Department | FT | 0.2 | 0
Bath | MORGAN | Berkeley Springs Volunteer Fire Department | Fire Department | FT | 0 | 0
Bath | MORGAN | Morgan County 911 Center | 911 Center | FT | 0 | 0
Community Engagement and Verification: Review the accuracy and completeness of all active essential facilities. Report any facilities that are missing. Verify the facilities and location using the Table and RiskMAP View of the WV Flood Tool.

## Slide 10
Community Assets
Community Name | County | Historical Place | Facility Type | Flood Tool Link | Flood Depth | Building Damage Percent
Berkeley County* | BERKELEY | Little Falls Chapel | Religious | FT | 6.4 | 11%
Martinsburg | BERKELEY | Holy Grace Church of God | Religious | FT | 3.4 | 11%
Martinsburg | BERKELEY | Martinsburg Sewage Treatment Plant | Utilities | FT | 4.8 | 9%
Bath | MORGAN | Morgan County Courthouse | Government | FT | 2.6 | 7%
Bath | MORGAN | Morgan County Public Library | Government | FT | 2.9 | 7%
Community Engagement and Verification: Review the accuracy and completeness of all active community assets. Report any structures that are missing. Verify the buildings and location using the Table and Risk MAP View of the WV Flood Tool. Review and identify mitigation strategies for the community assets vulnerable to flooding.

## Slide 11
Historical Community Assets
Community Name | County | Facility Name | Facility Type | Flood Tool Link | Flood Depth | Building Damage Percent
Berkeley County* | BERKELEY | Darkesville Historic District | National Register | FT | 5.2 | 22%
Berkeley County* | BERKELEY | Darkesville Historic District | National Register | FT | 4.7 | 13%
Martinsburg | BERKELEY | Tuscarora Creek Historic District | National Register | FT | 2.5 | 11%
Martinsburg | BERKELEY | Tuscarora Creek Historic District | National Register | FT | 2.1 | 14%
Berkeley County* | BERKELEY | Darkesville Historic District | National Register | FT | 2.1 | 8%
Berkeley County* | BERKELEY | Mill Creek Historic District | National Register | FT | 1.1 | 4%
Town Name | County | Building ID | Historical Name | Facility Type | Flood Tool Link | Flood Depth | Building Damage Percent
Bath | MORGAN | 33-03-001A-0015-0000_129 | Town of Bath Historic District | National Register | FT | 8.3 | 27%
Bath | MORGAN | 33-03-002A-0040-0000_33 | Town of Bath Historic District | National Register | FT | 7.8 | 40%
Bath | MORGAN | 33-03-002A-0041-0000_33A | Town of Bath Historic District | National Register | FT | 6.6 | 37%
The town of Bath (Berkeley Springs) in Morgan County is ranked 10th in the State for an incorporated area with the most historical buildings (47). For the most National Register Areas in the State that intersect the 1% floodplain, Morgan County ranks second (20 NR Areas) and Morgan County (2) nineteenth.
Mitigation: A designated historic structure can obtain the benefit of subsidized flood insurance through the NFIP even if it has been substantially improved or substantially damaged so long as the building maintains its historic designation.

## Slide 12
Residential versus Non-Residential
* Unincorporated 1 Group Rank on Community Type: County, Unincorporated, Incorporated Region 9 Tabular Community-Level Report: https://data.wvgis.wvu.edu/pub/RA/State/CL/ (Building Exposure)
Community | RESIDENTIAL |  |  |  | COMMERCIAL NON-RESIDENTIAL |  | OTHER NON-RESIDENTIAL |  | TOTAL BUILDING VALUE |  | 
Community Name | # | % Count | Value ($) | % Value | # | Value ($) | # | Value ($) | # | Value ($) | Rank1
Berkeley County* | 619 | 97% | $50,593K | 96% | 12 | $1,965K | 4 | $373K | 635 | $52,931K | 3
Martinsburg | 51 | 68% | $6,124K | 10% | 21 | $55,166K | 3 | $1,035K | 75 | $62,324K | 1
BERKELEY | 670 | 94% | $56,717K | 49% | 33 | $57,131K | 7 | $1,408K | 710 | $115,255K | 1
Bolivar | 3 | 100% | $251K | 100% | 0 | $0K | 0 | $0K | 3 | $251K | 8
Charles Town | 23 | 85% | $2,073K | 65% | 4 | $1,107K | 0 | $0K | 27 | $3,180K | 6
Harpers Ferry | 6 | 19% | $722K | 10% | 25 | $6,243K | 0 | $0K | 31 | $6,965K | 4
Jefferson County* | 505 | 96% | $60,022K | 85% | 14 | $4,889K | 7 | $5,349K | 526 | $70,260K | 1
Ranson | 79 | 99% | $5,206K | 98% | 0 | $0K | 1 | $100K | 80 | $5,305K | 5
Shepherdstown | 38 | 58% | $7,873K | 42% | 24 | $6,057K | 4 | $4,794K | 66 | $18,724K | 3
JEFFERSON | 654 | 89% | $76,146K | 73% | 67 | $18,295K | 12 | $10,243K | 733 | $104,685K | 3
Bath | 64 | 50% | $7,226K | 21% | 52 | $11,499K | 13 | $16,499K | 129 | $35,224K | 2
Morgan County* | 439 | 91% | $35,347K | 51% | 38 | $11,135K | 7 | $23,386K | 484 | $69,867K | 2
Paw Paw | 16 | 53% | $1,133K | 41% | 13 | $1,507K | 1 | $130K | 30 | $2,770K | 7
MORGAN | 519 | 81% | $43,705K | 41% | 103 | $24,141K | 21 | $40,015K | 643 | $107,862K | 2
SUMMARY | 1843 | 3 | $176,569K | 54% | 203 | $99,567K | 40 | $51,666K | 2086 | $327,802K | 

## Slide 13
Single Family Dwellings
* Unincorporated 1 Group Rank on Community Type: County, Unincorporated, Incorporated Region 9 Tabular Community-Level Report: https://data.wvgis.wvu.edu/pub/RA/State/CL/ (Building Exposure)
Community |  | SINGLE FAMILY HOME |  | MANUFACTURED (MOBILE) HOME |  |  | SINGLE FAMILY TOTAL |  | 
Community Name | County | Count | Value ($) | Count | % Count | Value ($) | Count | Value ($) | Group Rank1
Berkeley County* | BERKELEY | 404 | $45,448K | 206 | 34% | $3,947K | 610 | $49,396K | 2
Martinsburg | BERKELEY | 41 | $4,507K | 0 | 0% | $0K | 41 | $4,507K | 4
 | BERKELEY | 445 | $49,956K | 206 | 32% | $3,947K | 651 | $53,903K | 2
Bolivar | JEFFERSON | 3 | $251K | 0 | 0% | $0K | 3 | $251K | 8
Charles Town | JEFFERSON | 21 | $1,991K | 0 | 0% | $0K | 21 | $1,991K | 5
Harpers Ferry | JEFFERSON | 6 | $722K | 0 | 0% | $0K | 6 | $722K | 7
Jefferson County* | JEFFERSON | 421 | $56,946K | 77 | 15% | $2,311K | 498 | $59,257K | 1
Ranson | JEFFERSON | 65 | $4,494K | 10 | 13% | $351K | 75 | $4,845K | 3
Shepherdstown | JEFFERSON | 35 | $7,191K | 0 | 0% | $0K | 35 | $7,191K | 1
 | JEFFERSON | 551 | $71,595K | 87 | 14% | $2,663K | 638 | $74,257K | 1
Bath | MORGAN | 52 | $5,542K | 3 | 5% | $53K | 55 | $5,595K | 2
Morgan County* | MORGAN | 367 | $33,782K | 66 | 15% | $1,211K | 433 | $34,993K | 3
Paw Paw | MORGAN | 12 | $806K | 0 | 0% | $0K | 12 | $806K | 6
 | MORGAN | 431 | $40,130K | 69 | 14% | $1,265K | 500 | $41,394K | 3
SUMMARY |  | 1,427 | $161,680K | 362 | 20% | $7,875K | 1,789 | $169,555K | 

## Slide 14
Highly Valued ($) Buildings
* Unincorporated Region 9 Tabular Building-Level Report Link: https://data.wvgis.wvu.edu/pub/RA/Region9/BLRA/4_BldgDollarExposure
Highly valued buildings in 1% Floodplain for Morgan County. Which high-valued-structures are vulnerable to riverine flooding?
Community Engagement and Verification:
Building-Level Verification: Verify the highly valued buildings using the building-level table and Risk MAP View of the WV Flood Tool. For buildings inventoried in the 1% floodplains, review the most expensive residential and non-residential buildings located in the high-risk flood zones sorted on building appraisal value from largest to smallest value. Identify building-level mitigation and outreach strategies.
Community Name | WV Flood Tool Link | Owner Name or Building ID | Hazard Occupancy Code | General Occupancy | Building Appraisal
Morgan County* | FT | BOARD OF EDUCATION | EDU1 | Other | $ 15,000,000
Bath | FT | MORGAN CO BLDG COMM | GOV1 | Other | $ 10,591,500
Morgan County* | FT | BOARD OF EDUCATION | EDU1 | Other | $ 6,210,000
Morgan County* | FT | U S SILICA | IND4 | Commercial | $ 3,304,600
Morgan County* | FT | BOARD OF EDUCATION | EDU1 | Other | $ 1,650,000
Bath | FT | CATHOLIC CHURCH | REL1 | Other | $ 1,565,700
Bath | FT | MORGAN ARTS COUNCIL INC | COM8 | Commercial | $ 1,482,300
Bath | FT | CITIZENS NATIONAL BANK OF BERKELEY SPRINGS | COM5 | Commercial | $ 1,448,900

## Slide 15
Risk Assessment – Building $ & Type
Morgan County ranks second in the State for its countywide median building replacement value of $79,000 and much higher than the statewide median building replacement value of $37,000. It ranks fourth for median single-family dwelling replacement value of $88,000 and above the statewide median value of $44,000.
Morgan County – 81% of the primary buildings are residential whereas 59% of the countywide building stock dollar value is non-residential.
Morgan County – Manufactured homes comprise 14% of the single family dwelling building stock.
Morgan County ranks 11th in the State for the highest percentage of Post-FIRM structures or new development.
The town of Bath (Berkeley Springs) in Morgan County is ranked 10th in the State for an incorporated area with the most historical buildings (47).

## Slide 16
Substantial Damage Estimates
Community Name | County | Count Total | Value Total | TEIF Loss Total | TEIF Loss Ratio Total | Median Percent Damage | Median Dollar Damage | Debris Damage Total | High Damage Count (BldgDmgPct >= 50% OR BldgLossUSD > $10k)
Berkeley County* | BERKELEY | 635 | $52,931K | $5,729K | 11% | 65% | $15K | 6,172 | 188
Martinsburg | BERKELEY | 75 | $62,324K | $14,105K | 23% | 9% | $4K | 136 | 8
 | BERKELEY | 710 | $115,255K | $19,834K | 17% | 54% | $13K | 6,308 | 196
Jefferson County* | JEFFERSON | 526 | $70,260K | $6,047K | 9% | 39% | $21K | 4,434 | 183
Bolivar | JEFFERSON | 3 | $251K | $118K | 47% | 48% | $37K | 135 | 3
Charles Town | JEFFERSON | 27 | $3,180K | $27K | 1% | 4% | $3K | 12 | 0
Harpers Ferry | JEFFERSON | 31 | $6,965K | $4,785K | 69% | 74% | $131K | 4,683 | 30
Ranson | JEFFERSON | 80 | $5,305K | $16K | 0.3% | 4% | $2K | 4 | 0
Shepherdstown | JEFFERSON | 66 | $18,724K | $1,058K | 6% | 8% | $14K | 427 | 38
 | JEFFERSON | 733 | $104,685K | $12,052K | 12% | 30% | $21K | 9,695 | 254
Morgan County* | MORGAN | 484 | $69,867K | $7,057K | 10% | 41% | $16K | 4,368 | 166
Bath | MORGAN | 129 | $35,224K | $2,621K | 7% | 10% | $11K | 698 | 44
Paw Paw | MORGAN | 30 | $2,770K | $16K | 1% | 6% | $3K | 19 | 0
 | MORGAN | 643 | $107,862K | $9,695K | 9% | 22% | $14K | 5,085 | 210
Generated using FEMA’s Hazus flood loss software program for a 1%-annual-chance (100-yr) flood event
Statewide 17% $6K

## Slide 17
RA Verification Tables
https://data.wvgis.wvu.edu/pub/RA/Region9/BLRA/4-6_BLRA_Extract

## Slide 18
Repetitive Loss Area (Morgan)
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8724660&y=4793095&l=8&v=2
Repetitive Loss Areas
Substantial Damage Estimates
Buyout Properties

## Slide 19
Repetitive Loss Areas
Area of Mitigation Interest | County | Community | Steam Name | RL_Area | FT
540144_Cacapon_1 | Morgan | Morgan Unincorporated | Cacapon River | Yes | FT
540144_Cacapon_2 | Morgan | Morgan Unincorporated | Cacapon River | Yes | FT
540144_Cacapon_3 | Morgan | Morgan Unincorporated | Cacapon River | Yes | FT
540144_Cacapon_4 | Morgan | Morgan Unincorporated | Cacapon River | Yes | FT
540144_WarmSpringRun_1 | Morgan | Morgan Unincorporated | Warm Spring Run | Yes | FT
540144_Cacapon_5 | Morgan | Morgan Unincorporated | Cacapon River | Yes | FT
540144_Cacapon_6 | Morgan | Morgan Unincorporated | Cacapon River | Yes | FT
540144_Potomac_1 | Morgan | Morgan Unincorporated | Potomac River | No | FT

## Slide 20
Permanent Structures
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8663702&y=4797889&l=11&v=2
Building ID: 02-08-0001-0030-0000_3458

## Slide 21
Recreational Vehicles
<< WV Quick Guide resource >>
https://emd.wv.gov/MitigationRecovery/Documents/Floodplain%20Management%20in%20WV%20Quick%20Guide.pdf

## Slide 22
Short-Term Shelter Needs
Incorporated Areas
Unincorporated Areas
Generated using FEMA’s Hazus flood loss guidelines for a 1%-annual-chance (100-yr) flood event

## Slide 23
Debris Removal
Incorporated Areas
Unincorporated Areas
Generated using FEMA’s Hazus flood loss software program for a 1%-annual-chance (100-yr) flood event

## Slide 24
Road Inundation Models
Community Name | County | Roads in Flood Plain (miles) | Roads Flooded (miles) | Roads Below 1ft (Ratio) | Roads 1 to 3ft (Ratio) | Roads Above 3ft (Ratio)
Berkeley County* | BERKELEY | 25.7 | 17.0 | 21% | 22% | 57%
Martinsburg | BERKELEY | 0.8 | 0.5 | 60% | 20% | 20%
 | BERKELEY | 26.5 | 17.5 | 22% | 22% | 55%
Bath | MORGAN | 1.7 | 1.5 | 7% | 47% | 47%
Morgan County* | MORGAN | 35.7 | 22.0 | 13% | 17% | 70%
Paw Paw | MORGAN | 0.7 | 0.1 | 0% | 0% | 100%
 | MORGAN | 38.1 | 23.6 | 13% | 19% | 69%
1%-annual-chance (100-yr) flood event
I-81 Middle Creek
US 522 Warm Spring Run

## Slide 25
High Hazard Potential Dams
County | Total Count | High Hazard | Significant Hazard | Low Hazard | Undetermined Hazard
BERKELEY COUNTY | 11 | 3 | 3 | 0 | 5
JEFFERSON COUNTY | 6 | 0 | 1 | 2 | 3
MORGAN COUNTY | 24 | 12 | 3 | 1 | 8
Source: National Inventory of Dams 2020 Database
Community-Level Risk Assessment Tables: https://data.wvgis.wvu.edu/pub/RA/State/CL/

## Slide 26
Downstream Communities
DAM NAME | DAM HEIGHT (Feet) | MAX. STORAGE (Acre-Feet) | HAZARD CLASS | EAP | LINK | DAM JURISDICTION | IN-BETWEEN JURISDICTIONS | FARTHEST1 IMPACTED JURISDICTION
JENNINGS RANDOLPH DAM | 296 | 130,900 | High | Y | FT | Mineral | Mineral, Piedmont, Keyser, Carpendale, Ridgeley, Hampshire, Morgan, Paw Paw, Berkley, Jefferson, Shepherdstown | Harpers Ferry
SAVAGE RIVER DAM | 184 | 31,800 | High | Y | FT | Garrett | Mineral, Piedmont, Keyser, (?) | (?)
LAKE HOLIDAY DAM | 129 | 1,260 | High | Y | FT | Frederick | (?) | (?)
SLEEPY CREEK DAM | 38 | 4,890 | High | Y | FT | Berkeley | Morgan | (?)
GRASSHOPPER HOLLOW TAILINGS DAM | 129 | 1,260 | High | Y | FT | Morgan | Berkeley Springs | (?)
Community Engagement and Verification: Refer to the WV Flood Tool map and tables to evaluate high-hazard potential dams in which failure is expected to result in loss of life. Review the Emergency Action Plans (EAP) and dam failure inundation maps of all high hazard dams and identify the farthest downstream community impacted.

## Slide 27
Warm Spring Run Dams (Morgan)
Map Link: https://www.mapwv.gov/flood/map/?wkid=102100&x=-8708803&y=4809463&l=7&v=2
Eight high hazard flood-control dams upstream of Berkeley Springs

## Slide 28
Landslide Susceptibility
COMMUNITY IDENTIFICATION |  | LANDSLIDE SUSCEPTIBILITY |  |  |  |  |  |  |  |  | TOTALS Med-High | 
 |  | High Susceptibility |  |  | Medium Susceptibility |  |  | Low Susceptibility |  |  | Bldg. Count | Bldg. Value
Community Name | County | Total - H Count | Total-H Value | Total-H Percent | Total - M Count | Total-M Value | Total-M Percent | Total - L Count | Total-L Value | Total-L Percent | Total Count | Total Value
Berkeley County* | BERKELEY | 6 | $1,277K | 0.01% | 490 | $53,165K | 1.0% | 48086 | $6,630,364K | 99% | 496 | $54,442K
Hedgesville | BERKELEY | 0 | $0K | 0.00% | 2 | $114K | 1.1% | 177 | $15,352K | 99% | 2 | $114K
Martinsburg | BERKELEY | 1 | $111K | 0.01% | 17 | $2,694K | 0.2% | 9273 | $1,073,817K | 100% | 18 | $2,805K
 | BERKELEY | 7 | $1,388K | 0.01% | 509 | $55,973K | 0.9% | 57536 | $7,719,533K | 99% | 516 | $57,361K
Bath | MORGAN | 0 | $0K | 0.00% | 19 | $1,733K | 3.5% | 523 | $65,979K | 96% | 19 | $1,733K
Morgan County* | MORGAN | 9 | $503K | 0.07% | 328 | $29,704K | 2.6% | 12073 | $1,136,331K | 97% | 337 | $30,207K
Paw Paw | MORGAN | 0 | $0K | 0.00% | 0 | $0K | 0.0% | 345 | $16,166K | 100% | 0 | $0K
 | MORGAN | 9 | $503K | 0.07% | 347 | $31,437K | 2.6% | 12941 | $1,218,475K | 97% | 356 | $31,940K

## Slide 29
Landslide Risk
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8704711&y=4796138&l=4&v=2

## Slide 30
Risk Assessment Verification
Field Verification
Community Engagement

## Slide 31
Building Substantial Damaged
ADDENDUM INFORMATION
16 steps x 7” rise = 9 ft.
Large number of substantial damaged structures along Greenbrier River, Summers County
Substantial Damage of structure not adjusted for 9 ft. elevated First Floor
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8990248&y=4525455&l=11&v=2
Foundation and First Floor Height from Assessment Record are not correct. Needs to be modified.

## Slide 32
Buckhannon, WV
Mitigated Properties - Verification
https://mapwv.gov/flood/map/?wkid=102100&x=-8929946&y=4721378&l=10&v=2
Verify BUYOUT PROPERTY Parcel
Verify MITIGATED STRUCTURE
Elevation Certificate
of Elevated Structure (Bldg. Diagrams 5-8)

## Slide 33
Mitigated Structure – First Floor Height
Use Elevation Certificates and Building Pictures to identify Residential Elevated Structures > 5 ft.
16 blocks x 8” = 11 ft.
Elevation Certificate (Diagram 7)
631.0 ft. (C2b) – 619.0 ft. (C2f) = 12 ft.
19 steps x 7” rise = 11 ft.
Newly built Elevated Structure not shown on aerial imagery
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9056061&y=4648497&l=12&v=1
Building Picture
Base Flood Depth
is 6.7 ft.

## Slide 34
(7) Mitigated Structure – EC Bldg. #5
Building Diagram 5: Elevated Building with no Enclosure

## Slide 35
Mitigated Structure – EC Bldg. #6
Building Diagram 6: Elevated Building with Enclosure (using piers, piles, posts)
Partial Enclosure

## Slide 36
Mitigated Structure – EC Bldg. #7
Building Diagram 5
Building Picture
Building Diagram 7: Elevated Building on Solid Foundation Walls (Full-Story)
Walkout Opening
Full-Story Enclosure

## Slide 37
Mitigated Structure – EC Bldg. #8
Building Diagram 8: Elevated Building with Crawlspace (Enclosure)
Crawlspace Enclosure

## Slide 38
Complete Online Survey Form when Finished
Quick Verification Guide and Survey