## Slide 1
(1) Flood Tool: Desktop Version https://www.mapwv.gov/flood
(2) Flood Tool: Mobile Version https://www.mapwv.gov/flood/mmap
Public resource applications that support floodplain management and flood reduction activities
WV Flood Tool
(3) Property Search and Assessment Report https://www.mapwv.gov/property
Query search on flood hazard zones and state assessment records
New development
Prior ownership
Web Parcel Report
Flood Tool: Desktop
Mobile
11/07/2020

## Slide 2
WV Flood Tool
Flood Tool Views
(www.mapwv.gov/flood)
Public View for general public
Expert View for floodplain managers
RiskMAP View for flood risk planners

## Slide 3
WV Flood Tool Views
Public View
Expert View
RiskMAP View
Quick Determination if IN or Out of Flood Zone
Floodplain Management and Permits, Disaster Assessments
Building-Specific Flood Risk Assessments

## Slide 4
WV Flood Tool – Public View
Public View
https://www.mapwv.gov/flood/map/?v=0&pid=19-07-022B-0021-0000

## Slide 5
WV Flood Tool – Expert View
Expert View
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000

## Slide 6
WV Flood Tool – RiskMAP View
RiskMAP View
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000

## Slide 7
Flood Query Results Panel
Parcel ID Web Link: https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
# | Each Location Query Answers:
1 | In Flood Hazard Area? Flood Zone? Floodway?
2 | Stream & Watershed names?
3 | FEMA Issued Flood Map / NFHL links?
4 | Floodplain Manager Contact?
5 | Flood Height value & Vertical Datum?
6 | Water Depth value and source?
7 | HEC-RAS Model available?
8 | Flood Profile available?
9 | CRS community information?
10 | Coordinate x,y location?
11 | External Map Viewer Links?
12 | Ground elevation value and source?
13 | E-911 Address (link to address info)
14 | Parcel ID (link to property info)
15 | Flood risk assessment info?
16 | 3D flood visualization?
15
14
16
13
11
12
10
9
8
7
6
5
4
3
2
1
54 King St.
Performance Measure: Query Results display within 5 seconds

## Slide 8
Print Out for Permits, LOMAs, etc.
Print Flood Query Results

## Slide 9
Building 19-07-022B-0021-0000_7170
Web Parcel Assessment Report for Building Identification, Building Characteristics, and Cost Values
Cost Values
Main Building Information
Outbuildings
Owner and Property Location
Property Intersect Flood Zone
Legal Description

## Slide 10
Building 19-07-022B-0021-0000_7170
Building Sketches from parcel assessment records are available for all Residential and Farm properties. Very useful for Building Identification.
Building Sketch Diagram (main area and additions)

## Slide 11
Data Privacy at State Level
West Virginia Statewide Parcel Files and Attributes in Public Domain: The local and state governments have the authority to share property owner names and addresses with the public (2017 Senate Bill 588). For example, West Virginia’s parcel assessment data which includes names and addresses is publicly accessible; only sensitive information like phone numbers or security alarm information are redacted by the WV Property Tax Division before release. Both the WV Property Tax Division and county assessors are co-custodians of the parcel map files and assessment records. All the West Virginia parcel data and assessment information can be downloaded from the State Data Clearinghouse.

## Slide 12
Building 19-07-022B-0021-0000_7170
Flood Tool External Link to Google Street View
Building 19-07-022B-0021-0000_7170
Flood Tool External Link to Google Street View

## Slide 13
Information Links
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
FEMA Flood Maps
Flood Profile
Elevation Metadata
Street View Picture
Bldg. Flood Risk
Property Info
Flood Visualization

## Slide 14
Information Links
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
FEMA’s NFHL Viewer
FEMA Issued Flood Map
Flood Profile
Street View Image
Building 19-07-022B-0021-0000_7170

## Slide 15
Google Street View
High-Risk Advisory A Zone
Parcel ID: 33-01-0010-0033-0000
http://www.mapwv.gov/Assessment/?PID=33010010003300000000
Flood Visualization
Web Parcel Report
Flood Zone Map

## Slide 16
WV Flood Tool
3D Flood Visualizations

## Slide 17
RiskMAP View – 3D Visualization
Flood Depth – 3D Visualization
Street View Image
HAZUS Loss Estimate
Building Exposure

## Slide 18
Building 7170:19-07-022B-0021-0000
3D Flood Visualization

## Slide 19
3D Flood Visualizations
3D flood visualizations are available statewide for locations where flood depth grids exist. The parcel assessment data fields (land use, stories) are necessary to identify the correct property type: residential one- or two-story homes, mobile home, commercial/industrial, etc.
Mobile Home
      "The 3D visualization is really cool. Our citizen comes to the counter and says 'there is no way there can be a flood like that.' Then we show them how much water you will get in your house and how much it will cost to repair it. The 3d visual is really good! And then we like the way you can click on a parcel ID and it brings up all the information as far as property owner, tax map and parcel number, deed book, page number - everything is right there. And the building information is really good too because it tells what the structure is made of, whether it has a basement - all the information that we would have to go to another system to pull is right there.“ Source: 3D Flood Visualization Comment from Debbie Robinson, Kanawha County Planning and Development Office
Visualizations are easier for non-technical users to understand flood risks to their property in feet of water rather than comprehending the adjacent base flood elevation
Commercial
2-Story Home
1-Story Home

## Slide 20
3D Flood Visualizations
      “This is the coolest thing ever….thank you!!!”
      Source: 3D Flood Visualization Comment from Terri Jo Bennett, CFM, Upshur County Building Permit, Floodplain and Addressing and Mapping Coordinator
Brooke County
https://www.mapwv.gov/flood/map/?v=1&pid=05-07-W22P-0161-0000
1412 Charles St, Wellsburg, WV, 26070, Parcel ID: 05-07-W22P-0161-0000
Upshur County
https://www.mapwv.gov/flood/map/?v=0&pid=49-05-0003-0031-0000
673 Vicksburg RD, Buckhannon, WV, 26201, Parcel ID: 49-05-0003-0031-0000

## Slide 21
The objective is to make the 3D visualizations as realistic as possible in a minimal amount of processing time
3D Flood Visualization - Community
Basic Steps for Creating 3D Flood Visualizations
Start with High-Resolution Digital Terrain Model
Overlay High-Resolution Aerial Image
Then add Streets
Then add Building Footprints
Extrude Building Footprints to Known Heights (“sugar-cube” 3D buildings)
Generate Detailed 3D Building Models
Photo-Texture the 3D Building Models
Add Trees and other Landscape/Streetscape Features
Add Flood Overlay (Riverine 1% Annual Chance Flood) Source: NEMAC

## Slide 22
3D
3D Northwest View
Baltimore Street, Martinsburg, WV
WV Flood Tool Conceptual Slide
3D Flood Visualization - Community

## Slide 23
WV Flood Tool
Property Identification

## Slide 24
Property Identification – Bldg. ID
Share Link: https://www.mapwv.gov/flood/map/?wkid=102100&x=-8909292&y=4742427&l=12&v=1
X,Y COORD.
ADDRESS
SHARE LINK
PARCEL
Address: 604 Main St, Philippi, WV 26416
Building ID:
(Parcel ID + Address No.)
01-08-0011-0069-0000_604
604 S Main Street, Philippi, WV
Parcel ID: 01-08-0011-0069-0000

## Slide 25
Property Parcels and Assessment Reports
Share Link: https://mapwv.gov/Assessment/Detail/?PID=01080011006900000000
E-911 and County Assessor report location at 604 S Main Street
Building
Sketch Diagram
Property Assessment Report
Parcel Map
Map-Parcel Number 11-69

## Slide 26
Unique Building Identifier
Collect multiple spatial identifiers to verify location
Parcel | 01-08-0011-0069-0000
Address | 604 S Main St, Philippi, West Virginia, 26416
X,Y Coordinate | 39.144752, -80.033529
Share MAP URL Link | https://www.mapwv.gov/flood/map/?wkid=102100&x=-8909292&y=4742427&l=12&v=1
01 | - | 08 | - | 0011 | - | 0069 | - | 0000
County |  | District |  | Map |  | Parcel |  | Suffix
Building Identifier | 01-08-0011-0069-0000_604
Share Parcel Assessment URL Link | http://www.mapwv.gov/Assessment/Detail/?PID=01080011006900000000
Google Plus Code (11-digit) | 86FX4XV8+VHF
= Unique Identifiers
Notes: Owner Name from assessment records and Building Pictures (elevation certificates) can be helpful for property identification purposes
Proper Building and Property Identifiers are important for exchanging building-level data efficiently among local, state, and federal partners (including UDFs, LOMAs, Mitigated Buyout Properties, Elevation Certificates, Repetitive Loss Structures, etc.)

## Slide 27
Building Unique Identifier
Parcel ID | 01-08-0011-0069-0000
Address | 604 S Main St, Philippi, West Virginia, 26416
01 | - | 08 | - | 0011 | - | 0069 | - | 0000
County |  | District |  | Map |  | Parcel |  | Suffix
Building Identifier (Parcel ID + Address No.) | 01-08-0011-0069-0000_604
Link to Property Record
Link to Structure Record
Building Unique Identifier
10/11/2020

## Slide 28
Other WV Flood Tool Features
WV Flood Tool
Flood Operational Layers
Flood Zones and Symbology Types
Programming Logic (Flood Zone, Flood Height, Water Depth) for Flood Query Result Panel
High Resolution Ground Elevation Data
Property Identification / Unique Building Identifier
WV Property Viewer & Search
Uses of Flood Tool

## Slide 29
WV Flood Tool
Search and Zoom Tools

## Slide 30
Search by Parcel
Full Parcel ID
Step-by-Step Parcel ID
Property Owner
Search By:
Select “Parcel” from pull down search list
Results (Parcel 01-08-0011-0069-0000)
Smith John
01-08-0011-0069-0000

## Slide 31
WV Flood Tool
Operational
Flood Layers

## Slide 32
* External Agency Web Map Services ** Partial Statewide Coverage
Flood Hazard Layers
FLOOD LAYERS | Public View for general public | Expert View floodplain managers | RiskMAP View flood risk reduction
Flood Hazard: Management & Risk Layers NFHL Flood Zones (Effective, Preliminary, Draft) High-Risk Advisory Flood Zones Base Flood Elevations (X-Sections, BFE Lines) LOMAs / LOMRs (Verified LOMAs**) Panel Index (links to FEMA issued map) Structures, Levees, Mile Markers* Elevation Certificates** | Yes Yes No No No No No | Yes Yes Yes Yes Yes Yes Yes | Yes Yes Yes Yes Yes Yes Yes
Flood Risk Assessment Flood Water Depths (HEC-RAS model-backed)** Other Water Depths (Hazus, USGS HWM) Historical Flood High-Water Marks Building-Level Risk Assessments** Future Map, Exposure Cost, New Development, Damage Repetitive Loss Area Analysis (RLAA)** Flood-Prone Roads, Railroads, Bridges Dams Other Natural Hazards – Landslides | No No No No No No No No No | Yes No Yes No No No No No No | Yes Yes Yes Yes Yes Yes Yes Yes Yes
Property Mitigation Elevated Structures** Open Space Preserved (e.g., Buyout Properties) | No No | No No | Yes Yes
Real-Time Flood Prediction USGS Real-Time Stream Gages* | No | No | Yes
10/24/2020

## Slide 33
Flood Layers – Expert View

## Slide 34
WV Flood Tool
Flood Zones & Symbology

## Slide 35
Multiple Flood Zone Symbology Types
EXPERT View
Depth Grid Underlies Flood Zones
PUBLIC View
High Risk Regulatory (red) and Non-Regulatory (orange)
NFHL View
NFHL Viewer

## Slide 36
Flood Layer Symbols

## Slide 37
Zone A
Zone AE
Advisory
Regulatory Floodway
1-Percent-Annual-Chance Flood Hazard Area
With Base Flood Elevation (BFE)
1-Percent-Annual-Chance Flood Hazard Area
Without BFE
1-Percent-Annual-Chance Future Conditions
(High Risk Advisory Flood Zones)
Preliminary NFHL or Advisory A or Updated AE
WV Flood Tool PUBLIC VIEW - High Risk
HIGH RISK

## Slide 38
Zone A
Zone AE
Preliminary
Regulatory Floodway in AE Zone
1-Percent-Annual-Chance Flood Hazard Area (AE, AO, AH) With Base Flood Elevation (BFE)
1-Percent-Annual-Chance Flood Hazard Area
Without BFE (may have Advisory Flood Heights)
1-Percent-Annual-Chance Preliminary SFHA
Updated AE
Advisory A
High Risk Updated AE Boundary (1 PCT Future Conditions)
High Risk Advisory A Zone (1 PCT Future Conditions with Advisory Flood Heights)
WV Flood Tool EXPERT VIEW - High Risk
HIGH RISK
Floodway
also RiskMAP VIEW

## Slide 39
0.2-Percent-Annual-Chance Flood Hazard Area (500-YR Floodplain) Symbol: yellow stipple pattern
Area with Reduced Risk Due to Levee Symbol: yellow vertical hachure pattern
Areas in Close Proximity of Flood Zone Boundaries are presented as a MODERATE RISK on the Flood Results Query Panel of the WV Flood Tool
Zone X
WV Flood Tool – Moderate Risk
MODERATE RISK
Zone X

## Slide 40
(FEMA NFHL Viewer)
FEMA NFHL Viewer
HIGH RISK
MODERATE RISK

## Slide 41
WV Flood Tool
Print Function Legend Layouts

## Slide 42
Print Flood Map (Expert View)
http://www.mapwv.gov/floodtest/?wkid=102100&x=-8899682&y=4811867&l=13&v=1

## Slide 43
Print Flood Map (Public View)
http://www.mapwv.gov/floodtest/?wkid=102100&x=-8679232&y=4773901&l=12&v=0

## Slide 44
Flood Query Results Panel
Parcel ID Web Link: https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
# | Each Location Query Answers:
1 | In Flood Hazard Area? Flood Zone? Floodway?
2 | Stream & Watershed names?
3 | FEMA Issued Flood Map / NFHL links?
4 | Floodplain Manager Contact?
5 | Flood Height value & Vertical Datum?
6 | Water Depth value and source?
7 | HEC-RAS Model available?
8 | Flood Profile available?
9 | CRS community information?
10 | Coordinate x,y location?
11 | External Map Viewer Links?
12 | Ground elevation value and source?
13 | E-911 Address (link to address info)
14 | Parcel ID (link to property info)
15 | Flood risk assessment info?
16 | 3D flood visualization?
15
14
16
13
11
12
10
9
8
7
6
5
4
3
2
1
54 King St.
Performance Measure: Query Results display within 5 seconds
10/11/2020

## Slide 45
Flood Query Results Panel
Programming Logic Determinations for Flood Query Results Panel
Flood Zones – 13 zone status conditions
Flood Heights – Base Flood Heights, Advisory Flood Heights, Preliminary Flood Heights – 5 status conditions
Depth Grid – HEC-RAS Model-Backed (most accurate) or Hazus

## Slide 46
Flood Zone Determination Sequence
HIGH:
100-YR Effective Floodplain
HIGH:
Preliminary NFHL (AE or A)
MODERATE: 500-YR Effective Floodplain & Levee Reduced Risk
MODERATE:
Within 75-ft of Flood Zone
LOW:
No identified Flood Risk
HIGH
Draft NFHL (AE or A)
HIGH
Advisory A
Non-Regulatory
HIGH
Updated AE
Non-Regulatory
Flood zone determination sequence important for programming logic
WV Flood Tool first checks query location for High Risk effective flood zones (red warning color), High Risk advisory flood zones (orange), then Moderate Risk flood zones (yellow)

## Slide 47
Status # | Flood Risk Zone Designation | Message | Floodplain Type Label | WSEL Grid | Flood Degree Risk | Color Warning Status
1 | AE, AH (5), AO (2) | Location is WITHIN the FEMA 100-year floodplain. | Effective 100 yr Zone AE, AH, AO | BFE-R or BFE-NR | High | Red
2 | AE (Floodway) | Location is WITHIN the FEMA 100-year floodplain and floodway. | Effective 100 yr Zone AE, AH, AO - Floodway | BFE-R or BFE-NR | High | Red
3 | A | Location is WITHIN the FEMA 100-year floodplain. | Effective 100 yr Zone A | < None > | High | Red
4 | A (Advisory Flood Heights available) | Location is WITHIN the FEMA 100-year floodplain. Advisory Flood Heights available. | Effective 100 yr Zone A and Advisory Zone A | AFH or BFE-P | High | Red
5 | Preliminary NFHL Flood Zone | Location is WITHIN an updated FEMA 100-year flood hazard zone. The flood zone is preliminary and under review to become effective. | Preliminary 100 yr Zone AE or A (Shaded X not displayed or shown on Flood Query Results Panel) | BFE-P, then BRE-R, BFE-NR, AFH | High | Orange
6 | Preliminary Flood Zone (Floodway) | Location is WITHIN an updated FEMA 100-year flood hazard zone and floodway. The flood zone is preliminary and under review to become effective. | Preliminary 100 yr Zone AE – Floodway | BFE-P, then BFE-R, BFE-NR, AFH | High | Orange
7 | Draft NFHL Flood Zone (NEW) | Location is WITHIN an updated FEMA 100-year flood hazard zone. The flood zone is DRAFT and under review to become PRELIMINARY. | Draft 100 yr Zone AE or A | BFE-P (A or AE Zones only) | High | Orange
8 | Updated AE Floodplain Bdry. | Location is WITHIN an updated detailed floodplain boundary but NOT a FEMA 100-year effective floodplain. | Updated Zone AE | BFE-NR | High | Orange
9 | Advisory A | Location is WITHIN an advisory floodplain but NOT a FEMA 100-year effective floodplain. | Advisory Zone A | AFH | High | Orange
10 | Shaded X (500-YR Flood) | Location is WITHIN a moderate flood risk hazard such as a FEMA 500-year floodplain. | Zone X - 0.2 PCT ANNUAL CHANCE FLOOD HAZARD | < None > | Moderate | Yellow
11 | X (Levee Protected) | Location is PROTECTED by a levee from a 100-year flood | Zone X - AREA WITH REDUCED FLOOD RISK DUE TO LEVEE | < None > | Moderate | Yellow
12 | Near Flood Zone | Location is NOT WITHIN identified flood hazard area, but within 75 feet of an identified flood hazard area. | Separate Buffer Layer | < None > | Moderate | Yellow
13 | Out of Flood Zone | Location is NOT WITHIN any identified flood hazard area. Unmapped flood hazard areas may be present. | No Record Found | < None > | Low | Green
Flood Zone: < zone designation >
Three Degrees of Risk: High, Moderate, Low. Four Warning Status Colors: In 100-YR Effective Floodplains (red), Preliminary Flood Zones and non-regulatory Advisory A/Updated AE Floodplains, Draft (orange), moderate risk or close to high- risk zones (yellow), and low risk (green). The query consists of stacked floodplain boundary layers (see next slide)

## Slide 48
Status # | Flood Height Designation | Flood Zones | Message for FLOOD HEIGHT: | Source Message on Query Panel | More Info Link on Flood Query Results Panel
1 | Base Flood Elevation (Restudy) BFE Grid | AE Zones Flood Zone Statuses 1, 2, 5, 6 | < value> ft. (Display to 0.1) (Clickable GRID value) | (BFE Restudy) In future may include A Zones | Advisory Flood Heights (AFH) for Approximate A Zones: CAUTION CAUTION!! The advisory flood height should be used with caution in the proximity of a culvert, bridge, flood control structure or other impoundment since stream crossings were not included in the hydraulic analyses for approximate floodplains. Also, if the site is close to the confluence with a larger stream, compare the advisory flood height at the location of interest to the advisory flood height or Base Flood Elevation on the larger stream to determine whether the site is within the backwater influence of the larger stream. More information: http://www.mapwv.gov/flood/content/documents/AFHhandout.pdf Restudy and Non-Restudy AE Zones: To validate base flood elevations refer to the Flood Profiles and Flood Elevation Tables in the FIS Report. Vertical Datum for Flood Heights: The vertical datum of Base Flood Elevations (BFEs) for AE Zones recorded on official FIRMs in West Virginia is NAVD 88, except for the following counties where the FIRMs are referenced to the NGVD 29 Datum: Hampshire, Logan, McDowell, Mercer, Monroe, Ohio, and Putnam. The vertical datum of all Advisory Flood Height values for Approximate A Zones in West Virginia is NAVD 88, except for McDowell County which is NGVD 29. More information.
2 | Base Flood Elevation (Non-Restudy) Updated AE Grid | AE Zones Flood Zone Statuses 1, 2, 8 | < value> ft. (Display to 0.1) (Clickable value) | (BFE Non- Restudy) | 
3 | Base Flood Elevation (Non-Restudy) | AE Zones Flood Zone Statuses 1 & 2 | no value | Refer to FIS report for BFE | 
4 | Advisory Flood Height AFH Grid or BFE-P Grids | A Zones Flood Zone Statuses 4, 5, 6, & 9. Possible status 10. | About < value> ft. (Display to 0.1) (Clickable value) | (AFH) | 
5 | Preliminary Flood Height (BFE-P) | Flood Zone Statuses 5 to 7. BFE Preliminary Grid takes priority. | 5a, 6a, 7 = value 5b, 6b = no value | Grid value (BFE Preliminary), then BFE-R, BFE-NR, AFH No Value. “See FEMA Change Viewer link for Prelim. BFE” | 
6 | No Flood Height Information | Flood Zone Statuses 3 and 4; 9 through 13 | no value | None (Status 3 or 4) N/A (Statuses 9-13) | 
Flood Height: < Value >
Invisible Composite Query Rasters for flood height values of Water Surface Elevation Level (WSEL) layers: (1) Advisory Flood Height WSEL AFH Grid (WSEL_1PCT_AFH_5ft); (2) BFE Restudy WSEL BFE Grid (WSEL_1PCT_BFE_1m); Updated AE/BFE Non-Restudy (WSEL_1PCT_Updated_AE)

## Slide 49
Water Depth | Message | Sources
Water Depth: | About << value >> ft. | Model-Backed Depth Grids: Engineering Studies using modeling software like HEC-RAS: RiskMAP Restudy (Effective and Preliminary) Non-Restudy Updated AE Zones Advisory Flood Heights (Approximate A Zones) Other Depth Grids HAZUS generated USGS Inundation Layers
Water Depth: about <<value>>
A statewide “composite” Flood Risk Assessment Depth Grid is created from model-backed effective and advisory depth grids at a 1-meter cell resolution.
Water Depth Grids are a flood risk assessment product – not a flood regulatory product. Water depths are important for flood loss damages and by flood visualizations of site-specific structures.
Depth grids a source of credits for CRS communities.
See FEMA’s Flood Risk Assessment Guidance (May 2016) for guidance on composite depth grids:
https://www.fema.gov/media-library-data/1469146645661-31ad3f73def7066084e7ac5bfa145949/Flood_Risk_Assessment_Guidance_May_2016.pdf

## Slide 50
WV Flood Tool
Ground Elevation

## Slide 51
Ground Elevation
1-FOOT CONTOUR ELEVATION VALUE OF 2125 FEET MATCHES 1-METER GRID SURFACE ELEVATION OF 2125 FEET DISPLAYED IN QUERY RESULTS PANEL
http://www.mapwv.gov/floodtest/?wkid=102100&x=-8916536&y=4610651&l=13&v=1
FEMA LiDAR-Derived Products: 1-M DEM and 1-Ft. Contour
Source: FEMA 2016

## Slide 52
Ground Elevation: 1-ft. Contours
1-FOOT CONTOUR ELEVATION VALUE OF 600 FEET MATCHES 1-METER GRID SURFACE ELEVATION OF 600 FEET DISPLAYED IN QUERY RESULTS PANEL
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9177701&y=4611497&l=13&v=1
FEMA LiDAR-Derived Products: 1-Meter DEM and 1-Foot Contours
Elevation: 600 ft.
Source: FEMA 2018
1-ft Contours Display at two Highest Zoom Levels (1:564 and 1:282 Map Scales)
600 ft.
Make Contour Lines visible under REFERENCE LAYERS
1-foot contours published for 10 counties

## Slide 53
FEMA Purchased LiDAR Coverage
FEMA has purchased $10 million in QL2 LiDAR and entire State should be processed and delivered by 2022
Quality 2 (QL2) LiDAR support 1-foot contours

## Slide 54
Elevation Data Sources
WV Elevation Source Listing and Graphic: https://www.mapwv.gov/floodtest/docs/WV_FloodTool_ElevationSource_Metadata.pdf
Source Graphic
FEMA is purchasing Statewide QL2 LiDAR
Elevation Metadata
1-Ft. Contours for Areas 8A, 8B, 9A, 9B, 12A, 12B
2-Ft. Contours for Area 7

## Slide 55
WV Flood Tool
Dams and Landslides

## Slide 56
Dams and Landslides
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8771562&y=4715438&l=7&v=2
Dam and Landslide Risk Layers in RiskMAP View Hardy County, West Virginia
Landslide
Dam

## Slide 57
WV Flood Tool Updates
Mobile Application
Added Search by Property Owner Name
Added Search by Parcel Identifier
Mobile Home Page
flood

## Slide 58
WV Flood Tool (Mobile)
Mobile Home Page
Toggle Layers of Interest
682 Killarney Drive, Morgantown, WV
www.mapwv.gov/flood
Zoom to E-911 Address
flood

## Slide 59
WV Flood Tool (Mobile)
Touch Parcel for Flood Info
View Parcel Report
682 Killarney Drive, Morgantown, WV
View Flood Report
www.mapwv.gov/flood

## Slide 60
WV Flood Tool
WV Property Viewer
www.mapwv.gov/property
Companion Product to WV Flood Tool
Powerful compound query searches can be performed on flood hazard zones and state assessment records:
New Development in Floodplains
Prior Ownership (Deed Book, Previous Owner, Legal Description). Online search of the parcel history of deed book/page numbers and other ownership information to identify the correct positional location of LOMAs and Buyout Properties.

## Slide 61
WV Property App (Companion Product)
Chart: Total Visits
| 2017, Q4 | 2018, Q1 | 2018, Q2 | 2018, Q3 | 2018, Q4 | 2019, Q1 | 2019, Q2 | 2019, Q3
Flood Tool | 28911 | 33601 | 36216 | 38080 | 28954 | 34226 | 31978 | 30546
Parcel Viewer | 64 | 333 | 844 | 3782 | 16595 | 41391 | 48942 | 65507
Detailed Property Report
WV Property Viewer www.mapwv.gov/parcel WV Property Search www.mapwv.gov/ property
Property Search Tool
Property Viewer
Web Visits

## Slide 62
WV Property Search: New Development
Companion Product to WV Flood Tool
Search Parameters | Value
Flood Hazard | High
County | Preston
Building Year Minimum | 2017
Min. Building Year Appraisal | 50000
Property Class | Residential
Search Query Parameters for New Development in Floodplain
“Advanced” WV Property Search: www.mapwv.gov/property

## Slide 63
WV Property Search: New Development
Query Results for New Development in Floodplain
WV Property Search: www.mapwv.gov/property
Search Parameters | Value
Flood Hazard | High
County | Preston
Building Year Minimum | 2017
Min. Building Year Appraisal | 50000
Property Class | Residential
https://www.mapwv.gov/assessment/Assessment?Counties=39&PropertyClass=R&MinimumBuildingValue=50000&BuildingYearMin=2017&FloodRisk=High
2018 Structure at $315K Built in Advisory A
https://mapwv.gov/flood/map/?wkid=102100&x=-8873789&y=4820097&l=13&v=0

## Slide 64
WV Property Search: Deed Book
Search Query Parameters for Prior Ownership using Deed Book/Page No.
“Prior Ownership” WV Property Search: www.mapwv.gov/property
https://map1.msc.fema.gov/data/54/L/97-03-298A-540160.pdf?LOC=d08f245a47f18e659f1b75b1515425b6
LOMA 97-03-298A, Project ROUTE 27/3 - DILLON CREEK
Correct LOMA Location
Wrong LOMA Location
LOMA 97-03-298A is not located south of Kingwood, but 9 miles to the northwest in Preston County.
The WV Property Search Tool located the correct parcel through a Deed Book Number and Page search.
9 miles

## Slide 65
WV Property Search: Deed Book
Search Query Parameters for Prior Ownership using Deed Book/Page No.
“Prior Ownership” WV Property Search: www.mapwv.gov/property
LOMA 97-03-298A, Project ROUTE 27/3 - DILLON CREEK
LOMA 97-03-298A is not located south of Kingwood, but 9 miles to the northwest in Preston County.
The WV Property Search Tool located the correct parcel through a Deed Book Number and Page search.
Search Parameters | Value
County | Preston
Deed Book Number | 505
Deed Book Page | 177

## Slide 66
WV Property Search: Deed Book
LOMA 97-03-298A, Project ROUTE 27/3 - DILLON CREEK
Correct parcel location of LOMA 97-03-298A was identified by a prior owner and Deed Book Number 505/177 back to year 2008
https://mapwv.gov/assessment//Detail/?PID=39020013008400010000
Deed Book: 505/177

## Slide 67
WV Property Search: Deed Book
“Prior Ownership” WV Property Search: www.mapwv.gov/property
LOMA 97-03-298A, Project ROUTE 27/3 - DILLON CREEK
Correct positional location of LOMA 97-03-298A verified with LOMA Document by Deed Number (505/177), Parcel Size (1 acre), Flood Source (Dillon Creek), and Highway Number 27/3.
Parcel Detailed Report
Route 27/3
Dillan Creek
Prior Deed 505 / 177
See Parcel History in Assessment Report
1 Acre
Positionally Verified
LOMA 97-03-298A
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8882817&y=4797874&l=11&v=1

## Slide 68
WV Property Search: Deed Book
LOMA 97-03-298A, Project ROUTE 27/3 - DILLON CREEK
FEMA LOMA 97-03-298A: Positional Accuracy, Determination Status, and Revalidation Status in Error
Positionally Verified
LOMA 97-03-298A
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8882817&y=4797874&l=11&v=1
LOMA Determination and Revalidation Status in Error

## Slide 69
Flood Tool Applications
  Floodplain Management
    Property Identification
    Property Search Tools
    Flood Determinations
    NFIP / Community Rating System
  Risk Mapping, Assessment, and Planning
    Risk Identification and Mapping
    Risk Assessment
    Risk Mitigation & Planning
    Risk Communications
  Disaster Assessment

## Slide 70
WV Flood Tool
Disaster Assessments
FEMA Letter dated September 29, 2017, about WV Flood Tool support for Disaster Assessments

## Slide 71
Flood Risk Development Team
  WV GIS Technical Center West Virginia University Morgantown, WV http://wvgis.wvu.edu
Kurt Donaldson Manager
Yibing Han
GIS Programmer
Kevin Kuhn GIS Analyst / Address-Parcel Specialist
Maneesh Sharma GIS Analyst / Flood Risk Specialist
Eric Hopkins GIS Analyst / Flood Risk Specialist
Frank LaFone Systems Administrator
Xiannian Chen GIS Programmer
Jim Schindling Database Programmer
Behrang Bidadian GRA
Shelter Models
Kevin Shrader GRA Building Inventory, Flood Visualization
Full and Part-Time Staff

## Slide 72
Contact Information
  WVU GIS Technical Center, West Virginia University Kurt Donaldson, GIS Manager kurt.donaldson@mail.wvu.edu, phone: (304) 293-9467
  Maneesh Sharma, GIS Analyst
  Maneesh.Sharma@mail.wvu.edu, phone (304) 293-9466
  Eric Hopkins, GIS Analyst Eric.Hopkins@mail.wvu.edu, phone: (304) 293-9463