## Slide 1: Flood Risk Review (FRR) Meeting
Hampshire County, West Virginia
May 4, 2023

## Slide 2: Agenda
Welcome and Introductions
Where We Are - Draft Maps
Flood Study Update
Study Impacts
Using Flood Risk Data to Reduce Flood Risk
Floodplain Management
Discussion

## Slide 3: Welcome and Introductions

## Slide 4: Where We Are - Draft Maps

## Slide 5: 3 Reasons We Are Here Today
To preview and discuss the updated Flood Insurance Study (FIS) report and Flood Insurance Rate Map (FIRM) for Hampshire County, WV
To examine the new study areas, discuss how the analysis and mapping have changed since the previous study, and work collaboratively to ensure that the needs of the community and its partners are met. BECAUSE THE EARLIER YOU KNOW THE BETTER!
To present a timeline of next steps

## Slide 6: Timeline – Looking Back
5
Effective FIRM (Digital Conversion) November 2002
Flood Risk Review Meeting
May 4, 2023
Risk MAP Study Notification
May 2021
Risk MAP Kickoff Meeting
June 2021

## Slide 7: Timeline for Hampshire County
Flood Risk Review Meeting
May 4, 2023
Preliminary Maps and CCO Meeting
Fall 2023
Appeal Period
Spring 2024
End of Appeal Period
90-days after appeal
start
FEMA issues LFD
Winter 2024
Effective Date
6 months after LFD

## Slide 8: Flood Study Update

## Slide 9: Floodplain Map Overview
HIGH RISK
(Special Flood Hazard Area)
Regulatory Floodway
ZONE AE
1-Percent-Annual-Chance Flood Hazard Area with Base Flood Elevations (BFEs)
ZONE A
1-Percent-Annual-Chance Flood Hazard Area without published BFEs
MODERATE RISK
0.2-Percent-Annual-Chance Flood Hazard Area
Cross Sections with 1% Annual Chance Water Surface Elevation Value
“The 100-Year Flood Zone Explained”
Notes: Discuss 1% floodplain and 0.2% floodplain, floodway, cross sections, and BFEs
“Cross sections now show water surface elevations.”
“Transparent fills over aerial photography”
“new maps will look different”

## Slide 10: Floodplain Map Overview Part 2
HIGH RISK
(Special Flood Hazard Area)
Development is not allowed unless “no rise” in flood levels is certified
ZONE AE
ZONE A
Flood insurance is mandatory for structures with federally-back mortgages
MODERATE RISK
Flood insurance is not mandatory
Cross Sections with 1% Annual Chance Water Surface Elevation Value
“The 100-Year Flood Zone Explained”
Notes: Discuss 1% floodplain and 0.2% floodplain, floodway, cross sections, and BFEs
“Cross sections now show water surface elevations.”
“Transparent fills over aerial photography”
“new maps will look different”

## Slide 11: Floodplain Map Overview
6

## Slide 12: Study Overview
Countywide Revised Modeling and Mapping, including:
Updated GIS-based regulatory products, including:
    Updated maps / database / report formats based on new FEMA guidelines and specifications
Utilization of high-resolution topographic data (for modeling and mapping)
Model-backed Approximate ‘Zone A’ Studies – 445 miles
Detailed ‘Zone AE’ Studies – 70 miles
Production of associated non-regulatory flood risk data

## Slide 13: What We Studied Map
The Hampshire County Project Area

## Slide 14: Topographic Data
2016/17 LiDAR based DEM LiDAR = Light Detection and Ranging
  Uses light pulses and GPS to survey elevation data
  Improves the level of detail for hydraulic modeling and floodplain delineation

## Slide 15: Hydrologic Analyses
Hydrologic Study Method | Study Type | Stream Names | Reach Lengths (Miles)
Gage Analysis weighted with Regional Regression Equations | AE | South Branch Potomac River, South Fork Little Cacapon River, North Fork Little Cacapon River, Little Cacapon River 1, Cacapon River 1 | 44.9
Gage Analysis weighted with Regional Regression Equations | A | Cacapon River, Cacapon River 2, Little Cacapon River, South Branch Potomac River 1 | 84.9
Regional Regression Equations | AE | Green Spring Run, Mill Branch, North River 1 | 21.6
Regional Regression Equations | A | All remaining approximate studies | 359.6
HEC-HMS | AE | Big Run | 3.3
Peak discharges for the 10-, 4-, 2-, 1-, and 0.2-percent-annual-chance storm events were computed using Regional Regression Equations (RRE) defined in “Estimation of Flood-Frequency Discharges for Rural, Unregulated Streams in West Virginia” – USGS SIR2010-5033 (Wiley and Atkins, 2010)
Notes: Refers to the rate of precipitation, the quantity of water, the rate of surface runoff, and the timing of its arrival at a point of interest.

## Slide 16: Hydrologic Analyses
Key Finding
The proposed discharges are generally lower than the effective discharges (dating back to the 1980s).
Flows derived from flood frequency analyses at gaged locations are generally higher than both effective flows and regression-based flows, which may be due to the influence of more recent flood events (i.e. not accounted for in the regression analysis).
Regardless, proposed discharges will be used in place of effective discharges to reflect updates over the past half century in hydrologic methods (e.g. regression equations), topography, and land use.
Sample page from the Hampshire Risk MAP Hydrology Report
Summary information will be published in the forthcoming Flood Insurance Study Report (to a greater degree for detailed Zone AE study reaches)
But a more focused, comprehensive Hydrology Report has been already been prepared with full details of the sources and methodology, along with comparative evaluation between effective and draft / proposed restudied discharges.

## Slide 17: Hydraulic Analyses – Zone A
Model backed Approximate (Zone A Studies)
445 miles
Developed using HEC-RAS 6.1.0
Generally used in areas with low development / low development potential
Cross-sections generated from LiDAR used for hydraulics:
  Automated processes
  No structures are modeled
  No floodway or BFEs on FIRM, but cross section included in in FIRM database)
  Multi-frequency flood values computed but only 1% annual chance published on FIRMs/FIS, but Floodplain Administrators can use WSELs from model as best available data for permitting in Zone A
Notes: How surface and/or subsurface flows move from one point to the next.

## Slide 18: Hydraulic Analyses – Zone AE
Detailed Studies (Zone AE)
70 miles
Developed using HEC-RAS 6.1.0
Generally used in areas with higher development / higher development potential
Structures are modeled (e.g. culverts, bridges) – 49 structures surveyed.
Detailed hydraulic parameter refinement (coefficients, obstructions, Manning's ‘n’ values, etc.)
Encroachments computed and regulatory floodways mapped
Multiple flood profiles included in FIS.
Floodway, cross sections, BFES, 1%-annual-chance and 0.2%-annual-chance event floodplains shown on FIRMs

## Slide 19: Study Impacts

## Slide 20: WV Flood Tool
http://www.mapwv.gov/flood/

## Slide 21: WV Flood Tool
http://www.mapwv.gov/flood/

## Slide 22: National Flood Hazard Layer
Visit https://www.fema.gov/national-flood-hazard-layer-nfhl for multiple options to view and download NFHL data.

## Slide 23: Flood Risk Dashboard Layout
26
NFIP FLOOD CLAIM PAYOUTS
CLAIMS OUTSIDE OF SFHA
NFIP FLOOD
POLICIES
HIGH-RISK
STRUCTURES
REPETITIVE
LOSSES
AVERAGE
PREMIUM
AFFECTED RESIDENTS

## Slide 24: Flood Risk Dashboards
Total Number of paid flood insurance claims and the total amount paid for these claims in your community since 1978
This is the number of paid flood insurance claims for structures outside of your community’s flood high hazard area since 1978.
The current total number of NFIP flood insurance policies in your community and the number of those policies for structures in the effective SFHA.
A repetitive loss (RL) property is a structure for which FEMA has paid 2+ flood insurance claims of >$1,000 within a 10-year period since 1978.
Your community’s Flood Insurance Rate Map (FIRM) was last updated on this date.
These numbers are estimates of based on structure data. It shows how many are expected newly mapped into and mapped out of the flood high hazard area.
This map shows the updated draft floodplains in your community
Notes: Mention that communities can use this to reference the dashboards (both countywide and jurisdictional) that were sent to them prior to the meeting and that will be sent to them after the meeting along with this presentation.

## Slide 25: Hampshire County, WV  Countywide
Discovery Meeting
Effective Maps
Flood Risk Review Meeting
Letter of
Final Determination
Preliminary Map Issuance
Appeal Period
Community Coordination & Outreach Meeting
26
Paid claims outside of the effective flood high hazard area2
$5.3M
Total paid losses2
335
Total paid claims2
$2.4M
Repetitive Loss (RL) paid losses2
58
RL properties2
133
Flood insurance policies in force
98%
In Hampshire County Unincorporated Areas
Estimated structures newly mapped in
+120
Estimated structures newly mapped out
-590
16,650
Estimated structures in the community
950
Estimated structures in the draft flood high hazard area
KEEPING COMMUNITIES INFORMED: Your Risk MAP Timeline
~YEAR 1 YOU ARE HERE
~YEAR 5
93
Policies in the effective flood high hazard area
FEMA’s Risk Mapping, Assessment, and Planning (Risk MAP) Program helps strengthen communities by identifying actions they can take now to reduce their hazard risk, enhance local planning, improve outreach through risk communications, and increase local resilience to natural hazards. Below is an overview of some key items identified during the Changes Since Last FIRM1 impact assessment.
The information presented below are estimates as of April 2023.
4%
Of the population is in the draft flood high hazard area
$992
Average premium
51%
Higher than the national average
10
Flood-related presidential disaster declarations
Flood insurance is available to the entire county.
Flood insurance savings can be obtained by joining FEMA’s Community Rating System (CRS).
0 levees and
5 dams

## Slide 26: Town of Capon Bridge/Hampshire County, WV KNOW YOUR RISK (The information presented below are estimates as of April 2023. 1 Flood Insurance Rate Map. 2 Since 1978.)
KEEPING COMMUNITIES INFORMED: Your Risk MAP Timeline
16%
Of the population is in the draft flood high hazard area
23%
Of households spend 30% or more of their income on housing
4/1/1988
1
Initial FIRM date
11/7/2002
Effective FIRM date
6
Paid claims outside of the effective flood high hazard area2
$220K
Total paid losses2
12
Total paid claims2
$151K
Repetitive Loss (RL) paid losses2
4
RL properties2
2
Flood insurance policies in force
2
Policies in the effective flood high hazard area
Estimated structures newly mapped in
+1
Estimated structures newly mapped out
-15
200
Estimated structures in the community
30
Estimated structures in the draft flood high hazard area
~YEAR 1
~YEAR 5
10
Flood-related countywide presidential disaster declarations
Discovery Meeting
Effective Maps
Flood Risk Review Meeting
Letter of
Final Determination
Preliminary Map Issuance
Appeal Period
Community Coordination and Outreach Meeting
YOU ARE HERE

## Slide 27: Town of Romney/Hampshire County, WV KNOW YOUR RISK (The information presented below are estimates as of April 2023. 1 Flood Insurance Rate Map. 2 Since 1978.)
KEEPING COMMUNITIES INFORMED: Your Risk MAP Timeline
>1%
Of the population is in the draft flood high hazard area
34%
Of households spend 30% or more of their income on housing
6/15/1988
1
Initial FIRM date
11/7/2002
Effective FIRM date
0
Paid claims outside of the effective flood high hazard area2
$85K
Total paid losses2
4
Total paid claims2
$0
Repetitive Loss (RL) paid losses2
0
RL properties2
1
Flood insurance policies in force
0
Policies in the effective flood high hazard area
Estimated structures newly mapped in
+0
Estimated structures newly mapped out
-5
830
Estimated structures in the community
<5
Estimated structures in the draft flood high hazard area
~YEAR 1
~YEAR 5
10
Flood-related countywide presidential disaster declarations
Discovery Meeting
Effective Maps
Flood Risk Review Meeting
Letter of
Final Determination
Preliminary Map Issuance
Appeal Period
Community Coordination and Outreach Meeting
YOU ARE HERE

## Slide 28: Unincorporated Areas/Hampshire County, VA KNOW YOUR RISK (The information presented below are estimates as of April 2023. 1 Flood Insurance Rate Map. 2 Since 1978.)
KEEPING COMMUNITIES INFORMED: Your Risk MAP Timeline
5.8%
Of the population is in the draft flood high hazard area
21%
Of households spend 30% or more of their income on housing
1
8/1/1987
Initial FIRM date
11/7/2002
Effective FIRM date
20
Paid claims outside of the effective flood high hazard area2
$5M
Total paid losses2
319
Total paid claims2
$2.2M
Repetitive Loss (RL) paid losses2
54
RL properties2
130
Flood insurance policies in force
91
Policies in the effective flood high hazard area
Estimated structures newly mapped in
+115
Estimated structures newly mapped out
-570
15,620
Estimated structures in the community
930
Estimated structures in the draft flood high hazard area
~YEAR 1
~YEAR 5
10
Flood-related countywide presidential disaster declarations
Discovery Meeting
Effective Maps
Flood Risk Review Meeting
Letter of
Final Determination
Preliminary Map Issuance
Appeal Period
Community Coordination and Outreach Meeting
YOU ARE HERE

## Slide 29: Significant Impacts Overview
Compared to effective NFHL, widening and narrowing of the 1-percent-annual-chance floodplain (SFHA) extent was observed throughout the county.
Extended study reaches (with drainage areas of 2 square mile and greater, and not on current effective FIRM) result in new properties within the SFHA.
Most streams experienced both increases and decreases when comparing the computed model WSELs to the current regulatory base flood elevations.
After the map update, an estimated total of 950 structures are expected to be in the Zone AE SFHA.

## Slide 30: Where Can I Find NFHL Data?
www.msc.fema.gov

## Slide 31: Using Flood Risk Data to Identify and Reduce Risk

## Slide 32: Types of Flood Risk Products
Flood Depth & Analysis Grids
Changes Since Last FIRM
Water Surface Elevation Grids
Flood Risk Assessment / Economic Loss Calculations
Areas of Mitigation Interest

## Slide 33: Water Surface Elevation Grids
Represent the continuous water surface elevations as determined at modeled cross-sections and interpolated values between cross sections

## Slide 34: Changes Since Last FIRM
FEMA Region 3 Changes Since Last FIRM (CSLF) Viewer: https://arcg.is/9W8P8
Change in Floodplain Extents:
    Purple – Decrease
    Blue – Still Floodplain
    Yellow – Increase

## Slide 35: Depth Grids
Represent the difference between the ground surface and the water surface elevations

## Slide 36: WV Flood Tool
http://www.mapwv.gov/flood/

## Slide 37: Flood Hazard Mitigation Planning
Refer to the plan
and keep it current
Coordinated and participative planning process
Identify hazards that can affect the jurisdiction
Assess the risks from these hazards
Develop strategies to mitigate the risks
Adopt the plan and implement the mitigation strategy
Mitigation
Planning
Cycle
It’s time to start assessing the impacts of the new floodplain boundaries
We are here

## Slide 38: Using FRPs to Manage Development
Structure-based depth of flooding analyses
Prioritization of mitigation action
Residential/commercial density in the floodplain
Location/inundation area of historic events
Properties with insurance policies and as a percentage of the population
Areas of population growth
Areas requiring protection

## Slide 39: Floodplain Management
31

## Slide 40: Flood Risk Doesn’t Stop at a Line
25% of all flood insurance claims come from outside high- risk areas.
Your community can regulate to standards higher than the NFIP minimum standards. Consider strengthening regulations using:
  0.2% annual chance flood
  “Freeboard”
  Buffer around Special Flood Hazard Area (SFHA)
  Flood depth grids
HURRICANE HARVEY
GREATER HOUSTON

## Slide 41: Floodplain Management
Permits are Required for ALL Development in the floodplain!
Development means any manmade change to improved or unimproved real estate
Build it right and insurance premiums will be more affordable
Build it wrong and premiums will be very expensive
Photo taken from the Hampshire County Flood Protection Information Brochure.

## Slide 42: Floodplain Management
Communities must regulate based on FIRMs
Development should be reasonably safe from flooding
Permits are required for all development
State/federal permits are required
Elevate and/or construct with flood- resistant materials
Locate and design mechanicals to minimize or eliminate flood damage
Locate and design public utilities and facilities to minimize or eliminate flood damage
A Zones: top of lowest floor (residential) elevated to or above the base flood level

## Slide 43: Discussion

## Slide 44: Timeline – Looking Ahead
Flood Risk Review Meeting
(Draft Results)
Data Development
_______
Interim Coordination
Kick-Off / Discovery Meeting
06/28/2021
Preliminary Issuance of FIRMs / FIS
CCO Meeting
90 Day Appeal Period
LFD
start of 6-month ordinance adoption / compliance period
Effective
Maps

## Slide 45: We want to hear from you!
30-day review and comment period
WV Flood Tool: https://www.mapwv.gov/flood
Review the materials we will be sending you
We are available to answer questions
Thank you for your participation!

## Slide 46: For More Information
State NFIP/CTP Coordinator:
Tim Keaton, CFM
(304) 957-2571
Tim.W.Keaton@wv.gov
Mapping Partner
Jon Langley, CFM
Senior GIS Analyst (443) 514-8141
jonathan.langley@wsp.com
WVGISTC
Kurt Donaldson, GISP, CFM
Manager
(304) 293-9467
Kurt.Donaldson@mail.wvu.edu
Mitigation Planning Specialist
Elizabeth Ranson
(215) 347-0686
Elizabeth.Ranson@fema.dhs.gov
Project Officer
Kristen Jones, CFM
(267) 896-1116
Kristen.Jones@fema.dhs.gov
FEMA
Region 3
West Virginia
Other

## Slide 47: Final Slide – No Content