## Slide 1: CALHOUN COUNTY: Election District Mapping
Geo-SVRS Voter Match: Ensure Voter Registration Site Points are assigned to the correct geographic precinct. Refer to mismatch spreadsheet or red dots on G-SVRS Tool (www.mapwv.gov/SVRS). Consult with E-911 office about invalid addresses or spatially inaccurate addresses that cannot be mapped to the building footprint (less accurate street address match).
Precinct Boundary Definition Factors:
  E-911 Addresses & Road Centerlines
    All addresses of smaller roads or roads in hollows/narrow valleys should be in a single voting precinct to minimize multiple road segment definitions in the SVRS
    Street Geocodes: Geocode matches to street ranges are problematic for road precinct boundaries
  Incorporated Place Boundaries should be accurate and match precinct boundaries
  Topographic Ridge Boundaries. In rural counties, typically tax district and historical magisterial district line boundaries follow topographic ridgelines.
  Proximity to Polling Sites. Voter point travel time/distance to polling site of precinct
  Census Blocks. Follow existing census block edge boundaries if exist
Voting Precinct Boundary Alignment Issues/No Gaps:
  Precinct boundaries should align coincidentally with USGS 1:24,000-scale county boundary – not the less accurate Census boundary
  Precinct boundaries should align coincidentally with magisterial district lines

## Slide 2
CALHOUN COUNTY: PAST AND CURRENT MAGISTERIAL DISTRICTS
1
3
2
4
5
Tax District Boundaries (historical Magisterial District Boundary)
Today voting precinct boundaries primarily are defined by the E-911 roads instead of in the past following physical features (ridgelines, streams) of tax assessment district boundaries
1970 Magisterial/Tax Districts
2023 Magisterial Districts

## Slide 3
Voting Precinct & Magisterial Districts (Calhoun County)

## Slide 4
Precincts 6 Grantsville Corp. (Does not match Census or Tax District Bdrys)
https://data.wvgis.wvu.edu/pub/Clearinghouse/planningLanduseCadastres/wv_tax_maps/PDF/07_Calhoun_County/02_Grantsville_Corp/
Precinct Boundary
Census Municipal Boundary

## Slide 5
Precincts 6 Grantsville Corporation (Municipal boundary different on tax maps)
https://data.wvgis.wvu.edu/pub/Clearinghouse/planningLanduseCadastres/wv_tax_maps/PDF/07_Calhoun_County/02_Grantsville_Corp/
Tax Assessment Boundary

## Slide 6
Precincts 5-4-1 Bdrys, (Broomstick Rd – Precinct 5)
Broomstick Road
Broomstick Road

## Slide 7
Precincts 5-4-8 Bdrys, (Broomstick Rd – Precinct 5, Lovada Rd – Precinct 4)
Broomstick Road
Lovada Road

## Slide 8
Precincts 1-11 Bdrys (Tax District Boundary - Ridgeline)

## Slide 9
Precincts 10-7 Bdrys, (Sand Ridge Rd – Precinct 10)
Topo Bdry
Crummies Creek Road
Sand Ridge Road

## Slide 10
Precincts 10-7 Bdrys, (Intersection Crummies Creek Rd, Sand Ridge Rd)

## Slide 11
Precincts 10-19 Bdrys, (Sams Run Rd – Precinct 19)
Topo Ridge
Sams Run Road

## Slide 12
Precincts 1-4-11 Bdrys (Jockers Ridge Road – Precinct 4)
Jokers Ridge Road
Jokers Ridge Road

## Slide 13
Precincts 1-11 Bdrys (W. Little Kanawha Hwy west of Stutler road)
Stutler Rd
W Little Kanawha Highway

## Slide 14
Precincts 15-19 Bdrys, (Granny She Rd – Precinct 15)
Topo Ridge
Walnut Road