## Slide 1
West Virginia Statewide Flood Risk Assessment
Kurt Donaldson, GISP, CFM; Maneesh Sharma GISP, CFM;
Eric Hopkins, GISP, CFM
WV GIS Technical Center West Virginia University
Eastern Panhandle GIS Users Group
Annual Meeting (Virtual) August 13, 2021
Notes: Eric Hopkins, WVGISTC, 1998, Data Support and Cartography Lead for the WV Flood Tool, WV Statewide Building Level Flood Risk Assessment

## Slide 2
Flood Risk Development Team
  WV GIS Technical Center West Virginia University Morgantown, WV http://wvgis.wvu.edu
Kurt Donaldson Manager
Yibing Han
GIS Programmer
Kevin Kuhn GIS Analyst / Address-Parcel Specialist
Maneesh Sharma Flood Risk Specialist
Eric Hopkins GIS Analyst / Flood Risk Specialist
Frank LaFone Systems Administrator
Xiannian Chen GIS Programmer
Jim Schindling Database Programmer
Behrang Bidadian GRA
Shelter Models
Kevin Shrader Building Inventory, Flood Visualization
Full and Part-Time Staff
Shannon Maynard GIS Analyst
Johnna Murray GIS Analyst
Rachel Yesenchek GRA
Flood, Landslide BI
Notes: I’m a member of a large team of full-time staff, GRAs and undergraduate GIS interns, some key contributors are shown in this photograph

## Slide 3
Outline
Flood Risk Assessment Overview
  Hazard Mitigation Grant Project
Building Level Risk Assessment
  Building Inventory
    Essential Facilities/Community Assets
    Elevation Certificate
    Mitigated/Buyout Properties
  Model – Flood Assessment Structure Tool (FAST)
  Community Outreach/Feedback
WV Flood Tool
What’s Next
  Community Outreach/Feedback
  Community Profile
  Reports
Notes: Today we’ll look at the Statewide Flood Risk Assessment HMGP project, including Building Level RA, Delivery of results via the WV Flood Tool, and Next Steps in the process

## Slide 4: A Statewide Approach to Risk Studies Multi-Hazard Risk Assessments
Flood Risk #1 WV Hazard
Reference Data Development
Hazard Mitigation Grant Project
Landslide Risk #2 WV Hazard
Chart: 
| Flood Risk | Landslide Risk | Data Gap Services | Data Vendor Contracts | Professional Services
State HMGP Project | 697511 | 463332 | 385798 | 619509 | 85000
Inventory of Building-Level Flood-Risk Structures
Statewide
Budget Breakdown
Notes: The Statewide RA HMGP Project evaluates the number 1 and 2 WV Hazards; Reference data: GIS Parcels, Addresses, Aerial Photography to fill gaps, At-Risk Building Inventory

## Slide 5
Multi-Agency Coordination
Federal Agencies
State Agencies
Universities
Regional Councils
Local Counties
Private Companies
11 Regional Planning & Development Councils
55 Counties
Hazard Mitigation Grant
232 municipalities
Notes: The HMG involves multiple Governmental Agencies – Federal, State, Regional, Local levels, Academic Institutions, Private Companies

## Slide 6
Statewide Hazard Assessment
294 Statistical Geographies form 286 Communities which form
55 Counties which form
11 PDC Regions which form
1 Statewide Flood Risk Assessment
SPLIT COMMUNITY | COUNTY 1 | COUNTY 2
Alderson | Greenbrier | Monroe
Huntington | Cabell | Wayne
Montgomery | Fayette | Kanawha
Nitro | Kanawha | Putnam
Paden City | Tyler | Wetzel
Smithers | Fayette | Kanawha
Wheeling | Marshall | Ohio
Weirton | Brooke | Hancock
94% of WV Communities have Special Flood Hazard Areas (SFHA)
PDF Map
213 incorporated areas
+55 unincorporated areas 268 NFIP Communities +18 no SFHA communities
286 WV Communities
+ 8 split communities
294 Statistical Geographies
Notes: This map depicts the relationships between the local municipalities, counties, PDC regions and the state. 94% of WV communities have SFHAs

## Slide 7
268 Flood-Prone Communities
Region | # Counties | # Communities | Split Communities across County Boundary | Communities not participating in NFIP or no SFHA | # NFIP Communities1
Region 12 | 6 | 32 |  | Athens, Union | 30
Region 2 | 6 | 31 | Huntington |  | 31
Region 3 | 4 | 29 | Nitro |  | 29
Region 4 | 5 | 31 | Alderson, Montgomery, Smithers | Fayetteville3, Hillsboro, Lewisburg, Quinwood3, Thurmond | 26
Region 5 | 8 | 30 | Paden City | North Hills | 29
Region 6 | 6 | 45 |  | Brandonville, Tunnelton, White Hall | 42
Region 7 | 7 | 31 |  | Flatwoods | 30
Region 8 | 5 | 17 |  | Carpendale, Elk Garden | 15
Region 9 | 3 | 12 |  | Hedgesville | 11
Region 10 | 3 | 18 | Wheeling | Bethlehem, Clearview | 16
Region 11 | 2 | 10 | Weirton | Windsor Heights | 9
total | 55 | 286 | 8 | 18 | 268
1 Source: FEMA's Community Status Source Book 2 Region 1 dissolved community of Rhodell (Raleigh County) included in NFIP count. Town of Matoaka (Mercer County) is not included. 3 Communities include SFHA or non-regulatory floodplain |  |  |  |  | 
Split Communities Alderson, Montgomery and Smithers are members of Region 4
Split Community Paden City is a member of Region 5
Notes: 268 out of 286 WV Communities are flood-prone

## Slide 8
Statewide Flood Risk Assessment
Floodplain regulatory, advisory, and risk assessment products becoming available to the State and published on the WV Flood Tool
Community-level profiles are being generated that answer the questions
  what is at risk?
    what has been mitigated?
  what is the degree of risk?
The statewide vulnerability study quantifies the hazard risk
  Flood-prone communities can identify potential mitigation projects consistent with a community’s capabilities and goals
Notes: Context for the development of a statewide approach to FRA – New floodplain data available; Community-level profiles are being generated; Quantification, translation to Mitigation Actions

## Slide 9
Statewide Flood Risk Assessment
Support for…
  Local/State Hazard Mitigation Plans
  Floodplain Management Activities
  Community Rating System (CRS) Activities
  Community Assisted Visits
Flood Event Modeled
  Riverine 1% Annual Chance Flood Event for ALL Structures
    Regulatory and Non-Regulatory High Risk Flood Zones
    Estimate ~ 99,000 primary structures in West Virginia
  Riverine 0.2% Annual Event for Essential Facilities
Detailed Building Inventories
  User Defined Facilities Enhanced for spatial and attribute accuracy
    Key Reference Layers: parcels, assessment attributes, E-911 address points, leaf-off imagery, building footprints, community boundaries
  Flood Risk Assessment GIS (FRAGIS) Database
    State-level integration
    Identifies GIS Data Gaps or Deficiencies
Notes: HMGP Project Outcomes: Support for Local / Regional / State HMPs; FP Mgmt; CRS points; CAVs; RA keyed to 1% (0.2% for Essential Facilities); “User Defined Facilities” (not GBS) lead to a significant enhancement in accuracy and precision; FRAGIS DB integrated at state level with Gaps or Deficiencies identified

## Slide 10
WV Flood Risk Assessment
Statewide Depth Grid
  Composite Depth Grid of best available sources to include:
    Model-Backed HEC-RAS Depth Grids or Statewide 2010 Hazus Level-1 Depth Grid
Flood Model Software and Programs
  FEMA’s OpenHazus FAST (Flood Assessment Structure Tool) and other customized programming scripts.
  Most model outputs at the Building Level: Damage Loss, Debris Removal, Population Displacement
Outputs: Analytics / Reports / Publish Online
  Community and Building-Level Reports/GIS Files
  State GeoPlatform (WV Flood Tool - www.mapWV.gov/Flood)
  3D Flood Visualizations
Field Verification & Community Engagement
  Field verification of model inputs (building stock) and model outputs
  Iterative process of improving Flood Risk Assessment GIS
Notes: Inputs: Depth data, Current IAS Parcels; Tools: Modeling Software; Output GIS, Tabular and Narrative Reports published online – Flood Tool, Clearinghouse; Accuracy Improvements are achieved via Community Engagement

## Slide 11
Building-Level Flood Risk Assessments
DATA INPUTS
Flood Zones Depth Grids Building Stock
GIS Reference & Elevation Data
BUILDING INVENTORY & ACCURACY IMPROVEMENTS Building Location
Building Attributes
COMMUNITY ENGAGEMENT & FIELD ACCURACY CHECKS
Floodplain Managers
Local Govt. Officials
Methodology
Consistent methodology statewide
Semi-automated workflows
Continuous cycle to improve and update assessments
Building-Level Flood Risk Assessments support:
Hazard Mitigation Plans
Floodplain Management
Community Assisted Visits
Community Rating System
Benefits
More detailed and accurate assessments
Automated scripts generate outputs quickly
Cost savings through efficiencies
Helps multiple stakeholders
Comprehensive Building Risk Database
Building-Level Assessment Cycle (Flood-Risk Assessment GIS)
DATA OUTPUTS
Building Level Community Level
3D Visualizations
Published to WV Flood Tool
1
2
3
4
Tabular Output
Map Output
FAST
Notes: BLRA is expected to be an Iterative Process, with improvements realized at each phase due to new data or community feedback.

## Slide 12
Statewide Hazard Assessment
Building Inventory
Notes: Let’s take a deeper look into the statewide at-risk Building Inventory. BI was a major focus of this project.

## Slide 13
Site-Specific Building Inventories
BUILDING INVENTORY
Historical Flood Inundation / Flood Registry
NFIP Repetitive Loss (Internal Use Only)
HAZUS Flood Loss Estimates
Elevation Certificates
Flood Proof or Mitigated Structures
SFHA Building Counts
Levee/Dam Failure Inundation Studies
Building Inventories important for flood risk reduction activities
Notes: A precise and accurate BI benefits multiple flood risk reduction activities.

## Slide 14
301.a Definition of “Building”
2 or more exterior walls and a roof affixed to a site
Manufactured (mobile) home
Travel trailer without wheels
CRS Manual Page 300-4
Building Definition
Notes: The WVGISTC relied on guidance documents such as the FEMA CRS Manual to define variables and processes. For example, “What is a building?”

## Slide 15
“Not a Building”
Open pavilions, carports, underground pump stations, trailers, etc. are not buildings
Accessory structures are not counted
CRS Manual Page 300-5
Primary Structure: Not a Building
All primary structures in high-risk flood zones are inventoried.
Critical infrastructure in moderate-risk flood zones also inventoried.
Notes: Here are some examples of structures that are NOT considered buildings.

## Slide 16
Statewide Flood Risk Assessment
Building Inventory & Accuracy Improvements
Building Inventory Objectives
  Identify Primary Structures points
  Verify Building Identification
    E-911 Address
    Parcel geometry and assessment record
    Aerial and StreetView Images
    Building Sketches (parcel assessment record)
  Determine Building Characteristics (Occupancy Class, Cost, Basement, Foundation Type, Stories, Area, etc.)
    Default Characteristics derived from Assessment Records
    Overriding Modified Building Characteristics from user-defined values
  Ensure Building Point in most Restrictive Flood Zone
  Iterative Process and QC to make more accurate
Record Data Issues and Data Gaps
BUILDING INVENTORY & ACCURACY IMPROVEMENTS
Building Location
Building Attributes
Notes: BI Primary Structure point ID objectives were achieved using E911 addresses, parcel geometry and building sketches in the assessment record, as well as thinks like aerial and street-view imagery. Numerous characteristics were defined, such as Hazus Occupancy Class, Exposure (cost), Basement / Foundation, FFH, Stories; Conservative FP placement

## Slide 17
Building Identifier
Collect multiple spatial identifiers to verify location
Parcel | 01-08-0011-0069-0000
Address | 604 S Main St, Philippi, West Virginia, 26416
X,Y Coordinate | 39.144752, -80.033529
Share MAP URL Link | https://www.mapwv.gov/flood/map/?wkid=102100&x=-8909292&y=4742427&l=12&v=1
01 | - | 08 | - | 0011 | - | 0069 | - | 0000
County |  | District |  | Map |  | Parcel |  | Suffix
Building Identifier | 01-08-0011-0069-0000_604
Share Parcel Assessment URL Link | http://www.mapwv.gov/Assessment/Detail/?PID=01080011006900000000
Google Plus Code (11-digit) | 86FX4XV8+VHF
= Unique Identifiers
Notes: Owner Name from assessment records and Building Pictures (elevation certificates) can be helpful for property identification purposes
Proper Building and Property Identifiers are important for exchanging building-level data efficiently among local, state, and federal partners (including UDFs, LOMAs, Mitigated Buyout Properties, Elevation Certificates, Repetitive Loss Structures, etc.)
Notes: This simple but effective unique ID is at the heart of the BLRA

## Slide 18
Building Identification
Share Link: https://www.mapwv.gov/flood/map/?wkid=102100&x=-8909292&y=4742427&l=12&v=1
X,Y COORD.
ADDRESS
SHARE LINK
PARCEL
604 Main St, Philippi, WV 26416
0
Notes: In this capture of the WV Flood Tool we see the information associated with a specific building; All of these items will become part of the BI record for this structure. Note that this building has an Elevation Certificate associated with it.

## Slide 19
Building Inventory Outputs
Building Level GIS Files
Maps
Tables
Reports
Flood Tool Web Links
3D Flood Visualizations
Mitigation Action Recommendations
GIS Data Gap Reports
Flood Risk Assessment Outputs
GIS Risk Assessment Layers
Individual Building Assessment Tables
Notes: What do we do with our BI and RA results? This slide depicts the Building Level output products along with other outputs made possible by the analysis, including 3D Visualizations, Data Gap Reports, and Possible Mitigation Actions.

## Slide 20
Building Inventory
GIS Specialist conducting Building Inventory

## Slide 21
Critical Infrastructure
Essential Facilities
Community Assets
Religious Institution
National Register Structures
Utilities
Government Buildings
Notes: Certain structures are especially important for communities in the event of a disaster. Essential Facilities such as … and Community Assets are tagged in the BI process.

## Slide 22
Buckhannon, WV
Mitigated Properties
https://mapwv.gov/flood/map/?wkid=102100&x=-8929946&y=4721378&l=10&v=2
BUYOUT PROPERTY Parcel
MITIGATED STRUCTURE
Elevation Certificate
of Elevated Structure (Bldg. Diagrams 5-8)
Notes: Accurate damage estimates depend on having the correct information about a structure. First Floor Height is a prime example of this. A home that has been elevated so that the lowest living space is above the anticipated 1% annual chance flood will be at reduced risk of flood damage. Mitigated properties are shown in the WV Flood Tool.

## Slide 23
Mitigated Structure – EC Bldg. #5, #6
Building Diagram 5: Elevated Building with no Enclosure
Building Diagram 6: Elevated Building with Enclosure (using piers, piles, posts)
Partial Enclosure
Notes: The FEMA Elevation Certificate document includes Building Diagrams to compare with subject buildings in order to classify them and determine FFH. Here are two common methods of elevating structures.

## Slide 24
Mitigated Structure – EC Bldg. #7, #8
Building Diagram 5
Building Picture
Building Diagram 7: Elevated Building on Solid Foundation Walls (Full-Story)
Walkout Opening
Full-Story Enclosure
Building Diagram 8: Elevated Building with Crawlspace (Enclosure)
Crawlspace Enclosure
Notes: More methods for elevating buildings…

## Slide 25
Statewide Flood Risk Assessment
Model Data Inputs
GIS Reference Data
  Community Boundaries
  Parcels/Assessment Attributes (Building Stock)
  E-911 Addresses (Building Stock)
  Leaf-Off Aerial Imagery (Building Stock)
New Elevation Data
  Driver for Flood Studies (new flood zone boundaries)
  Depth Grids and WSEL Grids
  Ground Elevation: 1-ft contours, 1-m DEM
MODEL INPUTS
Flood Studies Depth Grids Building Stock
Notes: Input data sets for our risk assessment models include GIS boundary layers, parcels and assessment information and E-911 addresses. Aerial imagery is very important for verifying structures. New Lidar-based Elevation Data sets allow for finer resolution Depth and WSEL raster grids (1 m). Dropping 2010 Hazus depth as new studies arrive.

## Slide 26
Building-Level Flood Risk Assessments
DATA INPUTS
Flood Zones Depth Grids Building Stock
GIS Reference & Elevation Data
BUILDING INVENTORY & ACCURACY IMPROVEMENTS Building Location
Building Attributes
COMMUNITY ENGAGEMENT & FIELD ACCURACY CHECKS
Floodplain Managers
Local Govt. Officials
Methodology
Consistent methodology statewide
Semi-automated workflows
Continuous cycle to improve and update assessments
Building-Level Flood Risk Assessments support:
Hazard Mitigation Plans
Floodplain Management
Community Assisted Visits
Community Rating System
Benefits
More detailed and accurate assessments
Automated scripts generate outputs quickly
Cost savings through efficiencies
Helps multiple stakeholders
Comprehensive Building Risk Database
Building-Level Assessment Cycle (Flood-Risk Assessment GIS)
DATA OUTPUTS
Building Level Community Level
3D Visualizations
Published to WV Flood Tool
1
2
3
4
Tabular Output
Map Output
FAST
Notes: Referring back to the Building-Level Assessment Cycle, the Inputs include floodplain boundaries, depth grids and building stock (general); These inputs contribute to the BI, which is reviewed iteratively for visual and tabular accuracy. Outputs include detailed tables, community level aggregations and 3D visualizations. Community feedback refines results.

## Slide 27
Statewide Hazard Assessment
WV Flood Tool
Notes: I’d like provide some basic information now about the WV Flood Tool, and how we are using it to deliver the model outputs.

## Slide 28
(1) Flood Tool: Desktop Version https://www.mapwv.gov/flood
(2) Flood Tool: Mobile Version https://www.mapwv.gov/flood/mmap
Public resource applications that support floodplain management and flood reduction activities
WV Flood Tool
(3) Property Search and Assessment Report https://www.mapwv.gov/property
Query search on flood hazard zones and state assessment records
New development
Prior ownership
Web Parcel Report
Flood Tool: Desktop
Mobile
Notes: The WV Flood Tool first launched c. 2006 and has since undergone significant evolution. The desktop version functions down to the tablet screen size, while cell phones work best with the Mobile version. FT Queries link to Assessment info, and Assessment Reports include Flood Zone information and links to the FT. Several ways to get desired info.

## Slide 29
WV Flood Tool Views
Public View
Expert View
RiskMAP View
Quick Determination if IN or Out of Flood Zone
Floodplain Management and Permits, Disaster Assessments
Building-Specific Flood Risk Assessments
Notes: The FT has 3 primary “Views,” Public, Expert and RiskMAP. I will go a little more into each view in the next few slides.

## Slide 30
WV Flood Tool – Public View
Public View
https://www.mapwv.gov/flood/map/?v=0&pid=19-07-022B-0021-0000
Notes: The Public View has relatively simple cartography but retains the option to display reference layers, and places query results in the right panel, similary to Expert.

## Slide 31
WV Flood Tool – Expert View
Expert View
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
Notes: We find numerous additional Flood layers in the Expert View, along with a few additional lines in the query results panel (e.g. Depth, WSEL, Models).

## Slide 32
WV Flood Tool – RiskMAP View
RiskMAP View
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
Notes: The RiskMAP View is where we post risk assessment output data. Notice the “Risk” tab replaces the “Flood” tab. In addition to assessment and address information, there is now a link to flood Risk Assessment info in the results panel. Note the selected parcel boundary when the parcels Reference layer is on. View this location via the FT link at the bottom.

## Slide 33
WV Flood Tool – RiskMAP View
RiskMAP View
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
Notes: Here’s the Flood Risk Assessment information pop-up.

## Slide 34
Building Level Risk Symbology
Flood Zones
  Floodway
  Regulatory
  Non-Regulatory
Building Exposure
  Building Exposure ($) Community-wide
  Building Exposure ($) 100-YR Floodplains
Building Physical Damage
  Damage by Percent (%)
  Damage by Dollars ($)
Critical infrastructure
Dual Symbols: Property Class letters (R, F, C, I, A, U, X) combined with symbols. Also may contrast between building points that have been verified for accuracy and those that have not.
Notes: We use symbols to distinguish different flood zones and regulatory vs non-regulatory FPs. Additional symbols represent Building Exposure (risk) and expected damage by percentage and dollar amounts.

## Slide 35
Building Level Risk Symbology
WV Flood Tool (Risk MAP View)
Notes: Here is a more complete reference to the RiskMAP View layers and symbols. The Future Map symbols indicate expected changes with new studies. Use the remaining symbols to gather addition information about a subject property.

## Slide 36
Building Level Risk Symbology
High Risk Non-Regulatory
Preliminary Studies
Advisory A Zones
Updated AE Zones
Mapped Out of SFHA
Mapped IN SFHA
No Change
Regulatory Floodway
Notes: Letters indicate property type and the symbols show their status in regard to the floodplains present. High-Risk Non-Regulatory orange hachure fill floodplains may be hard to discern in the slide.

## Slide 37
Building –Future Map Condition
White Sulphur Springs
Mapped-In Draft Floodplain (Future SFHA)
Four Homes along Howard Creek with Total Building Value of $8.2 million mapped into new Draft Floodplain
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8942775&y=4547402&l=11&v=2
Notes: Building close to effective floodplain boundaries can have undesirable consequences. In this case, expensive homes will be mapped into the regulatory floodplain once the new draft study becomes effective.

## Slide 38
Building $ Exposure
White Sulphur Springs
Four Homes along Howard Creek with Total Building Value of $8.2 million mapped into new Draft Floodplain
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8942775&y=4547402&l=11&v=2
Notes: Here you see the Exposure symbols for the homes mentioned previously.

## Slide 39
Flood Risk Assessment
What’s Next
Notes: As we wind up the Building Inventory and Flood Risk Assessment phase of the project, let’s take a look at what happens next.

## Slide 40
Building Stock in Flood Zones
BUILDINGS IN SFHA
Estimate about 98,940
BUILDINGS IN REGULATORY ZONES
71,409(72%) Structures remains same
  7,760 structures in floodway
  63,649 in flood fringe
BUILDINGS IN NON-REGULATORY ZONES
13,621(13.7%) Structures potentially Mapped IN floodplain
BUILDINGS IN REGULATORY(NON) ZONES
13,909(14%) Structures potentially Mapped OUT of floodplain
Notes: Here are some statewide statistics to ponder. We estimate that there are about 98,940 buildings in the SFHA. 71% of already mapped-in structures remain unchanged. 13,621 structures are in non-regulatory flood zones and will be potentially mapped-in. Finally, 13,909 (14%) have the potential to be mapped out. A LOMA process may be required.

## Slide 41
Statewide Flood Risk Assessment
Community-Level Summary Reports
Notes: The WVGISTC will relay flood risk assessment information to communities through Community-Level Summary reports.

## Slide 42
WV RPDC Region | Address Count - SFHA | Address Count - Total | Residential | Farm | Commercial | Indistrial | Apartment | Utility | Tax Exempt | N/A
3 | 17519 | 22556 | 19062 | 128 | 226 | 2230 | 83 | 22 | 705 | 100
2 | 14952 | 19732 | 16190 | 34 | 555 | 1890 | 112 | 19 | 723 | 209
1 | 9118 | 13115 | 10489 | 3 | 233 | 1713 | 44 | 19 | 513 | 101
5 | 6401 | 7387 | 4744 | 40 | 1215 | 1101 | 21 | 7 | 218 | 41
4 | 4919 | 7161 | 5941 | 2 | 257 | 692 | 18 | 6 | 223 | 22
6 | 5504 | 7020 | 4965 | 27 | 683 | 1001 | 20 | 12 | 301 | 11
10 | 6393 | 6979 | 5137 | 118 | 311 | 1017 | 61 | 27 | 290 | 18
7 | 6017 | 6737 | 4810 | 16 | 499 | 1037 | 31 | 10 | 300 | 34
8 | 2863 | 4146 | 2687 | 0 | 679 | 521 | 24 | 6 | 184 | 45
9 | 2003 | 2464 | 1979 | 8 | 98 | 324 | 9 | 3 | 43 | 0
11 | 1461 | 1643 | 1189 | 12 | 6 | 326 | 12 | 0 | 96 | 2
Total | 77150 | 98940 | 77193 | 388 | 4762 | 11852 | 435 | 131 | 3596 | 583
Statewide Flood Risk Assessment
Region-Level Summary Primary Structure Summary*
Regions 3, 2 and 1 are top three regions with highest primary structures in SFHA
Region 3 - Putnam, Kanawha, Boone, Clay
Region 2 – Cabell, Lincoln, Wayne, Mingo
*Verification of tabular output ongoing
Notes: Statewide Summary Reports will include tabular information, such as address counts in the SFHA.

## Slide 43
WV RPDC Region | Mapped In | Mapped Out | Remains Same | Remains Same Floodway | Total Building Exposure Value | Total Building Loss Value
1 | 2,765 | 1,295 | 7,856 | 1,199 | $206,628,610,063 | $14,250,824,044
2 | 2,516 | 2,205 | 12,903 | 2,108 | $179,790,710,866 | $11,752,562,802
3 | 3,052 | 2,994 | 14,673 | 1,836 | 144,806,146,319 | 10,114,527,933
4 | 1,619 | 796 | 4,166 | 580 | 191,234,237,870 | 12,671,290,666
5 | 709 | 1,552 | 4,880 | 246 | $201,569,324,606 | $13,328,513,980
6 | 1,194 | 947 | 4,542 | 337 | $209,806,137,630 | $13,427,971,241
7 | 412 | 1,286 | 4,734 | 305 | $165,235,525,645 | $12,367,839,051
8 | 700 | 1,015 | 1,895 | 536 | $79,763,965,667 | $5,143,933,533
9 | 229 | 585 | 1,431 | 219 | $56,892,435,542 | $3,744,131,535
10 | 308 | 906 | 5,435 | 330 | $48,731,308,601 | $3,294,611,647
11 | 117 | 328 | 1,134 | 64 | $15,311,428,156 | $1,102,534,406
Statewide | 13,621 | 13,909 | 63,649 | 7,760 | $1,499,769,830,965 | $101,198,740,839
Statewide Flood Risk Assessment
Region-Level Future Map Condition Summary*
*Verification of tabular output ongoing
Region 3 - Putnam, Kanawha, Boone, Clay
Region 2 – Cabell, Lincoln, Wayne, Mingo
Notes: More Statewide results: Mapped-In, Mapped-Out, Unchanged, Floodway status table.

## Slide 44
Community Profile Dashboards
Story Maps of Flood Risk and Mitigation
Flood Risk
CRS Credits
Landslide Risk
http://mapwv.gov/flood/communities/?id=540285
WV Flood Tool Quick View of Bluefield
WV Flood Tool
Notes: Communities may access their Risk and CRS information by linking to their respective online dashboards. Visit the link at the bottom for an example of a flood story map.

## Slide 45
FEMA’s Community Rating System
Notes: Residents receive flood insurance premium discounts based on their community’s participation and measures above and beyond the minimum requirements. These activities are administered through FEMA’s Community Rating System or CRS. Several counties and individual municipalities currently participate in the CRS.

## Slide 46
Mitigation Actions
Identify Mitigation Actions derived from Risk Assessments
Slide courtesy of FEMA
Take sustained action to reduce or eliminate the long-term risk to human life and property from hazards
Communities can sustain action by building the capacity, knowledge, and understanding necessary to successfully advance action
Notes: Risk Assessment outputs strengthen Hazard Mitigation Plans and help communities prioritize mitigation efforts.

## Slide 47
Contact Information
  WV GIS Technical Center, West Virginia University Kurt Donaldson, GIS Manager kurt.donaldson@mail.wvu.edu, phone: (304) 293-9467 Maneesh Sharma, Project Lead
  Maneesh.Sharma@mail.wvu.edu, phone (304) 293-6694
  Eric Hopkins, GIS Analyst Eric.Hopkins@mail.wvu.edu, phone: (304) 293-9463

## Slide 48
Questions