## Slide 1
Flood Risk Analysis - Hazus
Hazus is a geographic information system-based natural hazard analysis tool developed and freely distributed by the Federal Emergency Management Agency (FEMA)

## Slide 2
Flood Risk Analysis

## Slide 3
301.a Definition of “Building”
2 or more exterior walls and a roof affixed to a site
Manufactured (mobile) home
Travel trailer without wheels
CRS Manual Page 300-4
Building Definition

## Slide 4
“Not a Building”
Open pavilions, carports, underground pump stations, trailers, etc. are not buildings
Accessory structures are not counted
CRS Manual Page 300-5
Not a Building

## Slide 5
Building Category
  Identify as a building or accessory structure
Flood-Risk Structure
  Is building footprint in floodplain?
  Does building point need to be pinpointed in floodplain?
Building Elevated
  Has structure been elevated? What is the estimated first floor height? View SteetView imagery.
Individual Building Value $$
  What is individual building value for multiple structures on a parcel. Review assessment records.
Bad Resource Data (imagery, parcels, addresses, etc.)
Validated by whom and when
Building Identification Questions

## Slide 6
Building Identification Resource Layers
Imagery
  Top Down (Best Leaf Off, 2018 NAIP, Commercial)
  Oblique
  Street View (Esri, Bing)
Parcels
  Property Lines
  Assessment Records (building identification, value, owner name, address)
Site Addresses
Building Footprints
Floodplain Boundaries
Resource Toolkit

## Slide 7
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9132529&y=4555837&l=13&v=1
Site address centroid not in the floodplain but building footprint is
Building Identification - Issues

## Slide 8
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9105243&y=4549177&l=12&v=1
2. Site point with no building in imagery
3. Site address accessory structures
Building Identification - Issues

## Slide 9
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9129149&y=4557222&l=12&v=1
4. Buildings in close proximity or under canopy combined into single building footprint
Building Identification - Issues

## Slide 10
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9129214&y=4557668&l=12&v=1
5. Building footprint but no building on the imagery
Building Identification - Issues

## Slide 11
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9130145&y=4557438&l=12&v=1
6. Building with no footprint
Building Identification - Issues

## Slide 12
Logan County Building Count
 | Logan Unincorporated | Logan Municipality | County Total
Building (Site Address) count | 5734 | 232 | 5966
Building Footprint count | 4678 | 247 | 4925
Average of Site and Footprint counts* | 5206 | 240 | 5446
*A visual check of random locations reveals that site address points overestimate and building footprints underestimate building counts (E.g.: Multiple site addresses in a single footprint, or missing footprints where buildings are observed in aerial imagery). So we take an average of the two values.
Table 1: Buildings in Floodplain (bSF) for Logan County, WV

## Slide 13
Jefferson County Mapping
Only Effective A Zone
Both Effective & Advisory A
Only Advisory A
Only Effective AE Zone
Both Effective & Updated AE
Only Updated AE
** PRODUCTS **
Updated AE Boundary
100-YR Depth Grid
Building Count and Floodplain Area comparisons for effective and non-regulatory (Advisory A/Updated AE) floodplains
Notes: Size we need

## Slide 14
Address: 427 S PRINCESS ST, Shepherdstown, WV, 25443
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8661318&y=4783197&l=10&v=1
Structures WITHIN Advisory Zone A ( ) but not Effective A
★
Building in Advisory A Zone and not Effective A Zone

## Slide 15
Address: 427 S PRINCESS ST, Shepherdstown, WV, 25443
https://binged.it/2kXqgfw
Structures WITHIN Advisory Zone A (Street View)
Building in Advisory A Zone and not Effective A Zone

## Slide 16
R
Advisory A Floodplain
Effective IN and Advisory A OUT
Both Effective
& Advisory
(No Change)
Advisory A Zones – Outreach Information
Union | Meaning | Building Changes | Area Changes | Percentage
No Change | IN both Effective and Advisory A | 163 | 3,289 Acres | 54.3%
Advisory A Only | Effective OUT and Advisory A IN | 46 | 242 Acres | 4%
Effective Only | Effective IN and Advisory A OUT | 156 | 2,531 Acres | 41.7%
Effective Regulatory Floodplain
Effective OUT and Advisory A IN
The geographic union of Effective and Advisory Floodplains generates a change polygon for flood risk analysis by area. Subsequently the union polygon can be intersected with site-specific structures to analyze the impact of the Advisory Floodplain changes to the Effective Regulatory Floodplain.
▲
★
●
▲
▲
▲
▲
★
●
★
Notes: intercept=erase

## Slide 17
Preliminary Building Counts
100-YR Flood (High Flood Risk) |  |  |  |  |  |  | 
 | (A) |  | (B) | (A+B) | (C) | (B+C) | (A+B)-(B+C)
FLOOD ZONE | ONLY Effective |  | BOTH Effective & Advisory A | SUM Effective | ONLY Advisory A | SUM Advisory A | Net
Approximate A Zone | 156 |  | 163 | 319 | 46 | 209 | 110
 | (A) |  | (B) | (A+B) | (C) | (B+C) | (A+B)-(B+C)
FLOOD ZONE | ONLY Effective |  | BOTH Effective & Update AE | SUM Effective | ONLY Updated AE | SUM Updated AE | Net
Detailed AE Zone | 229 |  | 122 | 351 | 16 | 138 | 213
500-YR Flood (Moderate Flood Risk) |  |  |  |  |  |  | 
500-YR |  |  |  | 45 |  |  | 
The flood at-risk buildings need to be verified 1) if they are primary or accessory structures; And 2) if on the edge of the flood zone
Jefferson County

## Slide 18
Primary building identification preview in Jefferson county
Jefferson County Pilot

## Slide 19
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8664125&y=4753054&l=12&v=1
Before
After
Jefferson County Pilot

## Slide 20
Jefferson County Pilot