## Slide 1: A Statewide Approach to Risk Studies Multi-Hazard Risk Assessment Proposal
Floods Risk (TEIF)
Reference Data Development
Hazard Mitigation Grant Project
Landslide Risk (TEAL)
Chart: 
| Flood Risk | Landslide Risk | Data Gap Services | Data Vendor Contracts | Professional Services
State HMGP Project | 697511 | 463332 | 385798 | 619509 | 85000
Identify Site-Specific At-Risk Structures
Statewide
Budget Breakdown
Notes: WV Map indicating population density

## Slide 2
Statewide Hazard Assessment
FEMA/WVDHSEM Hazard Mitigation Grant
Flood Risk Assessments (287 communities)
Landslide Assessments (55 counties)
GIS Data Development (parcels, addresses, imagery)
Technical support for (1) Local/State Hazard Mitigation Plans and for the (2) Community Rating System (CRS)
Site-specific building-level inventories for hazard exposure and loss estimates

## Slide 3
Multi-Agency Coordination
Federal Agencies
State Agencies
Universities
Regional Councils
Local Counties
Private Companies
11 Regional Planning & Development Councils
55 Counties
Hazard Mitigation Grant Proposal
287 communities

## Slide 4
Statewide Hazard Assessment
(1) Flood Risk Assessments

## Slide 5
Devastating 2016 June Flood

## Slide 6
2016 June Flood Report

## Slide 7
2016 June Flood Report
https://www.fema.gov/media-library/assets/documents/167736
Joint FEMA and USGS publication

## Slide 8
Flood Risk Assessment
Site-Specific Flood Risk Assessment Results published on WV Flood Tool (www.mapWV.gov/Flood)
Building-Level Flood Damage Methodology: Hazus Level-2 Flood Loss

## Slide 9
WV Flood Tool Views
Public View
Expert View
RiskMAP View
Quick Determination if IN or Out of Flood Zone
Used by Floodplain Managers to Identify Water Flood Heights
Building-Specific Flood Risk Assessments

## Slide 10
Flood Risk Structures of Martinsburg
The Risk MAP view allows for viewing flood loss estimates at the building or structure level for a 1%-annual-chance flood event.
Building Flood Loss Damage
57% of Residential Home Damaged at a Loss of $88,834
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8678481&y=4788856&l=11&v=2
Flood Risk Assessment Building Link
Flood Risk Building Info

## Slide 11
WV Flood Tool: Reporting Flood Risk
https://www.mapwv.gov/flood/map/?v=1&pid=02-06-0006-0048-0000
(1) Click on Parcel ID to open Parcel Tab
(2) Click on Parcel ID to link to Web Report

## Slide 12
Flood Tool: Assessment Report
http://www.mapwv.gov/Assessment/?PID=02060006004800000000
Detailed Property
Report

## Slide 13
Flood Tool: RiskMAP View
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8678412&y=4788996&l=11&v=2
Flood Risk Awareness & Mitigation Planning

## Slide 14
RiskMAP View – 3D Visualization
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8678412&y=4788996&l=11&v=2

## Slide 15
RiskMAP View – 3D Visualization
Flood Depth
Street View Image
HAZUS Loss Estimate
Building Exposure

## Slide 16
Flood Risk Analysis – Hazus
Hazus is a geographic information system-based natural hazard analysis tool developed and freely distributed by the Federal Emergency Management Agency (FEMA). The Hazus methodology is used to compute flood damage and loss estimates for buildings.

## Slide 17
Flood Risk – Berkeley Springs
Berkeley Springs
https://www.mapwv.gov/flood/map/?v=0&pid=33-03-002A-0032-0000
WV Flood Tool Application (www.mapWV.gov/flood)

## Slide 18
Building-Level Flood Damage
Water Damage Estimate

## Slide 19
Building-Level Flood Damage
Building Damage Estimate

## Slide 20
Building Flood Risk by Property Type
Berkeley Springs

## Slide 21
Building Flood Risk by % Damage
Berkeley Springs

## Slide 22
Flood Risk Assessment
Building Inventories

## Slide 23
Site-Specific Building Inventories
BUILDING INVENTORY
Historical Flood Inundation / Flood Registry
NFIP Repetitive Loss (Internal Use Only)
HAZUS Flood Loss Estimates
Elevation Certificates
Flood Proof or Mitigated Structures
SFHA Building Counts
Levee/Dam Failure Inundation Studies
Building Inventories important for flood reduction activities

## Slide 24
Statewide Flood Risk Structure File
Structure-specific (called “User-Defined Facilities”, or UDFs, in Hazus) flood risk assessments produce loss estimates at the building or structure level, and can often help facilitate flood risk discussions with individual home- or business-owners in a community. These types of risk assessments can provide valuable information to communities to help pre-screen properties and projects before going through a more in-depth Benefit-Cost Analysis (BCA). Personally-identifiable information (PII) such as property address, name of owner, etc. will not be included in FEMA's Flood Risk Assessment dataset (S_UDF_Pt and L_RA_UDF_Results). Source: Flood Risk Assessment Guidance - https://www.fema.gov/media-library-data/1469146645661-31ad3f73def7066084e7ac5bfa145949/Flood_Risk_Assessment_Guidance_May_2016.pdf
Various Flood Risk Reports by community, watershed, stream name, flood zones, etc. can be generated from the Flood Risk Assessment GIS (FRAGIS).

## Slide 25
301.a Definition of “Building”
2 or more exterior walls and a roof affixed to a site
Manufactured (mobile) home
Travel trailer without wheels
CRS Manual Page 300-4
Building Definition

## Slide 26
“Not a Building”
Open pavilions, carports, underground pump stations, trailers, etc. are not buildings
Accessory structures are not counted
CRS Manual Page 300-5
Not a Building

## Slide 27
Building Identification Resource Layers
Imagery
  Top Down (Best Leaf Off, 2018 NAIP, Commercial)
  Oblique
  Street View (Esri, Bing)
Parcels
  Property Lines
  Assessment Records (building identification, value, owner name, address)
Site Addresses
Building Footprints
Floodplain Boundaries
Building Identification Resources

## Slide 28
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9132529&y=4555837&l=13&v=1
Site address centroid not in the floodplain but building footprint is
Building Identification – Issue #1

## Slide 29
Preliminary Building Counts (bSF)
Preliminary Estimates reveal 100,000 structures in Special Flood Hazard Area

## Slide 30
Primary building identification preview in Jefferson county
Jefferson County Pilot

## Slide 31
Flood Risk Assessment
New Flood Zones

## Slide 32
Flood Zone Types
HIGH RISK (1% Annual Chance Event)
Regulatory – Special Flood Hazard Area (SFHA): Approximate A, Detailed AE
Non-Regulatory: Advisory A, Updated AE
MODERATE RISK
.2% Annual Chance Flood (500-YR Flood)
Within 75 feet of High Risk Flood Zone
LOW RISK
No Flood Hazard Identified

## Slide 33
Status # | Flood Risk Zone Designation | Message | Flood Degree Risk | Color Warning Status
1 | AE, AH (5), AO (2) | Location is WITHIN the FEMA 100-year floodplain. | High | Red
2 | AE (Floodway) | Location is WITHIN the FEMA 100-year floodplain and floodway. | High | Red
3 | A | Location is WITHIN the FEMA 100-year floodplain. | High | Red
4 | A (Advisory A) | Location is WITHIN the FEMA 100-year floodplain. Advisory Flood Heights available. | High | Red
5 | Updated AE Floodplain Boundary | Location is WITHIN an updated detailed floodplain boundary but NOT a FEMA 100-year effective floodplain. | High | Orange
6 | Advisory A | Location is WITHIN an advisory floodplain but NOT a FEMA 100-year effective floodplain. | High | Orange
7 | Shaded X | Location is WITHIN a moderate flood risk hazard such as a FEMA 500-year floodplain. | Moderate | Yellow
8 | Near Flood Zone | Location is NOT WITHIN identified flood hazard area, but within 75 feet of an identified flood hazard area. | Moderate | Yellow
9 | Out of Flood Zone | Location is NOT WITHIN any identified flood hazard area. Unmapped flood hazard areas may be present. | Low | Green
Flood Zone: < zone designation >
Three Degrees of Risk: High, Moderate, Low. Four Warning Status Colors: In 100-YR Effective Floodplains (red), Advisory A/Updated AE Floodplains (orange), moderate risk or close to high risk zones (yellow), low risk (green). Three Stacked Floodplain Boundary GIS Files: (1) 100-YR NFHL effective, (2) 100-YR Advisory A-Updated AE, (3) 500-YR NFHL Effective

## Slide 34
Flood Zone Determination Sequence
HIGH: 100-YR Effective Floodplain
HIGH: Advisory A or Updated AE Floodplain
MODERATE: 500-YR Effective Floodplain
MODERATE:
Within 75-ft of Flood Zone
LOW: Not in Flood Zone
Flood zone determination sequence important for programming logic
WV Flood Tool first checks query location for High Risk flood zones, then Moderate Risk flood zones.

## Slide 35
Flood Zone – Structure in Advisory A
Parcel ID: 33-01-0010-0033-0000
Structure is WITHIN an Advisory A Floodplain but NOT a FEMA 100-year effective floodplain. Parcel ID 33-01-0010-0033-0000 in Morgan County, WV.
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8698746&y=4815674&l=12&v=2

## Slide 36
Google Street View
Flood Zone – Structure in Advisory A
Parcel ID: 33-01-0010-0033-0000
http://www.mapwv.gov/Assessment/?PID=33010010003300000000
Flood Visualization
Web Parcel Report
Flood Zone Map

## Slide 37
Flood Zone – Updated AE
Parcel ID: 19-07-0018-0026-0000
http://www.mapwv.gov/flood/map/?v=1&pid=19-07-0018-0026-0000
Structure is WITHIN an Updated AE Floodplain Boundary but NOT a FEMA 100-year effective floodplain. Parcel ID 19-07-0018-0026-0000, Address: 288 OUR LN, Kearneysville, WV, 25430. Opequon Creek in Jefferson County, WV.

## Slide 38
Flood Zone – Updated AE
Parcel ID: 19-07-0018-0026-0000
http://www.mapwv.gov/Assessment/?PID=19070018002600000000
Flood Visualization
Web Parcel Report
Flood Zone Map
https://goo.gl/maps/AQACNLC4XD62
Google 3D View

## Slide 39
Flood Hazard Zones

## Slide 40
Flood Risk Assessment
New Flood Maps (Risk MAP Studies)
& Water Depth Grids (Risk Assessment)

## Slide 41
FEMA Flood Risk MAP Studies

## Slide 42
Model-Backed Depth Grids
Jefferson County: 162 stream miles of Approximate A Zones, 77 miles of Detailed Flood Zones
Advisory A Depth Grid (AECOM)
Depth Grid from Updated AE Floodplain Boundary (WVU)
Preliminary “Model-Backed” Depth Grid for 1% Annual Event Flood for all of Jefferson County
Depth grids derived from FEMA 2010 1-meter lidar elevation data
Water Depth important for 3D flood visualizations and flood risk building loss estimates
Communities receive CRS credit for published water depth grids
Jefferson County

## Slide 43
Flood Risk Assessment
Community Rating System

## Slide 44
FEMA’s Community Rating System

## Slide 45
Support for Community Rating System
Communities with CRS Participation Ranked by CRS Class |  |  | 
Community ID | Community | CRS Class | Flood Insurance Policies
540065 | Jeffereson County | 6 | 158
540282 | Berkeley County | 7 | 181
540226 | Hampshire County | 8 | 177
540199 | City of Buckhannon | 8 | 164
540194 | City of Parsons | 8 | 107
540004 | City of Phillipi | 8 | 78
540006 | City of Martinsburg | 8 | 21
540073 | City of Charleston | 9 | 389
540164 | Putnam County | 9 | 330
540144 | Morgan County | 9 | 131

## Slide 46
Statewide Hazard Assessment
(2) Landslide Risk Assessments

## Slide 47
Goals
Develop a landslide inventory
Create valid landslide models for specific WV regions
Generate county-level resolution landslide maps
Create an interactive web map application for displaying landslide models and landslide variables
Use the new landslide models and information to update the State Hazard Mitigation Plan
Did you know?
Landslides are the #2 Hazard in West Virginia
2015 Yeager Airport Slide
Landslide Risk Assessment

## Slide 48
www.mapWV.gov/Landslide
Landslide Incident Inventory

## Slide 49
Landslide susceptibility map showing generalized USGS map and detailed WVGISTC map
Landslide
Risks
Risk Assessment table showing building counts along with estimated replacement costs in landslide zones of concern
Buildings Exposed to Landslide Risks
Landslide Susceptibility Maps

## Slide 50
Statewide Hazard Assessment
(3) Spatial Data Development

## Slide 51
Spatial Data Layers
Parcels Site Addresses Aerial Imagery Elevation
State Spatial Data Infrastructure

## Slide 52
State-Level Integration
Parcels
Addresses
SOURCE: County Assessors
Property Tax Division
Statewide Master Parcel File / IAS
SOURCE: Local Addressing Offices
Division of Homeland Security & Emergency Management
Statewide Addressing & Mapping System
State-level integration allows for statewide mapping products and services
SOURCE: County Offices
WV GIS Technical Center
Statewide Leaf-Off Imagery Service
Imagery
SOURCE: Local, State, primarily FEMA
WV DEP WV GISTC
Statewide Elevation Web Services
Elevation

## Slide 53
Spatial Data Development
Parcels

## Slide 54
Statewide Digital Parcel File
599 Tax Districts
347 Districts
252 Corporations
Digital Parcel Sources
Assessor Offices
E-911 Offices
State Tax Department
Estimated $6 Million Value for Statewide Parcel File and Assessment Records

## Slide 55
West Virginia Parcel Property Class Breakdown for Tax Year 2017
Assessment Building Info
Code | Property Class | # of Parcels | Percent (%)
R | Residential | 1,164,470 | 79.61%
F | Farm | 121,384 | 8.30%
A | Apartment | 3,222 | 0.22%
C | Commercial | 65,784 | 4.50%
I | Industrial | 3,105 | 0.21%
X | Exempt | 97,773 | 6.68%
U | Utility | 192 | 0.01%
Other | Not classified | 6,837 | 0.47%
 |  | 1,462,767 | 100.00%
Assessment records are important for building inventories and are used to estimate the total building exposure ($) and building loss ($) for multi-hazards. Often building inventories and corresponding loss estimates are organized by property class.

## Slide 56
Residential or Farm Property
BUILDING INFORMATION | 
Property Class Type | R- Residential
Land Use | 101 - Residential 1 Family
Year Built | 1911
Architectural style | Conventional
Exterior Wall | Aluminum
Stories | 2
Total Rooms | 8
Building Grade | C
Basement Type | Full
Structure Area | 1,320
Building (card) Number | 1
# of main BLDGs (cards) | 1
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8899684&y=4811867&l=13&v=0
DESCRIPTION | 
GIS Parcel ID | 31-10-0029-0130-0000
Legal Description | BL 12-1/2 LOT 10
Acreage (deed) | 0.0373
Tax Year | 2015
Tax Class | 4
Deed Book / Page | 1259 / 45
PROPERTY OWNER(S) | 
Property Owner(s) | Smith John
APPRAISED VALUES | 
Land Appraisal | $33,200
Building Appraisal | $29,000
Total Appraisal | $62,200
Parcels link to Owner/Building Info
629 PENNSYLVANIA AVE, Morgantown, WV, 26501

## Slide 57
Commercial or Industrial Property
BUILDING INFORMATION | 
Property Class Type | C- Commercial
Land Use | 373 - Retail-Single Occupancy
Year Built | 1994
Stories | 2
Exterior Wall | Brick or Stone
Construction Type | Pre-Engineered Steel
Building Grade | D+
Basement Type | None
Business Living Area | 15,255
Cubic Feet | 292,380
Use Type | 34-Retail Store, 82- Multi-Use Office
https://www.mapwv.gov/flood/map/?v=0&pid=31-14-0031-0101-0000
DESCRIPTION | 84 Lumber
GIS Parcel ID | 31-14-0031-0101-0000
Legal Description | 5.0922 AC;SABRATON
Acreage (deed) | 5.09
Deed Book / Page | 1376 / 234
PROPERTY OWNER(S) | 
Property Owner(s) | SPIRIT SPE PORTFOLIO
APPRAISED VALUES | 
Land Appraisal | $378,800
Building Appraisal | $294,700
Total Appraisal | $673,500
Parcels link to Owner/Building Info
1501 DECKERS CREEK BLVD, Morgantown, West Virginia, 26505
COST VALUES | 
Other Bldg/Yard Values | $67,020
Commercial Value | $227,700

## Slide 58
GIS Digital Tax Conversion Status
Six counties need assistance with digital tax map conversion

## Slide 59
PAPER TAX MAP (static map)
DIGITAL TAX MAP
(interactive, seamless, aerial photo reference, map link to attributes (property info) and graphics (building sketch)
18 Colonial Drive, Ripley, WV
Parcel 04-29-45.5
Parcel
04-29-45.5

## Slide 60
What is in a Parcel Identifier
The GIS Parcel ID is a unique number that is the basis for identifying all parcels in West Virginia. The GIS Parcel ID consists of five elements: County code, District code, Map number, Parcel Prefix, and Parcel Suffix.
GIS Parcel ID: 31-05-0007-0031-0015
County | 31 (Monongalia County)
District | 05 (Clinton Tax District)
Map | 7
Parcel Prefix | 31
Parcel Suffix | 15
7-31.15

## Slide 61
Tax Mapping 2018
SB 588 New Revenue for Mapping

## Slide 62
Funding from WV Statute §59-1-10(8)
8) Of the fees collected pursuant to subdivision (1), subsection (a) of this section, $10 shall be deposited in the county general fund in accordance with section twenty-eight of this article, $5 shall be deposited in the county reappraisal fund and dedicated to the operation of the assessor’s office mapping division,
http://www.wvlegislature.gov/WVcode/ChapterEntire.cfm?chap=59&art=1&section=10
New $10 Deed Recording fee under SB 588, of which $5 portion for county assessor’s mapping office

## Slide 63
SB 588 Revenue Dedicated for Mapping Purposes
Based on revenue collected for the WV Courthouse Facilities Improvement Authority, it is possible to project that over $600,000 in revenue is being generated annually for the assessors’ mapping programs from the $5.00 portion of the fee. This is almost ten times the revenue generated under the old system.
Once FY17-18 is complete we will get the audited actual numbers!
Some members of the mapping community are concerned that the new SB 588 revenue will not be fully allocated by assessors for mapping resources.
Increased revenue should be directed towards mapping-related expenses, GIS hardware, map software, map maintenance, digital parcel conversion, web applications, aerial photography, etc.

## Slide 64
WV Property Viewer
Statewide Parcel Application and Web Services
  WV Property Viewer application (www.mapwv.gov/property)
  Online Tax PDF Maps
  Web Parcel Reports

## Slide 65
WV Property Viewer (Mobile)
Mobile Home Page
Toggle Layers of Interest
682 Killarney Drive, Morgantown, WV
www.mapwv.gov/property
Zoom to E-911 Address

## Slide 66
WV Property Viewer (Mobile)
Touch Parcel for More Info
Link to Detailed Report
682 Killarney Drive, Morgantown, WV
www.mapwv.gov/property
View Parcel Attributes

## Slide 67
WV Property Viewer - www.mapwv.gov/property
Developed in collaboration with WV Property Tax Division
Modelled after Tennessee Property Viewer
FEMA/State Hazard Mitigation is a business driver for identifying flood hazards. Serves as a gateway to WV Flood Tool.
Key Features:
  Statewide parcel attribute searches (e.g., owner name, acreage)
    www.mapwv.gov/assessment Integrated with E-911 Statewide Addressing & Mapping System
  General info on all properties (R, F, C, A, I, X, U)
  Counties/State Agencies can link to Statewide Parcel Web Services
    PDF Full-Version Tax Maps https://www.mapwv.gov/taxmaps/?m=31-15-0054 (County Code - District No. - Map ID)
    Web Parcel Reports – displays multiple records (e.g., structures)
      http://mapwv.gov/Assessment/?PID=28110039000100000000
Free property viewer for county offices with limited resources
Formal release with 2018 Tax Year data in September

## Slide 68
Spatial Data Development
E-911 Addresses

## Slide 69
Statewide E-911 Address & Mapping File
Property Identification for disaster assessments
Address Match Locators – Geocoding
Validate Parcel Addresses
Emergency Service Zone Boundaries
Other uses:
  Fire insurance rates
  Flood insurance discounts
  Broadband, emergency, hazard reduction, and transportation planning

## Slide 70
Statewide E-911 Addresses
Address Issues
Missing Address Site Numbers
Wrong Addresses (98 Graham St. should be 315 Graham St.)
Fairmont, WV
Elkins, WV

## Slide 71
Statewide E-911 Addresses
Missing Address Site Numbers
Berkeley Springs, WV

## Slide 72
WV Address Issues
 | Address Issues |  |  |  | Community Name
 | Missing Address Information |  |  |  | Boone County*(4) – Danville, Madison, Sylvester, Whitesville, Cabell County*, Calhoun County*, Gilmer County (2) – Glenville, Sand Fork, Grant County (1) – Petersburg, Lewis County*, Marion County*(6) – Barrackville, Fairmont, Farmington, Rivesville, White Hall, Worthington, McDowell County (1) – Bradshaw, Mingo County (1) – Williamson, Morgan County*(2) – Bath, Great Cacapon, Pleasants County (1) – Belmont, Pocahontas County*(3) – Durbin, Hilsboro, Marlinton, Putnam County (6) – Bancroft, Buffalo, Eleanor, Hurricane, Poca, Winfield, Summers County (1) – Bluestone, Tyler County (1) – Friendly, Wayne County*, Webster County*(3) – Addison, Camden-On-Gauley, Cowen, Wyoming County (1) - Mullens
 | Counties 9 |  |  |  | 
 | Municipalities 33 |  |  |  | 
 | Incorrect Address Information |  |  |  | Putnam County*
 | Counties 2 |  |  |  | Randolph County (1) – Elkins
 | Municipalities 3 |  |  |  | Roane County* (2) – Reedy, Spencer
 | Misaligned Addresses or Parcels |  |  |  | Hardy County* (1) – Moorefield
 | Counties 1 |  |  |  | Jefferson County (1) – Shepherdstown
 | Municipalities 3 |  |  |  | Randolph County (1) – Womelsdorf
* Address issues with the entire county

## Slide 73
Spatial Data Development
Leaf-Off Imagery

## Slide 74
Leaf-Off Aerial Imagery Web Service
2018 Mercer County Aerial Imagery
https://services.wvgis.wvu.edu/arcgis/rest/services/ImageryBaseMaps/wv_aerial_photos_mixed_resolutions_wm/MapServer?f=jsapi
32 Counties have provided leaf-off imagery for State Imagery Web Service

## Slide 75
Leaf-Off Imagery
60% of the counties have acquired leaf-off imagery since 2010
What is the cost?
$70 per square mile for aerial imagery
Ideally, leaf-off imagery should not be older than 5 years. Imagery is important for identifying at-risk structures and accurate disaster mapping.

## Slide 76
Leaf-Off Imagery Service
https://services.wvgis.wvu.edu/arcgis/rest/services/ImageryBaseMaps/wv_aerial_photos_mixed_resolutions_wm/MapServer?f=jsapi
2018 Jefferson County Aerial Imagery

## Slide 77
Spatial Data Development
Elevation

## Slide 78
Statewide Elevation Layers
Layer | Source | Coverage
SAMB | 2003 SAMB, 3-meter, 10-foot contours | Statewide
Lidar | Lidar, 2-foot or 1-foot contours | Select Areas
Elevation Grids, Hillshade Grids, Contours, used for Flood Depths, Imagery Orthorectification
SAMB ELEVATION
LIDAR ELEVATION
WV DEP SAMB-Lidar Hillshade

## Slide 79
High Resolution Elevation
New FEMA LiDAR Elevation Data is 10x better than 2003 Statewide Elevation Data Set
SAMB Elevation 10 FT Contours
FEMA LiDAR 1 FT Contours

## Slide 80
LiDAR-Based 1-FT Contours
Elevation data can be accessed through State Data Clearinghouse - www.mapwv.gov/lidar

## Slide 81
FEMA Purchased QL2 LiDAR

## Slide 82
Spatial Data Development
Public Lands

## Slide 83
Protected Areas Database (PAD-US)

## Slide 84
DATA LAYERS | Morgan | Berkeley | Jefferson
Assessment Data | 2018 | 2018 | 2018
Tax Parcels | 2018 | 2018 | 2018
E-911 Addresses | 2015 |  | 2018
Building Footprints (county source). 2018 BING Source. | None | 2008 | 2018
Aerial Imagery | 2010 | 2018 | 2018
Elevation LiDAR QL2 | 2016 | 2012 | 2012
Water Depth Grid | A Zone | A Zone | A and AE Zones
Data Gap Analysis

## Slide 85
Contact Information
  WVU GIS Technical Center Kurt Donaldson, GIS Manager kurt.donaldson@mail.wvu.edu, phone: (304) 293-9467 Eric Hopkins, GIS Analyst Eric.Hopkins@mail.wvu.edu, phone: (304) 293-9463 Maneesh Sharma, GIS Analyst
  Maneesh.Sharma@mail.wvu.edu, phone (304) 293-9466
  Kevin Kuhn, GIS Analyst
  kkuhn2@wvu.edu, phone (304) 293-9462