## Slide 1
WV Flood Tool Upgrades
Flood Query Results Panel
External Links
Shared Links
Parcel Search
Building-Specific Risk Assessments
3D Flood Visualizations
Mobile Enhancements
Improved Data Layers
  Flood Layers
  Advisory Floodplains
  Mitigated/Buyout Properties
  Local Data (parcels, addresses, imagery, elevation)
Other Enhancements
Future Statewide Coverage Goals
July 2017
www.mapWV.gov/Flood

## Slide 2
Flood Query Results Panel
Parcel ID Web Link: http://www.mapwv.gov/flood/Map/?v=1&pid=02-04-037M-0020-0000
256
Rodeo Dr.
# | Each Location Query Answers:
1 | In Flood Hazard Area? In Floodway?
2 | Stream name?
3 | Watershed name?
4 | FEMA Issued Flood Map?
5 | Floodplain Manager Contact?
6 | Flood Height value?
7 | Water Depth value?
8 | HEC-RAS Model available?
9 | Flood Profile available?
10 | In a CRS community?
11 | Coordinate x,y location?
12 | Ground elevation value?
13 | Street address location?
14 | Parcel ID location?
15 | Flood risk assessment info?
16 | 3D flood visualization?
15
14
16
13
11
12
10
9
8
7
6
5
4
3
2
1
Click Here

## Slide 3
External links launched from WV Flood Tool
New External Links
1
2
3
4
5
EXTERNAL WEB LINKS
Google Street View (address required)
Zillow.com (single address required)
View FEMA Flood Map (panel ID required)
Download FEMA Flood Map (panel ID)
(5) FEMA’s National Flood Hazard Layers (NFHL) web viewer (map extent and zoom level passed as parameters)
256 Rodeo Drive
Parcel ID Web Link: http://www.mapwv.gov/flood/Map/?v=1&pid=02-04-037M-0020-0000

## Slide 4
More Shared Links
Exchange flood info with others using various link types: (1) Map Click, (2) Map Center, (3) Parcel ID, (4) Address
Parcel ID Web Link: http://www.mapwv.gov/flood/Map/?v=1&pid=02-04-037M-0020-0000
256 Rodeo Drive
Share Link

## Slide 5
Parcel Search
Locate and zoom to parcels using various search parameters
Parcel Search for 256 Rodeo Drive
Search by:
Parcel Owner
Parcel Address
Parcel Number
256 Rodeo Drive
Parcel Search Results
IAS Parcel ID:
04 37M002000000000
GIS Parcel ID:
02-04-037M-0020-0000
Parcel Search

## Slide 6
Web Link: http://www.mapwv.gov/flood/Map/?v=1&pid=02-04-037M-0020-0000
Building-Specific Flood Risk Assessments (Currently only Berkeley & Morgan Counties)
The tax parcel centroids and associated building characteristic data (YRBLT, STYLE, STORIES, EXTWALL, GRADE, BSMT, AREASUM) from the Integrated Assessment System --along with RS Means construction cost values, flood inundation areas, and water depth inputs -- are used by Hazus Flood Model software to estimate flood damages to each structure for a riverine 1% annual flood event.
Click on Parcel ID (Building Info), Flood Risk Assessment, and 3D Flood Visualization links in bottom right of Flood Query Results Panel
256 Rodeo Drive

## Slide 7
Flood Risk Assessment (Cont.)
      Structure-specific (called “User-Defined Facilities”, or UDFs, in Hazus) flood risk assessments produce results and loss estimates at the building or structure level, and can often help facilitate flood risk discussions with individual home- or business-owners in a community. Source: “Guidance for Flood Risk Analysis and Mapping, Flood Risk Assessments”
Web Link: http://www.mapwv.gov/flood/Map/?v=1&pid=02-04-037M-0020-0000
Example flood risk assessment information for 256 Rodeo Drive. Includes 3D flood visualization with water depth-flood damage information for homeowner.

## Slide 8
3D Flood Visualizations
3D flood visualizations are available statewide for locations where flood depth grids exist. The parcel assessment data fields (land use, stories) are necessary to identify the correct property type: residential one- or two-story homes, mobile home, commercial/industrial, etc.
Mobile Home
      "The 3D visualization is really cool. Our citizen comes to the counter and says 'there is no way there can be a flood like that.' Then we show them how much water you will get in your house and how much it will cost to repair it. The 3d visual is really good! And then we like the way you can click on a parcel ID and it brings up all the information as far as property owner, tax map and parcel number, deed book, page number - everything is right there. And the building information is really good too because it tells what the structure is made of, whether it has a basement - all the information that we would have to go to another system to pull is right there.“ Source: 3D Flood Visualization Comment from Debbie Robinson, Kanawha County Planning and Development Office
Visualizations are easier for non-technical users to understand flood risks to their property in feet of water rather than comprehending the adjacent base flood elevation
Commercial
2-Story Home
1-Story Home

## Slide 9
3D Flood Visualizations
      “This is the coolest thing ever….thank you!!!”
      Source: 3D Flood Visualization Comment from Terri Jo Bennett, CFM, Upshur County Building Permit, Floodplain and Addressing and Mapping Coordinator
Brooke County
https://www.mapwv.gov/flood/map/?v=1&pid=05-07-W22P-0161-0000
1412 Charles St, Wellsburg, WV, 26070, Parcel ID: 05-07-W22P-0161-0000
Upshur County
https://www.mapwv.gov/flood/map/?v=0&pid=49-05-0003-0031-0000
673 Vicksburg RD, Buckhannon, WV, 26201, Parcel ID: 49-05-0003-0031-0000

## Slide 10
Mobile Application Enhancements
Added Floodway
Advisory Floodplain Notification
http://www.mapwv.gov/flood/mmap/

## Slide 11
Italics Text = New Layers Added * External Agency Web Map Services
New Flood Layers Added
FLOOD LAYERS | Public View for general public | Expert View for floodplain managers | RiskMAP View for flood risk planning
Flood Hazard Layers Flood Hazard Zones Panel Index X-Sections BFE’s / Advisory Flood Heights LOMAs / LOMRs* Structures, Levees, Mile Markers* | Yes No No No No No | Yes Yes Yes Yes Yes Yes | Yes No No No No No
Flood Prediction USGS Real-Time Stream Gages* | No | Yes | No
Flood Mitigation Mitigated/Buyout Properties | No | Yes | Yes
Flood Risk Flood Water Depths Historical High Water Marks Site-Specific Flood Risk Assessment Data Flood/Dam Inundation Maps (future) | No No No No | Yes Yes No No | Yes Yes Yes Yes

## Slide 12
New Flood Layers Added
NWIS
Stream Gage
Laurel Run
Levee
Example: Levee structure and real-time stream gage located at Parkersburg, WV
http://www.mapwv.gov/flood/Map/?wkid=102100&x=-9080275&y=4759882&l=8&v=1

## Slide 13
NWIS Stream Gage
Example: Real-Time Stream Gage Data for Dry Fork at Beartown, WV (Expert View) https://www.mapwv.gov/flood/map/?wkid=102100&x=-9104675&y=4491964&l=6&v=1
Beartown
Stream Gage

## Slide 14
New advisory flood heights, depth grids, and floodplain boundaries are being added to the WV Flood Tool and will exist for all counties in the near future
Advisory Floodplains
A new flood zone status (orange/mango color) has been added to the WV Flood Tool when the location is WITHIN an advisory floodplain but NOT a regulatory floodplain. In the example on the left note how a the Swanson Industries building is located in the new model-backed Advisory A Zone (blue water depth grid) but not the effective Approximate A Zone (red vertically hachured polygon). This example represents an Advisory A Zone but the same could be done for new Advisory AE Zones generated from re-delineated AE Non-Restudy areas using new topography.
Example: 437 Goshen Road, Morgantown, WV (Swanson Industries Plant)
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8903099&y=4798561&l=12&v=1
437 Goshen Road
Advisory A

## Slide 15
Redelineated Floodplain Using New Topo
Advisory AE Floodplain
Advisory AE Floodplain
Location: Clear Fork, Oceana, Wyoming County, WV
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9086441&y=4536103&l=9&v=1
Regulatory AE Floodplain
Oceana
Clear Fork
Advisory AE
Zone

## Slide 16
Advisory AE Depth Grid
Location: Clear Fork, Oceana, Wyoming County, WV
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9086441&y=4536103&l=9&v=1
Regulatory AE Floodplain
Oceana
Clear Fork
Advisory AE Water Depth
Advisory AE
Water Depth

## Slide 17
Advisory AE Determinations
Structures IN Regulatory AE Zone and OUT Advisory AE Zone
Advisory AE Zone
Regulatory AE Zone
Regulatory IN but Advisory OUT
What do you tell the public? Acquire an elevation certificate and use the advisory flood elevation to request a LOMA to amend the effective NFIP map.

## Slide 18
Advisory AE Determinations
Structures OUT Regulatory AE Zone and IN Advisory AE Zone
Advisory
AE Zone
Regulatory
AE Zone
Regulatory OUT but Advisory IN
What do you tell the public? Advisory information indicates a flood hazard area and will likely be incorporated into future effective NFIP maps. New development should not occur in Advisory Floodplains without a detailed study to show development reasonably safe from flooding. Recommend purchasing flood insurance for existing structures.

## Slide 19
Regulatory vs. Advisory Floodplains
Regulatory
Advisory
Integration
Required

## Slide 20
Mitigated/Buyout Properties
Example: 145 Riverbend Blvd, Saint Albans, WV (adjacent to Coal River)
House still visible in default imagery of WV Flood Tool and Google StreetView; however, in Google Maps oblique view the structure has been removed.
https://www.mapwv.gov/flood/map/?v=0&pid=20-16-012E-0125-0000
Address: 145 Riverbend Blvd
Parcel ID: 20-16-012E-0125-0000
WV
Flood Tool
Google Maps

## Slide 21
Improved Local Data Integration
Site Addresses Tax Parcels Aerial Imagery Elevation Contours
41
E-911 offices updated addresses to the Statewide Addressing & Mapping System which links to WV Flood Tool
30
county assessors have given permission to have parcels added to the WV Flood Tool
28
counties have submitted their more current aerial imagery to be included in the WV Flood Tool
3
counties have requested that their 2-foot elevation contours be displayed in the WV Flood Tool
County data reference layers are very important for flood determinations and flood risk products
Roane County

## Slide 22
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8899684&y=4811867&l=13&v=0
Parcels link to Owner/Building Info
Residential or Farm Property
629 PENNSYLVANIA AVE, Morgantown, WV, 26501

## Slide 23
Residential or Farm Property
BUILDING INFORMATION | 
Property Class Type | R- Residential
Land Use | 101 - Residential 1 Family
Year Built | 1911
Architectural style | Conventional
Exterior Wall | Aluminum
Stories | 2
Total Rooms | 8
Building Grade | C
Basement Type | Full
Structure Area | 1,320
Building (card) Number | 1
# of main BLDGs (cards) | 1
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8899684&y=4811867&l=13&v=0
DESCRIPTION | 
GIS Parcel ID | 31-10-0029-0130-0000
Legal Description | BL 12-1/2 LOT 10
Acreage (deed) | 0.0373
Tax Year | 2015
Tax Class | 4
Deed Book / Page | 1259 / 45
PROPERTY OWNER(S) | 
Property Owner(s) | Smith John
APPRAISED VALUES | 
Land Appraisal | $33,200
Building Appraisal | $29,000
Total Appraisal | $62,200
Parcels link to Owner/Building Info
629 PENNSYLVANIA AVE, Morgantown, WV, 26501

## Slide 24
Commercial or Industrial Property
BUILDING INFORMATION | 
Property Class Type | C- Commercial
Land Use | 373 - Retail-Single Occupancy
Year Built | 1994
Stories | 2
Exterior Wall | Brick or Stone
Construction Type | Pre-Engineered Steel
Building Grade | D+
Basement Type | None
Business Living Area | 15,255
Cubic Feet | 292,380
Use Type | 34-Retail Store, 82- Multi-Use Office
https://www.mapwv.gov/flood/map/?v=0&pid=31-14-0031-0101-0000
DESCRIPTION | 84 Lumber
GIS Parcel ID | 31-14-0031-0101-0000
Legal Description | 5.0922 AC;SABRATON
Acreage (deed) | 5.09
Deed Book / Page | 1376 / 234
PROPERTY OWNER(S) | 
Property Owner(s) | SPIRIT SPE PORTFOLIO
APPRAISED VALUES | 
Land Appraisal | $378,800
Building Appraisal | $294,700
Total Appraisal | $673,500
Parcels link to Owner/Building Info
1501 DECKERS CREEK BLVD, Morgantown, West Virginia, 26505
COST VALUES | 
Other Bldg/Yard Values | $67,020
Commercial Value | $227,700

## Slide 25
West Virginia Parcel Property Class Breakdown for Tax Year 2017
Assessment Building Info
Code | Property Class | # of Parcels | Percent (%)
R | Residential | 1,164,470 | 79.61%
F | Farm | 121,384 | 8.30%
A | Apartment | 3,222 | 0.22%
C | Commercial | 65,784 | 4.50%
I | Industrial | 3,105 | 0.21%
X | Exempt | 97,773 | 6.68%
U | Utility | 192 | 0.01%
Other | Not classified | 6,837 | 0.47%
 |  | 1,462,767 | 100.00%
Assessment records are important for building inventories and are used to estimate the total building exposure ($) and building loss ($) for multi-hazards. Often building inventories and corresponding loss estimates are organized by property class.

## Slide 26
Addresses Link to Parcels
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8901769&y=4816526&l=13&v=0
Site Address Match
Parcel Building Info
Multi-Unit Addresses
3
2
1
3
2
1

## Slide 27
Statewide Digital Parcel File
606 Tax Districts
5% or 33 tax districts have incomplete or no digital parcel boundaries
Digital Parcel Sources
Assessor Offices
E-911 Offices
State Tax Department

## Slide 28
Statewide Digital Parcel File
High Priority
of
2013 State Hazard Mitigation Plan

## Slide 29
Statewide Digital Parcel File
# | Missing/ Obsolete Data Parcels
1 | Boone
2 | Braxton
3 | Calhoun
4 | Clay
5 | Jackson
6 | Logan
7 | McDowell
8 | Roane
9 | Tucker
10 | Tyler
11 | Wirt
12 | Wyoming
Cost estimate of $250K to achieve a current and accurate Digital Parcel Boundary file
What is the cost for parcel conversion?
$3.00 per parcel

## Slide 30
Statewide Digital Parcel File
# | Missing/ Obsolete Data Parcels
1 | Boone
2 | Braxton
3 | Calhoun
4 | Clay
5 | Jackson
6 | Logan
7 | McDowell
8 | Roane
9 | Tucker
10 | Tyler
11 | Wirt
12 | Wyoming
Estimated mapping cost of $250K to achieve a current and accurate Digital Parcel Boundary file
SB 588 – As of July 5 will cost about $25 instead of $165,000 to acquire Statewide Parcel File

## Slide 31
Counties using GIS

## Slide 32
Paper to Digital Tax Maps
MANUAL (Paper) TRANSITION DIGITAL
Mapper: “I was apprehensive four years ago when our newly elected assessor decided to digitize our parcel mapping system; but with the work done by the mapping contractor then and their continual assistance today, I cannot imagine returning to the manual system.” Source: 2017 Tax Map Survey
Manual drafting of tax maps is becoming obsolete!!!
There are no schools that teach manual drafting skills
Manual drafting supplies are becoming scarce
Tax Division may remove itself from drafting contract services
5 counties 7 counties 43 counties

## Slide 33
Statewide Digital Parcel File
606 Tax Districts
5% or 33 tax districts have incomplete or no digital parcel boundaries
Digital Parcel Sources
Assessor Offices
E-911 Offices
State Tax Department

## Slide 34
Parcels in WV Flood Tool
Contact your assessor about including parcels in WV Flood Tool

## Slide 35
Aerial Imagery
55% of the counties have acquired leaf-off imagery since 2010
Ideally, leaf-off imagery should not be older than 5 years. Imagery is important for identifying at-risk structures and accurate disaster mapping.
What is the cost?
$70 per square mile for aerial imagery

## Slide 36
Leaf-Off Aerial Imagery Web Service
2017 Monongalia County Aerial Imagery
https://services.wvgis.wvu.edu/arcgis/rest/services/ImageryBaseMaps/wv_aerial_photos_mixed_resolutions_wm/MapServer?f=jsapi
28 Counties have provided leaf-off imagery for State Imagery Web Service

## Slide 37
Aerial Imagery Costs
Currentness
Yellow highlighted counties indicates imagery older than 5 years.
Resolution
6-inch resolution or better
Leaf-Off
WV 3rd most forested state (78% forested)
Funding Sources
Assessor Valuation or County Commission Funds

## Slide 38
State-Level Integration
Parcels
55 County Assessor Offices
WV Tax Department
Master Surface File & Assessment Records
Local Level
55 County E-911 Offices
WV Division of Homeland Security & Emergency Management
Statewide Addressing & Mapping System
Various Local & Regional Sources
WV GIS Technical Center
Statewide Imagery Web Service
State Level
State Product
Addresses
Imagery

## Slide 39
Other Enhancements Accomplished
  Added Leaf-on USDA NAIP 2016 Statewide Imagery & WV DEP Hillshade
  Best Leaf-Off imagery updated with aerial imagery from 28 counties
  Parcels added for 30 counties, with 3 counties pledged by end of summer
  Added Tug Fork Detailed Restudy
  Improved Parcel ID Search tool
  Embedded FloodSmart.gov Cost Calculator (currently out of service due to security breach)
  Link to National Weather Service Advanced Hydrologic Prediction Service (AHPS)
  Links to Flood Smart and Flood Risk Documents
  Updated WV Address Locator Services
  Re-programmed toolbar icons for restrictive settings on federal IE web browsers
  Improved drawing and text markup tools
  Update contact list of Floodplain Managers
  Update statewide mitigated buyout properties flood layer
  Added floodway to mobile application, updated data layers, services, flood queries
  Added nearly 1.5 million assessor attribute records for Tax Year 2017 to include building specific information for commercial/industrial/apartment properties
Future Enhancements
  Add Upper Mon. Detailed Restudy (includes BFE grid)
  Add new advisory floodplains and depth grids for A and AE Zones
  Update statewide elevation grid with new lidar acquisitions
  Acquire digital parcel and addressing layers for all counties
  Add flood risk assessments and products for all counties
  Improve building and essential facility inventories for risk planning
  Incorporate 3D flood visualization models of communities (requires building footprints)
  Add Historical Flood Inundation and Dam Break Inundation maps from external sources
  Reclassify statewide water depth grid
Other & Future Enhancements

## Slide 40
Clear Browser Cache
Remember to clear browser cache to access all the current information and updates of Flood Tool
Step 1
  Press [Control]+[F5] on the keyboard. This is a FORCED refresh.
Step 2
  This process is more complicated. To do it thoroughly follow these steps.
    close all browser windows
    open a single browser
    go to [Tools] on the top menu
    select [Internet Options]
  You will get a dialog box similar to the one shown below.
  Press the [Delete Files] button. This should clear all the files in your browser cache.

## Slide 41
Statewide Coverage Goals
In 2 years…
  Advisory Flood Heights (AFH) for Approximate A Zones and model Ordinance
In 3 years…
  Building-Specific Inventories
  Site-Specific Flood Risk Assessments
  Statewide Parcel File
  Composite Depth Grid
    Restudies
    Advisory A & AE Zones

## Slide 42
Technical Questions about Tool?
WVU GIS Technical Center
Eric Hopkins eric.hopkins@mail.wvu.edu, phone: 304-293-9463
Kurt Donaldson kurt.donaldson@mail.wvu.edu, phone: 304-293-9467