## Slide 1
Goal 4: Statewide Depth Grid
Depth grids are important for (1) water depth visualization in the WV Flood Tool and for (2) estimating building damage costs using Hazus-MH flood loss software. Its is preferred to use more accurate depth grids from various sources than a generalized depth grid from the Hazus Enhanced Quick Look tool.
Depth Grid Sources
  Risk MAP Studies (HEC-RAS hydraulic models)
  Model-Backed Zone A Studies (HEC-RAS hydraulic models)
  FIS X-Sections to Water Elevation Conversion (no models)
    Water surface elevations derived from x-sections of detailed flood studies

## Slide 2: Depth Grids (Regulatory versus Planning)
Regulatory | Planning
Risk MAP Studies (Upper Mon, Tug Fork, etc.) | Hazus Enhanced Quick Look Tool
Advisory Flood Heights (Model-backed A Studies) | Statewide Hazus Level 1
FIS X-Sections(???????) Conversion | FIS X-Sections(???????) Conversion
Questions:
Is Region III interested in creating a uniform statewide depth grid for regulatory flood determinations from multiple sources that is consistent across flood hazard zones (AE, A, etc.) and matches with the official flood zone boundaries?
What about depth grids from FIS X-Sections to Water Elevation Conversion? Is this endeavor worthwhile? Should it be shown in the regulatory (Expert View) or planning (RiskMAP) view of the WV Flood Tool?

## Slide 3
Risk MAP Study Depth Grid (model based)
Model-Backed A Zone Depth Grid
Depth Grid generated from
FIS x-sections
Depth Grid Sources

## Slide 4: Tracking Flood Risk Products in GIS - Depth Grids – 1% Annual Chance
Courtesy of Lee Brancheau, FEMA Region III
Did you know?
A million dollars has been dedicated for Model-Backed A Zone Depth Grids in West Virginia

## Slide 5
Building Damage Loss Estimates $$$
197 Rodeo Dr.
197 Rodeo Dr.

## Slide 6
Parcel/Address Identity Info
County ID | 2 (Berkeley)
Parcel ID | 04037M001300000000
Street Address | 197 Rodeo Drive
City | Martinsburg
Zip Code | 25403
Deed or GIS Acreage | 2.3 Acres
Legal Description | LOT 13 SOUTH SEC PHASE II
Property Owner(s) | XXXXXXXXXXXXXXXX
CAMA
Assessment Data
Land Appraisal | 55,100
Building Appraisal | 321,700
Total Appraisal | 376,800
CAMA Building
Data
Tax Year | 2015
Tax Card | 1
Tax Class | 2
Land Use Code | 101
STORIES | 2
Exterior Wall – Construction Type | 7
Style | 8
Year Built | 2010
Total Rooms | 8
AREASUM | 3,981
GRADE – Building Condition | A-
Basement – Foundation Type & First Floor Height | 4
DWELVAL | 398,400
OBYVAL | 8,450
COMVAL | 0
Exposure/
Replacement Cost (BI)
ReplCost | 506,940
ContCost | 603,075
BldgArea | 3,981
hzOccCode | Res1
NumStories | 2
YearBuilt | 2010
BldgConstruction | Brick
BldgCondition | High
BldgFoundation | Basement
FirstFloorHt | 4
Damage Estimates (UDF)
BldgDmgPct | 51.6
BldgLossUSD | 261,354
ContDmgPct | 47.9
ContLossUSD | 121,326
A unique parcel identifier links assessment/building data, replacement costs, and damage loss estimates for each structure

## Slide 7
One-Story Home Two-Story Duplex High Rise Apartment
0 Feet
WATER DEPTH
12 Feet
4 Feet
Courtesy of Pinellas County Emergency Management, Florida (http://egis.pinellascounty.org/apps/stormsurgeprotector/index.html)
3D Flood Visualization – Individual Structures
Notes: Duplex 0 3/4/5 11/13
Apartment Building
Hotel

## Slide 8
1% Flood Impact, 11-ft. Water Depth
3D Flood Visualization of Structure at
197 Rodeo Drive
WV Flood Tool Conceptual Slide

## Slide 9
3D
3D Flood Visualization – Neighborhood
3D Northwest View
Baltimore Street, Martinsburg, WV
WV Flood Tool Conceptual Slide