## Slide 1: A Statewide Approach to Risk Studies WVU Multi-Hazard Risk Assessment Proposal
Kurt Donaldson & Eric Hopkins
WV GIS Technical Center
West Virginia University
27 October 2016
Technical Support to Local Natural Hazard Mitigation Planning for Flood, Landslide, and Dam/Levee Failure
Floods
Dam / Levee Failures
Landslides
Notes: WV Map indicating population density

## Slide 2
PROJECT OVERVIEW
Risk Assessments for Local Hazard Mitigation Plans (55 Counties)
  Riverine 1% Annual Chance Flood
  Dam/Levee Failure (led by USACE)
  Landslides
Detailed Building Inventories (State-Level Integration)
  GIS Parcels – 55 county assessor GIS parcel files standardized and integrated
  Centralized CAMA/Assessment Records for building characteristics
  GIS Addresses – WV DHSEM Statewide Addressing & Mapping System
Risk Assessments Published on State/Federal GeoPlatforms
  State GeoPlatform (WV Flood Tool - www.mapWV.gov/Flood)
  Federal GeoPlatform (www.geoplatform.gov)
Preliminary Proposal Accepted by State Hazard Mitigation Office
  Funding proposed through Hazard Mitigation Grant Program (HMGP)

## Slide 3
PROJECT HISTORY
2014 | Project concept initiated by Cynthia McCoy, FEMA Region III
2015 | West Virginia selected by FEMA for Building Inventory Tool pilot
2015 | The Polis Center at IUPUI Completes Project Workflow for Hazus-MH Model Building Inventory for West Virginia
2016 | Flood and Landslide Risk Assessment studies completed for pilot county
2016 | Preliminary proposal accepted by State Hazard Mitigation Office for state technical support services to regional and local governments for Local Hazard Mitigation Plans

## Slide 4
Multi-Agency Coordination
Risk Assessment Lifecycle
Goal 1: Communication and Training Network
Establish a communication and training network for exchanging risk assessment information and technical skills among local, state, federal, and other entities.

## Slide 5
Risk
Assessment Lifecycle
Diagram courtesy of Cynthia McCoy, FEMA Region X
Start Early - Best Practice!
Local Hazard Mitigation Plan updates should begin a minimum of one year in advance, preferably two years before the expiration date

## Slide 6
Multi-Agency Coordination
Federal Agencies
State Agencies
Universities
Regional Councils
Local Counties
Private Companies
11 Regional Planning & Development Councils
55 Counties

## Slide 7
Best Available Risk Assessment Data
Historical Flood Data
Online Map Validation Tools
Goal 2: Exchange Best Available Data
Exchange the best available risk assessment data among local, state, and federal GeoPlatforms. Incorporate historical flood data into risk assessment studies. Use online map validation tools for local communities to validate risk assessment data.

## Slide 8
Best Available Site-Specific Data
Parcel/Assessment/Address Spatial Database
GIS Parcels
GIS Addresses
CAMA Records
What is the “sweet spot” for comprehensive information about structures and ownership?
Answer: Statewide integration of multiple data sources, especially (1) parcels, (2) CAMA assessment records, and (3) E-911 addresses

## Slide 9
External Map Links
Local Data Sources
CAMA
BLDG
INFO
GEOCODE ADDRESS
OWNER
INFO
GIS PARCEL
GIS ADDRESS
CAMA Assessment
GEOCODE ADDRESS
GIS ADDRESS
GIS PARCEL
GOOGLE MAP LINK
GOOGLE MAP LINK
197 Rodeo Drive, Martinsburg, WV
2016 AERIAL PHOTOS
AERIAL PHOTOS
FEMA MAP LINK
FEMA MAP LINK
WV Flood Tool Beta
Seamless Data Integration

## Slide 10
Goal 3: Statewide Building Inventories
Create a statewide inventory of all buildings and facilities exposed (with replacement costs) in flood hazard, dam/levee failure, and landslide susceptibility zones.

## Slide 11
Building Inventory
(site specific)
GBS (aggregate buildings)
UDF (individual buildings)
Hazus GBS and UDF Inventory Data. The General Building Stock (aggregate buildings) and User Defined Facilities (individual buildings) are derived from the Building Inventory.
Work Flow for Building Inventory & Flood Risk Assessments
Building
Inventory

## Slide 12
Building Inventory Exposure ($) for Multi-Hazards

## Slide 13
Goal 4: Statewide Depth Grid
Depth grids are important for (1) water depth visualization in the WV Flood Tool and for (2) estimating building damage costs using Hazus-MH flood loss software. Its is preferred to use more accurate depth grids from various sources than a generalized depth grid from the Hazus Enhanced Quick Look tool.
Depth Grid Sources
  Risk MAP Studies (HEC-RAS hydraulic models)
  Model-Backed Zone A Studies (HEC-RAS hydraulic models)
  FIS X-Sections to Water Elevation Conversion (no models)
    Water surface elevations derived from x-sections of detailed flood studies

## Slide 14
Risk MAP Study Depth Grid (model based)
Model-Backed A Zone Depth Grid
Depth Grid generated from
FIS x-sections
Depth Grid Sources

## Slide 15: Tracking Flood Risk Products in GIS - Depth Grids – 1% Annual Chance
Courtesy of Lee Brancheau, FEMA Region III
Did you know?
A million dollars has been dedicated for Model-Backed A Zone Depth Grids in West Virginia

## Slide 16
Goal 5: County-Level Risk Assessments
Perform county-level risk assessments for 55 counties using site-site specific building inventories.
Riverine Floods (1% Annual Chance)
Dam/Levee Failure
Landslides

## Slide 17: Devastating 2016 June Flood

## Slide 18
Building Damage Loss Estimates $$$
197 Rodeo Dr.
197 Rodeo Dr.

## Slide 19
Debris Generated
Shelters Needed

## Slide 20
Dam/Levee Failure Risk Assessment
Goals
Prioritize dam inspections in accordance with risk and those that do not have an EAP digitized
Integrate Dam and Levee safety action class (class 1 - 5) for every USACE dam and levee into HIRA and THIRA.
Produce documentaries about/on aging dam structures around endangered communities (Develop a list of potential dams on which to focus).
Create a task force to address levee safety in West Virginia (Coordination between NRCS and USACE on levee safety issues).
Bluestone Dam
In recent years, it was discovered that Bluestone Dam would be unable to pass the Probable Maximum Flood possible at the site, which could cause failure of the dam. To remedy the problem, the U.S. Army Corps of Engineers has undertaken a Dam Safety Assurance program for Bluestone.

## Slide 21
Dam/Levee Failure – USACE Technical Lead
Joe Trimboli MSc CFM
U.S. Army Corps of Engineers
Silver Jackets WV Liaison http://wvsj.us/

## Slide 22
Landslide Risk Assessment
Goals
Develop a landslide inventory
Create valid landslide models for specific WV regions
Generate county-level resolution landslide maps
Create an interactive web map application for displaying landslide models and landslide variables
Use the new landslide models and information to update the State Hazard Mitigation Plan
Did you know?
Landslides are the #2 Hazard in West Virginia
2015 Yeager Airport Slide

## Slide 23
Landslide susceptibility map showing generalized USGS map and detailed WVGISTC map
Landslide
Risks
Risk Assessment table showing building counts along with estimated replacement costs in landslide zones of concern
Buildings Exposed to Landslide Risks

## Slide 24
Goal 6: Identify Data Gaps
Review and identify data gaps for key GIS data layers for risk assessment studies (parcels, addresses, imagery, elevation, flood layers, critical infrastructure, etc.).
Provide recommendations to the appropriate organizations to improve data management and governance.

## Slide 25
Data Gap Analysis for Region 9 Counties located in the Eastern Panhandle of West Virginia
Data Gap Analysis

## Slide 26
Goal 7: Publish Risk Assessment Reports
Publish supplemental risk assessment reports for local and state hazard mitigation plans.

## Slide 27
Goal 8: Publish Model Data
Publish input and output model data associated with risk assessments on state and federal GeoPlatforms.
FEMA and USACE GeoPlatforms
State GeoPlatforms
  WV Flood Tool
  State Data Clearinghouse

## Slide 28
More detailed flood risk assessments from local mitigation plans can be vertically integrated to state and federal GeoPlatforms.
FEMA’s Total Exposure in Floodplain (TEIF)
http://bit.ly/1r1vRBg
Courtesy of Lee Brancheau, FEMA Region III

## Slide 29
Goal 9: RiskMAP View of WV Flood tool
Upload 2D/3D flood risk and dam failure maps to the RiskMAP View of the WV Flood Tool (www.mapWV.gov/Flood).
Provide a web planning tool to estimate physical building damage, debris removal, and temporary shelter needs.
This flood risk assessment information permits communities or individual property owners to decide how to allocate resources for the most effective and efficient response and recovery, and to prioritize mitigation measures to reduce future loss.

## Slide 30
Total Assets Exposed
Building Damage
Debris Removal
Shelters Needed
RiskMAP View: Hazus Level 2 Data
Update RiskMAP View with more detailed Hazus Level 2 “User Modified” Data for Building Damage Estimates, Debris Removal, and Shelter Needs

## Slide 31
One-Story Home Two-Story Duplex High Rise Apartment
0 Feet
WATER DEPTH
12 Feet
4 Feet
Courtesy of Pinellas County Emergency Management, Florida (http://egis.pinellascounty.org/apps/stormsurgeprotector/index.html)
3D Flood Visualization – Individual Structures
Notes: Duplex 0 3/4/5 11/13
Apartment Building
Hotel

## Slide 32
1% Flood Impact, 11-ft. Water Depth
3D Flood Visualization of Structure at
197 Rodeo Drive
WV Flood Tool Conceptual Slide

## Slide 33
Parcel/Address Identity Info
County ID | 2 (Berkeley)
Parcel ID | 04037M001300000000
Street Address | 197 Rodeo Drive
City | Martinsburg
Zip Code | 25403
Deed or GIS Acreage | 2.3 Acres
Legal Description | LOT 13 SOUTH SEC PHASE II
Property Owner(s) | XXXXXXXXXXXXXXXX
CAMA
Assessment Data
Land Appraisal | 55,100
Building Appraisal | 321,700
Total Appraisal | 376,800
CAMA Building
Data
Tax Year | 2015
Tax Card | 1
Tax Class | 2
Land Use Code | 101
STORIES | 2
Exterior Wall – Construction Type | 7
Style | 8
Year Built | 2010
Total Rooms | 8
AREASUM | 3,981
GRADE – Building Condition | A-
Basement – Foundation Type & First Floor Height | 4
DWELVAL | 398,400
OBYVAL | 8,450
COMVAL | 0
Exposure/
Replacement Cost (BI)
ReplCost | 506,940
ContCost | 603,075
BldgArea | 3,981
hzOccCode | Res1
NumStories | 2
YearBuilt | 2010
BldgConstruction | Brick
BldgCondition | High
BldgFoundation | Basement
FirstFloorHt | 4
Damage Estimates (UDF)
BldgDmgPct | 51.6
BldgLossUSD | 261,354
ContDmgPct | 47.9
ContLossUSD | 121,326
A unique parcel identifier links assessment/building data, replacement costs, and damage loss estimates for each structure

## Slide 34
3D
3D Flood Visualization – Neighborhood
3D Northwest View
Baltimore Street, Martinsburg, WV
WV Flood Tool Conceptual Slide

## Slide 35
Resources: WV Flood Risk Reports
October 2016 | Flood Risk Assessment Supplement to 2017 Region 9 Planning and Development Council Hazard Mitigation Plans – WV GIS Technical Center Berkeley County, WV ftp://ftp.wvgis.wvu.edu/pub/temp/FEMA/FRA/Berkeley_FloodRiskRpt_20161026.pdf Morgan county, WV ftp://ftp.wvgis.wvu.edu/pub/temp/FEMA/FRA/Morgan_FloodRiskRpt_20161026.pdf

## Slide 36
Resources: Previous NCR HUG Calls
Dec. 2013 | Total Exposure in Floodplain (TEIF) 2.0 – Glenn Locke, Tetra Tech http://www.usehazus.com/uploads/forum/December192013_NationalCapitolRegionHUG_Presentaiton_FINAL.pdf http://www.usehazus.com/ncrhug
March 2015 | Cook County HMP Risk Assessment – Carol Bauman, Tetra Tech http://www.usehazus.com/uploads/forum/March262015_NationalCapitolRegionHUG_Presentaiton.pdf
Feb. 2016 | Multi-Hazard Risk Assessment Lifecycle Cradle-to-Cradle - Rethinking the Way We Use Risk Assessments – Cynthia McCoy, FEMA Region X http://www.usehazus.com/uploads/forum/February252016_NationalCapitolRegionHUG_Presentaiton2.pdf
March 2016 | Data Creation Geared to the World as We Know it! – Steve Kocsis, Cambria County, PA GIS Center; Visualization of the Month – 3D Flood Impact http://www.usehazus.com/uploads/forum/March312016_NationalCapitolRegionHUG_Presentaiton.pdf

## Slide 37
FUTURE DIRECTIONS
Officially Start Project in 2017
Refine Building Inventory Tool
  Better integration of parcels/assessment records with E-911 addresses
  Review CAMA default values/null values/assumptions
    Null values for certain building characteristics of commercial and industrial properties
    Tax-Exempt Properties
  Upgrade to current Hazus-MH software version
Upgrade RiskMAP View of WV Flood Tool
  Add Hazus Level 2 Data (building loss estimates, debris removal, shelter needs)
  At-Risk Structures in Flood Zones
    Display parcel/assessment/address and building loss info for individual structures
    Create 3D flood visualizations of at-risk structures
  Incorporate flood/levee inundation maps
Coordinate with Technical Partners
  Statewide Depth Grid, Dam/Levee Assessments, Landslide Model Validation, etc.

## Slide 38
SPECIAL THANKS
Special thanks for support from FEMA
WV Division of Homeland Security and Emergency Management The Polis Center at Indiana University–Purdue University Indianapolis

## Slide 39
CONTACT INFORMATION
Kurt Donaldson GIS Manager WV GIS Technical Center West Virginia University kdonalds@wvu.edu
Eric Hopkins GIS Specialist WV GIS Technical Center West Virginia University Eric.Hopkins@mail.wvu.edu