## Slide 1
Climate Tools Overview and Panel – West Virginia
Kurt Donaldson
WV GIS Technical Center West Virginia University July 28, 2022

## Slide 2
Climate Change Web Tools
Riverine Flood Hazard #1 hazard of State Hazard Mitigation Plan
  Web Tools: WV Flood Tool (www.mapwv.gov/flood) & WV Property Viewer
  Current Focus: 1% Annual Chance (100-yr) flood event
  Climate Change Models: Incorporate higher flood depths (500-yr flood, BFE + 2’ & 3’, climate change models)
  Risk Communications: Show higher risks and various mitigation measures
    Estimate higher building damage losses due to climate change
    Show 3D flood visualizations with climate change scenarios
    New Structures: Build to higher freeboard standard to increase resiliency
    Existing Structures: Identify building stock suitable for mitigation measures
Landslide Hazard #2 hazard of State Hazard Mitigation Plan
  Web Tools: WV Landslide Tool (www.mapwv.gov/landslide) & WV Flood Tool
  Current Focus: Statewide Landslide Susceptibility Map
  Climate Change Models: Incorporate rainfall intensity-duration thresholds
  Risk Communications: Predict when landslides may occur

## Slide 3
Climate Scenario Damage Estimates
RiskMAP View
https://www.mapwv.gov/flood/map/?v=1&pid=19-07-022B-0021-0000
Flood Risk Building Info
100-Yr Damage Loss Estimate
Flood Risk Assessment Building Link
Building Loss Estimate (100-Yr)
Loss estimates for climate scenarios can be added
Concept Slide

## Slide 4
Climate Change 3D Visualizations
Building ID: 19-07-022B-0021-0000_7170
FEMA 100-Yr
FEMA 500-Yr
2052 Climate Model
Flood Depth
Add 3D Visualizations Depths for FEMA 500-Yr and 2052 Climate Model
Concept Slide

## Slide 5
Baltimore Street, Martinsburg, WV
Climate Change 3D Visualizations
<< Harpers Ferry Flood Risk 3D Visualization Movie >>
<<Map Link (turn movie layer on) >>
3D Movie Play Button
Add Climate Change Models for 3D Loss Estimates
Harpers Ferry
100-yr Flood Event

## Slide 6
Build to Higher Standard (Freeboard)
RISK COMMUNICATIONS
Build new structures to higher freeboard standard for changing climate conditions
The WV Flood Tool’s query panel displays the community’s Freeboard and CRS Class
WV Flood Tool Map Link
Source Graphic
Jefferson County Unincorporated has a freeboard requirement of 3 feet and CRS Class 6 rating
Jefferson County

## Slide 7
Mitigate Existing Structures
Source Graphic
RISK COMMUNICATIONS To increase resiliency to changing climate conditions, identify residential structures with crawl space foundations that could qualify for flood vents
Source: Statewide Building-Level Risk Assessment

## Slide 8
Landslide Hazard
2019 Slide Route 112
near Ingleside, WV (Mercer County)
Landslide Web Map Link: https://www.mapwv.gov/flood/map/?wkid=102100&x=-9034072&y=4480092&l=10&v=2
Landslide Incidents | Landslide Susceptibility | Landslide Methodology Scholarly Paper (2020)

## Slide 9
Landslide Susceptibility
April 2020 Landslide
Wood County Impacted home moved from foundation
Landslide Susceptibility Zone
Impacted Home
Landslide Susceptibility
Spring 2020 Aerial Imagery
Higher Risk
Web Map Link
Landslide Reports/ Maps

## Slide 10
Landslides and Climate Change
https://www.mapwv.gov/flood/map/?wkid=102100&x=-8704711&y=4796138&l=4&v=2
RISK COMMUNICATIONS For landslide prone areas, predict when higher incidents of landslides may occur based on rain intensity-duration thresholds
Incorporate Climate Change Data

## Slide 11
Contact Information
  WVU GIS Technical Center, West Virginia University Kurt Donaldson, Manager kurt.donaldson@mail.wvu.edu, phone: (304) 293-9467 Maneesh Sharma, GIS Analyst
  Maneesh.Sharma@mail.wvu.edu, phone (304) 293-9466
Flood Risk #1 WV Hazard
Landslide Risk #2 WV Hazard