## Slide 1
Flood Characteristics
Category | Flood Characteristic | White Sulphur Springs | Rainelle
Frequency (new flood maps) | Probability that a flood of a specific size will be equaled or exceeded in any given year |  | 
 | FEMA Flood Models: 10-, 25-, 50-, 100-, 100+, and 500-year flood elevations. FEMA’s 1%+ flood elevations measure how high the 100-year flood could be given the statistical uncertainties in flood modeling (upper 84-percent confidence limit). | See models | See models
 | First Street Foundation Flood Models: 5-, 20-, 100-, and 500-year flood elevations. Climate models based on 2052 or 30 years in the future. | See models | See models
Depth | Flood depth or water surface elevation above the ground surface. Source USGS high-water marks. | 6 feet | 8 feet
Velocity | Speed at which the floodwaters are flowing | High | Moderate
Duration | Measure of how long water remains above normal levels | 24 hours | 72 hours
Rise and Fall | Floodwater that rises very quickly with little or no warning | Quick Rise | Quick Rise
Notes: Flood characteristics are based on the 2016 flood and FEMA’s new flood studies

## Slide 2
Notes: Drone Video flood elevation: 2,392.5 ft.; Base Flood (100-yr elevation) is 2,930.0 ft., or a half foot above video footage; 2016 Flood Elevation high-water mark: 2,396.4 ft. (about 4 feet higher than video); 500-yr Flood elevation is 2,399.0 ft. or 6.5 feet above video elevation.
Video Link
2016 Flood Drone Video (Rainelle, WV)

## Slide 3
Flood Characteristics
Flood Characteristics Impacting Community
Frequency: Probability that a flood of a specific size will be equaled or exceeded in any given year
  5-, 10-, 20-, 25-, 50-, 100-, and 500-year flood elevations (above sea level) refer to expected water levels of the 20%, 10%, 5%, 4%, 2%, 1%, and 0.2% annual chance flood events. A 1000-yr flood has a 0.1% chance of happening in any given year.
  FEMA’s 1%+ flood elevations measure how high the 100-year flood could be given the statistical uncertainties in flood modeling. It represents the upper 84-percent confidence limit of the statistical error for calculating the 1-percent annual chance event.
  The relative frequency of any given flood (e.g., 5-year or 10-year) serves as a useful reference point when selecting a mitigation options and evaluating cost effectiveness.
Depth: Flood depth or water surface elevation above the ground surface
  Critical during design considerations, as it is often the primary factor in evaluating the potential for flood damage
  Flood depth sources include flood models and high water marks which measure the degree of flooding
Velocity: Speed at which the floodwaters are flowing
  Flowing water often causes erosion and scour, as well as debris impacts and hydrodynamic forces.
  FEMA’s detailed engineering studies provide river/stream flows
Duration: Measure of how long water remains above normal levels.
  Prolonged contact with floodwaters may make some mitigation measures, including dry flood-proofing, inappropriate because of the increased chance of seepage and potential structural failure.
  Long periods of inundation are more likely to cause greater damage to structural members and finishes than short periods of flooding.
Rate of Floodwater Rise and Fall: Floodwater that rises very quickly with little or now warning
  Steep topography and locations with small drainage areas may experience flash flooding in which floodwater can rise very quickly with little or no warning.
  High-velocity water flows usually accompany flash floods and preclude certain types of flood mitigation measures, especially those requiring human intervention
  Rapid rates of the rise and fall of floodwater can also lead to unequal hydrostatic pressures on a building. The probability of unequal hydrostatic pressures increases when building exteriors are designed to be watertight
Historical Information: Use past information like the high-water marks of the 2016 Flood as an indication of the nature and severity of effects likely to occur during future events.
Source: FEMA 2013

## Slide 4
USGS High Water Marks: 2016 Flood Depths

## Slide 5
Preliminary FEMA Flood Maps Effective 2023

## Slide 6
FEMA Flood Models: Likelihood and Magnitude
FEMA |  |  |  | 
Return Period (Likelihood) and Flood Size (Magnitude) | Annual Probability | Cumulative Probability - Flooding at least once over 30 years | FEMA Risk Description | Climate Model
10 yr (1 in 10) | 10% | 96% | High Risk | 
25 yr (1 in 25) | 4% | 71% | High Risk | 
50 yr (1 in 50) | 2% | 45% | High Risk | 
100 yr (1 in 100) | 1% | 26% | High Risk | 
100 yr (1 in 100) Plus | 1%+ | 26% | High Risk | Yes
500 yr (1 in 500) | 0.2% | 6% | Moderate Risk | 
Rainelle, WV

## Slide 7
FEMA Flood Model: 10-Year Flood Depth

## Slide 8
FEMA Flood Model: 100-Year Flood Depth

## Slide 9
FEMA Flood Model: 100-Year Plus Flood Depth
Climate
Change

## Slide 10
FEMA Flood Model: 500-Year Flood Depth

## Slide 11
FSF Flood Model: 500-Year Flood Depth 2052
Climate
Change

## Slide 12
FEMA Flood Models: Likelihood and Magnitude

## Slide 13
FEMA Flood Models: Likelihood and Magnitude

## Slide 14
FSF Flood Models: Likelihood and Magnitude

## Slide 15
FEMA 10% Annual Chance (10-year) Rainelle, WV
0 ft.
FLOOD DEPTH
35 ft.
96% probability of flooding at least once over 30 years
Notes: FEMA 10year Aerial

## Slide 16
FEMA 4% Annual Chance (25-year) Rainelle, WV
0 ft.
FLOOD DEPTH
35 ft.
71% probability of flooding at least once over 30 years
Notes: FEMA 25year Aerial

## Slide 17
FEMA 2% Annual Chance (50-year) Rainelle, WV
0 ft.
FLOOD DEPTH
35 ft.
45% probability of flooding at least once over 30 years
Notes: FEMA 50year Aerial

## Slide 18
FEMA 1% Annual Chance (100-year) Rainelle, WV
0 ft.
FLOOD DEPTH
35 ft.
26% probability of flooding at least once over 30 years
Notes: FEMA 100year Aerial

## Slide 19
FEMA 1%+ Annual Chance (100-year) Rainelle, WV
0 ft.
FLOOD DEPTH
35 ft.
26% probability of flooding at least once over 30 years
Climate
Change
Notes: FEMA 100year PLUS Aerial

## Slide 20
FEMA 0.2% Annual Chance (500-year) Rainelle, WV
0 ft.
FLOOD DEPTH
35 ft.
6% probability of flooding at least once over 30 years
Notes: FEMA 500year Aerial

## Slide 21
FEMA 10% Annual Chance (10-year) Rainelle, WV
Notes: FEMA 10 year NLCD Hillshade

## Slide 22
FEMA 4% Annual Chance (25-year) Rainelle, WV
Notes: FEMA 25 year NLCD Hillshade

## Slide 23
FEMA 2% Annual Chance (50-year) Rainelle, WV
Notes: FEMA 50 year NLCD Hillshade

## Slide 24
FEMA 1% Annual Chance (100-year) Rainelle, WV
Notes: FEMA 100 year NLCD Hillshade

## Slide 25
FEMA 1%+ Annual Chance (100-year) Rainelle, WV
Notes: FEMA 100 year PLUS NLCD Hillshade

## Slide 26
FEMA 0.2% Annual Chance (500-year) Rainelle, WV
Notes: FEMA 500 year NLCD Hillshade

## Slide 27
FEMA 10% Annual Chance (10-year) Rainelle, WV
Notes: FEMA 10 year Grey Hillshade

## Slide 28
FEMA 4% Annual Chance (25-year) Rainelle, WV
Notes: FEMA 25 year Grey Hillshade

## Slide 29
FEMA 2% Annual Chance (50-year) Rainelle, WV
Notes: FEMA 50 year Grey Hillshade

## Slide 30
FEMA 1% Annual Chance (100-year) Rainelle, WV
Notes: FEMA 100 year Grey Hillshade

## Slide 31
FEMA 1%+ Annual Chance (100-year) Rainelle, WV
Notes: FEMA 100 year PLUS Grey Hillshade

## Slide 32
FEMA 0.2% Annual Chance (500-year) Rainelle, WV
Notes: FEMA 500 year Grey Hillshade