## Slide 1: Kurt Donaldson
Manager
West Virginia GIS Technical Center
West Virginia University
Notes: Kurt Donaldson is the manager of the WV GIS Technical Center located at West Virginia University. Since 2003, Mr. Donaldson has been a cooperating technical partner in support of FEMA’s NFIP and Risk MAP programs.

## Slide 2: WVU Faculty Supporting Hazard Mitigation Projects
HAZARD MITIGATION PROJECT | FUNDING SOURCE | FACULTY MEMBER | ORGANIZATION & EXPERTISE | LINK
Statewide Risk Assessments | HMGP, CTP | Kurt Donaldson | WVU GIS Technical Center (online interactive map viewing applications, TEIF/TEAL1 risk assessments, flood visualizations) | WV Flood Tool Statewide RA Products & Data WV Region 3 Plan w TEIF data
Landslide Susceptibility Modeling | HMGP | Aaron Maxwell | WVU Geography Professor (landslide modeling, machine learning, remote sensing) | Published Landslide Paper
Flood Buyouts | NRCS | Katherine Garvey | WVU Land Use and Sustainability Law Clinic (legal and planning services) | Region 3 Resilience Report WV Public Broadcasting
Community Recovery and Resiliency | NSF | Jamie Shinn | Adjunct WVU Geography Professor (social science, community engagement) | WV Public Broadcasting
Partnerships among faculty members expand the subject matter expertise for hazard mitigation planning
1 Total Exposure in Floodplain (TEIF), Total Exposure Area Landslide (TEAL)

## Slide 3: Example 1: Landslide Hazard Risk Assessment
A statewide landslide susceptibility (high, moderate, low risk) map was created from FEMA-purchased QL2 LiDAR data
April 2020 Landslide
Wood County, WV Impacted home moved from foundation
Landslide Susceptibility Zone
Impacted Home
Spring 2020 Imagery
Higher Risk
WV Flood Tool
WV Landslide Tool
Landslide Susceptibility
Mitigation Planning
Landslide Risk

## Slide 4: Example 2: Voluntary Floodplain Buyout Mitigation
WV Flood Tool: Building-Level Risk Assessments
FEMA R3 Resiliency Report | WVPBS | Buyout Report
Risk assessments using FEMA’s Hazus methodology helped NRCS identify 310 properties in McDowell County for flood buyouts
Flood Mitigation Measure

## Slide 5: Example 3: Community Hazard Planning (Focus Group Meetings)
White Sulphur Springs, WV (11/17/2022; 5/24/2023)
Rainelle, WV (11/18/2022; 5/23/2023)
Feedback desired from Focus Groups:
  What lessons were learned from the immediate response and longer-term recovery from the 2016 flood?
  What priorities are needed for a stronger flood response and recovery plan in the event of a future flood?
Feedback of Flood Study Products:
  Flood Characteristics and Models
  Flood Risk Assessment (vulnerability, exposure, loss)
  Mitigation Maps
  Flood Visualization Tools
Mitigation Planning

## Slide 6: Example 3: Community Hazard Planning (Flood Risk Characteristics)
FEMA 1%+ Annual Chance (Rainelle, WV)
Climate
Change
26% probability of flooding at least once over 30 years
Category | Flood Characteristic (in context to 2016 Flood) | White Sulphur Springs | Rainelle
Frequency (new flood maps) | Probability that a flood of a specific size will be equaled or exceeded in any given year. FEMA Flood Models (new): 10-, 25-, 50-, 100-, 100+, and 500-year flood elevations. First Street Foundation Flood Models: 5-, 20-, 100-, and 500-year flood elevations. | 2016 Flood Between 100- and 500-year FEMA Climate BFE+6ft FSF Climate 2052 or 30 years in the future | 2016 Flood Between 100- and 500-year FEMA Climate BFE+1ft FSF Climate 2052 or 30 years in the future
Depth | Flood depth. Source USGS high-water marks | 6 feet | 8 feet
Velocity | Speed at which the floodwaters are flowing | High | Moderate
Duration | Measure of how long water remains above normal levels | 24 hours | 72 hours
Rise and Fall | Floodwater that rises very quickly with little or no warning | Quick Rise | Quick Rise
Flood Characteristics

## Slide 7: Example 3: Community Hazard Planning (Risk Indicators)
Vulnerability, Exposure, and Hazus Loss Indicators for the disadvantaged communities of Rainelle and White Sulphur Springs
Flood Risk Factors

## Slide 8
Risk and Mitigation Dashboards Community Hazard Planning
Risk & Mitigation Dashboards, Rainelle, WV
Mitigation Dashboard
Risk Dashboard

## Slide 9
Findings:
Rainelle: 35% of residential structures in 100-year floodplain elevated to DFE (n=87, res./non-res.)
White Sulphur Springs: 59% of residential structures in 100-year floodplain elevated to DFE (n=217, res./non-res.)
Elevated Structures to Design Flood Elevation (DFE) Mitigation Planning
Rationale:
How communities have applied flood adaptive measures in response to major flood events
DFE: 100-Year or Base Flood Elevation (BFE) + 2 feet
Building ID: 13-17-0008-0152-0000_195
Flood Tool Link
White Sulphur Springs
Building ID: 13-13-0001-0069-0000_108
Flood Tool Link
Rainelle
Examples of Mitigation Reconstruction
Mitigation Reconstruction

## Slide 10
Elevated Mitigation Reconstruction Still At Risk Mitigation Planning
3.9’ (FEMA 1% / 100-Yr)
6.5’ (2016 High Water)
9.9’ (FEMA; 0.2% / 500-Yr)
12.2’ (FSF 0.2% / 500-Yr )
First Floor Height BELOW: FEMA/FSF 0.2-percent chance (500-yr) floods
Mitigation Reconstruction
How well are mitigated structures protected from new flood maps or changing environmental factors due to climate change? New FEMA flood maps for Rainelle reveal that the mitigated structure above is a risk for the 1%+ (100-yr) and 0.2-percent chance (500-yr) floods.

## Slide 11
Flood Visualization 7 feet
First Floor Height ABOVE: 2016 Flood High Water Mark

## Slide 12
Flood Visualization 10 feet
First Floor Height BELOW: 0.2% Chance (500-yr) Flood Models

## Slide 13
Risk Assessment/Planning using WV Flood Tool
White Sulphur Springs’ primary structures viewable on the Risk MAP View of the WV Flood Tool. Symbol letters indicate general occupancy (Residential, Commercial, Other Non-Residential).
Residential Structure in Floodway Bldg. 13-17-0008-0139-0000
Buyout Property
Base Flood Depth – 3D Visualization
Street View Image
HAZUS Loss Estimate
Building Exposure

## Slide 14
Rainelle
Recommendations:
Mitigation plans should correspond to the AoMI priorities
Areas of Mitigation Interest (AoMI) Mitigation Planning
Mitigation Planning Priorities

## Slide 15
Areas of Mitigation Interest (AoMI) Mitigation Planning
Rationale:
Identifying priority zones for mitigation:
PRIORITY ZONE FACTORS
Flood Characteristics (frequency, depth, velocity)
High Water Marks
Repetitive Loss Areas
Substantial Damaged Structures
Vulnerable Structures (floodway, mobile homes, subgrade basements, minus-rated, red tag structures, etc.)
Mitigated Structures
Buyout Parcels (Open Space Preservation
Mitigation Planning Priorities
Flood Characteristics: Flood maps/models help to define mitigation zones

## Slide 16
Rainelle: $2.3M
Recommendations:
Mitigation efforts of elevating buildings above the base flood and buyouts should be considered as investment and not expense
Loss Avoidance Studies Mitigation Planning
7th St.
Mitigation Saves $
Rationale:
Difference between loss estimates for buildings with a first-floor height of 1 foot and elevated to DFE or removed entirely;
The losses avoided by federally funded riverine flood mitigation projects far exceeds the money spent (7x return on investment)*
* FEMA. “Natural Hazard Mitigation Saves Interim Report”

## Slide 17: Example 3: Community Hazard Planning (Mitigation Measures)
Mitigation Map (Rainelle, WV)
Field verification and analysis of mitigation measures implemented by property owners and the community in context of the 2016 flood and local floodplain management regulations
Mitigation Measures & Planning