## Slide 1
Flood Characteristics
Notes: Flood characteristics are based on the 2016 flood and FEMA’s new flood studies
Howard Creek Flood Study Profile
2022 Preliminary 1% Base Flood (100-Yr) Elevation 1850.7 ft for Building 13-17-0009-0026-0000_138
Video Link
2016 Damage Video (White Sulphur Springs)
USGS High Water Marks: 2016 Flood Depths
Preliminary FEMA Flood Maps Effective 2023
FEMA Flood Model: 10-Year Flood Depth
FEMA Flood Model: 100-Year Flood Depth
FEMA Flood Model: 100-Year Plus Flood Depth
FEMA Flood Model: 500-Year Flood Depth
FSF Flood Model: 500-Year Flood Depth 2052
FEMA Flood Models: Likelihood and Magnitude
FSF Flood Models: Likelihood and Magnitude
FEMA 10% Annual Chance (10-year) White Sulphur Springs, WV
FEMA 0.2% Annual Chance (500-year) White Sulphur Springs, WV
Category | Flood Characteristic | White Sulphur Springs | Rainelle
Frequency (new flood maps) | Probability that a flood of a specific size will be equaled or exceeded in any given year |  | 
 | FEMA Flood Models: 10-, 25-, 50-, 100-, 100+, and 500-year flood elevations. FEMA’s 1%+ flood elevations measure how high the 100-year flood could be given the statistical uncertainties in flood modeling (upper 84-percent confidence limit). | See models | See models
 | First Street Foundation Flood Models: 5-, 20-, 100-, and 500-year flood elevations. Climate models based on 2052 or 30 years in the future. | See models | See models
Depth | Flood depth or water surface elevation above the ground surface. Source USGS high-water marks. | 6 feet | 8 feet
Velocity | Speed at which the floodwaters are flowing | High | Moderate
Duration | Measure of how long water remains above normal levels | 24 hours | 72 hours
Rise and Fall | Floodwater that rises very quickly with little or no warning | Quick Rise | Quick Rise
https://data.wvgis.wvu.edu/pub/NSF/FloodProfiles/54025CV002B.pdf#page=43
Preliminary 2022 FEMA Maps
2022 Base Flood Elevation increased 1 to 1.5 feet from the 2012 FEMA Map between Dry Creek Bridge (Big Draft Rd) and Wades Creek Bridge (Garden St)
Bldg. 13-17-0009-0026-0000_138 1% WSEL 1850.7 ft.
Confluence of Dry Creek
Confluence of Wades Creek
For bridges shown on the flood profile, the structure is represented by an “I” symbol. The top of the bridge symbol represents the top of road and the bottom of the symbol represents the low chord (or low steel) of the bridge.
1.5’ ponding upslope
of Garden Street Bridge
FEMA FIS Technical Reference 2019
3.5’ ponding upslope
of Big Draft Bridge
2016 Flood
1,852.5 ft. (BFE + 1.8 ft. to reach HWM)
Video Link
Climate
Change
Climate
Change
0 ft.
FLOOD DEPTH
35 ft.
96% probability of flooding at least once over 30 years
0 ft.
FLOOD DEPTH
35 ft.
26% probability of flooding at least once over 30 years
FEMA 1% Annual Chance (100-year) White Sulphur Springs, WV
0 ft.
FLOOD DEPTH
35 ft.
26% probability of flooding at least once over 30 years
Climate
Change
FEMA 1%+ Annual Chance (100-year) White Sulphur Springs, WV
0 ft.
FLOOD DEPTH
35 ft.
6% probability of flooding at least once over 30 years