## Slide 1
Slides related to the April 2024 Flood Extracted

## Slide 2
WV Flood Resiliency Framework Toolkit
Hazard identification using WV Flood Tool
Wheeling Island
Mt. Zion Cemetery (Ohio County)

## Slide 3
Recent Flood Event (Wheeling Island)
Wheeling Island Hotel Casino Racetrack, WV
Stream Gauge
I-70
Drone Link
40 VIRGINIA ST, Wheeling, WV
40 Virginia St, Wheeling

## Slide 4
2024 Flood Crest 41.5 feet (April 5)
High Water Mark from 1936 Flood
Source: USGS Ohio River Gauge Height

## Slide 5
4.1’ (FEMA 2% / 50 YR)
7.2’ (FEMA 1% / 100 YR)
10.1’ (FEMA 0.2% / 500 YR)
Flood Depth Probabilities (ft.) |  |  | 
FIRM Effective Date | 50 year (2%) | 100 year (1%) | 500 year (0.2%)
2006 | 4.1 | 7.2 | 10.1
13.0 ft. (1936 HWM)
0.0 ft. (2024 HWM) (41.5’ flood stage)
Building: 35-10-0W43-0134-0000_40
1% Annual Chance (100-YR) Flood Event for 40 Virginia St., Wheeling, WV
7.2 ft. base flood depth above ground (Source: FEMA)
49 ft. flood stage gauge height (Source: USGS/NWS)
40 VIRGINIA ST, Wheeling, WV
Wheeling Flood Probabilities

## Slide 6
Wheeling (40 VIRGINIA ST, Wheeling, WV, 26003
1936 HWM = 607.3 ft. (gauge height = 0) + 55.2 ft. = 662.5 ft. The 1936 Flood Depth (662.5 ft. HWM minus LAG 649.5) estimate is 13 feet flooding above ground level. In structure, estimate four feet of water above lowest floor for 1936 flood.
2024 HWM = 41.5 feet crest on 5 April 2024. 607.3 ft. (gauge height = 0) + 41.5 ft. = 648.8 feet. Flooding should not have impacted this property. House just outside of drone footage.
High Water Mark from 1936 Flood (13 ft.)
WV Flood Tool link

## Slide 7
Vehicular Fatality (Wood County)
Valerie Swisher, 49, drowned on Nicolette Road (County Highway 47/3) on a small tributary of the Little Kanawha River.
The driver entered the flooded area of Nicolette Road at a deep dip in the roadway. The water flipped the blue SUV vehicle over in approximately 15-20 feet of water off the roadway edge.
Vehicular Drowning

## Slide 8
Landslides (Ohio County)
WTRF.com
Drone Link
1311 PARK VIEW RD, Wheeling, WV,

## Slide 9
Landslides (Ohio County)
Drone Link
1311 PARK VIEW RD, Wheeling, WV,
County-Level Scale, Generalized Susceptibility Maps