## Slide 1: NFIP: Substantial Damage in Practice
Melanie Thomas
WV Homeland Security & Emergency Management

## Slide 2: National Flood Insurance Program (NFIP) Background
Created by National Flood Insurance Act of 1968
Participation is voluntary
  Adopt and enforce regulations
  Eligible for flood insurance
Benefits of participation
  Flood insurance
  Grants and loans
  Disaster assistance
  Federally-backed mortgages
Goals of the NFIP include
  Save lives and protect property
  Encourage a comprehensive approach to floodplain management
Notes: https://www.fema.gov/media-library/assets/documents/18562
FEMA P-758
(SI/SD desk reference pdf)
https://www.fema.gov/media-library/assets/documents/18692

## Slide 3: NFIP Roles: Federal and State
Federal
  National program oversight
  Risk identification (mapping)
  Establish development/building standards
  Provide technical assistance to state/local communities/agencies
  Provide insurance coverage
State
  State program oversight
  Establish development/building standards
  Provide technical assistance to local communities/agencies
  Evaluate and document floodplain management activities

## Slide 4: NFIP Roles: Local
Local Officials and Floodplain Administrators
  Adopt and enforce floodplain management ordinance compliant with Federal/State laws
  Issue or deny development
  Inspect development and maintain records
  Make substantial damage determinations
Development oversight is a local responsibility

## Slide 5: Duties of the Floodplain Administrator
Review applications
Make floodplain determinations
Make Substantial Improvement / Damage determination
Issue or deny permits
Review plans and specifications
Ensure all other permits are obtained
Notification of watercourse alterations
Maintain and help update flood data and maps
Inspect development
Recordkeeping
Remedy violations
Keep good records! A project file should be kept for each development permit application to demonstrate that the project was built in compliance with your regulations.

## Slide 6: Duties of the Floodplain Administrator
Training and education: Understand the NFIP regulations, State regulations, and local ordinances
Community Outreach: Educate residents on the need for permits, the benefits of floodplains, the economic sustainability of good floodplain management, and the benefits of flood insurance
Coordinate with other agencies: State agencies, adjacent communities, public works, zoning, code enforcement, or building dept.
Apply ordinances consistently: Get specific guidance from your community’s legal counsel as necessary
Common legal questions and answers about floodplain regulations in the courts can be found in Appendix C of ASFPM’s No Adverse Impact: A Toolkit for Common Sense Floodplain Management.

## Slide 7: Reduce Risk to Existing Structures: Intent of the Substantial Damage Provision
Opportunity to break the cycle of disaster damage, reconstruction, and repeated damage
Reduce future costs associated with property damages
Opportunity to build stronger, safer, and smarter communities that are better able to reduce impacts from future flooding and disasters
Communities that participate in the NFIP are required to determine whether damages to structures within the Special Flood Hazard Area (SFHA) meet the NFIP criteria for substantial damage(44 CFR § 59.22 and §60.3)

## Slide 8: Definition of Substantial Damage
Damage of any origin sustained by a structure whereby the cost of restoring the structure to its pre-damage condition would equal or exceed 50% of the market value of the structure before the damage occurred
Cost of Repairs
Percent Damage = Pre-Damage Market Value of Structure
Middletown Borough, Dauphin County, PA (from PEMA)
Town of Bloomsburg, Columbia County, PA (from PEMA)

## Slide 9: Post-Flood Event Checklist
Review floodplain management ordinance
Notify property owners of permit and building requirements
Require permits for all development, not just for substantial damage
Make floodplain determination for permitting using FIRMs
Determine BFEs using FIS
Perform substantial damage determination
Notify property owners of determination results and subsequent building requirements in writing
Tour floodplain to ensure development/rebuilding is compliant
Middletown Borough, Dauphin County, PA (PEMA)
Allegheny County, PA (from PEMA)

## Slide 10: Community SD Responsibilities
Administering the SI/SD requirements requires officials to perform four major actions:
Determine costs
Determine market value
Make SI/SD determination
Require owners to obtain permits to bring substantially improved or substantially damaged buildings into compliance with the floodplain management requirements
Be Consistent: document the decisions and the documentation should be retained in the community’s permit records

## Slide 11: Property Owner Responsibility
Comply with the requirements that are enforced by the community, including floodplain management requirements
Find out if a permit is required
Submit complete information about all proposed improvements and all repairs to be undertaken
Comply with the approved plans and limitation specified in the issued permit

## Slide 12: Substantial Damage Determination Process
Assess Damage
Make Substantial Damage Determinations
Notify Damaged Structures of Ordinance Requirements
Less Than Substantially Damaged
Substantially Damaged
Use Flood Resistant Materials Below BFE
Elevate/ Floodproof Utilities At or Above BFE
Use Flood Resistant Materials Below BFE
Elevate/ Floodproof Utilities At or Above BFE
Elevate Lowest Floor At or Above BFE

## Slide 13: Assess the Damage
Prepare the “Go-Bag”: tape measure(s), cameras / cell phones, portable GPS, clipboards, and tablets if available
Review property access protocol
Review safety procedures
Notify police or sheriff of proposed inspection schedule and daily work areas in advance
Perform Substantial Damage inspections and record data

## Slide 14: Permits Are Required Post-Event
A permit is required regardless of whether or not the repairs rise to the level of substantial damage.
  Permits are required for repairs
  The permit fee can be waived
  The permit requirement cannot be waived
Non-compliance post-disaster will have negative insurance implications and could result in sanctions.

## Slide 15: Post-Disaster Permitting
Assume that structure owners:
Are unaware of the SD requirements
May disregard the need for permits
Are anxious to initiate repairs and may start repairs within a day or two of the disaster
Pressure from officials and owners to start repairs
Repairs made without the required permits may:
Need to be removed and require enforcement actions
Make it difficult to determine between new construction and what was in-place prior to the disaster

## Slide 16: Making Substantial Damage Determinations
Foundation failure, West Pittston, PA (from FEMA Region III)
Substantial damage determinations are a local responsibility
Ways to determine market value:
    Appraisal (licensed professional)
    Tax assessed value
    Actual cash value, including depreciation
    “Qualified estimates” based on professional judgment of local official
Notes: Professional Property Appraisals – appraisal is recent, pre-damage condition and strictly the building value (not to include value of land, land improvement, and accessory structures)
Tax accessed value: some limitations – appraisal cycle, land values, and assessment / adjustment factor that yields the “adjusted assessed value”
Actual Cash Value - replace building of like minus depreciation (age, use, neglect) / tool gives 7 options
Qualified Estimates: recent permit records, home sales, regional cost data, eetc.

## Slide 17: Repair Cost
Included Costs:
  Materials and labor
  Site preparation (excavation)
  Demolition and construction debris disposal
  Elevating structure
  Sales taxes on materials
  Structural elements, exterior & interior finishes, and utility & service equipment
Excluded Costs: Items that are directly associated with the building
    Clean-up and trash removal
    Costs to obtain or prepare plans
    Land survey costs
    Permit fees and inspection fees
    Outside improvements

## Slide 18: The Substantial Damage Estimator (SDE) Tool 3.0
The Substantial Damage Estimator (SDE) Version 3.0 Tool was developed by the Federal Emergency Management Agency (FEMA) to assist state and local officials in estimating Substantial Damage to residential and non-residential structures
The SDE tool allows community officials with limited appraisal or construction backgrounds to develop reasonable estimates of structure values and structure-specific damages in accordance with the NFIP requirements
The SDE tool may be used in conjunction with an industry-accepted residential construction cost-estimating guide
Notes: https://www.fema.gov/media-library/assets/documents/18692

## Slide 19: Substantial Damage Notification
Less Than Substantially Damaged:
Use flood resistant materials below BFE
Elevate/floodproof utilities at or below BFE
Substantially Damaged:
Use flood resistant materials below BFE
Elevate/floodproof utilities at or above BFE
Elevate lowest floor at or above BFE
NOTICE OF SUBSTANTIAL DAMAGE DETERMINATION

## Slide 20: Increased Cost of Compliance (ICC)
Many flood insurance policy holders are unaware that:
They have ICC coverage
ICC is a flood insurance claim and not a grant
Up to $30,000 that can be used for elevation, demolition, relocation or floodproofing (for non-residential structures)
The structure must be located in the SFHA and be substantially damaged due to flooding