## Slide 1
Landslide Risk Assessment in the Mountain State: Random Forest Modelling in Major Land Resource Areas Helps Surmount Gaps
in the West Virginia Landslide Inventory and Better Align LiDAR-Based Mapping with Local Geologic Knowledge
KITE, J. Steven, MAXWELL, Aaron Edward, SHARMA, Maneesh, DONALDSON, Kurt,
MAYNARD, Shannon Marie, BELL, Matthew, HANWELL, Elizabeth, & YESENCHAK, Rachel
WV GIS Technical Center, Department of Geology & Geography, West Virginia University
Session 194: Landslide Hazard Assessments & Risk Reduction: Data Collection & Modelling Challenges
Geological Society of America Annual Meeting Virtual Poster Presentation, Thursday, 29 October 2020: 10:00 AM - 12:00 PM
Leave Empty
This space will be automatically filled with a QR code and number for easy sharing
Will be covered by controls if you define slides
West Virginia Landslide Risk Assessment 2018-2021
Funded by FEMA Hazard Mitigation Grant Program &
WV Division of Homeland Security & Emergency Preparedness
Step 1: Statewide digital landslide inventory
> 93,000 previously mapped landslides (WVGES, USGS, etc.)
> 65,000 more landslides mapped on LiDAR-based DEMs
Step 2: Susceptibility models built from LiDAR-based mapping
Separate model for each major NRCS Major Land Resource
Area (MLRA) (≈ physiographic units) in West Virginia
* MLRA 147 Northern Appalachian Ridges & Valleys Focus
Random Forest Machine Learning: best predictive power
(Maxwell et al. 2020, Remote Sensing v. 12 no. 486)
Strongest Correlations: Topographic Attributes
Geology has weaker correlations than Topography
Step 3: Landslide Risk Model - in progress, not in this poster
Northern Appalachian Ridges & Valleys + bits of Blue Ridge & Southern Appalachian Ridges & Valleys
MLRA Map by Jim Thompson, WVU
https://jamesthompson.plantandsoil.wvu.edu/files/d/edafb843-93e2-4cc7-9287-b0e95519585f/mlraregionsmap.pdf
MLRA 147 Northern Appalachian Ridges & Valleys
Landslide Susceptibility Model
WV
VA
MD
LiDAR DEM Landslide Map
WV
VA
MD
West Virginia Landslide Tool Inventory Images (October 2020)
https://wvu.maps.arcgis.com/apps/webappviewer/index.html?id=cb01c47cfa884309b4f38dcd7542f805/
Previously Mapped Landslides
Landslides Mapped on LiDAR- Based DEMs by WV GIS Tech Center
Geology is Significant WVGES Geological Map Unit | Slide Count | Debris Flow % | Slides /100 Mi2
Alluvium | 10 | 0 | 11
Price = Pocono Group | 67 | 4 | 35
Hampshire Fm. | 107 | 3 | 22
Chemung Group | 210 | 2 | 34
Brallier Fm. & Harrell Shale | 228 | 0 | 56
Middle Devonian shale | 140 | 1 | 34
Oriskany SS & Huntersville Chert | 210 | 11 | 75
Oriskany & Helderberg, undivided | 23 | 4 | 68
Helderberg Group | 79 | 23 | 79
Tonoloway, Wills Crk. & W’msport | 130 | 11 | 73
McKenzie Fm. & Clinton Group | 301 | 5 | 191
Tuscarora Sandstone | 96 | 34 | 134
Juniata & Oswego Fm. | 27 | 48 | 59
Martinsburg & Reedsville | 139 | 14 | 102
Cambro-Ordovician carbonates | 20 | 0 | 6
Overall Ridges & Valleys | 1799 | 8 | 50
West Virginia Landslide Tool
Image (October 2020)
Topographic Attributes (e.g. Slope & Slope Area Ratio) show very strong correlation to landslide initiation points
80 % of Landslides Initiate on 20-40°slopes
80 % of Debris Flows Initiate on 25-45°slopes
Random Forest Susceptibility Model, WV Eastern Panhandle
Known Landslide Issues exist near Harpers Ferry, but mapping shows only one landslide
Model Predicted Medium to High Susceptibility based on correlations elsewhere in MLRA
Virginia
Maryland