## Slide 1
Statewide Hazard Assessment
Landslide Risk Assessment

## Slide 2
Landslide susceptibility map showing generalized USGS map and more detailed prototype map
Landslide
Risks
Risk Assessment table showing building counts along with estimated replacement costs in landslide zones of concern
Buildings Exposed to Landslide Risks
Landslide Maps – Old versus New
Old Way - Very Generalized
New Way – More Detailed

## Slide 3
Goals
Develop landslide inventory
Create valid landslide models for specific WV regions
Generate county-level resolution landslide maps
Create an interactive web map application for displaying landslide models and variables
Use the new landslide models and information to update the State Hazard Mitigation Plan
Did you know?
Landslides are the #2 Hazard in West Virginia
2015 Yeager Airport Slide
Landslide Risk Assessment

## Slide 4
Landslide Incident Inventory
Collected data from various sources
  WVGES
    Landers and Smosna, 1973
    Lessing et al, 1976
    Kite, 1985
  NPS/WVGES
    Yates and Kite, 2014-15
  USGS
    Ohlmacher et al, 1978-85
    Jacobson et al, 1993
  WVDHSEM
    State Hazard Mitigation office
  WVDOT
    Geospatial Transportation Information (GTI) Section, 1973-2016
  WVU
    Kite, 1983-97
    Konsoer et al, 2008
    WVGISTC, 2018-ongoing

## Slide 5
Landslide Incident Inventory
301,711 landslide features
# | Agency | Year | Author or Source Agency | Title/Description | General Location | Purpose | Total Incidence Data
1 | WVGES | 1973 | Landers and Smosna | Final Report on Landslides of July 9, 1973 in Kanawha City Area of Charleston, West Virginia | Charleston, West Virginia | Landslide mapping | 10
2 | WVGES | 1976-80 | Lessing et al. | WV Landslides and Slide-Prone Areas; funded by Appalachian Regional Commission | Statewide (39 topo quads) | Landslide mapping | 46,330
3 | USGS | 1978-85 | USGS (various) | Landslide Quad Maps: Open File Maps | Statewide (382 topo quads) | Landslide mapping | 41,307
4 | USGS | 1993 | Jacobson et al | U.S. Geological Survey Bulletin 1981: Geomorphic studies of the storm and flood of November 3-5, 1985, in the upper Potomac and Cheat River basins in West Virginia and Virginia | Cheat and Potomac River basins; Wills Mountain Anticline; Eastern WV | Research study (1985) | 3,571
5 | WVU | 1983-97 | WVU | Landslide incidences with Images | Statewide | Instruction & landslide inventory | 46
6 | WVU | 1996 | Kite and Grubb | Update of 1976 Landslide Maps, Morgantown North and South Quadrangles | Morgantown, West Virginia | Landslide inventory | 41
7 | WVU | 2008 | Konsoer et al | LiDAR, GIS, and multivariate statistical analysis to assess landslide risk, Horseshoe Run watershed, West Virginia | Horseshoe Run Watershed, Tucker County | Surficial Geology Mapping | 149
8 | NPS/WVGES | 2014 | Yates and Kite | Unpublished Digital Surficial Geologic Map of Bluestone National Scenic River and Vicinity, West Virginia (NPS, GRD, GRI, BLUE, BLUS digital map) adapted from a West Virginia University and West Virginia Geological and Economic Survey Open File Map by Yates and Kite (2014) | Bluestone National Scenic River and Vicinity | Surficial Geology Mapping | 12
9 | NPS/WVGES | 2015 | Yates and Kite | Digital Surficial Geologic Map of New River Gorge National River, West Virginia (NPS, GRD, GRI, NERI, NERS digital map) adapted from a West Virginia University and West Virginia Geological and Economic Survey Open File Report map by Yates and Kite (and Gooding) (2015) | New River Gorge National River | Surficial Geology Mapping | 212
10 | WVDOT | 2016 | Geospatial Transportation Information (GTI) Section | Road landslide inventory | Statewide | Landslide inventory | 1,406
11 | WVDHSEM | 2025 | State Hazard Mitigation Office | FEMA Buyout Properties for Landslides | Southern West Virginia | Landslide mitigation | 19
12 | WVU | 2023 | WVGISTC | Statewide Landslide Risk Assessment; Funded by FEMA and WV Division of Homeland Security and Emergency Management | Statewide | Landslide risk assessment (QL2 LiDAR) | 116,420
13 | WVU | 2026 | WVGISTC | Polygons and lines mapped using previously mapped LiDAR landslide incidence points. Project funded by USGS. | Statewide | Landslide Mapping (QL2 LiDAR) | 92,188
Updated 2026

## Slide 6
Landslide Incident Inventory
Landslide Incidence Points with Images
  From Dr. Kite
    Slides were scanned and tagged with geographical information, dates taken, and descriptions
    Added to the landslide incidence database

## Slide 7
Kanawha Section
Logan Plateau
Allegheny Mountains
Ridge & Valley
Great Valley
Blue Ridge
Mapping Landslides from new DEM
FEMA is purchasing statewide Quality Level 2 lidar for the entire State that will improve the mapping of existing landslides. Lidar-derived products include 1-meter DEM and 1-foot Contours

## Slide 8
Mapping Landslides from new DEM
Best-Available Elevation Sources for West Virginia: https://www.mapwv.gov/floodtest/docs/WV_FloodTool_ElevationSource_Metadata.pdf

## Slide 9: Old DEM
Mapping Landslides from new DEM
Comparison of Old and New 1 meter DEM
New DEM

## Slide 10
Landslide Incident Inventory
Landslide mapping from new LiDAR-derived DEM
  Identifying following types of landslides
    Slide
    Fall
    Flow
    Lateral Spread
    Multiple Failures
    Unknown

## Slide 11
Landslide Incident Inventory
Images from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
*Description from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
Mineral County, WV
Slide (includes rotational and translational movement)*: mass movements, where there is a distinct zone of weakness that separates the slide material from more stable underlying material

## Slide 12
Landslide Incident Inventory
Images from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
*Description from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
Pendleton County, WV
Debris Flow*: A form of rapid mass movement in which a combination of loose soil, rock, organic matter, air, and water mobilize as a slurry that flows downslope; they are often associated with steep gullies, and debris-flow deposits are usually indicated by the presence of debris fans at the mouths of gullies

## Slide 13
Landslide Incident Inventory
Images from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
*Description from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
Greenbrier County, WV
Lateral Spread*: When coherent material, either bedrock or soil, rests on materials that liquefy, the upper units may undergo fracturing and extension and may then subside, translate, rotate, disintegrate, or liquefy and flow; usually occur on very gentle slopes or flat terrain

## Slide 14
Landslide Incident Inventory
Multiple Failures: This classification is used when multiple (>4) failures, usually small debris flows, occur in a restricted area
Images from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
*Description from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
Pendleton County, WV

## Slide 15
Landslide Incident Inventory
Images from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
*Description from https://pubs.usgs.gov/fs/2004/3072/fs-2004-3072.html
Undetermined: Some failure is present, but it is not possible to determine the type of movement
Pendleton County, WV
Fall*: Abrupt movements of masses of geologic materials, such as rocks and boulders, that become detached from steep slopes or cliffs

## Slide 16
WV GIS TC
Landslide Mapping
March-September 2019
1 m
2 m
>3 m
WV GIS TC Mapping on LiDAR-Based DEMs
8,991 Failures (>10 m wide) Most from 1 m DEMs
334 Debris Flows
241 Lateral Spreads
8,416 Other Failures
  >97 % “Slides” (or Slumps)
Few Rock Falls Identified
Mapped Landslides Verified on best available DEMs
1,082 WVGES (1976-80) Monongalia Co. Slides
Best Available DEMs
Landslide Incident Inventory

## Slide 17
Landslide Incident Inventory
Type of Movement | Number of user identified points | Percentage of user identified points | Description
Slide | 113,931 | 97.9 | A zone of weakness separates the slide from the underlying material; can be translational or rotational
Fall | 17 | 0 | Rocks or other geologic materials dislocate from steep slopes
Debris Flow | 1,632 | 1.4 | Fluid mobilizes material into a slurry that flows downslope; often associated with gullies or steep channels
Lateral Spread | 672 | 0.6 | Extension along very shallow or horizontal slopes which causes material to break into block-like shapes
Multiple Failures | 146 | 0.1 | Usually a combination of multiple small debris flows in a restricted location
Undetermined | 22 | 0 | Some failure is clearly present, but it is difficult to determine the type of movement
Updated 2026

## Slide 18
Landslide Method Development
The West Virginia University Study Team includes Dr. Steve Kite (Geomorphologist), Dr. James Thompson (Soil Scientist), Dr. Aaron Maxwell (Geologist/Modeler), and Dr. Maneesh Sharma (Geologist/GIS)

## Slide 19
West Virginia
Physiography
& NRCS MLRAs
Existing Physiographic Maps Inadequate for WV Landslide Project
MLRA Boundaries Better
Provinces & Subdivisions Appalachian Plateaus
Kanawha Section
Logan Plateau
Allegheny Mountains
Valley & Ridge
Ridge & Valley
Great Valley
Blue Ridge
Red = Landslide-Prone
Kanawha Section
Logan Plateau
Allegheny Mountains
Ridge & Valley
Great Valley
Blue Ridge
Landslide Method Development

## Slide 20
Landslide Method Development
Goal: Generate predictive models of slope failure probability/occurrence

## Slide 21: Machine Learning = Learning from Examples
Machine learning algorithm
Thing you want to predict
Things you know that might help you predict the new thing
New things to predict
Predictions
Trained Model
Landslide Method Development

## Slide 22: Training the Model
Based on visual interpretation of terrain data
1,799 examples
Landslide Method Development

## Slide 23: Modeling Methods: Predictor Variables
Terrain Derivatives:
  Topographic Slope
  Mean Slope
  Topographic Roughness
  Slope Position
  Topographic Dissection
  Heat Load Index
  Aspect Linear Transformation
  Surface Area Ratio
  Surface Relief Ratio
  Site Exposure Index
  Longitudinal Curvature
  Cross Sectional Curvature
  Profile Curvature
  Plan Curvature
Landslide Method Development

## Slide 24: Modeling Methods: Predictor Variables
Non-Terrain:
  Roads
    Distance from US Roads
    Distance from State Roads
    Distance from Local Roads
    Cost Distance from US Roads
    Cost Distance from State Roads
    Cost Distance from Local Roads
  Hydrology
    Distance from Streams
    Cost Distance from Streams
  Geology
    Geologic Rock Type (Categorical)
    Modified Geologic Rock Type (Categorical)
  Soils
    DPSM (Categorical)
    Drainage Class (Categorical)
Landslide Method Development

## Slide 25: Modeling Method
Random Forest
Provide predictor variables
Provide presence and absence data
Landslide Method Development

## Slide 26: Predict to Entire Extent
Tile-by-tile
Python scripts
~1 week to process
Landslide Method Development

## Slide 27: Results
AUC – 0.94
Landslide Method Development
Notes: The area under the curve (AUC) that relates the hit rate to the false alarm rate has become a standard measure in tests of predictive modeling accuracy. The AUC is an estimate of the probability that a classifier will rank a randomly chosen positive instance higher than a randomly chosen negative instance.

## Slide 28: Important Variables
Surface Area Ratio
Slope
Surface Relief Ratio
Slope Position
Curvature
Topographic Roughness
Topographic Dissection
Landslide Method Development

## Slide 29: Moving Forward
Semi-automate with scripting
Develop models for different physiographic regions
Predict entire state
Further validate results
Landslide Method Development

## Slide 30: Susceptibility and Hazard Assessment
Produce landslide susceptibility map by county
Calculate at risk properties for each county
Landslide Susceptibility Prediction

## Slide 31
Landslide Incident Inventory
Over 100,000 landslide incident point and polygon features have been inventoried into a digital geodatabase
www.mapWV.gov/Landslide (in development)

## Slide 32
www.mapWV.gov/Landslide (in development)
Landslide Incident Inventory
Over 100,000 landslide incident point and polygon features have been inventories into a digital geodatabase

## Slide 33
www.mapWV.gov/Landslide (in development)
Landslide Incident Inventory
According to Dr. Kite “Looks to be in the 5000-8000 square meter range in total. One of the biggest observed slides I know about in the state”. Feb 25, 2019

## Slide 34
Two StoryMaps In Development
Landslide Outreach Material
  West Virginia Landslides and Slide-Prone Areas, WVGES 1976
Causes of Landslides in Mountain State, West Virginia
https://arcg.is/1KDnvq
https://arcg.is/1SW0Sn

## Slide 35
Goals
Develop a landslide inventory
Create valid landslide models for specific WV regions
Generate county-level resolution landslide maps
Create an interactive web map application for displaying landslide models and variables
Use the new landslide models and information to update the State Hazard Mitigation Plan
QUESTIONS?
2015 Yeager Airport Slide
Landslide Risk Assessment

## Slide 36
HMGP Landslide FY19 1st Quarterly Report
Five Major Landslide Goals and Deliverables
Q2: Published 41 landslide incidence data with photos
Q2: Mapped 1100 incidence points using 1m Lidar-derived DEM
Q2: Dominant Soil Parent Material variable was added to gSSURGO
Q2: Road and Stream layer was prepared for modelling
Q2: Continued modelling with new input variables

## Slide 37
HMGP Landslide Quarterly Report (Cont.)
Five Major Landslide Goals and Deliverables
Q2: Published new operational, reference and background layers to Landslide Inventory Tool
Q2: Started developing two online Story Maps

## Slide 38
Landslide Method Development
Goal: Generate predictive models of slope failure probability/occurrence
Random Forest Model has been run for Ridge and Valley physiographic region for eastern part of the state.