## Slide 1
Community Coordination & Outreach (CCO) Meeting
Hardy County, West Virginia June 21, 2022

## Slide 2: Agenda
1
Welcome and Introductions
Where We Are - Preliminary Maps
Impacts
Floodplain Management
Public Outreach
What You Should Do

## Slide 3: Welcome and Introductions
2

## Slide 4: Where We Are - Preliminary Maps
3

## Slide 5: Timeline – Looking Back
5
DFIRM Conversion
September 2009
Flood Risk Review Meeting
September 15, 2021
Advisory Flood
Height (AFH) Data
February 2020
Risk MAP Study Notification
July 2020
Discovery
September 2018
Notes: Discovery meeting was the South Branch Potomac River Watershed Flood Risk meeting that included officials from Grant, Hampshire, Hardy, Highland, and Pendleton Counties.

## Slide 6: Timeline – Looking Ahead
5
Preliminary Issuance
April 14, 2022
CCO Meeting
June 21, 2022
Appeal Period
Fall 2022
Effective Date
6 months after LFD
End of
Appeal Period
90-days after appeal start
FEMA issues LFD
Spring 2023
CCO: Community Coordination and Outreach
LFD: Letter of Final Determination
Notes: Discovery meeting was the South Branch Potomac River Watershed Flood Risk meeting that included officials from Grant, Hampshire, Hardy, Highland, and Pendleton Counties.

## Slide 7: Flood Study Update
6

## Slide 8: Floodplain Map Overview
HIGH RISK (Special Flood Hazard Area) |  |  | Regulatory Floodway
 |  |  | 1-Percent-Annual-Chance Flood Hazard Area with Base Flood Elevations (BFEs)
 |  |  | 1-Percent-Annual-Chance Flood Hazard Area without published BFEs
MODERATE RISK |  |  | 0.2-Percent-Annual-Chance Flood Hazard Area
 |  |  | Cross Sections with 1% Annual Chance Water Surface Elevation Value
ZONE AE
ZONE A
“The 100-Year Flood Zone Explained”
Notes: Discuss 1% floodplain and 0.2% floodplain, floodway, cross sections, and BFEs
“Cross sections now show water surface elevations.”
“Transparent fills over aerial photography”
“new maps will look different”

## Slide 9: Floodplain Map Overview
HIGH RISK (Special Flood Hazard Area) |  |  | 
MODERATE RISK |  |  | 
 |  |  | Cross Sections with 1% Annual Chance Water Surface Elevation Value
Development is not allowed unless “no rise” in flood levels is certified
Flood insurance is not mandatory
ZONE AE
ZONE A
Flood insurance is mandatory for structures with federally-back mortgages
“The 100-Year Flood Zone Explained”
Notes: Discuss 1% floodplain and 0.2% floodplain, floodway, cross sections, and BFEs
“Cross sections now show water surface elevations.”
“Transparent fills over aerial photography”
“new maps will look different”

## Slide 10: Floodplain Map Overview
6
Notes: Acknowledgement of AMP – objective and refinements

## Slide 11: Study Recap (from FRR in Sept 2021)
Revised Modeling and Mapping, including:
Updated GIS-based regulatory products, including updated maps / database / report formats based on new FEMA guidelines and specifications
Utilization of high-resolution topographic data (for modeling and mapping)
Model-backed Approximate ‘Zone A’ Studies – 332 miles
  Modeled cross-sections are not published on FIRM, but included in the database.
  Approximate Zone A models include additional flood frequencies (0.2% annual chance flood event)
Production of associated non-regulatory flood risk datasets
** Ongoing levee recertification effort in Moorefield ** will follow separate path/update

## Slide 12: Study Overview
Zone A streams (studied for this project, but completely outside of PMR)
Zone A streams (part of the PMR)
Zone AE restudy associated with Moorefield Levees
Area not included as part of this PMR
Hardy County Boundary
LEGEND
HARDY
COUNTY
WARDENSVILLE
MOOREFIELD
The “PMR” Project Area

## Slide 13: LOMCs and SOMAs
Preliminary Summary of Maps Actions (SOMA)
Now available with preliminary maps
Identifies previously issued Letter of Map Change (LOMCs) and how those determinations are impacted by the new mapping effort

## Slide 14: Where Can I Find My Flood Maps?
The FEMA Map Service Center (MSC) is the official public source for flood hazard information: https://msc.fema.gov/portal/home
Enter an address for location search
5
Menu Search

## Slide 15
National Flood Hazard Layer
Visit https://www.fema.gov/national-flood-hazard-layer-nfhl for multiple options to view and download NFHL data.

## Slide 16: How Did the Floodplain Maps Change?
FEMA Region 3 Changes Since Last FIRM (CSLF) Viewer: https://arcg.is/1y44Ov
Change in Floodplain Extents:
    Purple – Increase
    Blue – Still Floodplain
    Yellow – Decrease
FEMA Flood Map Changes Viewer: https://msc.fema.gov/fmcv

## Slide 17: WV Flood Tool
http://www.mapwv.gov/flood/

## Slide 18
Study Impacts

## Slide 19: Flood Risk Dashboard
17
NFIP FLOOD CLAIM
PAYOUTS
AVERAGE PREMIUM
NFIP FLOOD
POLICIES
REPETITIVE
LOSSES
HIGH-RISK
STRUCTURES
AFFECTED RESIDENTS
CLAIMS OUTSIDE OF SFHA

## Slide 20: Flood Risk Dashboard
Estimated structures in the draft high hazard area
364
+145
-179
4%

## Slide 21: Flood Risk Dashboard
Estimated structures in the draft high hazard area
431
+145
-179
4%

## Slide 22: Flood Risk Dashboard
Estimated structures in the draft high hazard area
431
+145
-179
4%

## Slide 23: County Public Assistance
16
Category | Federal Funding | # of Projects
Protective Measures | $72,821 | 10
Public Buildings | $133,832 | 2
Public Utilities | $50,000 | 6
Recreational or Other | $1,125 | 1
Roads and Bridges | $30,535 | 3
State Management | $9,302 | 3
TOTAL | $297,616 | 25
This information reflects projects in Hardy County related to severe storms and hurricanes since 2003.
https://www.fema.gov/data-visualization/public-assistance-program-summary-obligations
Notes: For entire state of WV

## Slide 24: Significant Impacts Overview
Compared to effective NFHL, widening and narrowing of the 1-percent-annual-chance floodplain (SFHA) extent was observed throughout the county.
Extended study reaches (with drainage areas of 2 square mile and greater, and not on current effective FIRM) result in new properties within the SFHA.
Most streams experienced both increases and decreases when comparing the computed model WSELs to the current regulatory base flood elevations.
After the map update, an estimated total of 364 structures (excl. Moorefield) are expected to be in the SFHA.
Slightly more structures will be mapped out (-179) than mapped in (+145).

## Slide 25: Floodplain Management
31

## Slide 26: Floodplain Management
Permits are Required for ALL Development in the floodplain!
Development means any manmade change to improved or unimproved real estate
Build it right and insurance premiums will be more affordable
Build it wrong and premiums will be very expensive
Taken from U.S. Route 48 Bridge, Hardy County, West Virginia (Eastern Panhandle Working Fires)

## Slide 27: Floodplain Management
Communities must regulate based on FIRMs
Development should be reasonably safe from flooding
Permits are required for all development
State/federal permits are required
Elevate and/or construct with flood- resistant materials
Locate and design mechanicals to minimize or eliminate flood damage
Locate and design public utilities and facilities to minimize or eliminate flood damage
A Zones: top of lowest floor (residential) elevated to or above the base flood level

## Slide 28: Update Ordinance
Communities agree to adopt ordinances that meet or exceed the minimum requirements of the NFIP to participate in the program
New maps = new ordinances
No postponement waivers or extensions will be granted
The time to update your ordinance will be after the Appeals Period and after the LFD is issued
Remember, without a compliant floodplain ordinance adopted and effective prior to the effect date of the new maps a community will be suspended from the National Flood Insurance Program (NFIP)

## Slide 29: Types of Ordinances
Zoning Ordinances
Building Codes
  Subdivision Regulations
  Sanitary Regulations
“Stand Alone”
Ordinance
*Remember severability clause and most restrictive local regulation applies!

## Slide 30: Establish a Timeline (After LFD)
Existing Ordinance
Update or adopt NEW
State Review
Community Revises and Adopts
Final Review and Compliance Check
Effective Date
Anticipate your local procedural requirements and timeline for the process for adoption meetings, postings, reviews, adoption

## Slide 31: Planning Recommendations
Set a date for adoption and notify state of scheduled date
Signed, adopted ordinances should be submitted to State NFIP Coordinator
All communities need to have adopted a compliant ordinance
  Failure to do so will result in suspension from the NFIP
  Following state review, ordinances will be forwarded to FEMA
It is strongly recommended that communities adopt and submit their ordinances as early as possible to avoid last minute complications
FEMA can not guarantee last minute reviews by effective date
Don’t wait until the deadline!

## Slide 32: Permitting with Preliminary Data
Recommend using preliminary data to build / rebuild safely
  Permit with two sets of data and regulate to the most restrictive
  Inform applicants of the future risk and insurance implications
  Potential community liability
Recommendation vs. requirement
  Unless formally adopted by the community, use of preliminary data is not required
  Communities must regulate at least to current effective data

## Slide 33: Public Outreach
21

## Slide 34: Public Outreach
35
Local Officials Toolkit
Resource to support community outreach following the CCO meeting until maps become effective
Templatized letters, messaging, and more to help communicate your community’s flood risk and flood insurance requirements
Compilation of FEMA resources and tools to support your work to make your community safer and stronger

## Slide 35: Outreach Messaging for Residents
NEW Flood Risk Communication Video Series available on FEMA YouTube Channel
Eight short videos
Help understand, relate to, and communicate about the flood map update process
Introduction to the NFIP
Flood Insurance & Communities
Flood Risk Basics & Communities
Introduction to Risk MAP*
Providing Input as Maps are Developed
Collecting Data to Create the Maps*
We Have a Map Now What?*
Mitigation

## Slide 36: Resources for Property Owners
WV Flood Tool (updated end-user brochure)
Advise property owners to contact their insurance agents
Call the FEMA Flood Mapping and Insurance Exchange: 1-877-336-2627
Visit: www.floodsmart.gov and www.fema.gov/national-flood-insurance-program for additional info

## Slide 37: Timeline for Hardy County
27
Preliminary
Maps Issued
April 14, 2022
Effective Date
6 months after LFD
Insurance is not impacted by Preliminary Maps.
Mandatory purchase requirements change with Effective Maps.
There is time between to reach out to impacted property owners.

## Slide 38
Risk Rating 2.0

## Slide 39: Risk Rating 2.0
Transformational leap forward for NFIP
Since the 1970s, flood insurance rates have been predominantly based on relatively static measurements, emphasizing a property’s location / elevation within a zone on a FIRM
Risk Rating 2.0 will consider more flood risk variables (including cost to rebuild) to more accurately reflect property-specific flood risk
www.fema.gov/NFIPtransformation

## Slide 40: Risk Rating 2.0
PHASED IMPLEMENTATION
  Phase I
    Beginning Oct. 1, 2021, new policies will be subject to the new rating methodology. And existing policyholders eligible for renewal will be able to take advantage of immediate decreases in their premiums.
  Phase II
    All remaining policies renewing on or after April 1, 2022, will be subject to the new rating methodology.
www.fema.gov/NFIPtransformation

## Slide 41: Risk Rating 2.0
WHAT IS NOT CHANGING?
Limiting Annual Premium Increases (no more than 18%)
Using FIRMs for Mandatory Purchase and Floodplain Management
FEMA is maintaining some features to simplify the transition to Risk Rating 2.0 by offering premium discounts to eligible policyholders:
Offer premium discounts for pre-FIRM subsidized and newly mapped properties
Policyholders will still be able to transfer their discount to a new owner by assigning their flood insurance policy when their property changes ownership.
Discounts to policyholders in communities who participate in the Community Rating System will continue.

## Slide 42: Risk Rating 2.0
www.fema.gov/NFIPtransformation
Immediate Decreases
2,325 Policies
Risk Rating 2.0 in West Virginia
Risk Rating 2.0 in Hardy County
Chart: 
| Category 1
Series 1 | 17
Series 2 | 60
Series 22 | 9
Series 3 | 14
7,947 Policies
1,939 Policies
1,130
Policies
2,325 Policies
Immediate Decreases
Average $0 - $10 Per Month Increases ($0 - $120 Per Year)
Average $10 - $20 Per Month Increases ($120 - $240 Per Year)
Average >$20 Per Month Increases (>$240 Per Year)
Risk Rating 2.0 State Profiles
Risk Rating 2.0 Data Analysis for
States and Counties is accessible at:
20 Policies
71 Policies
11 Policies
16 Policies

## Slide 43: Risk Rating 2.0
Interactive maps from ASFPM in collaboration with The Pew Charitable Trusts which offer summaries by zip code (# of policies within specified $ decrease/increase ranges) for existing single-family home policies at no.floods.org/rr2sfh and for all existing NFIP policies at no.floods.org/rr2all.
The data compares a snapshot of policyholder premiums from May 31, 2020 with Risk Rating 2.0 premiums, applying statutory increase limits. The comparison does not attempt to estimate premium increases that might have occurred without the new Risk Rating 2.0 pricing methodology.

## Slide 44: Risk Rating 2.0
For a deeper dive into Risk Rating 2.0:
Introduction to Risk Rating 2.0 (MAFSM Conference Nov 2021 – 22 min) Rich Sobota – R3 Senior Insurance Specialist
FEMA Risk Rating 2.0 – Recorded Webinar (Aug 2021 – 60 min)
  Tony Hake - Director for the Transformation of the National Flood Insurance Program (NFIP)
  Andy Neal - Chief Actuary of the National Flood Insurance Program and Branch Chief of FEMA’s Federal Insurance and Mitigation Administration’s Actuarial and Catastrophic Modeling branch.
FEMA Risk Rating 2.0 – Fact Sheet

## Slide 45: What You Should Do
33

## Slide 46: Community Action Items
34
Comment on Preliminary Information
Appeal Preliminary Map If Desired
Reach out to Community Members
Wait for LFD to Adopt
Review Preliminary Map, FIS
and SOMA
FIS: SOMA: LFD:
Flood Insurance Study Summary of Map Actions Letter of Final Determination

## Slide 47: The Statutory 90-Day Appeal Period
35
(Prerequisite) Confirm Community Map Repository and publish in the Federal Register (FR).
Appeal Start Letters will be sent to communities to explain the appeal period. These letters are issued ~4 weeks after the FR, and ~1 week before the 1st local newspaper notice (legal classified ad). A 2nd local newspaper notice follows ~1 week after the 1st.
The Appeal Period begins with the 2nd local newspaper notice and lasts for 90 days... It cannot be shortened or extended.
FEMA issues a supplemental press release to Radio / TV / Print media in conjunction with the legal classified ads.
Appeals must be submitted by community representatives to FEMA during the 90-day period and contain scientific or technical data. Appeals will be acknowledged and resolved before the project advances to final stages.

## Slide 48: Your Role
35
Leverage federal and state resources (such as FEMA’s Local Officials Toolkit and the WV Flood Tool) to understand and communicate your community’s flood risk and flood insurance requirements.
Consider mitigation actions that could make your community safer and more resilient to disasters.
Work with property owners on risk reduction (e.g., FEMA Brochure: Protect Your Home from Flooding – Low-Cost Projects You Can Do Yourself).
KNOW YOUR RISK – INSURE YOUR RISK – REDUCE YOUR RISK

## Slide 49: Timeline for Hardy County
5
Preliminary Issuance
April 14, 2022
CCO Meeting
June 21, 2022
Appeal Period
Fall 2022
Effective Date
6 months after LFD
End of
Appeal Period
90-days after appeal start
FEMA issues LFD
Spring 2023
CCO: Community Coordination and Outreach
LFD: Letter of Final Determination
Notes: Discovery meeting was the South Branch Potomac River Watershed Flood Risk meeting that included officials from Grant, Hampshire, Hardy, Highland, and Pendleton Counties.

## Slide 50: Project Contacts
State NFIP / CTP:
Tim Keaton
(304) 414-7659 Tim.W.Keaton@wv.gov
FEMA Region III:
Elizabeth Ranson
Mitigation Planning Specialist (215) 347-0686 Elizabeth.Ranson@fema.dhs.gov
Mapping Partner:
Brandon Cramer
Study Manager
(715) 864-9656 brandon.cramer@woodplc.com
Robert Pierson, PMP
Project Officer (215) 931-5650
Robert.Pierson@fema.dhs.gov
WVGISTC:
Kurt Donaldson, GISP, CFM
Manager
(304) 293-9467
Kurt.Donaldson@mail.wvu.edu

## Slide 51: General Assistance
Map specialists are available at the FEMA Mapping and Insurance eXchange (FMIX) to assist customers. FMIX also connects stakeholders with a wide range of technical subject matter experts.
1-877-FEMA MAP
(1-877-336-2627)
FEMAMapSpecialist@riskmapcds.com
Online Chat: www.floodmaps.fema.gov/fhm/fmx_main.html