## Slide 1
WV Flood Resiliency Framework Toolkit
Hazard identification using WV Flood Tool
Wheeling Island
Mt. Zion Cemetery (Ohio County)

## Slide 2
Recent Flood Event (Wheeling Island)
Wheeling Island Hotel Casino Racetrack, WV
Stream Gauge
I-70
Drone Link
40 VIRGINIA ST, Wheeling, WV
40 Virginia St, Wheeling

## Slide 3
2024 Flood Crest 41.5 feet (April 5)
High Water Mark from 1936 Flood
Source: USGS Ohio River Gauge Height

## Slide 4
4.1’ (FEMA 2% / 50 YR)
7.2’ (FEMA 1% / 100 YR)
10.1’ (FEMA 0.2% / 500 YR)
Flood Depth Probabilities (ft.) |  |  | 
FIRM Effective Date | 50 year (2%) | 100 year (1%) | 500 year (0.2%)
2006 | 4.1 | 7.2 | 10.1
13.0 ft. (1936 HWM)
0.0 ft. (2024 HWM) (41.5’ flood stage)
Building: 35-10-0W43-0134-0000_40
1% Annual Chance (100-YR) Flood Event for 40 Virginia St., Wheeling, WV
7.2 ft. base flood depth above ground (Source: FEMA)
49 ft. flood stage gauge height (Source: USGS/NWS)
40 VIRGINIA ST, Wheeling, WV
Wheeling Flood Probabilities

## Slide 5
Wheeling (40 VIRGINIA ST, Wheeling, WV, 26003
1936 HWM = 607.3 ft. (gauge height = 0) + 55.2 ft. = 662.5 ft. The 1936 Flood Depth (662.5 ft. HWM minus LAG 649.5) estimate is 13 feet flooding above ground level. In structure, estimate four feet of water above lowest floor for 1936 flood.
2024 HWM = 41.5 feet crest on 5 April 2024. 607.3 ft. (gauge height = 0) + 41.5 ft. = 648.8 feet. Flooding should not have impacted this property. House just outside of drone footage.
High Water Mark from 1936 Flood (13 ft.)
WV Flood Tool link

## Slide 6
Vehicular Fatality (Wood County)
Valerie Swisher, 49, drowned on Nicolette Road (County Highway 47/3) on a small tributary of the Little Kanawha River.
The driver entered the flooded area of Nicolette Road at a deep dip in the roadway. The water flipped the blue SUV vehicle over in approximately 15-20 feet of water off the roadway edge.
Vehicular Drowning

## Slide 7
Landslides (Ohio County)
WTRF.com
Drone Link
1311 PARK VIEW RD, Wheeling, WV,

## Slide 8
Landslides (Ohio County)
Drone Link
1311 PARK VIEW RD, Wheeling, WV,
County-Level Scale, Generalized Susceptibility Maps

## Slide 9
WV Flood Resiliency Framework Toolkit
WV Flood Risk Index Tool (future)
Rainelle, WV
Marlinton, WV
The WV Flood Risk Index Tool aggregates hazard data to indicate the communities most at risk of riverine flooding. It incorporates flood visualizations at community and building level scales for communicating risk.

## Slide 10
Community Impact Study (Marlinton, WV)
November 1985 Flood (47 fatalities)

## Slide 11
Community Impact Study (Marlinton, WV)
Statewide Stream Scale
Buildings in SFHA
Buildings in Floodway
Marlinton, WV
Marlinton, WV
Flood Risk Indicators
Stream Name | Total Building Count
Ohio River | 7,237
Kanawha River | 7,116
Elk River | 2,253
Greenbrier River | 1,821
Stream Name | Total Floodway Count
Island Creek | 632
Greenbrier River | 513
Stream Name | Substantially Damaged
Ohio River | 920
Greenbrier River | 368

## Slide 12
Community Impact Study (Marlinton, WV)
Regional Scale
Building Counts & Building Values
Marlinton, WV
Flood Risk Indicators

## Slide 13
Community Impact Study (Marlinton, WV)
Community Scale
Floodplain Building Ratio
266 Flood-Prone Communities
94% of WV Communities have Special Flood Hazard Areas (SFHA)
Marlinton, WV
Flood Risk Indicator

## Slide 14
Flood Visualization (Marlinton, WV)
Community Scale
Greenbrier River
Knapp Creek
309 8th St, Marlinton, WV, 24954
FEMA 1% Annual Chance (100-year)
26% probability of flooding at least once over 30 years
309 8th St, Marlinton, WV

## Slide 15
Flood Visualization (Marlinton, WV)
Building Scale
309 8th St, Marlinton, WV, 24954
7’ (1985 High Water Mark)
8.8’ (Preliminary NFHL 0.2% / 500-Yr )
3.6’ (FEMA 1% / 100-Yr)
2.7’ (FEMA 2% / 50-Yr)
Building: 38-08-0003-0023-0000
5.2’ (FEMA Preliminary NFHL 1% / 100-Yr)
1985 Flood High Water Mark
Commercial Structure built in 1900

## Slide 16
Flood Risk Assessment (Marlinton)
High-Risk Effective & Advisory
1%-Annual-Chance (100-Yr) Floodplains
FLOODPLAIN AREA: High percentage of municipality’s area in Special Flood Hazard Area (SFHA)
WV Flood Tool link
Marlinton
Floodplain Characteristics
High percentage of community in in flood zone
Building Counts
High building counts in SFHA and floodway
Floodway
Damage Loss $
High percentage of previous losses
BUILDING COUNTS: Marlinton has the highest number of structures in the floodway of all incorporated places
1
DAMAGE LOSS: Marlinton has a high percentage of repetitive loss structures and flood loss claims ($)
Top 10% rankings among 229 incorporated places
People
Many residents displaced from major flood event
PEOPLE: High number of people reside in high-risk flood zone

## Slide 17
Critical Infrastructure (Marlinton)
INFRASTRUCTURE: High number of essential facilities and roads subject to flooding from a major event
WV Flood Tool link
Marlinton
Top 10% rankings among 229 incorporated places
Critical Infrastructure
High number of essential facilities & flooded roads
Flooded fire station in Marlinton, Nov. 1985
Marlinton Police Department
Highest EF Flood Depth (4 ft)
(Building ID: 38-08-0001-0096-0000_709A)
Pocahontas Center (Nursing Home)
(Building ID: 38-08-0005-0065-0002_5)

## Slide 18
Community Assets (Marlinton)
WV Flood Tool link
Marlinton
COMMUNITY ASSETS: Marlinton has a high percentage community assets including historical
Top 10% rankings among 229 incorporated places
Community Assets
High number of non-historical community assets
Marlinton Water Plant
Highest Non-Hist. CA Value ($8.9M)
(Building ID: 38-08-0005-0088-0000_1002)
Value source inflation adjustment to 2021
Marlinton Opera House
Highest Hist. CA Depth (4.7 ft) & Value ($148K)
(Building ID: 38-08-0002-0159-0000_818)

## Slide 19
Partnerships and Interagency Coordination