## Slide 1: Unit 5: Substantial Improvement/Substantial Damage

## Slide 2: E0273 Course Map Unit 5

## Slide 3: Unit 5 Objective
After completing this unit, you should be able to:
  Identify the NFIP requirements related to Substantial Improvement/Substantial Damage (SI/SD)

## Slide 4: Why is Determining SI/SD Important?
  Reduce number of buildings exposed to flood damage
  Lower flood insurance
  Protect people and property
  More compliant structures
Making SI/SD determinations is a challenge, particularly after major flooding events

## Slide 5: Substantial Improvement (Part 1 of 2)
Substantial improvement means any reconstruction, rehabilitation, addition, or other improvement of a structure, the cost of which equals or exceeds 50 percent of the market value of the structure before the “start of construction” of the improvement.
Includes structures which have incurred "substantial damage,'' regardless of the actual repair work performed.
Community must make the "substantially improved" determination

## Slide 6: What is included in cost of Substantial Improvement?
  Reconstruction cost
  Rehabilitation cost
  Cost of addition
  Cost of any other improvements
Substantial improvement of any structure in the floodplain is considered new construction under the local floodplain ordinance.

## Slide 7: Substantial Improvement: Special Cases
  Alteration of a “historic structure”
  Correcting previously cited violations:
    Health codes
    Sanitary codes
    Safety codes

## Slide 8: Examples: Exterior and Interior Improvements

## Slide 9: What Makes it Substantial?
Improvement costs must be equal or greater than 50% of the market value of the structure

## Slide 10: Discussion: Improvement Costs
How do you determine the total costs of improvement? How do you know it is approaching 50%?

## Slide 11: Estimating Improvement Costs
  Itemized estimates from licensed contractors or design professionals
  Professional estimating guidelines
  Independent professional estimators

## Slide 12: Market Value
Market value can be determined by:
  Recent independent appraisals by a professional appraiser
  Replacement cost, only if depreciated
  Tax assessor data (structure only)
However you do it, be consistent

## Slide 13: Substantial Improvement (Part 2 of 2)
(Cost of Improvement) / (Market Value) 100 = X%
  Check the Substantial Improvement/Substantial Damage Desk Reference and the Items to be Included and Excluded tables
  Ratios between 40% - 60% merit a second look
  Community should require precise cost determination methods for close calls

## Slide 14: Activity 5.1: Substantial Improvement Case Study
Whole group discussion
Case Study #1--Addition to a Restaurant
  Read the scenario and information provided in your Student Manual
  Answer the questions

## Slide 15: Activity 5.1: Substantial Improvement Case Study
  Total cost of constructing the proposed addition: $325,000
  Appraised value of property: $645,000
  Appraised value of the structure: $600,000
  Appraised value of the land: $45,000
Considering only the information provided, is this a Substantial Improvement?
As the local Floodplain Administrator, is there more you should ask yourself as you determine whether this is a Substantial Improvement?

## Slide 16: Substantial Improvement/Substantial Damage
  Substantial improvement: Cost to rebuild/improve a structure in the Special Flood Hazard Area (SFHA), whether damaged or not, is equal to or more than 50 percent of market value prior to work
  Substantial damage: Cost to restore a structure in the SFHA to pre-damage condition equals or exceeds 50 percent of the market value of the structure before damage occurred

## Slide 17: What is Damage?
  Any source (fire, tornado, car or tree impacts the building)
  Structures in the SFHA

## Slide 18: Substantial Damage
A Substantially Damaged structure must meet the following conditions:
  Located in the Special Flood Hazard Area(SFHA)
  Non-compliant with current floodplain standards
  Formally declared substantially damaged by community authority
  Cost of post-damage repair ≥ 50 percent of pre-damage market value
  Pre-Flood Insurance Rate Map (FIRM) and Post-FIRM

## Slide 19: Why is Determining Substantial Damage Important?
  Structures in the SFHA damaged by fire, tornado, or any other cause are subject to Substantial Damage ordinance provisions.
  Repair/rebuilding:
    Automatically becomes a Substantial Improvement
    Must meet current design requirements of local regulations
    Must meet other identified health, sanitary, or safety code requirements

## Slide 20: Community Responsibility
The community is the only entity that can make a substantial improvement/substantial damage determination.
  Must assure accuracy and consistency of:
    Full cost of improvements or repairs.
    Market value of structure.
  Only local community can make a Substantial Damage determination
  Must issue a determination letter
  Must have an appeal process
  Must assure:
    Accuracy of improvement cost and actual repair/damage value
    Consistent market value estimates

## Slide 21: Making Substantial Damage Determinations
FPAs administer SI/SD requirements by:
  Requiring permits for improvements and repairs
  Determining improvement and repair costs
  Determining market value of structures
  Making the Substantial Improvement/Substantial Damage determinations
FPAs administer Substantial Damage (SD) requirements by:
  Determining repair costs
  Determining market values
  Making SD determinations
  Requiring appropriate permits

## Slide 22: Market Value vs. Replacement Cost
  Market value is the actual cash value of the structure
  Market value does not equal replacement cost
  Replacement cost may be used to estimate market value only if depreciated

## Slide 23: Recommendations
  Adopt a conservative method for determining market value
  Seek accuracy, use precise methods for close calls
  Apply structure value and improvement cost methods consistently
  If applicant objects to the estimate, allow option to provide a certified appraisal
  Develop an appeals process for disagreements on appraisals

## Slide 24: Activity 5.2: Substantial Damage Case Study
Whole group discussion
Case Study #2--Substantially Damaged?
Discuss the image on the slide
Answer the questions:
  How likely is this residence to be found Substantially Damaged?
  What do you see in this photograph that leads you to form this opinion?

## Slide 25: Higher Standards for SI/SD
  Cumulative Substantial Improvements
  Repetitive loss property
  Lower SI/SD threshold
  Historic structures

## Slide 26: Activity 5.3: Unit 5 Communication Corner
How would you answer these questions from property owners?
  Why do I have to have a permit for repairs?
  Can I do half of it now and half later?
  Why do I have to mitigate if my house wasn’t flooded?

## Slide 27: Activity 5.4: Unit 5 Knowledge Check
Table group activity
  The instructor will assign each group a topic discussed in this unit.
  Table groups will summarize the key points for their topic(s).