## Slide 1
Kurt Donaldson, GISP, CFM
5/20/2025 WV Assessors Conference
Member, Property Valuation Training & Procedures Commission
Manager, WV GIS Technical Center, WVU (kdonalds@wvu.edu)
GIS Data Development

## Slide 2
Key Reference Layers: GIS Data Development
Parcels Addresses Aerial Imagery Boundaries Elevation
Local and State Spatial Data Infrastructures
Parcel geometry not misaligned or shifted
Assessment attributes of improvements or structures tagged to correct parcel
E-911 addresses current and accurate
County Leaf-off imagery < than 5 years
Statewide 1-meter DEM and 1-ft. contours.
Current and Accurate Cadastral, Legal, & Election Boundaries

## Slide 3
Data Development & Integration
  Local-Level  Data Development
  State-Level  Integration

## Slide 4
State-Level Integration
Parcels
Addresses
SOURCE: County Assessors
WV Property Tax Division
Statewide Master Parcel File / IAS
SOURCE: Local Addressing Offices
WV Emergency Management Division
Statewide Addressing & Mapping System
State-level integration allows for statewide mapping products and services.
At the state level, WVGISTC creates and hosts these framework spatial data layers.
SOURCE: County Offices
WV GIS Technical Center
Statewide Leaf-Off Imagery Service
Imagery
SOURCE: Local, State, Federal
WV GIS Technical Center
Statewide Elevation Web Services
Elevation
SOURCE: Local Offices, County Clerks
WV GIS Technical Center
Statewide Boundary Web Services
Boundaries
LOCAL DATA SOURCE
STATE INTEGRATION
STATE WEB SERVICES (WVGISTC)

## Slide 5
Map Reference Layers
Aerial Imagery
Accessibility to quality, up-to-date aerial photography

## Slide 6
Statewide Imagery Contract (2019-25)
Vendor: Thrasher Group.
Flying Season: February to Mid-April (during leaf-out and no snow conditions).
Non-Exclusive Contract: County offices still had the option to contract with other companies for the same services.
Public Domain: State-contracted “top-down” aerial imagery resides in the public domain.
Oblique Imagery: Not part of contract; oblique imagery usually requires proprietary software.
Pixel Resolution (Detail Level) | 3-inch | 4-inch | 6-inch | 12-inch
Cost per square mile1,2 | $106 | $77 | $62 | $42
Map Scale | 1” = 50’ | 1” = 67’ | 1” = 100’ | 1” = 200’
Horizontal Accuracy (ASPRS 1) | 0.5 feet | 0.66 feet | 1.0 feet | 2.0 feet
Unit Costs: All counties using the state contract typically acquire imagery at 4- or 3-inch pixel resolution.
1 2.5% annual inflation rate increase 2 The county border buffer is 1000 feet

## Slide 7
County Aerial Imagery: Year Acquired
Some counties fly annually or every two years
Ideally, leaf-off imagery should not be older than 5 years
PDF Map
Trend: More counties are routinely purchasing aerial imagery
Make sure “top-down” imagery is licensed to county for sharing purposes

## Slide 8
Statewide Mosaic
WV GIS Technical Center creates a statewide mosaic of county imagery from different county acquisition dates, formats (e.g., GeoTIFF, MrSID), and resolutions
PDF Map
West Virginia does not have a statewide orthophoto program
WV Leaf-Off Mosaic Imagery Map Service

## Slide 9
County Aerial Imagery: Vendor
6 companies have acquired imagery for counties
Select counties for 2019-22 received funding support through HMGP grant
PDF Map
Majority of counties have been acquired via the state contract

## Slide 10
County Aerial Imagery: Resolution
Aerial Imagery of most counties (98%) is captured at a countywide spatial cell resolution of 6 inches or higher
Select counties for 2019-22 received funding support through HMGP grant
PDF Map
Trend: Past decade spatial resolution has increased from 12” to 6”, with more counties flying 3”
A target spatial resolution of 6” is recommended for counties that can afford this level of detail

## Slide 11
Resolution (Cows in Wayne Co.)
Cows in the Floodway
West Fork Twelvepole Creek, Wayne County
Choose WV Best Leaves Off Base Map
4-Inch Pixel Resolution
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9176629&y=4583554&l=13&v=1

## Slide 12
Resolution (Eagle in Pendleton Co.)
Bald Eagle in Pendleton County
6-Inch Pixel Resolution

## Slide 13
Map Reference Layers
Parcels / Assessment Records

## Slide 14
Digital Parcel Mapping in 2004
In 2004 only five counties had GIS parcels.
Early digital parcels systems were CAD and not GIS.
GIS ADVANTAGE
Geographic Information Systems (GIS) link to IAS
By 2021 all 55 counties had converted their tax maps from paper to digital
January 2004

## Slide 15
Tax Map Maintenance in 2013
In 2013, 20 counties outsourced their tax map maintenance
In 2025, 37counties outsource their tax map maintenance

## Slide 16
Digital Parcel Mapping in 2014
In 2014, 39 counties had GIS parcels
By 2021, all 55 counties had converted their tax maps from paper to digital

## Slide 17
In 2015… Future Mapping 15-YR Predictions
All 55 counties will have adopted GIS mapping
  Successful State Digital Maintenance Program
  Digital Conversion Funding Support from State
The Property Tax Division will have integrated all 55 counties into a seamless GIS database linked to the IAS and viewable to authorized users
Map maintenance and publishing standards for manually drafting paper tax maps will be dropped
Funding from FEMA Grant (2019-2021)
Open Public Access
Revised Tax Map Procedural Rule 189-3 standard needs to be published

## Slide 18
Digital Parcel Mapping in 2025
MAP MAINTENANCE
All counties use GIS
67% of counties outsource map maintenance
Trend: More counties are outsourcing their tax maintenance
COUNTY TAX MAP VIEWER
85% of counties have public online viewers
PDF Map

## Slide 19
Tax Map Issue 1: Parcel Misalignment
Parcel Shift
Tax parcel geometry shifted or misaligned
Tax maps do not represent legal boundaries but should be remapped when parcels are shifted and do not align with the correct structure on accurately geo-referenced aerial photography

## Slide 20
Tax Map Issue 2: IAS-Parcel Mismatches
816FP
817
819FP
824FP
826FP
813FP
812FP
808FP
807FP
Harry’s Market
814FP
811FP
809
USACE Tract 812FP: Switch IAS Records of Parcels 43A-17 and 43A-11
USACE Tract 811FP: Copy IAS Record IAS 43A-11.1 to IAS Record 43A-12
USACE Tract 808FP: Replace IAS Record 43A-22 with IAS Record 43A-27
USACE Tract 809: Copy IAS Record/Geometry of 43A-24.1 to north end of 43A-22
Replace IAS Record 43A-25.2 with IAS Record 43A-22
USACE 2006 Nonstructural O&M Manual (Page 96)
IAS-Parcel Mismatches
Missing IAS records or parcel geometry
IAS records mapped erroneously to wrong parcel, or not tagged to parcel with location of improvement

## Slide 21
Tax Map Issue 3: Outside Parcels
Outside County Parcel Viewer | Graphic 1 | Graphic 2 | Assessor & County Clerk Transfer Recommendations
Fall 2023 Audit
Hardy County
Hampshire County
Outside Parcels Parcels assessed in the wrong county

## Slide 22
Tax Map Issue 4: E-911 Addresses
Parcel Physical Address
IAS physical address of parcel should be E-911 address

## Slide 23
Daniel’s Privacy Law
§ 5A-8-24. Protection of personal information relating to judicial officers, prosecutors, and law-enforcement officers. Effective: July 9, 2021
When we receive Daniel’s Law requests, we perform the following actions on the following statewide geodatabases:
· E-911 Address: Coordinate with WV Emergency Management Division. Flag the address in the E-911 database as a “sensitive record” and do not display the address label on applications.
· Parcel Record: Coordinate with WV State Tax Department. Remove the owner's name, address, and legal description from the tax assessment database while preserving the parcel geometry. Update the data records on the Data Clearinghouse so sensitive parcel records cannot be downloaded. County assessors are responsible for redacting “covered people” from their publicly accessible databases and map viewers.
· State Voter Registration System (SVRS): Coordinate with the Secretary of State’s Office which is responsible to set a sensitive flag for voting records in the SVRS
Chart: Daniel's Law Redacted Parcel Records (n=20)
| Berkeley | Cabell | Greenbrier | Jefferson | Kanawha | Mercer | Morgan | Ohio | Pocahontas | Putnam
Count | 2 | 7 | 1 | 1 | 2 | 1 | 1 | 3 | 1 | 1

## Slide 24
Map Reference Layers
Boundaries

## Slide 25: Kimball, McDowell County
51 primary structures in current Kimball municipality
85 primary structures in revised Kimball municipality
Legal Boundaries (Municipal)
Previously Incorrect Boundary
Correct Boundary
Legal Boundaries
Official municipal boundary changes need to be submitted to the State and U.S. Census BAS Program
Tax Boundaries: Corporation Tax District Boundaries & Tax Sales
Election Boundaries: Municipal Precincts & Census Redistricting
Legal Boundaries are referenced in many applications such as floodplain management

## Slide 26
Map Reference Layers
Elevation (Topographic)

## Slide 27
Elevation Data
This past decade FEMA purchased $10 million QL2 LiDAR (2012-2020) consisting of 6 major project acquisitions
Quality 2 (QL2) LiDAR support 1-foot contours
PDF Map
2020
2012
2020
2019
2017
2016
2017

## Slide 28
Kurt Donaldson, GISP, CFM
5/20/2025 WV Assessors Conference
Member, Property Valuation Training & Procedures Commission
Manager, WV GIS Technical Center, WVU (kdonalds@wvu.edu)
Contact: