## Slide 1: Flood Risk Review Meeting
FEMA Region 3
Flood Risk Review Meeting
Morgan County, WV - May 9, 2025

## Slide 2: Agenda
Welcome and Introductions
Where We Are - Draft Maps
Flood Study Update
Using Flood Risk Data to Reduce Risk
Floodplain Management
Discussion

## Slide 3: Introductions
  Please Introduce Yourself
  Name.
  Position.
  Organization.

## Slide 4: Where We Are – Draft Maps

## Slide 5: 3 Reasons We Are Here Today
To preview and discuss the updated Flood Insurance Study (FIS) report and Flood Insurance Rate Map (FIRM) for Morgan County, West Virginia
To examine the new study areas, discuss how the analysis and mapping have changed since the previous FIRM, and discuss current and future implications for these changes
To present a timeline of next steps

## Slide 6: Timeline – Looking Back
Advisory Flood Height Modeling/Mapping
~2012
Kick-Off Meeting
November 2021
Risk MAP Study Notification
October 2021 and November 2022
Flood Risk Review Meeting
Preliminary Maps and CCO Meeting
Appeal Period Start
End of Appeal Period
FEMA Issues Letter of Final Determination (LFD)
Updated Effective Maps
Current Effective Maps (Digital Conversion)
September 2009

## Slide 7: Timeline – Looking Ahead
Advisory Flood Height Modeling/Mapping
Kick-Off Meeting
Risk MAP Study Notification
Flood Risk Review Meeting
May 9, 2025
Preliminary Maps and CCO Meeting
Fall/Winter 2025
Appeal Period Start
Spring 2026
End of Appeal Period
90 days after Appeal Start
FEMA Issues Letter of Final Determination (LFD)
Fall/Winter 2026
Updated Effective Maps
6 months after LFD
Current Effective Maps (Digital Conversion)

## Slide 8: Flood Study Update

## Slide 9: Flood Insurance Rate Maps and Studies
Key Terms:
Flood Insurance Rate Map (FIRM)
Flood Insurance Study (FIS) Report
Special Flood Hazard Area (SFHA)
Flood Zone
Base Flood Elevation (BFE)
Regulatory Floodway
Cross Section

## Slide 10: Typical FIRM Panel and Flood Zones
Zone AE
Floodway
Zone AE
Zone X
Shaded
Zone X
Zone A

## Slide 11: Floodplain Map Overview
HIGH RISK (Special Flood Hazard Area) |  |  | Regulatory Floodway
 |  |  | 1%-Annual-Chance Flood Hazard Area with BFEs
 |  |  | 1%-Annual-Chance Flood Hazard Area without published BFEs
MODERATE RISK |  |  | 0.2%-Annual-Chance Flood Hazard Area
 |  |  | Cross Sections with 1%-Annual-Chance Water Surface Elevation Value
ZONE AE
ZONE A
Notes: Discuss 1% floodplain and 0.2% floodplain, floodway, cross sections, and BFEs
“Cross sections now show water surface elevations.”
“Transparent fills over aerial photography”
“new maps will look different”

## Slide 12: Floodplain Map Overview
HIGH RISK (Special Flood Hazard Area) |  |  | 
MODERATE RISK |  |  | 
 |  |  | Cross Sections with 1%-Annual-Chance Water Surface Elevation Value
ZONE AE
ZONE A
Development is not allowed unless “no rise” in flood levels is certified
Flood insurance is mandatory for structures with federally backed mortgages
Flood insurance is not mandatory
Notes: It is highly recommended that owners get flood insurance in areas of moderate risk even though it is not required

## Slide 13: Study Overview
Revised Modeling and Mapping, including:
        Updated GIS-based regulatory products, including:
          Updated FIRMs / GIS database / FIS report formats based on new FEMA guidelines and specifications
        High-resolution topographic data (for modeling and mapping)
        Detailed “Zone AE” Studies – 22 miles
        Model-backed Approximate “Zone A” Studies – 165 miles
        Floodplains on the Potomac River are NOT being updated as part of this study

## Slide 14: Study Overview (continued)
Revised Modeling and Mapping, including:
        Evaluation of Letters of Map Change (LOMCs)
          Case-by-case results shown in a Summary of Map Actions (SOMA) that is sent to applicable communities with Preliminary Maps and Letters of Final Determination (LFDs)
          Letters of Map Revision (LOMRs)
          Letters of Map Amendment (LOMAs) – including rectified LOMA locations on the WV Flood Tool
      Production of associated non-regulatory flood risk
Notes: Presenter should define LOMC, LOMA, LOMR, and talk about reasons why some LOMCs might be revalidated, incorporated, or superseded.

## Slide 15: Study Area

## Slide 16: Topographic Data
2012 LiDAR-Based Digital Elevation Model LiDAR = Light Detection and Ranging
  Uses light pulses and GPS to survey elevation data
  Improves the level of detail for hydraulic modeling and floodplain delineation

## Slide 17: Hydrologic Analyses
Hydrologic study methods included:
  USGS Regression Equations
  Regression Equations Supplemented with USGS Gage Analysis (Bulletin 17C)
  HEC-HMS 4.10, Rainfall-Runoff for Davis Road Run, Warm Spring Run, and Yellow Run.
A comprehensive Hydrology Report details the study methods for each reach and compares the effective and proposed discharges.
The hydrologic study methods will be summarized and published in the forthcoming FIS Report.
Sample page from the Risk MAP Hydrology Report
Notes: The study used updated hydrologic analyses to estimate 1-percent-annual-chance flow rates.

## Slide 18: Hydraulic Analyses – Zone A
Approximate “Zone A” Base Level Study (165 miles)
Generally used in areas with lower development or lower development potential
Cross sections generated from LiDAR
  Does not include channel bathymetry
  No hydraulic structures are surveyed or modeled
FIRMs will not show Floodway or BFEs (but FIRM database will include cross sections and their associated water surface elevations in the FIRM GIS Database)
FIS Report will not show flood profiles for Zone A reaches

## Slide 19: Hydraulic Analyses – Zone AE
Detailed “Zone AE” Study (22 miles)
Generally used in areas with higher development or higher development potential
Cross sections use information from survey and field reconnaissance
  Include channel bathymetry
  Structures are modeled (e.g., culverts, bridges)
Detailed hydraulic parameter refinement (coefficients, obstructions, Manning's ‘n’ values)
FIRMs will show Floodway, BFEs, 1% and 0.2%-annual-chance event floodplains
FIS Report will show flood profiles for 10-, 4-, 2-, 1-, 0.2-, and 1% Plus flood frequencies

## Slide 20: LOMCs and SOMAs
Summary of Maps Actions (SOMA)
Forthcoming with preliminary maps and again with Letters of Final Determination (LFDs)
Identifies previously issued Letter of Map Change (LOMCs) and how those determinations are impacted by the new mapping effort.

## Slide 21: Study Impacts

## Slide 22: Significant Impacts Overview
Compared to the effective FIRMs, widening and narrowing of draft 1%-annual-chance floodplain (SFHA) extents were observed throughout the county.
  SFHA increases: Sleepy Creek
  SFHA decreases: Cacapon Creek, Warm Spring Run
Extended study reaches (with drainage areas of 1 square miles and greater, and not on current effective FIRMs) result in new properties within the SFHA.
More structures will be mapped out than mapped in: -200/ +70
WV Flood Tool – SFHA Future Map Conditions*
Community | No Change SFHA | Mapped In SFHA | Mapped Out SFHA | Total Structures
Bath, Town of | 381 (+1 Floodway) | 206 (+1 Floodway) | 153 | 742
Morgan County, Unincorporated Areas | 39 (+6 Floodway) | 21 | 19 | 85
Total | 420 (+7 Floodway) | 227 (+1 Floodway) | 172 | 827
* Town of Hedgesville does not have any SFHA

## Slide 23: Flood Risk Dashboard
NFIP FLOOD CLAIM
PAYOUTS
CLAIMS OUTSIDE OF THE SFHA
NFIP FLOOD
POLICIES
HIGH-RISK
STRUCTURES
REPETITIVE
LOSSES
AVERAGE PREMIUM
AFFECTED RESIDENTS

## Slide 24: Flood Risk Dashboard
Notes: Messaging - how are you going to message to your community about these new maps.

## Slide 25: Flood Risk Dashboard (page 2)
Notes: This is the second page of the jurisdictional dashboard.

## Slide 26: Flood Risk Dashboard
Notes: Messaging - how are you going to message to your community about these new maps.

## Slide 27: Flood Risk Dashboard
Notes: Messaging - how are you going to message to your community about these new maps.

## Slide 28: Flood Risk Dashboard
Notes: Messaging - how are you going to message to your community about these new maps.

## Slide 29: How Did the Floodplain Maps Change?
FEMA Region 3 Changes Since Last FIRM (CSLF) Viewer: https://arcg.is/1HmKLT1
Change in Floodplain Extents:
  Purple – Decrease
  Blue – Still Floodplain
  Yellow – Increase
*Map view has scale-dependent layers

## Slide 30: West Virginia Flood Risk Tool
WV Flood Tool (mapwv.gov)

## Slide 31: Using Flood Risk Data to Identify and Reduce Risk

## Slide 32: FEMA Flood Risk GIS Datasets
Flood Depth
and Analysis
Grids
Changes Since Last FIRM
Water Surface Elevation
Grids
Flood Risk
Assessment

## Slide 33: Where to Find Flood Risk Data
FEMA’s Flood Map Service Center (MSC)
  Here, you can view effective maps online. You can also download current effective flood hazard data and additional hazard and risk data.
  https://msc.fema.gov/portal/home
National Flood Hazard Layer (NFHL)
  This geospatial data viewer contains current effective flood hazard data.
  https://www.fema.gov/flood-maps/national-flood-hazard-layer
State Flood Tool
  This geospatial data viewer contains current effective flood hazard data and additional hazard and risk data.

## Slide 34: Where Can I Find My Flood Maps?
The FEMA Map Service Center (MSC) is the official public source for flood hazard information: https://msc.fema.gov/portal/home.
Enter an address for location search

## Slide 35: National Flood Hazard Layer
The NFHL shows the effective FEMA flood map data, including Letters of Map Revision (LOMRs).Visit https://www.fema.gov/national-flood-hazard-layer-nfhl for multiple options to view and download NFHL data.

## Slide 36: Additional Hazard and Risk Data
If additional hazard and risk data are available for your community, the MSC Search Results will allow you to expand the Flood Risk Products folder.

## Slide 37: Water Surface Elevation Grids
Represents the continuous water surface elevations (as determined at modeled cross sections and interpolated between cross sections) for each of the modeled flood frequencies.

## Slide 38: Depth Grids
Represents the difference between the ground surface elevation and the water surface elevations in feet for each of the modeled flood frequencies.

## Slide 39: West Virginia Flood Tool
WV Flood Tool (mapwv.gov)

## Slide 40: West Virginia Risk Explorer
New Building-Level Risk Tools enable further exploration of impacted buildings:
  Berkeley Mapped-In Structures
  Berkeley Mapped-Out Structures
  Berkeley Risk Index (incl. Top 20% Risk Indicators Report)

## Slide 41: West Virginia Risk Explorer
New Building-Level Risk Tools enable further exploration of impacted buildings:
  Berkeley Mapped-In Structures
  Berkeley Mapped-Out Structures
  Berkeley Risk Index (incl. Top 20% Risk Indicators Report)

## Slide 42: Flood Hazard Mitigation Planning
It’s time to update the risk assessment in your hazard mitigation plan
The Berkeley County HMP is here

## Slide 43: Using Flood Risk Data to Manage Development
Structure-based depth of flooding analyses
Prioritization of mitigation action
Residential/commercial density in the floodplain
Location/inundation area of historic events
Properties with insurance policies and as a percentage of the population
Areas of population growth
Areas requiring protection

## Slide 44: Floodplain Management

## Slide 45: Flood Risk Doesn’t Stop at a Line
40% of all flood insurance claims come from outside high-risk areas.
Your community can regulate to standards higher than the NFIP minimum standards. Consider strengthening regulations using:
  0.2%-annual-chance flood zone
  “Freeboard” – require additional feet above a BFE
  Buffer around SFHA
  Flood depth grids
HURRICANE HARVEY
GREATER HOUSTON

## Slide 46: Floodplain Management at FRR
Look at where there are changes to the SFHA in your community
Share with permitting, planning, and other colleagues to direct development outside of the SFHA today and in future
Consider higher standards or joining the Community Rating System to support your community
FRR:
SFHA:
Flood Risk Review
Special Flood Hazard Area
Notes: It is not too early to plan ahead.

## Slide 47: Floodplain Management Big Picture
Build it right and lower the impact of future flood losses while improving resiliency | Build it wrong and the result could be increased flood losses and higher flood insurance premiums
Notes: Where it rains it can flood - A significant number of NFIP claims are outside the SFHA
Flood risk changes
  FRR draft maps represent change for you community
  Climate change could further increase flood risk in your community

## Slide 48: Discussion

## Slide 49: Timeline – Looking Ahead
Advisory Flood Height Modeling/Mapping
Kick-Off Meeting
Risk MAP Study Notification
Flood Risk Review Meeting
May 9, 2025
Preliminary Maps and CCO Meeting
Fall/Winter 2025
Appeal Period Start
Spring 2026
End of Appeal Period
90 days after Appeal Start
FEMA Issues Letter of Final Determination (LFD)
Fall/Winter 2026
Updated Effective Maps
6 months after LFD
Current Effective Maps (Digital Conversion)

## Slide 50: Project Contacts – West Virginia
State NFIP/CTP Office:
Ginger Barnett
Chief of Mitigation and Recovery
304-414-7632
ginger.sc.barnett@wv.gov
Kevin Sneed
CTP Project Officer
304-957-2571
kevin.l.sneed@wv.gov
FEMA Region 3:
Amanuel Ghebreegziabher FEMA Project Officer (202) 718-2759 amanuel.ghebreegziabher@fema.dhs.gov
Bill Kuhn Community Planner william.kuhn@fema.dhs.gov
Betsy Ranson
Floodplain Management Specialist (215) 347-0686
elizabeth.ranson@fema.dhs.gov
Bill Bradfield
Insurance Specialist (202) 880-5906 william.b.bradfield@fema.dhs.gov
Julia Sears
State NFIP Coordinator
304-989-8330
julia.r.sears@wv.gov

## Slide 51: Department of Homeland Security logo - FEMA