## Slide 1: Template Notes
FEMA Region 3 has developed this template to:
      Ensure some level of consistency between Risk MAP meetings and
      Integrate key messages related to flood mapping, floodplain management, hazard mitigation planning and flood insurance.
Please do not add or remove content without consulting the Risk Analysis Branch Project Officer for this project.
The Flood Study Update section has more flexibility, It can be modified to reflect the engineering methodologies for this project. However, FEMA still wants some level of consistency.
Please keep the methodology section clear and concise.
Use bullet points, avoid too much text, and avoid tables showing methods for each stream.
There are typically 1-2 slides on hydrologic analyses and 2-5 slides on hydraulic analyses.
This presentation template was last updated in Summer 2024, in coordination with Lee Brancheau, Mari Radford, Bobby Cobelli, Bill Bradford, and Benjamin Accurti.

## Slide 2
FEMA Region 3
Flood Risk Review Meeting
Wyoming County May 30, 2025

## Slide 3: Agenda
Welcome and Introductions
Where We Are - Draft Maps
Flood Study Update
Using Flood Risk Data to Reduce Risk
Floodplain Management
Discussion

## Slide 4: Introductions
  Please Introduce Yourself
  Name.
  Position.
  Organization.

## Slide 5: Where We Are – Draft Maps

## Slide 6: 3 Reasons We Are Here Today
To preview and discuss the updated Flood Insurance Study (FIS) report and Flood Insurance Rate Map (FIRM) for Mercer County, West Virginia
To examine the new study areas, discuss how the analysis and mapping have changed since the previous FIRM, and discuss current and future implications for these changes
To present a timeline of next steps

## Slide 7
Timeline
Updated Effective Maps
Preliminary Maps and CCO Meeting
Appeal Period Start
FEMA Issues Letter of Final Determination (LFD)
Current Effective Maps
May 2006
Discovery Meeting
Risk MAP Study Notification
August 2021
Flood Risk Review Meeting
05/30/2025
End of Appeal Period
We are here!
Notes: Notification means 620 letter?
Put a start at FRR and show we are here

## Slide 8: Flood Study Update

## Slide 9: Flood Insurance Rate Maps and Studies
Key Terms:
Flood Insurance Rate Map (FIRM)
Flood Insurance Study (FIS) Report
Special Flood Hazard Area (SFHA)
Flood Zone
Base Flood Elevation (BFE)
Regulatory Floodway
Cross Section

## Slide 10: Typical FIRM Panel and Flood Zones
Zone AE
Floodway
Zone X
Shaded
Zone X
Zone AE
Zone A

## Slide 11: Floodplain Map Overview
HIGH RISK (Special Flood Hazard Area) |  |  | Regulatory Floodway
 |  |  | 1%-Annual-Chance Flood Hazard Area with BFEs
 |  |  | 1%-Annual-Chance Flood Hazard Area without published BFEs
MODERATE RISK |  |  | 0.2%-Annual-Chance Flood Hazard Area
 |  |  | Cross Sections with 1%-Annual-Chance Water Surface Elevation Value
ZONE AE
ZONE A
Notes: Discuss 1% floodplain and 0.2% floodplain, floodway, cross sections, and BFEs
“Cross sections now show water surface elevations.”
“Transparent fills over aerial photography”
“new maps will look different”

## Slide 12: Floodplain Map Overview
HIGH RISK (Special Flood Hazard Area) |  |  | 
MODERATE RISK |  |  | 
 |  |  | Cross Sections with 1%-Annual-Chance Water Surface Elevation Value
ZONE AE
ZONE A
Development is not allowed unless “no rise” in flood levels is certified
Flood insurance is not mandatory
Flood insurance is mandatory for structures with federally backed mortgages
Notes: It is highly recommended that owners get flood insurance in areas of moderate risk even though it is not required

## Slide 13
Study Overview
Revised Modeling and Mapping, including:
        Updated GIS-based regulatory products, including:
          Updated FIRMs / GIS database / FIS report formats based on new FEMA guidelines and specifications
        Used high-resolution topographic data (for modeling and mapping)
        “Zone AE” Studies – 158 miles
        Model-backed“Zone A” Studies – 263 miles
Notes: Update the number of miles

## Slide 14
Study Overview (continued)
Revised Modeling and Mapping, including:
        Evaluation of Letters of Map Change (LOMCs)
          Case-by-case results shown in a Summary of Map Actions (SOMA) that is sent to applicable communities with Preliminary Maps and Letters of Final Determination (LFDs)
          Letters of Map Revision (LOMRs)
          Letters of Map Amendment (LOMAs) – including rectified LOMA locations on the WV Flood Tool
      Production of associated non-regulatory flood risk
Notes: Presenter should define LOMC, LOMA, LOMR, and talk about reasons why some LOMCs might be revalidated, incorporated, or superseded.
We need to check if all these apply for wyoming

## Slide 15: Study Area
The Project Area
Notes: The legend has McDowell County

## Slide 16: Topographic Data
2018-2020 LiDAR-Based Digital Elevation Model (DEM – 2’ contours on WV Flood Tool) LiDAR = Light Detection and Ranging
  Uses light pulses and GPS to survey elevation data
  Improves the level of detail for hydraulic modeling and floodplain delineation

## Slide 17: Hydrologic Analyses
Hydrologic study methods included:
  USGS Regression Equations
  Regression Equations Supplemented with USGS Gage Analysis (Bulletin 17C)
  Regulated Flow Analysis
A comprehensive Hydrology Report details the study methods for each reach and compares the effective and proposed discharges.
The hydrologic study methods will also be published in the FIS Report.
Sample page from the Risk MAP Hydrology Report
Notes: The study used updated hydrologic analyses to estimate 1-percent-annual-chance flow rates.

## Slide 18: Hydraulic Analyses – Zone A
Approximate "Zone A" Base Level Study (263 miles)
Generally used in areas with lower development or lower development potential
Cross sections generated from LiDAR (automated processes)
  Does not include channel bathymetry
  No hydraulic structures are surveyed or modeled
FIRM will not show Floodway or BFEs (but FIRM database will include cross sections and their associated water surface elevations in the FIRM GIS Database)
FIS Report will not show flood profiles for Zone A reaches

## Slide 19: Hydraulic Analyses – Zone AE
Detailed "Zone AE” Study (158 miles)
Generally used in areas with higher development or higher development potential
Cross sections use information from survey and field reconnaissance
  Include channel bathymetry
  Structures are modeled (e.g., culverts, bridges)
Detailed hydraulic parameter refinement (coefficients, obstructions, Manning's ‘n’ values)
FIRM will show Floodway, BFEs, 1% and 0.2%-annual-chance event floodplains
FIS Report will show flood profiles for 10-, 4-, 2-, 1-, 0.2-, and 1% Plus flood frequencies

## Slide 20: Hydraulic Analyses – 1D vs 2D
1D: most existing NFIP studies; confined flow; flow generally in one direction
2D: unconfined, split/diverted flows; flow in multiple directions; wide/flat floodplains; shallow flooding
Reality
Notes: Remove this slide after Bob’s review because Wyoming does not have 2D

## Slide 21: Study Impacts

## Slide 22: Significant Impacts Overview
Compared to the effective NFHL, widening and narrowing of the 1%-annual-chance floodplain (SFHA) extent was observed throughout the county.
Extended study reaches (with drainage areas of 1 square miles and greater, and not on current effective FIRM) result in new properties within the SFHA.
Most streams experienced both increases and decreases when comparing the computed model WSELs to the current regulatory BFEs.
More structures will be mapped in than mapped out. Basic estimate: -423 / +972
Future Map Conditions
No Change SFHA | Mapped In SFHA | Mapped Out SFHA | Total Structures
2,089 | 972 | 423 | 3,061
Notes: Structure in out . Consult with WV GIS center?
Ask ale if she updated them

## Slide 23
Flood Risk Dashboard
NFIP FLOOD CLAIM
PAYOUTS
AVERAGE PREMIUM
NFIP FLOOD
POLICIES
REPETITIVE
LOSSES
HIGH-RISK
STRUCTURES
AFFECTED RESIDENTS
CLAIMS OUTSIDE OF THE SFHA

## Slide 24
Flood Risk Dashboard (Example in slide. Will update later)
Notes: Messaging - how are you going to message to your community about these new maps.
Update after Bob’s review

## Slide 25
Flood Risk Dashboard (page 2)
HMP EXPIRATION INFO
STEPS BEFORE PRELIMINARY ISSUANCE
STEPS AFTER PRELIMINARY ISSUANCE
FLOOD MITIGATION ACTIONS

## Slide 26
Flood Risk Dashboard (page 2)
Notes: This is the second page of the jurisdictional dashboard.

## Slide 27: How Did the Floodplain Maps Change?
FEMA Region 3 Changes Since Last FIRM (CSLF) Viewer: https://arcg.is/1GS0T80
Change in Floodplain Extents:
  Purple – Decrease
  Blue – Still Floodplain
  Yellow – Increase
*Map view has scale-dependent layers
Notes: Update the link after William puts our data on the tool

## Slide 28: Using Flood Risk Data to Identify and Reduce Risk

## Slide 29: FEMA Flood Risk GIS Datasets
Flood Depth
Grids
Water Surface Elevation
Grids
Changes Since Last FIRM
Notes: Removed Flood risk assessment picture. Don’t have it for upper guy but have it for Big Sandy

## Slide 30: Where to Find Flood Risk Data
FEMA’s Flood Map Service Center (MSC)
  Here, you can view effective maps online. You can also download current effective flood hazard data and additional hazard and risk data.
  https://msc.fema.gov/portal/home
National Flood Hazard Layer (NFHL)
  This geospatial data viewer contains current effective flood hazard data.
  https://www.fema.gov/flood-maps/national-flood-hazard-layer
State Flood Tool
  This geospatial data viewer contains current effective flood hazard data and additional hazard and risk data.

## Slide 31: Where Can I Find My Flood Maps?
The FEMA Map Service Center (MSC) is the official public source for flood hazard information: https://msc.fema.gov/portal/home.
Enter an address for location search

## Slide 32: National Flood Hazard Layer
The NFHL shows the effective FEMA flood map data, including Letters of Map Revision (LOMRs).Visit https://www.fema.gov/national-flood-hazard-layer-nfhl for multiple options to view and download NFHL data.

## Slide 33: Additional Hazard and Risk Data
If additional hazard and risk data are available for your community, the MSC Search Results will allow you to expand the Flood Risk Products folder.

## Slide 34: Water Surface Elevation Grids
Represents the continuous water surface elevations (as determined at modeled cross sections and interpolated between cross sections) for each of the modeled flood frequencies.

## Slide 35: Depth Grids
Represents the difference between the ground surface elevation and the water surface elevations in feet for each of the modeled flood frequencies.

## Slide 36: West Virginia Flood Risk Tool
WV Flood Tool (mapwv.gov)

## Slide 37: Flood Hazard Mitigation Planning
It’s time to update the risk assessment in your hazard mitigation plan
The West Virginia Region I HMP is here

## Slide 38: Using Flood Risk Data to Manage Development
Structure-based depth of flooding analyses
Prioritization of mitigation action
Residential/commercial density in the floodplain
Location/inundation area of historic events
Properties with insurance policies and as a percentage of the population
Areas of population growth
Areas requiring protection

## Slide 39: Floodplain Management

## Slide 40: Flood Risk Doesn’t Stop at a Line
40% of all flood insurance claims come from outside high-risk areas.
Your community can regulate to standards higher than the NFIP minimum standards. Consider strengthening regulations using:
  0.2%-annual-chance flood zone
  “Freeboard” – require additional feet above a BFE
  Buffer around SFHA
  Flood depth grids
HURRICANE HARVEY
GREATER HOUSTON

## Slide 41: Floodplain Management at FRR
Consider higher standards or joining the Community Rating System to support your community
Look at where there are changes to the SFHA in your community
Share with permitting, planning, and other colleagues to direct development outside of the SFHA today and in future
FRR:
SFHA:
Flood Risk Review
Special Flood Hazard Area
Notes: It is not too early to plan ahead.

## Slide 42: Floodplain Management Big Picture
Build it right and lower the impact of future flood losses while improving resiliency | Build it wrong and the result could be increased flood losses and higher flood insurance premiums
Notes: Where it rains it can flood - A significant number of NFIP claims are outside the SFHA
Flood risk changes
  FRR draft maps represent change for you community
  Climate change could further increase flood risk in your community

## Slide 43: Discussion

## Slide 44: We want to hear from you!
30-day review and comment period
WV Flood Tool: https://www.mapwv.gov/flood
Review the materials we will be sending you
We are available to answer questions
Talk about mitigation actions in your community
Thank you for your participation!

## Slide 45: Project Contacts – West Virginia
Kevin Sneed
CTP Project Officer
(304) 957-2571
kevin.l.snead@wv.gov
Bill Kuhn Community Planner william.kuhn@fema.dhs.gov
Julie Sears
State NFIP Specialist
(304) 989-8330
julia.r.sears@wv.gov
Bob Pierson FEMA Project Officer [(215) 931-5650 robert.pierson@fema.dhs.gov
Betsy Ranson
Floodplain Management Specialist (215) 347-0686
elizabeth.ranson@fema.dhs.gov
Bill Bradfield
Insurance Specialist (202) 880-5906 william.b.bradfield@fema.dhs.gov
State NFIP/CTP Office:
FEMA Region 3: