## Slide 1
Kurt Donaldson & Frank LaFone
WV DOT GIS DAY – November 2021

## Slide 2
WV Trail Inventory
Trail Inventory and Applications

## Slide 3
WV Trail Inventory
https://www.mapwv.gov/Trails

## Slide 4
WV Trail Inventory
Chart: Land Trails (miles)
| Non-Motorized | Motorized
Total Distance (Mi) | 3959 | 706
 | Non-Motorized | Motorized | Sum
Total Number | 3,373 | 430 | 3,803
Total Distance (Mi) | 3,959 | 706 | 4,665
Chart: Water Trails (miles)
| Flatwater | Whitewater
Total Distance (Mi) | 1241 | 2105
 | Flatwater | Whitewater | Sum
Total Number | 22 | 275 | 297
Total Distance (Mi) | 1,241 | 2,105 | 3,346
LAND TRAILS
WATER TRAILS
Non-Motorized
Motorized
September 2021

## Slide 5
Land Trails

## Slide 6
Rail-Trails (n=89)

## Slide 7
Water Trails
Verifying Flatwater Trails designated by WV DOT Recreational Trail Advisory Board

## Slide 8
WVRTP Official Designation
Tim Sedosky is the current contact at DOH for the WV Recreational Trails Program.
Bill Currey, Chair, Flatwater Trails Commission, co-founder and chairman of nonprofit Coal River Group
The commission was created by the West Virginia Legislature in 2020 to support a growing demand for water-based trails in West Virginia.
Flatwater Trails

## Slide 9
Flatwater Trails – Fishing Regulations
WVDNR is using the Statewide Trail Inventory to report Flatwater Trails for WV DNR Fishing Regulations
<< Trail Geodatabase Update >> trailSurface = Water for "Float Trips" but added trailSurface = Flatwater for official "Water Trails"
Updating Page 19 of the WV DNR Fishing Regulations
Jessica Perkins, GISP
GIS & Technical Support Program Manager
Wildlife Resources Section, WVDNR

## Slide 10
WV DNR Flatwater Trails Map
Revised Flatwater Trails Map for WVD NR Fishing Regulations (Page 19)

## Slide 11
Standalone Trail Mobile Application
Start Screen
Offline Trails List
Offline Maps by State Parks

## Slide 12
Trail Mobile Application
Normal Map Display
Identify Individual Trails and Showing Attributes
Offline Maps Use Same Data As Online Map

## Slide 13
Trail Mobile Application
Measuring Distances (miles or feet)
Legend View – layers can be turned on/off

## Slide 14
Trail Mobile Application
Online Map – Connects To Same Server As Web Map
Same Attribute Display as Web Map

## Slide 15: WV DOT Scanning Project

## Slide 16
Improved Management and Archival System
  Electronic database manages the plan sets and associated documents
  Eliminates lost drawings, misfiled drawings, and deterioration of drawings
  Long-term digital storage integrated with ProjectWise content management system
  Consolidates record plan sets in one location in digital database
    Engineering plans, right of way plans, shop drawings, bridge plans, and roadway plans stored in multiple physical locations
Faster and Easier Access to Drawings
  By anyone, at any time, from anywhere.
  Improved document accessibility for both internal and external users
  Access by non-spatial or spatial map queries
WV DOT Plan Scanning Project

## Slide 17
WV DOT Plan Scanning Project

## Slide 18
Developing the project key
Transmittal Sheet

## Slide 19: WV DOT Scanning Project
Scanning
Scanning
Scanning
Image Processing
Scanning and Processing

## Slide 20
Highway Plans Locator
https://www.mapwv.gov/dotplans
Plan sets range in date between 1900 and 2014

## Slide 21
Online Highway Plans Locator
Detailed Record
Map It View
Non-Spatial and Spatial Searches

## Slide 22: Microsoft SQL Server & Enterprise ArcGIS Geodatabase
System Design

## Slide 23: Microsoft SQL Server & Enterprise ArcGIS Geodatabase
Multi-user ability
Used for recording scanning activity
Supports web feature mapping and image services
Updates are made automatically; not necessary to re-publish ArcGIS services in order to add new scan rasters
Backups are run using SQL Server Agent process
Geodatabase contains 3 primary objects
  Raster mosaic as source of image service
  Feature class of map footprints
  Database view for published plans and web-based query interface
Python scripts automate processes
  Renaming files
  Calculate map extents
  Copying GeoTiffs to publication folder
  Building raster mosaic
  Building footprints
System Features

## Slide 24
Scanning progress report for November 2021
Scanning Progress

## Slide 25
Change Detection and Conflation
WV DOT-SAMS Road Conflation
Pilot to integrate Statewide Address and Mapping and WV DOT roads

## Slide 26
Other Projects
Other Projects

## Slide 27
Statewide Flood Risk Assessment
Flood Vulnerability Risk Assessment
Greenbrier
Pocahontas
Webster
Nicholas
Fayette
Milestone: Statewide Inventory of Structures in 100-Yr Floodplain

## Slide 28
Transportation Flood Models
Roads
Railroads
Bridges

## Slide 29
Transportation Infrastructure Impacted by 100-Year Flood
Sample Flood Hazard Map on Transportation Infrastructure
WATER DEPTH | VEHICLES
<= 1 foot | A foot of water will float many vehicles.
1 – 3 feet of water | Two feet of water will carry away most vehicles. Three feet of water will easily float a bus.
> 3 feet | All vehicles incur substantial water damage and can be carried away by flood waters.
WATER DEPTH | RESCUE RESPONSE
<= 1 foot | Response focused on those who need additional assistance.
1 – 3 feet of water | A high-water vehicle rescue limit is about 3 feet.
> 3 feet | Boats and helicopters are required to perform high water rescues when water depths exceed three feet. The risk to people increases with higher water velocities and flood depths.
Jefferson County, West Virginia

## Slide 30
Landslide Susceptibility

## Slide 31
Landslide Susceptibility Maps
April 2020 Landslide
Wood County
Higher Risk

## Slide 32
Landslide Susceptibility Maps
https://www.youtube.com/watch?v=vWSUWKeoKNo
2020 Landslide (Mercer County)

## Slide 33
Reference Layers
Reference Layers
Elevation (FEMA purchase)
Aerial Imagery (Local Counties)
E-911 Addresses (WV EMD)
Parcels / Assessment Records (WV Property Tax)
Building Footprints (Computer Generated?)
9/2021 Update

## Slide 34
State Contracts for GIS Development
GIS Data Development: Parcels, E-911 Addresses, & Aerial Imagery

## Slide 35
Spatial Reference Layers
Elevation Update

## Slide 36
Elevation (High Resolution)
Statewide FEMA Elevation LiDAR QL2
  1-foot contours; 1-meter resolution Digital Elevation Model (DEM)
  Download from https://data.wvgis.wvu.edu/elevation/
Elevation Map Services (MapWV.gov) or WV Flood Tool Viewer
  Statewide 1-meter Digital Elevation Model
  Statewide 1-meter Hillshade (grayscale 3D representation of the surface)
  1-ft and 2-ft Contours cached to 1:282 Map Scale (computer caching ongoing)
Updated Source Elevation Metadata https://www.mapwv.gov/lidar-metadata
Milestone: Statewide QL2 LiDAR obtained

## Slide 37
Statewide Elevation Layers
Layer | Source | Coverage
SAMB | 2003 SAMB, 3-meter, 10-foot contours | Statewide
Lidar | Lidar, 2-foot or 1-foot contours | Select Areas
Elevation Grids, Hillshade Grids, Contours, used for Flood Depths, Imagery Orthorectification
SAMB ELEVATION
LIDAR ELEVATION
WVGISTC LiDAR Hillshade

## Slide 38
Statewide Hillshade Basemap Product
A hillshade is a grayscale 3D representation of the surface
Hillshade Basemap

## Slide 39
High Resolution Contours
New FEMA LiDAR-Derived Contours are 10x better than 2003 Statewide Elevation Data Set
SAMB Elevation 10 FT Contours
FEMA LiDAR 1 FT Contours

## Slide 40
Statewide Hillshade Basemap Product
A hillshade is a grayscale 3D representation of the surface
Hillshade Basemap

## Slide 41
Ground Elevation: 1-ft. Contours
1-FOOT CONTOUR ELEVATION VALUE OF 600 FEET MATCHES 1-METER GRID SURFACE ELEVATION OF 600 FEET DISPLAYED IN QUERY RESULTS PANEL
https://www.mapwv.gov/flood/map/?wkid=102100&x=-9177701&y=4611497&l=13&v=1
FEMA LiDAR-Derived Products: 1-Meter DEM and 1-Foot Contours
Elevation: 600 ft.
Source: FEMA 2018
1-ft Contours Display at two Highest Zoom Levels (1:564 and 1:282 Map Scales)
600 ft.
Make Contour Lines visible under REFERENCE LAYERS
1-foot contours published for 10 counties

## Slide 42
Ground Elevation: 1-ft. Contours
1-FOOT CONTOUR ELEVATION VALUE OF 2390 FEET MATCHES 1-METER GRID SURFACE ELEVATION OF 2390 FEET DISPLAYED IN QUERY RESULTS PANEL
FEMA LiDAR-Derived Products: 1-Meter DEM and 1-Foot Contours
Elevation: 2390 ft.
Source: FEMA 2016
1-ft Contours Display at two Highest Zoom Levels (1:564 and 1:282 Map Scales)
Contour Elevation: 2390 ft.
High-resolution aerial imagery and elevation contours cached at 15 map level scales from 1: 4,622,324 to 1:282
1:282
Map Scale

## Slide 43
FEMA Purchased LiDAR Coverage
FEMA has purchased $10 million in QL2 LiDAR for entire state
Quality 2 (QL2) LiDAR support 1-foot contours
https://www.mapwv.gov/lidar-metadata
LiDAR captured 2012-20 time frame

## Slide 44
Spatial Reference Layers
Aerial Imagery Update

## Slide 45
New Aerial Imagery
2018 USDA National Agriculture Imagery Program (NAIP) 2-ft pixel resolution. Statewide Coverage. 2020 NAIP Coverage?
2018-22 County Leaf-Of Aerial Imagery (Statewide Contract)
Imagery can vary greatly in resolution. Pixel resolution refers to the actual distance on the ground that each pixel represents in the orthophotography. For example, four-inch pixel resolution means that each pixel in the image covers four inches on the ground.
Over 30 Counties have tapped into the State Aerial Imagery Contract supported by the Hazard Mitigation Grant for the acquisition of 2019-22 leaf-off imagery. Most counties were captured at 4-inch resolution. Imagery resides in the public domain.
Milestone: Replaced all of 2010-12 Sheriffs Imagery with current Local Imagery

## Slide 46
County Aerial Imagery (2021)
Year | Number
2010 | 3
2014 | 1
2016 | 3
2017 | 2
2018 | 19
2019 | 20
2020 | 17
2021 | 8
Ideally, leaf-off imagery should not be older than 5 years. Imagery is important for identifying at-risk structures and accurate disaster mapping.
New 2021 Imagery
Cabell
Doddridge
Marion County
Monongalia
Pendleton
Putnam
Wayne
Wetzel
Select counties for 2019-21 received funding support through HMGP grant
https://data.wvgis.wvu.edu/pub/RA/_resources/Status/CountyImageryYearAcquired.pdf

## Slide 47
Leaf-Off Aerial Imagery Web Service
2021 Harrison County Aerial Imagery
https://services.wvgis.wvu.edu/arcgis/rest/services/Imagery_BaseMaps_EarthCover/wv_imagery_WVGISTC_leaf_off_mosaic/MapServer
Counties provide leaf-off imagery
for State Imagery Web Service
Cached to 1:282 Zoom Level or Map Scale

## Slide 48
New County Leaf-Off Aerial Imagery
http://www.mapwv.gov/floodtest/?wkid=102100&x=-9176629&y=4583554&l=13&v=1
Cows in the Floodway
West Fork Twelvepole Creek, Wayne County
Choose WV Best Leaves Off Base Map
4-Inch Pixel Resolution

## Slide 49
Spatial Data Development
Parcels Update

## Slide 50
Statewide Digital Parcel File
599 Tax Districts
347 Districts
252 Corporations
WV Property Tax Division provides annual update
Milestone: In 2021 all 55 counties migrated from paper to digital tax maps

## Slide 51
Parcel Mis-Alignment Map Errors

## Slide 52
Chart: Total Visits
| 2017, Q4 | 2018, Q4 | 2019, Q4 | 2020, Q4 | 2021, Q2
Flood Tool | 28911 | 28954 | 29677 | 36395 | 43488
Parcel Viewer | 64 | 16595 | 94614 | 208558 | 241830
WV Property Applications
Detailed Property Report
WV Property Viewer www.mapwv.gov/parcel WV Property Search www.mapwv.gov/ assessment
Property Search Tool
Property Viewer
Web Visits
Parcel Property Viewer
Flood Tool

## Slide 53
Spatial Reference Layers
E-911 Addresses

## Slide 54
Statewide E-911 Addresses
Putnam County, WV
Authoritative Source for Correct Addresses is E-911 Office – NOT Tax Assessor Geodatabases

## Slide 55
County Geocoding Match Rates
Countywide match rate should be 90% or higher

## Slide 56
County Redistricting - Precincts
Voter Precinct redistricting support for County Clerk Offices
Voting Precinct 1
Voting Precinct 2
Voter Registration System recorded as Precinct 2 error instead of Precinct 1

## Slide 57
Contact Information
  WVU GIS Technical Center West Virginia University Kurt Donaldson kurt.donaldson@mail.wvu.edu, phone: (304) 293-9467
  Frank Lafone, GIS Manager Frank.LaFone@mail.wvu.edu, phone: (304) 293-9466